## Slide 1: Review
CS168, Fall 2014
Sylvia Ratnasamy
http://inst.eecs.berkeley.edu/~cs168/

## Slide 2: Logistics
Test is closed book, closed notes
Will start on time + “settling in” delay
Two two-sided “cheat sheet”, hand written
No calculators, electronic devices, etc.
  Test does not require any complicated calculation

## Slide 3: General Guidelines (1)
Exam format (tentative!)
  Similar to the midterm but between 50-75% longer
  (Q1) A set of multiple choice questions
    ordered roughly from easiest to hardest
  (Q2) Design scenarios
    ordered roughly from easiest to hardest within each scenario
  (Q3+) more traditional problem solving
    ordered from easiest to hardest
Pace yourself accordingly.

## Slide 4: General Guidelines (2)
Test based on material covered in lecture & sections from the entire semester
    Text: only to clarify details and context for the above
More emphasis on post-midterm material
    But you really can’t tackle post-midterm material without thoroughly understanding the pre-midterm material!

## Slide 5: General Guidelines (3)
Be prepared to:
  Weigh design options outside of the context we studied them in
  e.g., run BGP between datacenter sites?
  Contemplate new designs we haven’t talked about
    e.g., HTTP-like protocol built on top of UDP
  Consider the `complete picture’ (esp. Q1 and Q2)
    e.g., persistent TCP connection when my DNS server fails…
  If you’re unsure, put down your assumptions

## Slide 6: From here on…
Walk through what I expect you to know: key topics, important aspects of each
  Focus on post-midterm material; see midterm review for pre-midterm material
Just because I didn’t cover it in review doesn’t mean you don’t need to know it
  But if I covered it today, you should know it
My plan: summarize, not explain
  Stop me when you want to discuss something further!

## Slide 7: Expect a question on …
Congestion control: TCP and advanced CC
HTTP performance
E2E operation: “steps when A talks to B” (lec 18)
Wireless
Ethernet spanning tree and self learning
Datacenters

## Slide 8: TCP Congestion Control (lecture 12)
Why?
  Because a sender shouldn’t overload the network itself
  But yet, should make efficient use of available network capacity
  While sharing available capacity fairly with other flows
  And adapting to changes in available capacity
How?
  Quickly find current available capacity (slow start)
  Then adapt to changes (congestion avoidance, AIMD)
  With optimizations (fast recovery)
  Study the TCP state machine diagram from the text!

## Slide 9: TCP State Machine (partial)
slow start
congstn. avoid.
fast recovery
cwnd > ssthresh
timeout
dupACK=3
timeout
dupACK=3
new ACK
dupACK
new ACK
timeout
new ACK
dupACK
dupACK

## Slide 10: Congestion Control: Details to know
Slow Start:
  Why: discover available bandwidth from a cold start
  How: exponential increase per RTT (every ACK, cwnd = cwnd + 1)
Congestion Avoidance:
  Why: adapt to variations in available bandwidth
  How: AIMD (every ACK, cwnd = cwnd + 1/cwnd)
  Why AIMD? For fairness
Fast Recovery:
  Keeps packets “in flight” after an isolated loss (why?)
  How: artificially inflate the CWND on every duplicate ACK (for a while)

## Slide 11: Advanced CC and Fairness (lecture 14)
TCP throughput equation
  Know the equation
  Understand the implications
Max-Min Fairness / Fair queuing
  Definition, know how to calculate fair rate (e.g., HW3)
  Know pros and cons of FQ (isolation, router complexity)
Router assisted congestion control
  pros (better info.) and cons (complexity in routers)
  e.g., explicit rate allocation (RCP): basic idea + pros/cons
  e.g., explicit cong. notification (ECN) : basic idea only

## Slide 12: Application Layer (lecture 15, 16)
Domain Name System (DNS)
  What’s behind (e.g.) xyz.cs.berkeley.edu
HTTP and the Web
  What happens when you click on a link?

## Slide 13: Internet Names & Addresses
Machine addresses: e.g., 169.229.131.109
  router-usable labels for machines
  conforms to network structure (the “where”)
Machine names: e.g., inst.eecs.berkeley.edu
  human-usable labels for machines
  conforms to organizational structure (the “who”)
The Domain Name System (DNS) is how we map from one to the other

## Slide 14: Key to DNS design: Hierarchy
Three intertwined hierarchies
  Hierarchical namespace
    As opposed to original flat namespace
  Hierarchically administered
    As opposed to centralized
  (Distributed) hierarchy of servers
    As opposed to centralized storage

## Slide 15: Things to know about DNS
Steps in resolving a DNS request
  from the viewpoint of three different hierarchies
  make sure you can walk through the sequence of messages exchanged between different servers
Role of caching
  impact on performance, availability, consistency
  repeat above walk-through with “cold” vs. “warm” cache
Pros/cons of the design

## Slide 16: Web and HTTP
Web content is named using URLs
  URLs use DNS hostnames
  Thus, content names are tied to specific hosts
HTTP is the protocol for exchanging information
  Synchronous request/reply protocol
  Runs over TCP, Port 80
  Stateless (modulo cookies)
Client-server architecture
  server is “always on” and “well known”
  clients initiate contact to server

## Slide 17: Steps in HTTP Request/Response
Client
Server
TCP Syn
TCP syn + ack
TCP ack + HTTP GET
.
.
.
Establish
connection
Request
response
Client
request
Close connection

## Slide 18: Things to know about HTTP
Steps in HTTP request/response
Broad form of request/response messages
  only to the level of detail covered in lecture/section
  not details of request/response headers
Performance
  persistent vs. concurrent vs. pipelined connections
    why they’re needed; what performance benefit they offer
  when and how caching and replication help performance

## Slide 19: Broadcast Ethernet (Lecture 16)
Traditional Ethernet: broadcast medium
  dedicated vs. shared
Challenge with broadcast media
  Must avoid having multiple nodes speaking at once
  Otherwise, collisions lead to garbled data
  Need algorithm that determines which node can transmit
(Old) Ethernet used random access protocols
  Contrast: a priori partitioning among nodes

## Slide 20: Random Access Protocols
A node may send at any time
  Contrast: node waits for its turn
Two or more transmitting nodes  collision
  Data lost
Random access MAC protocol specifies:
  How to detect or avoid collisions
  How to recover from collisions

## Slide 21: Key Ideas of Random Access
Carrier sense
  Before sending, check if someone else is already sending data
Collision detection
  If someone else starts talking at the same time, stop
    But make sure everyone knows there was a collision!
Collision avoidance
  Explicit ACK from receiver signals (lack of) collision and impending communication
Randomness
  If you can’t talk, wait for a random time before trying again

## Slide 22: Broadcast Ethernet, CSMA/CD (lecture 16)
Things to know/understand
  why CSMA alone does not eliminate all collisions (because of nonzero propagation delay)
  That collision detection is easy in wired (broadcast) LANs but difficult in wireless LANs (hence CSMA/CA)
  That collision detection imposes a bound on max length of a wire and minimum length of frame

## Slide 23: Switched Ethernet (Lecture 17, 18)
switch
A
B
C
D
Why? Concurrent communication
  Host A can talk to C, while B talks to D
  No collisions  no need for CSMA, CD
  No constraints on link lengths, etc.

## Slide 24: Switched Ethernet (Lecture 17, 18)
What you should know about switched Ethernet
  Ethernet frame format
  Concept of framing and sentinel bits
  Ethernet addresses
  Why spanning tree and self-learning are needed
  How the spanning tree is constructed
    role of soft state
  How self-learning works
    role of caching (see HW3 problem)
  contrast style of Ethernet vs. IP addressing and routing
    with implications that follow
      scalability, plug-n-play, portability, …

## Slide 25: Switched Ethernet (Lecture 17, 18)
How? Two pieces
  Build a spanning tree
    Why? For loop-free flooding
      Why flooding?: plug-n-play
    How? Shortest path tree rooted at node with the lowest ID (MAC address)
  “Self Learning” switches
    Why? Optimization; so switches can reach destination without flooding
    How? If packet from A arrives on port X, switch learns to send packets to A via port X

## Slide 26: Naming and Discovery (Lecture 18)
What you should know
  Naming schemes at different layers (Ethernet, IP, DNS)
    format; what they represent; what role they play
  How we discover and translate between names
    DNS, ARP, DHCP
    role of broadcast, soft state and caching

## Slide 27: Naming
Application layer: URLs and domain names
  names “resources” -- hosts, content, program
Network layer: IP addresses
  host’s network location
Link layer: MAC addresses
  host identifier
Use all three for end-to-end communication!

## Slide 28: Discovery
A host is “born” knowing only its MAC address
Must discover lots of information before it can communicate with a remote host B
  what is my IP address?
  what is B’s IP address? (remote)
  what is B’s MAC address? (if B is local)
  what is my first-hop router’s address? (if B is not local)
  …

## Slide 29: ARP and DHCP
Link layer discovery protocols
Serve two functions
  Discovery of local end-hosts
    for communication between hosts on the same LAN
  Bootstrap communication with remote hosts
    what’s my IP address?
    who/where is my local DNS server?
    who/where is my first hop router?

## Slide 30: DHCP
“Dynamic Host Configuration Protocol”
A host uses DHCP to discover
  its own IP address
  its netmask
  IP address(es) for its DNS name server(s)
  IP address(es) for its first-hop “default” router(s)

## Slide 31: DHCP: operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers responds with a DHCP “offer” message
Client broadcasts a DHCP request message
Selected DHCP server responds with an ACK

## Slide 32: ARP: Address Resolution Protocol
ARP provides IP-to-MAC translation
Every host maintains an ARP table
  list of (IP address  MAC address) pairs
But: what if IP address not in the table?
  Sender broadcasts: “Who has IP address 1.2.3.156?”
  Receiver responds: “MAC address 58-23-D7-FA-20-B0”
  Sender caches result in its ARP table

## Slide 33: Key Ideas in Both ARP and DHCP
Broadcasting: used for initial bootstrap
Caching: remember the past for a while
  Store the information you learn to reduce overhead
  Key optimization for performance
Soft state: eventually forget the past
  Associate a time-to-live field with the information
  … and either refresh or discard the information
  Key for robustness

## Slide 34: Putting the pieces together (Lec 18)
Assume: `cold start’ -- nothing cached anywhere
Assume: yourDNS on a different subnet from yourDHCP
Ignore intra- and interdomain routing protocols
Google’s datacenter
Dorm
You
yourDHCP
UCB
yourDNS
R
router
Understand this!
Walk through the steps required to download www.google.com/index.html from your laptop

## Slide 35: Wireless (lecture 19)
Things you need to know:
Properties of the medium
  broadcast
     collisions happen
  but broadcast has limited range
    no concept of a “global” collision
     simultaneous transmissions are possible
  can’t receive while transmitting
    can’t detect collisions

## Slide 36: Wireless (lecture 19)
Things you need to know:
Properties of the medium
Canonical scenarios
  hidden terminal (carrier sense fails to prevent collisions)
  exposed terminal (carrier sense needlessly limits commn.)

## Slide 37: Wireless (lecture 19)
Things you need to know:
Properties of the medium
Canonical scenarios
Techniques for collision avoidance
  carrier sense
  explicit request/response (RTS/CTS)
  backoff

## Slide 38: Wireless (lecture 19)
Things you need to know:
Properties of the medium
Canonical scenarios
Techniques for collision avoidance
How to analyze a given media access protocol that uses the above techniques
  We’ll give you the protocol rules; you analyze how (and how well) data exchange proceeds
  You don’t need to memorize protocol rules
  e.g., Q7 on HW3

## Slide 39: Wireless (lecture 19)
Things you need to know:
Properties of the medium
Canonical scenarios
Techniques for collision avoidance
How to analyze a given media access protocol that uses the above techniques
Things we don’t expect you to know
  mathematical understanding of wireless signals (free space loss, interference, attenuation, etc.)
  details of specific wireless protocols (e.g., 802.11)

## Slide 40: Datacenters (lectures 20, 21)
What you should know
How and why DC networks are different (vs. WAN)
  in terms of workload, goals, characteristics
How traditional solutions fare in this environment
  e.g., IP, Ethernet, TCP
Understand Fat-Tree DC networks
  Why “fat”; how we do addressing and routing on a fat-tree
High level understanding of DC-TCP and pFabric
  mostly the “why” for the approach taken

## Slide 41: Typical datacenter architecture
Servers organized in racks
Each rack has a `Top of Rack’ (ToR) switch
An `aggregation fabric’ interconnects ToR switches
Connected to the outside via `core’ switches

## Slide 42: Typical datacenter traffic workload
“North-South traffic”
  Traffic between outside world and the datacenter
  Primarily latency sensitive
“East-West traffic”
  Traffic between machines in the datacenter
  Commn. within “big data” computations (e.g. Map Reduce)
  Throughput intensive
“Elephants and Mice”

## Slide 43: Characteristics of a datacenter network
Huge scale
Limited geographic scope
Limited heterogeneity
  regular topologies, link speeds, technologies, latencies, …
Single administrative domain
Control over network and endpoints
Control over the placement of traffic sources/sinks
Control over topology (e.g., trees/fat-trees)
Lower concern: interoperability, backward compatibility
New degrees of design freedom

## Slide 44: Fat-Tree Topologies
What: “scale out” approach to building a high bisection bandwidth network
  “high bisection BW”  high BW between servers
Why?
  Lots of east-west traffic
    (think shuffle in map-reduce)
  But traditional tree topologies expensive to scale
    (“scale up”  links near root exorbitantly expensive)
How? Topology in which each switch has many links going “up”

## Slide 45: E.g., “Fat Tree” Topology [Sigcomm’08]
All links have same (reasonable) speed and #ports
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 46: Routing / addressing on a Fat Tree
Option 1: Extend DV/LS
  With per packet/flow load balancing
  Simple, incremental, but scales poorly
Option 2: Topology-aware addressing
  IP address reflects position in the topology
  Simple, scalable, not migrateable
Option 3: SDN w/ source routing
  Centralized route calculation.; path vector as address
  Simple, scalable (as SDN), not backward compatible

## Slide 47: Datacenter Transport Designs
Know: rationale and approach at a high level only
E.g., DC-TCP
  Why? Datacenters need both high throughput and low latency but TCP isn’t good at this
  What? Incremental change to TCP to achieve both
  How?: two ideas
    react early (using ECN)
    react in proportion to the extent of congestion (by adapting CWND based on fraction of packets with ECN set)

## Slide 48: Datacenter Transport Designs
Know: rationale and approach at a high level only
E.g., pFabric
  Why? Minimizing flow completion time (FCT) is the ultimate goal but TCP isn’t good at this
    Why? Mice get stuck behind elephants  both finish late
  What? Clean-slate design for low FCT
  How?:
    Each packet has priority value set to #remaining bytes in flow
    Switches send highest priority / drop lowest priority / packet
    Loose intuition: mice finish first (approx. shortest job first sched.)

## Slide 49: IPv6 (lecture 22)
Know: see detailed post on piazza
Motivation: IPv4 address exhaustion
What IPv6 does/doesn’t change in overall architecture
Details: IPv6 address and header formats
  with rationale for changes
  and understanding of what gets simpler/harder
Basics of IP address assignment
  EUI, network-interface split, etc.
Note: unless stated otherwise, assume “IP” means “IPv4”

## Slide 50: SDN (lecture 23)
Why?: modern networks face a multitude of control requirements (access control, isolation, etc.) but we have no coherent management architecture
How?
  10,000 ft view: modularity with abstractions
  1,000 ft view: three new abstractions
    Forwarding: <match, action> rules
    Control: global view of physical network + abstract network view

## Slide 51: SDN (lecture 23)
Why?: modern networks face a multitude of control requirements (access control, isolation, etc.) but we have no coherent management architecture
How?
  10,000 ft view: modularity with abstractions
  1,000 ft view: three new abstractions
  100 ft view: decouple data and control plane
    Data plane: switches (implement/expose forwarding abstraction)
    Control plane: servers (implement physical/abstract network views)
      Runs “Network OS” that queries switches to construct global physical view
      Virtualization layer runs over NOS; translates physicalvirtual network
      Management apps highest layer; express policy on virtual view

## Slide 52: SDN (lecture 23)
Why?: modern networks face a multitude of control requirements (access control, isolation, etc.) but we have no coherent management architecture
How?
  10,000 ft view: modularity with abstractions
  1,000 ft view: three new abstractions
  100 ft view: decouple data and control plane
What you should know
    Overall idea to 100 ft. view; no details beyond Scott’s slides
    E.g., do not need to know VLANs, Traffic engg., ACLs, MPLS
    E.g., do not need to know details of NOS, OpenFlow, Virt. layer, etc

## Slide 53: Reminder: Attend the EECS Colloquium!
Software-Defined Networks and the Maturing of the Internet
Wednesday, December 3, 2014 306 Soda Hall (HP Auditorium) 4:00 - 5:00 pm
Nick McKeown
Professor of Computer Science and Electrical Engineering, Stanford

## Slide 54: Final points
  On advanced topics:
    E.g., router-assisted congestion control (RCP, RC3, ECN), datacenter designs such as DC-TCP, pFabric, SDN, IPv6
    Figure primarily in multiple choice and design questions (Q1,Q2)
    For most such questions: we’ll provide the design goals and options; your job only to analyze the design we describe
  If you look over exams from previous years, note changes
    We did not cover security
    We covered datacenters, IPv6 and SDN in more detail
  We will hold additional OHs and post review material
    Will post details on piazza

## Slide 55: Thanks & Good luck!