## Slide 1: The Camera
CS180/280A: Intro to Comp. Vision, and Comp. Photo
Angjoo Kanazawa & Alexei Efros, UC Berkeley, Fall 2023

## Slide 2: Project 1 Class Choice Award!
1st. Bryan Li:
https://inst.eecs.berkeley.edu/~cs180/fa23/upload/files/proj1/bryanli0/
2nd. Minseok Son:
https://inst.eecs.berkeley.edu/~cs180/fa23/upload/files/proj1/tom5079/
3rd. Jeffrey Tan
https://inst.eecs.berkeley.edu/~cs180/fa23/upload/files/proj1/tanjeffreyz02/

## Slide 3: Image Formation
Digital Camera
The Eye
Film

## Slide 4: How do we see the world?
Let’s design a camera
  Idea 1: put a piece of film in front of an object
  Do we get a reasonable image?
Slide by Steve Seitz

## Slide 5: Pinhole camera
Add a barrier to block off most of the rays
  This reduces blurring
  The opening known as the aperture
  How does this transform the image?
Slide by Steve Seitz
Notes: It gets inverted

## Slide 6: Camera Obscura: the pre-camera
First Idea: Mo-Ti, China (470-390 BC)
First build: Al Hacen, Iraq/Egypt (965-1039 AD)
Drawing aid for artists: described by Leonardo da Vinci (1452-1519)
Gemma Frisius, 1558
Camera Obscura near Cliff House

## Slide 7: 8-hour exposure (Abelardo Morell)
http://www.abelardomorell.net/books/books_m02.html
From Grand Images Through a Tiny Opening, Photo District News, February 2005

## Slide 9: “Trashcam” Project
http://petapixel.com/2012/04/18/german-garbage-men-turn-dumpsters-into-giant-pinhole-cameras/

## Slide 10: Pinhole cameras everywhere
Tree shadow during a solar eclipse
photo credit: Nils van der Burg http://www.physicstogo.org/index.cfm
Slide by Steve Seitz
© Trina Singley

## Slide 11: Accidental pinhole cameras
A. Torralba and W. Freeman, Accidental Pinhole and Pinspeck Cameras, CVPR 2012

## Slide 12: Torralba and Freeman, CVPR’12

## Slide 16: Pinspeck Camera: the anti-pinhole

## Slide 17: Pinhole camera model
Pinhole model:
  Captures pencil of rays – all rays through a single point
  The point is called Center of Projection (COP)
  The image is formed on the Image Plane
  Effective focal length d is distance from COP to Image Plane
Slide by Steve Seitz

## Slide 18: Modeling projection
The coordinate system
  We will use the pin-hole model as an approximation
  Put the optical center (Center Of Projection) at the origin
  Put the image plane (Projection Plane) in front of the COP
    Why?
  The camera looks down the negative z axis
    we need this if we want right-handed-coordinates
Slide by Steve Seitz
Notes: This way the image is right-side-up

## Slide 19: Modeling projection
Projection equations
  Compute intersection with PP of ray from (x,y,z) to COP
  Derived using similar triangles (on board)
  We get the projection by throwing out the last coordinate:
Slide by Steve Seitz

## Slide 20: Dimensionality Reduction Machine (3D to 2D)
Figures © Stephen E. Palmer, 2002
3D world
2D image
But there is a problem…

## Slide 21: Emission Theory of Vision
“For every complex problem there is an answer that is clear, simple, and wrong.”
-- H. L. Mencken
Supported by:
Empedocles
Plato
Euclid (kinda)
Ptolemy
…
50% of US college students*
*http://www.ncbi.nlm.nih.gov/pubmed/12094435?dopt=Abstract
Eyes send out “feeling rays” into the world

## Slide 22: How we see the world
Figures © Stephen E. Palmer, 2002
3D world
2D image

## Slide 23: How we see the world
3D world
2D image
Painted
backdrop

## Slide 24: Fooling the eye

## Slide 25: Fooling the eye
Making of 3D sidewalk art: http://www.youtube.com/watch?v=3SNYtd0Ayt0

## Slide 26: Dimensionality Reduction Machine (3D to 2D)
3D world
2D image
Why did evolution opt for such strange solution?
  Nice to have a passive, long-range sensor
  Can get 3D with stereo or by moving around, plus experience

## Slide 27: Dimensionality Reduction Machine (3D to 2D)
Figures © Stephen E. Palmer, 2002
3D world
2D image
What have we lost?
  Angles
  Distances (lengths)

## Slide 28: Funny things happen…

## Slide 29: Parallel lines aren’t…
Figure by David Forsyth

## Slide 30: Exciting New Study!

## Slide 31: Lengths can’t be trusted...
Figure by David Forsyth
B’
C’
A’

## Slide 32: …but humans adopt!
http://www.michaelbach.de/ot/sze_muelue/index.html
Müller-Lyer Illusion
We don’t make measurements in the image plane

## Slide 33: Other projections: Orthographic
Special case of perspective projection
  Distance from the COP to the PP is infinite
  Also called “parallel projection”
  x’ = x
  y’ = y
Image
World
Slide by Steve Seitz

## Slide 34: Scaled Orthographic or “Weak Perspective”

## Slide 35: Scaled Orthographic or “Weak Perspective”

## Slide 36: Spherical Projection
What if PP is spherical with center at COP?
In spherical coordinates, projection is trivial:
(q,f) = (q,f,d)
Note: doesn’t depend on focal length f!

## Slide 37: Building a real camera

## Slide 38: Another way to make pinhole camera
http://www.debevec.org/Pinhole/
Why so
blurry?

## Slide 39: Shrinking the aperture
Why not make the aperture as small as possible?
  Less light gets through
  Diffraction effects…
Less light gets through
Slide by Steve Seitz

## Slide 40: Shrinking the aperture

## Slide 41: The reason for lenses
Slide by Steve Seitz

## Slide 42: Replacing pinholes with lenses
Photography,
London et al

## Slide 43: Focus

## Slide 44: Focus and Defocus
A lens focuses light onto the film
  There is a specific distance at which objects are “in focus”
    other points project to a “circle of confusion” in the image
  Changing the shape of the lens changes this distance
“circle of
confusion”
Slide by Steve Seitz

## Slide 45: Thin lenses
Thin lens equation:
  Any object point satisfying this equation is in focus
  What is the shape of the focus region?
  Thin lens applet: http://www.phy.ntnu.edu.tw/java/Lens/lens_e.html (by Fu-Kwun Hwang )
Slide by Steve Seitz
Notes: focal point is where all the rays meet through the lens, the distance bwetetn the focal point and the lens is the focal length with lenses.

## Slide 46: Varying Focus
Ren Ng

## Slide 47: Varying Focus

## Slide 48: Depth Of Field

## Slide 49: Depth of Field
http://www.cambridgeincolour.com/tutorials/depth-of-field.htm
Notes: DoF = regions that look like are in focus (not a single plane)

## Slide 50: Aperture controls Depth of Field
Changing the aperture size affects depth of field
  A smaller aperture increases the range in which the object is approximately in focus
  But small aperture reduces amount of light – need to increase exposure
Notes: phone cameras all have cheap lens and small aperture (everything is kind of in focus, expensive cameras give you stuf like above)

## Slide 51: F-number: focal length / aperture diameter

## Slide 52: Varying the aperture
Wide apeture = small DOF
Narrow apeture = large DOF

## Slide 53: Nice Depth of Field effect

## Slide 54: Field of View (Zoom)

## Slide 55: Field of View (Zoom)

## Slide 56: Field of View (Zoom) = Cropping

## Slide 57: FOV depends of Focal Length
f
Smaller FOV = larger Focal Length
f

## Slide 58: Expensive toys…

## Slide 59: Field of View / Focal Length
Large FOV / small f
+ Camera close to car
Small FOV / large f
+ Camera far from the car
Notes: IS the left Wider FOV or Narrow? FOV is just zoom (cropping), but this effect is two things happening at the same time, you move back (these images don’t share the same center of projection)

## Slide 60
From Zisserman & Hartley

## Slide 61: Focal length / distance in portraiture
Notes: exaggerated perspective effects on the nose, step back and zoom in.

## Slide 62: Dolly Zoom (“Vertigo Shot”)
http://filmmakermagazine.com/83872-hitchcock-to-scorcese-47-years-of-the-dolly-zoom/#.VBNtn_ldVac

## Slide 63: Exposure

## Slide 64: Shutter Speed
http://en.wikipedia.org/wiki/Shutter_speed
Notes: Blur in time

## Slide 65: Exposure: shutter speed vs. aperture
Notes: why pick one over the other? When is the right preferable over the other? wide DoF which one do you want? (A: smaller aperture), if things are moving, then you open it up and won’t need to wait as much

## Slide 66
Notes: very long apertureso much that the earth moved (1hr~)

## Slide 67: Fun with slow shutter speeds
Photos by Fredo Durand

## Slide 68: More fun
http://vimeo.com/14958082

## Slide 69: Lens Flaws

## Slide 70: Lens Flaws: Chromatic Aberration
Dispersion: wavelength-dependent refractive index
  (enables prism to spread white light beam into rainbow)
Modifies ray-bending and lens focal length: f()
color fringes near edges of image
Corrections: add ‘doublet’ lens of flint glass, etc.

## Slide 71: Chromatic Aberration
Slide by Carl Doersch

## Slide 72: Chromatic Aberration
Near Lens Center
Near Lens Outer Edge

## Slide 73: Radial Distortion (e.g. ‘Barrel’ and ‘pin-cushion’)
  straight lines curve around the image center

## Slide 74: Radial Distortion
Radial distortion of the image
  Caused by imperfect lenses
  Deviations are most noticeable for rays that pass through the edge of the lens
No distortion
Pin cushion
Barrel

## Slide 75: Radial Distortion