## Slide 1: Convolution and Image Derivatives
CS194: Intro to Comp. Vision and Comp. Photo
Alexei Efros, UC Berkeley, Fall 2021

## Slide 2: Moving Average
Can add weights to our moving average
Weights […, 0, 1, 1, 1, 1, 1, 0, …] / 5

## Slide 3: Weighted Moving Average
bell curve (gaussian-like) weights […, 1, 4, 6, 4, 1, …]

## Slide 4: Moving Average In 2D
What are the weights H?
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Slide by Steve Seitz
Notes: ones, divide by 9

## Slide 5: Gaussian filtering
A Gaussian kernel gives less weight to pixels further from the center of the window
This kernel is an approximation of a Gaussian function:
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 2 | 1
2 | 4 | 2
1 | 2 | 1
Slide by Steve Seitz

## Slide 6: Mean vs. Gaussian filtering
Slide by Steve Seitz

## Slide 7
Weight contributions of neighboring pixels by nearness
0.003 0.013 0.022 0.013 0.003
0.013 0.059 0.097 0.059 0.013
0.022 0.097 0.159 0.097 0.022
0.013 0.059 0.097 0.059 0.013
0.003 0.013 0.022 0.013 0.003
5 x 5,  = 1
Slide credit: Christopher Rasmussen
Important filter: Gaussian
Notes: 7

## Slide 8: Gaussian Kernel
Standard deviation : determines extent of smoothing
Source: K. Grauman
σ = 2 with 30 x 30 kernel
σ = 5 with 30 x 30 kernel

## Slide 9: Gaussian filters
= 30 pixels
= 1 pixel
= 5 pixels
= 10 pixels

## Slide 10: Choosing kernel width
The Gaussian function has infinite support, but discrete filters use finite kernels
Source: K. Grauman

## Slide 11: Practical matters
How big should the filter be?
Values at edges should be near zero
Rule of thumb for Gaussian: set filter half-width to about 3 σ
Side by Derek Hoiem
Notes: 11

## Slide 12: Cross-correlation vs. Convolution
cross-correlation:
A convolution operation is a cross-correlation where the filter is flipped both horizontally and vertically before being applied to the image:
It is written:
Convolution is commutative and associative
Slide by Steve Seitz

## Slide 13: Convolution
Adapted from F. Durand

## Slide 14: Convolution is nice!
Notation:
Convolution is a multiplication-like operation
  commutative
  associative
  distributes over addition
  scalars factor out
  identity: unit impulse e = […, 0, 0, 1, 0, 0, …]
Conceptually no distinction between filter and signal
Usefulness of associativity
  often apply several filters one after another: (((a * b1) * b2) * b3)
  this is equivalent to applying one filter: a * (b1 * b2 * b3)

## Slide 15: Gaussian and convolution
Removes “high-frequency” components from the image (low-pass filter)
Convolution with self is another Gaussian
  Convolving twice with Gaussian kernel of width = convolving once with kernel of width
Source: K. Grauman
*
=
Notes: Linear vs. quadratic in mask size

## Slide 16: Image half-sizing
This image is too big to
fit on the screen. How
can we reduce it?
How to generate a half-
sized version?

## Slide 17: Image sub-sampling
Throw away every other row and column to create a 1/2 size image
  - called image sub-sampling
1/4
1/8
Slide by Steve Seitz

## Slide 18: Image sub-sampling
1/4 (2x zoom)
1/8 (4x zoom)
Aliasing! What do we do?
1/2
Slide by Steve Seitz

## Slide 19: Sampling an image
Examples of GOOD sampling

## Slide 20: Undersampling
Examples of BAD sampling -> Aliasing

## Slide 21: Gaussian (lowpass) pre-filtering
G 1/4
G 1/8
Gaussian 1/2
Solution: filter the image, then subsample
  Filter size should double for each ½ size reduction. Why?
Slide by Steve Seitz

## Slide 22: Subsampling with Gaussian pre-filtering
G 1/4
G 1/8
Gaussian 1/2
Slide by Steve Seitz

## Slide 23: Compare with...
1/4 (2x zoom)
1/8 (4x zoom)
1/2
Slide by Steve Seitz

## Slide 24: More Gaussian pre-filtering

## Slide 25: Iterative Gaussian (lowpass) pre-filtering
G 1/4
G 1/8
Gaussian 1/2
filter the image, then subsample
  Filter size should double for each ½ size reduction. Why?
  How can we speed this up?
Slide by Steve Seitz

## Slide 26: Image Pyramids
Known as a Gaussian Pyramid [Burt and Adelson, 1983]
  In computer graphics, a mip map [Williams, 1983]
  A precursor to wavelet transform
Slide by Steve Seitz

## Slide 27
A bar in the big images is a hair on the zebra’s nose; in smaller images, a stripe; in the smallest, the animal’s nose
Figure from David Forsyth

## Slide 28: Gaussian pyramid construction
filter mask
Repeat
  Filter
  Subsample
Until minimum resolution reached
  can specify desired number of levels (e.g., 3-level pyramid)
The whole pyramid is only 4/3 the size of the original image!
Slide by Steve Seitz

## Slide 29: What are they good for?
Improve Search
  Search over translations
    Classic coarse-to-fine strategy
    Project 1!
  Search over scale
    Template matching
    E.g. find a face at different scales

## Slide 30
Taking derivative by convolution

## Slide 31: Partial derivatives with convolution
Remember:
Image is function f(x,y)
Approximate:
Another one:
-1
1
-1
0
1

## Slide 32: Partial derivatives of an image
Which shows changes with respect to x?
-1 1
1 -1
or
-1 1

## Slide 33: Image gradient
The gradient points in the direction of most rapid increase in intensity
The gradient of an image:
The gradient direction is given by
Source: Steve Seitz
The edge strength is given by the gradient magnitude
How does this direction relate to the direction of the edge?
Notes: give definition of partial derivative: lim h->0 [f(x+h,y) – f(x,y)]/h

## Slide 34: Image Gradient

## Slide 35: Partial Derivatives

## Slide 36: Gradient magnitude

## Slide 37: Gradient Orientation
atan2(dy,dx)
I’m making the lightness equal to gradient magnitude
Source: D. Fouhey

## Slide 38: Image Gradient
Now I’m showing all the gradients
Source: D. Fouhey

## Slide 39: Image Gradient
Why is there structure at 1 and not at 2?
1
2
Source: D. Fouhey

## Slide 40: Effects of noise
Consider a single row or column of the image
  Plotting intensity as a function of position gives a signal
Where is the edge?
Source: S. Seitz
Notes: How to fix?

## Slide 41: Solution: smooth first
To find edges, look for peaks in
f
g
f * g
Source: S. Seitz

## Slide 42: Noise in 2D
Noisy Input
Ix via [-1,01]
Zoom
Source: D. Fouhey

## Slide 43: Noise + Smoothing
Smoothed Input
Ix via [-1,01]
Zoom
Source: D. Fouhey

## Slide 44: Derivative theorem of convolution
This saves us one operation:

## Slide 45: Derivative of Gaussian filter
* [1 -1] =

## Slide 46: Derivative of Gaussian filter
Which one finds horizontal/vertical edges?
x-direction
y-direction

## Slide 47: Compare to classic derivative filters
Source: K. Grauman

## Slide 48: Filtering: practical matters
What is the size of the output?
(MATLAB) filter2(g, f, shape) or conv2(g,f,shape)
  shape = ‘full’: output size is sum of sizes of f and g
  shape = ‘same’: output size is same as f
  shape = ‘valid’: output size is difference of sizes of f and g
f
g
g
g
g
f
g
g
g
g
f
g
g
g
g
full
same
valid
Source: S. Lazebnik
Notes: 48

## Slide 49: Practical matters
What about near the edge?
  the filter window falls off the edge of the image
  need to extrapolate
  methods:
    clip filter (black)
    wrap around
    copy edge
    reflect across edge
Source: S. Marschner
Notes: 49

## Slide 50: Low Pass vs. High Pass filtering
-
Image
Smoothed
=
Details

## Slide 51: Filtering – Sharpening
+α
Image
Details
=
“Sharpened” α=1

## Slide 52: Filtering – Sharpening
=
+α
Image
Details
“Sharpened” α=0

## Slide 53: Filtering – Sharpening
=
+α
Image
Details
“Sharpened” α=2

## Slide 54: Filtering – Sharpening
=
+α
Image
Details
“Sharpened” α=0

## Slide 55: Filtering – Extreme Sharpening
=
+α
Image
Details
“Sharpened” α=10

## Slide 56: Unsharp mask filter
Gaussian
unit impulse
Laplacian of Gaussian
image
blurred image
unit impulse (identity)
Notes: f + a(f - f * g) = (1+a)f-af*g = f*((1+a)e-g)