## Slide 1: CS252 Graduate Computer Architecture Fall 2015 Lecture 6: Out-of-Order Processors
Krste Asanovic
krste@eecs.berkeley.edu
http://inst.eecs.berkeley.edu/~cs252/fa15

## Slide 2: Supercomputers
Definitions of a supercomputer:
Fastest machine in world at given task
A device to turn a compute-bound problem into an I/O bound problem
Any machine costing $30M+
Any machine designed by Seymour Cray
CDC6600 (Cray, 1964) regarded as first supercomputer

## Slide 3: CDC 6600 Seymour Cray, 1963
A fast pipelined machine with 60-bit words
  128 Kword main memory capacity, 32 banks
Ten functional units (parallel, unpipelined)
  Floating Point: adder, 2 multipliers, divider
  Integer: adder, 2 incrementers, ...
Hardwired control (no microcoding)
Scoreboard for dynamic scheduling of instructions
Ten Peripheral Processors for Input/Output
  a fast multi-threaded 12-bit integer ALU
Very fast clock, 10 MHz (FP add in 4 clocks)
>400,000 transistors, 750 sq. ft., 5 tons, 150 kW, novel freon-based technology for cooling
Fastest machine in world for 5 years (until 7600)
  over 100 sold ($7-10M each)

## Slide 4: CDC 6600: A Load/Store Architecture
Separate instructions to manipulate three types of reg.
  8x60-bit data registers (X)
  8x18-bit address registers (A)
  8x18-bit index registers (B)
All arithmetic and logic instructions are register-to-register
Only Load and Store instructions refer to memory!
Touching address registers 1 to 5 initiates a load
6 to 7 initiates a store
        - very useful for vector operations
opcode i j k Ri  Rj op Rk
opcode i j disp Ri M[Rj + disp]
6
3
3
3
6
3
3
18

## Slide 5: CDC 6600: Datapath
Address Regs Index Regs
8 x 18-bit 8 x 18-bit
Operand Regs
8 x 60-bit
Inst. Stack
8 x 60-bit
IR
10 Functional
Units
Central
Memory
128K words,
32 banks,
1µs cycle
result
addr
result
operand
operand
addr

## Slide 6: CDC6600 ISA designed to simplify high-performance implementation
Use of three-address, register-register ALU instructions simplifies pipelined implementation
  Only 3-bit register specifier fields checked for dependencies
  No implicit dependencies between inputs and outputs
Decoupling setting of address register (Ar) from retrieving value from data register (Xr) simplifies providing multiple outstanding memory accesses
  Software can schedule load of address register before use of value
  Can interleave independent instructions inbetween
CDC6600 has multiple parallel but unpipelined functional units
  E.g., 2 separate multipliers
Follow-on machine CDC7600 used pipelined functional units
  Foreshadows later RISC designs

## Slide 7: CDC6600: Vector Addition
    B0  - n
loop: JZE B0, exit
    A0  B0 + a0 load X0
    A1  B0 + b0 load X1
    X6  X0 + X1
    A6  B0 + c0 store X6
    B0  B0 + 1
    jump loop
Ai = address register
Bi = index register
Xi = data register

## Slide 8: CDC6600 Scoreboard
Instructions dispatched in-order to functional units provided no structural hazard or WAW
  Stall on structural hazard, no functional units available
  Only one pending write to any register
Instructions wait for input operands (RAW hazards) before execution
  Can execute out-of-order
Instructions wait for output register to be read by preceding instructions (WAR)
  Result held in functional unit until register free

## Slide 9
[© IBM]

## Slide 10: IBM 360/91 Floating-Point Unit R. M. Tomasulo, 1967
Mult
1
1
2
3
4
5
6
load
buffers
(from
memory)
1
2
3
4
Adder
1
2
3
Floating-Point
Regfile
store buffers
(to memory)
...
instructions
Common bus ensures that data is made available immediately to all the instructions waiting for it.
Match tag, if equal, copy value & set presence “p”.
Distribute
reservation stations
to
functional
units
< tag, result >
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
2
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data

## Slide 11: Out-of-Order Fades into Background
Out-of-order processing implemented commercially in 1960s, but disappeared again until 1990s as two major problems had to be solved:
Precise traps
  Imprecise traps complicate debugging and OS code
  Note, precise interrupts are relatively easy to provide
Branch prediction
  Amount of exploitable instruction-level parallelism (ILP) limited by control hazards
Also, simpler machine designs in new technology beat complicated machines in old technology
  Big advantage to fit processor & caches on one chip
  Microprocessors had era of 1%/week performance scaling

## Slide 12: Separating Completion from Commit
Re-order buffer holds register results from completion until commit
  Entries allocated in program order during decode
  Buffers completed values and exception state until in-order commit point
  Completed values can be used by dependents before committed (bypassing)
  Each entry holds program counter, instruction type, destination register specifier and value if any, and exception status (info often compressed to save hardware)
Memory reordering needs special data structures
  Speculative store address and data buffers
  Speculative load address and data buffers

## Slide 13: In-Order Commit for Precise Traps
In-order instruction fetch and decode, and dispatch to reservation stations inside reorder buffer
Instructions issue from reservation stations out-of-order
Out-of-order completion, values stored in temporary buffers
Commit is in-order, checks for traps, and if none updates architectural state
Fetch
Decode
Execute
Commit
Reorder Buffer
In-order
In-order
Out-of-order
Trap?
Kill
Kill
Kill
Inject handler PC

## Slide 14: Phases of Instruction Execution
Fetch: Instruction bits retrieved from instruction cache.
I-cache
Fetch Buffer
Issue Buffer
Functional Units
Architectural
State
Execute: Instructions and operands issued to functional units. When execution completes, all results and exception flags are available.
Decode: Instructions dispatched to appropriate issue buffer
Result Buffer
Commit: Instruction irrevocably updates architectural state (aka “graduation”), or takes precise trap/interrupt.
PC
Commit
Decode/Rename

## Slide 15: In-Order versus Out-of-Order Phases
Instruction fetch/decode/rename always in-order
  Need to parse ISA sequentially to get correct semantics
  Proposals for speculative OoO instruction fetch, e.g., Multiscalar. Predict control flow and data dependencies across sequential program segments fetched/decoded/executed in parallel, fixup if prediction wrong
Dispatch (place instruction into machine buffers to wait for issue) also always in-order
  Some use “Dispatch” to mean issue, but not in these lectures

## Slide 16: In-Order Versus Out-of-Order Issue
In-order issue:
  Issue stalls on RAW dependencies or structural hazards, or possibly WAR/WAW hazards
  Instruction cannot issue to execution units unless all preceding instructions have issued to execution units
Out-of-order issue:
  Instructions dispatched in program order to reservation stations (or other forms of instruction buffer) to wait for operands to arrive, or other hazards to clear
  While earlier instructions wait in issue buffers, following instructions can be dispatched and issued out-of-order

## Slide 17: In-Order versus Out-of-Order Completion
All but the simplest machines have out-of-order completion, due to different latencies of functional units and desire to bypass values as soon as available
Classic RISC 5-stage integer pipeline just barely has in-order completion
  Load takes two cycles, but following one-cycle integer op completes at same time, not earlier
  Adding pipelined FPU immediately brings OoO completion

## Slide 18: In-Order versus Out-of-Order Commit
In-order commit supports precise traps, standard today
  Some proposals to reduce the cost of in-order commit by retiring some instructions early to compact reorder buffer, but this is just an optimized in-order commit
Out-of-order commit was effectively what early OoO machines implemented (imprecise traps) as completion irrevocably changed machine state
  i.e., complete == commit in these machines

## Slide 19: OoO Design Choices
Where are reservation stations?
  Part of reorder buffer, or in separate issue window?
  Distributed by functional units, or centralized?
How is register renaming performed?
  Tags and data held in reservation stations, with separate architectural register file
  Tags only in reservation stations, data held in unified physical register file

## Slide 20: “Data-in-ROB” Design (HP PA8000, Pentium Pro, Core2Duo, Nehalem)
Managed as circular buffer in program order, new instructions dispatched to free slots, oldest instruction committed/reclaimed when done (“p” bit set on result)
Tag is given by index in ROB (Free pointer value)
In dispatch, non-busy source operands read from architectural register file and copied to Src1 and Src2 with presence bit “p” set. Busy operands copy tag of producer and clear “p” bit.
Set valid bit “v” on dispatch, set issued bit “i” on issue
On completion, search source tags, set “p” bit and copy data into src on tag match. Write result and exception flags to ROB.
On commit, check exception status, and copy result into architectural register file if no trap.
On trap, flush machine and ROB, set free=oldest, jump to handler
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Oldest
Free

## Slide 21: Managing Rename for Data-in-ROB
If “p” bit set, then use value in architectural register file
Else, tag field indicates instruction that will/has produced value
For dispatch, read source operands <p,tag,value> from arch. regfile, and also read <p,result> from producing instruction in ROB, bypassing as needed. Copy to ROB
Write destination arch. register entry with <0,Free,_>, to assign tag to ROB index of this instruction
On commit, update arch. regfile with <1, _, Result>
On trap, reset table (All p=1)
Tag
p
Value
Tag
p
Value
Tag
p
Value
Tag
p
Value
One entry per arch. register
Rename table associated with architectural registers, managed in decode/dispatch

## Slide 22: Data Movement in Data-in-ROB Design
ROB
Architectural Register File
Read operands during decode
Source Operands
Write sources in dispatch
Read operands at issue
Functional Units
Write results at completion
Read results for commit
Bypass newer values at dispatch
Result Data
Write results at commit

## Slide 23: Unified Physical Register File (MIPS R10K, Alpha 21264, Intel Pentium 4 & Sandy/Ivy Bridge)
Rename all architectural registers into a single physical register file during decode, no register values read
Functional units read and write from single unified register file holding committed and temporary registers in execute
Commit only updates mapping of architectural register to physical register, no data movement
Unified Physical Register File
Read operands at issue
Functional Units
Write results at completion
Committed Register Mapping
Decode Stage Register Mapping

## Slide 24: Lifetime of Physical Registers
ld x1, (x3)
addi x3, x1, #4
sub x6, x7, x9
add x3, x3, x6
ld x6, (x1)
add x6, x6, x3
sd x6, (x1)
ld x6, (x11)
ld P1, (Px)
addi P2, P1, #4
sub P3, Py, Pz
add P4, P2, P3
ld P5, (P1)
add P6, P5, P4
sd P6, (P1)
ld P7, (Pw)
Rename
When can we reuse a physical register?
When next writer of same architectural register commits
Physical regfile holds committed and speculative values
Physical registers decoupled from ROB entries (no data in ROB)

## Slide 25: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
ROB
Rename Table
Physical Regs
Free List
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
p
p
p
P0
P1
P3
P2
P4
(LPRd requires third read port on Rename Table for each instruction)
<x1>
P8
p

## Slide 26: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8

## Slide 27: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1

## Slide 28: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1
P5
P3
x sub p P6 p P5 x6 P3

## Slide 29: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1
P5
P3
x sub p P6 p P5 x6 P3
P1
P2
x add P1 P3 x3 P2

## Slide 30: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1
P5
P3
x sub p P6 p P5 x6 P3
P1
P2
x add P1 P3 x3 P2
x ld P0 x6 P4
P3
P4

## Slide 31: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
x ld p P7 x1 P0
x addi P0 x3 P1
x sub p P6 p P5 x6 P3
x ld p P7 x1 P0
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
P5
P3
P1
P2
x add P1 P3 x3 P2
x ld P0 x6 P4
P3
P4
Execute & Commit
p
p
p
<x1>
P8
x

## Slide 32: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
x sub p P6 p P5 x6 P3
x addi P0 x3 P1
x addi P0 x3 P1
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
P8
x x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
P5
P3
P1
P2
x add P1 P3 x3 P2
x ld P0 x6 P4
P3
P4
Execute & Commit
p
p
p
<x1>
P8
x
p
p
<x3>
P7

## Slide 33: MIPS R10K Trap Handling
Rename table is repaired by unrenaming instructions in reverse order using the PRd/LPRd fields
The Alpha 21264 had similar physical register file scheme, but kept complete rename table snapshots for each instruction in ROB (80 snapshots total)
  Flash copy all bits from snapshot to active table in one cycle

## Slide 34: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)