## Slide 1: CS252 Graduate Computer Architecture Fall 2015 Lecture 16: Virtual Memory and Caches
Krste Asanovic
krste@eecs.berkeley.edu
http://inst.eecs.berkeley.edu/~cs252/fa15

## Slide 2: Address Translation in CPU Pipeline
Need to cope with additional latency of TLB:
  slow down the clock?
  pipeline the TLB and cache access?
  virtual address caches
  parallel TLB/cache access
PC
Inst TLB
Inst. Cache
D
Decode
E
M
Data TLB
Data Cache
W
+
TLB miss? Page Fault?
Protection violation?
TLB miss? Page Fault?
Protection violation?

## Slide 3: Virtual-Address Caches
one-step process in case of a hit (+)
cache needs to be flushed on a context switch unless address space identifiers (ASIDs) included in tags (-)
aliasing problems due to the sharing of pages (-)
maintaining cache coherence (-)
CPU
Physical
Cache
TLB
Primary
Memory
VA
PA
PA
Alternative: place the cache before the TLB
Virtual Cache
CPU
VA
(StrongARM)
PA
TLB
Primary
Memory
VA

## Slide 4: Virtually Addressed Cache (Virtual Index/Virtual Tag)
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Instruction data
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?
Translate on miss

## Slide 5: Aliasing in Virtual-Address Caches
VA1
VA2
Page Table
Data Pages
PA
VA1
VA2
1st Copy of Data at PA
2nd Copy of Data at PA
Tag
Data
Two virtual pages share one physical page
Virtual cache can have two copies of same physical data. Writes to one copy not visible to reads of other!
General Solution: Prevent aliases coexisting in cache
Software (i.e., OS) solution for direct-mapped cache
  VAs of shared pages must agree in cache index bits; this ensures all VAs accessing same PA will conflict in direct-mapped cache (early SPARCs)
Notes: Two processes sharing the same file,
Map the same memory segment to different
Parts of their address space.

## Slide 6: Concurrent Access to TLB & Cache (Virtual Index/Physical Tag)
Index L is available without consulting the TLB
  cache and TLB accesses can begin simultaneously!
Tag comparison is made after both accesses are completed
Cases: L + b = k, L + b < k, L + b > k
VPN L b
TLB
Direct-map Cache
2L blocks
2b-byte block
PPN Page Offset
=
hit?
Data
Physical Tag
Tag
VA
PA
Virtual
Index
k

## Slide 7: Virtual-Index Physical-Tag Caches: Associative Organization
How does this scheme scale to larger caches?
VPN a L = k-b b
TLB
Direct-map
2L blocks
PPN Page Offset
=
hit?
Data
Phy.
Tag
Tag
VA
PA
Virtual
Index
k
Direct-map
2L blocks
2a
=
2a
After the PPN is known, 2a physical tags are compared
Notes:   Consider 4-Kbyte pages and caches with 32-byte blocks
  32-Kbyte cache  2a = 8
    4-Mbyte cache  2a =1024 No !

## Slide 8: Concurrent Access to TLB & Large L1 The problem with L1 > Page size
Can VA1 and VA2 both map to PA ?
VPN a Page Offset b
TLB
PPN Page Offset b
Tag
VA
PA
Virtual Index
L1 PA cache
Direct-map
=
hit?
PPNa Data
PPNa Data
VA1
VA2
Notes: If they differ in the lower ‘a’ bits alone, and share a physical page.

## Slide 9: A solution via Second Level Cache
Usually a common L2 cache backs up both Instruction and Data L1 caches
L2 is “inclusive” of both Instruction and Data caches
  Inclusive means L2 has copy of any line in either L1
CPU
L1 Data Cache
L1 Instruction Cache
Unified L2 Cache
RF
Memory
Memory
Memory
Memory

## Slide 10: Anti-Aliasing Using L2 [MIPS R10000,1996]
Suppose VA1 and VA2 both map to PA and VA1 is already in L1, L2 (VA1  VA2)
After VA2 is resolved to PA, a collision will be detected in L2.
VA1 will be purged from L1 and L2, and VA2 will be loaded  no aliasing !
VPN a Page Offset b
TLB
PPN Page Offset b
Tag
VA
PA
Virtual Index
L1 PA cache
Direct-map
=
hit?
PPNa Data
PPNa Data
VA1
VA2
Direct-Mapped L2
PA a1 Data
PPN
into L2 tag

## Slide 11: Anti-Aliasing using L2 for a Virtually Addressed L1
VPN Page Offset b
TLB
PPN Page Offset b
Tag
VA
PA
Virtual
Index & Tag
Physical
Index & Tag
L1 VA Cache
L2 PA Cache
L2 “contains” L1
PA VA1 Data
VA1 Data
VA2 Data
“Virtual Tag”
Physically-addressed L2 can also be used to avoid aliases in virtually-addressed L1

## Slide 12: Atlas Revisited
One PAR for each physical page
PAR’s contain the VPN’s of the pages resident in primary memory
Advantage: The size is proportional to the size of the primary memory
What is the disadvantage ?
VPN
PAR’s
PPN

## Slide 13: Hashed Page Table: Approximating Associative Addressing
Hashed Page Table is typically 2 to 3 times larger than the number of PPN’s to reduce collision probability
It can also contain DPN’s for some non-resident pages (not common)
If a translation cannot be resolved in this table then the software consults a data structure that has an entry for every existing page (e.g., full page table)
hash
Offset
Base of Table
+
PA of PTE
Primary
Memory
VPN PID PPN
Page Table
VPN d
Virtual Address
VPN PID DPN
VPN PID
PID

## Slide 14: Power PC: Hashed Page Table
Each hash table slot has 8 PTE's <VPN,PPN> that are searched sequentially
If the first hash slot fails, an alternate hash function is used to look in another slot
All these steps are done in hardware!
Hashed Table is typically 2 to 3 times larger than the number of physical pages
The full backup Page Table is managed in software
Base of Table
hash
Offset
+
PA of Slot
Primary
Memory
VPN PPN
Page Table
VPN d
80-bit VA
VPN

## Slide 15: VM features track historical uses:
Bare machine, only physical addresses
  One program owned entire machine
Batch-style multiprogramming
  Several programs sharing CPU while waiting for I/O
  Base & bound: translation and protection between programs (supports swapping entire programs but not demand-paged virtual memory)
  Problem with external fragmentation (holes in memory), needed occasional memory defragmentation as new jobs arrived
Time sharing
  More interactive programs, waiting for user. Also, more jobs/second.
  Motivated move to fixed-size page translation and protection, no external fragmentation (but now internal fragmentation, wasted bytes in page)
  Motivated adoption of virtual memory to allow more jobs to share limited physical memory resources while holding working set in memory
Virtual Machine Monitors
  Run multiple operating systems on one machine
  Idea from 1970s IBM mainframes, now common on laptops
    e.g., run Windows on top of Mac OS X
  Hardware support for two levels of translation/protection
    Guest OS virtual -> Guest OS physical -> Host machine physical

## Slide 16: Virtual Memory Use Today - 1
Servers/desktops/laptops/smartphones have full demand-paged virtual memory
  Portability between machines with different memory sizes
  Protection between multiple users or multiple tasks
  Share small physical memory among active tasks
  Simplifies implementation of some OS features
Vector supercomputers have translation and protection but rarely complete demand-paging
(Older Crays: base&bound, Japanese & Cray X1/X2: pages)
  Don’t waste expensive CPU time thrashing to disk (make jobs fit in memory)
  Mostly run in batch mode (run set of jobs that fits in memory)
  Difficult to implement restartable vector instructions

## Slide 17: Virtual Memory Use Today - 2
Most embedded processors and DSPs provide physical addressing only
  Can’t afford area/speed/power budget for virtual memory support
  Often there is no secondary storage to swap to!
  Programs custom written for particular memory configuration in product
  Difficult to implement restartable instructions for exposed architectures

## Slide 18: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)