## Slide 1: CS252 Graduate Computer Architecture Spring 2014 Lecture 1: Introduction
Krste Asanovic
krste@eecs.berkeley.edu
http://inst.eecs.berkeley.edu/~cs252/sp14

## Slide 2: Welcome to CS252!
An exciting time for computer architecture
Which means a terrifying time for computer users

## Slide 3: Upheaval in Computer Design
Most of last 50 years, Moore’s Law ruled
  Technology scaling allowed continual performance/energy improvements without changing software model
Last decade, technology scaling slowed/stopped
  Dennard scaling over (supply voltage ~fixed)
  Moore’s Law (cost/transistor) over?
  No competitive replacement for CMOS anytime soon
  Energy efficiency constrains everything
No “free lunch” for software developers, must consider:
  Parallel systems
  Heterogeneous systems

## Slide 4: Today’s Dominant Target Systems
Mobile (smartphone/tablet)
  >1 billion sold/year
  Market dominated by ARM-ISA-compatible general-purpose processor in system-on-a-chip (SoC)
  Plus sea of custom accelerators (radio, image, video, graphics, audio, motion, location, security, etc.)
Warehouse-Scale Computers (WSCs)
  100,000’s cores per warehouse
  Market dominated by x86-compatible server chips
  Dedicated apps, plus cloud hosting of virtual machines
  Starting to see some GPU usage, but mostly general-purpose CPU code
Embedded computing
  Wired/wireless network infrastructure, printers
  Consumer TV/Music/Games/Automotive/Camera/MP3

## Slide 5: CS252 Goals
Provide background for Berkeley architecture oral prelim exam
Prepare graduate students for research in computer architecture
Provide advanced architecture material for graduate students in related areas (operating systems, compilers, networking, high-performance programming)

## Slide 6: CS252 Prerequisites
Upper division graduate architecture class (CS152 or equivalent)
Thoroughly familiar with ISAs, assembly programming, in-order pipelining and caches.
Should have seen and understood most of following:
  Out-of-order superscalar
  Vectors
  VLIW
  Multithreading
  Virtual memory
  Cache coherency
Will be quickly reviewing this material, but no time to catch up if you have not seen material before

## Slide 7: Prereq Pop Quiz
10 minute multiple choice quiz
Write name, ungrad or grad, and year, email
No books/computers/phones

## Slide 8: CS252 Approach
Understand computer architecture through:
History
Applications
Technology Trends
Architectural Design Patterns
Programming models
Business models

## Slide 9: Why Study Architecture History (1)?
Appreciate the rich architecture lore
Understand how the current architecture landscape was shaped by design decisions driven by earlier application, technology, or business concerns
Help write better related work sections in your research papers

## Slide 10: Why Study Architecture History (2)?
“Those who don't know history are doomed to repeat it.” Edmund Burke
Many mistakes made in mainframe design, were repeated in minicomputers, then again in microprocessors, …
Many proposed “revolutionary” computer architecture ideas repeat earlier proposals that were investigated and later abandoned for good reason
  Negative results not well recorded in literature, as advocates only occasionally reflect on mistakes
  (Of course, applications and technology might change to make an old bad idea a new good idea)

## Slide 11: Applications
Computers exist to run applications
Need to understand demands of current and future applications to guide architecture design decisions
  Also, historical applications that guided current designs
Real applications are complex, and include much legacy code (if only in OS and libraries)
Important to understand how applications are written, tuned, and maintained by developers
  Architects often overoptimistic about effort developers will expend on exploiting hardware features
Benchmarks and kernels are often substituted for applications in architecture studies, but often with poor correlation to real application behavior
  Understand limitations of workloads used in evaluation

## Slide 12: Technology Trends
Computing technology is a very fast-moving field, so must constantly track changing technology abilities
New emerging technologies in 2014:
  Non-volatile memory, possible NAND flash replacements
  Integrated silicon photonics
  Extensive 3D stacking and new packaging technologies

## Slide 13: Applications and Technology Trends
A virtuous circle between applications and technology trends:
New technologies make new applications possible
  E.g., the microprocessor enabled personal computing
Revenues from popular applications fund and guide technology development
  E.g., flash memory for digital cameras and MP3 players

## Slide 14: Architectural Design Patterns
Understand architecture space through long-lived, recurring standard architectural design patterns, for processors, memory systems, and interconnect
Almost any “new” architecture can be understood as composition of standard architecture design patterns
  Including custom accelerators
We will be looking at case studies of real machines and breaking down into standard patterns

## Slide 15: Programming Models
Major architectural design patterns are usually associated with an expected programming model
  Serial code for uniprocessors (C)
  Loop nests for vector machines (FORTRAN)
  Element function code for GPUs (CUDA/OpenCL)
  Annotated loops for shared memory multiprocessors (OpenMP)
  Explicit message passing for clusters (MPI)
  CSP or Kahn process networks for distributed embedded systems (Occam)

## Slide 16: Business Models
Viability of different designs depends on expected business model
Some factors to consider:
  Volume of design: billions of units/year (smartphone) or 100s of units/year (supercomputer)
  Non-recurring engineering costs: new complex custom chip requires $50M, new FPGA board $100K
  Horizontal (Wintel) versus Vertical models (Embedded)

## Slide 17: CS252 Architectural Design Patterns
Microcoding/Pipelining/Decoupling
In-order/Out-of-order superscalars
SIMD (Vectors, Packed SIMD, GPUs)
VLIW
Multithreading
Memory system (Regfiles, Caches, DRAM)
Message-Passing systems (MPPs, WSCs)
Shared-Memory systems (coherence, synchronization)
Protection,Security,Virtual Memory&Virtual Machines
Other parallel (Associative, Systolic, Dataflow)
Networking and NICs
Storage and device interfaces

## Slide 18: CS252 Architectural Design Issues
Applications, workloads, and benchmarks
Technology trends
Business Models
Power/Energy/Thermal issues
Resiliency, coping with faults and soft errors
Simulation methodologies

## Slide 19: CS252 Course Grade Allocation
Reading assignments and summaries (25%)
Midterm Exam (25%)
Course project (50%)

## Slide 20: Reading assignments and summaries (25%)
You’ll be reading many papers this semester (~2 per class) – mostly “must read” papers for architects
Require 200-300 word review (NOT summary) per paper (review as if on program committee, describing strengths and weaknesses)
Review must be ASCII plain text in email to krste@eecs before class (zero credit after 10:30AM)
Lowest 3 days’ scores ignored (so can skip up to 3)
Each class starts with discussion of papers (~20 minutes) before lecture (~60 minutes)
Want good discussion, will call upon all students
15% grade for text, 10% for discussion participation

## Slide 21: Midterm (25%)
In-class midterm (80 minutes)
April 2 (Wednesday, week after spring break)
Covers lecture material up till spring break
Closed book, no notes, no computer, no phone, …
Test will emphasize understanding not memorization

## Slide 22: Course Project (50%)
Students work in groups of 2 to complete a project
Topic that could be paper at top architecture conference (ISCA, ASPLOS, MICRO, HPCA)
Two-page proposal due Monday March 17
Two weeks of 1-1 project advising during class time
  No TA for CS252 this semester, so must find/support own infrastructure for project
Final presentation (15%) in RRR week, date TBD
Final paper (35%) due Friday May 9, 11:59PM Pacific Time, mail to krste@eecs
  Must be in PDF, conference format (10-page, 2-column)
  No extensions

## Slide 23: A Good Project Proposal
Must have title and two authors’ names.
Should answer:
What are you are trying to improve
How is it currently done, or what has been tried before
What is your potential upside if successful
How will you evaluate your idea
What are intermediary milestones to measure progress

## Slide 24: Krste’s Office Hours
Mondays 5-6pm in ASPIRE Lab
Email ahead of time to confirm
Can arrange other times to meet (M-W only) if this doesn’t work

## Slide 25: Class Website
http://inst.eecs.berkeley.edu/~cs252
Class schedule
Course info
Lecture slides, posted morning before lecture
Reading assignments
Supplementary material (additional reading on each topic)

## Slide 26: Video Taping
Will experiment with video taping of class for external use.
Will not video discussion or use student faces/voices, but will repeat/use questions asked.

## Slide 27: Next Time Reading Assignments
“Architecture of the IBM System/360”, Amdahl, Blaauw, Brooks, 1964
“Design of the B5000 System”, Lonergan, King, 1961

## Slide 28: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)