## Slide 1: CS252 Graduate Computer Architecture Spring 2014 Lecture 12: Synchronization and Memory Models
Krste Asanovic
krste@eecs.berkeley.edu
http://inst.eecs.berkeley.edu/~cs252/sp14

## Slide 2: Last Time in Lecture 11
Cache Coherence
Snoopy coherence protocols
Inclusive L2 snoop filtering
Directory coherence protocols
MSI versus MESI cache states
4th C: Communication misses
False sharing

## Slide 3: Synchronization
The need for synchronization arises whenever there are concurrent processes in a system (even in a uniprocessor system).
Two classes of synchronization:
Producer-Consumer: A consumer process must wait until the producer process has produced data
Mutual Exclusion: Ensure that only one process uses a resource at a given time
producer
consumer
Shared Resource
P1
P2

## Slide 4: Simple Producer-Consumer Example
Memory
sd xdata, (xdatap)
li xflag, 1
sd xflag, (xflagp)
spin: ld xflag, (xflagp)
beqz xflag, spin
ld xdata, (xdatap)
data
flag
Producer
Consumer
Is this correct?
xflagp
xdatap
xflagp
xdatap
Initially flag=0

## Slide 5: Memory Model
Sequential ISA only specifies that each processor sees its own memory operations in program order
Memory model describes what values can be returned by load instructions across multiple threads

## Slide 6: Simple Producer-Consumer Example
sd xdata, (xdatap)
li xflag, 1
sd xflag, (xflagp)
spin: ld xflag, (xflagp)
beqz xflag, spin
ld xdata, (xdatap)
data
flag
Producer
Consumer
Can consumer read flag=1 before data written by producer?
Initially flag=0

## Slide 7: Sequential Consistency A Memory Model
“ A system is sequentially consistent if the result of any execution is the same as if the operations of all the processors were executed in some sequential order, and the operations of each individual processor appear in the order specified by the program”
Leslie Lamport
Sequential Consistency = arbitrary order-preserving interleaving of memory references of sequential programs
M
P
P
P
P
P
P

## Slide 8: Simple Producer-Consumer Example
sd xdata, (xdatap)
li xflag, 1
sd xflag, (xflagp)
spin: ld xflag, (xflagp)
beqz xflag, spin
ld xdata, (xdatap)
data
flag
Producer
Consumer
Initially flag =0
Dependencies from sequential ISA
Dependencies added by sequentially consistent memory model

## Slide 9: Implementing SC in hardware
Only a few commercial systems implemented SC
  Neither x86 nor ARM are SC
Requires either severe performance penalty
  Wait for stores to complete before issuing new store
Or, complex hardware
  Speculatively issue loads but squash if memory inconsistency with later-issued store discovered (MIPS R10K)

## Slide 10: Software reorders too!
Compiler can reorder/remove memory operations unless made aware of memory model
  Instruction scheduling, move loads before stores if to different address
  Register allocation, cache load value in register, don’t check memory
Prohibiting these optimizations would result in very poor performance
//Producer code
*datap = x/y;
*flagp = 1;
//Consumer code
while (!*flagp)
;
d = *datap;

## Slide 11: Relaxed Memory Models
Not all dependencies assumed by SC are supported, and software has to explicitly insert additional dependencies were needed
Which dependencies are dropped depends on the particular memory model
  IBM370, TSO, PSO, WO, PC, Alpha, RMO, …
How to introduce needed dependencies varies by system
  Explicit FENCE instructions (sometimes called sync or memory barrier instructions)
  Implicit effects of atomic memory instructions
How on earth are programmers supposed to work with this????

## Slide 12: Fences in Producer-Consumer Example
sd xdata, (xdatap)
li xflag, 1
fence.w.w //Write-write fence
sd xflag, (xflagp)
spin: ld xflag, (xflagp)
beqz xflag, spin
fence.r.r //Read-read fence
ld xdata, (xdatap)
data
flag
Producer
Consumer
Initially flag =0

## Slide 13: Simple Mutual-Exclusion Example
Memory
// Both threads execute:
ld xdata, (xdatap)
add xdata, 1
sd xdata, (xdatap)
data
Thread 1
Thread 2
Is this correct?
xdatap
xdatap

## Slide 14: Mutual Exclusion Using Load/Store
A protocol based on two shared variables c1 and c2.
Initially, both c1 and c2 are 0 (not busy)
What is wrong?
Process 1
  ...
  c1=1;
L: if c2=1 then go to L
  < critical section>
  c1=0;
Process 2
  ...
  c2=1;
L: if c1=1 then go to L
  < critical section>
  c2=0;
Deadlock!

## Slide 15: Mutual Exclusion: second attempt
To avoid deadlock, let a process give up the reservation
(i.e. Process 1 sets c1 to 0) while waiting.
Deadlock is not possible but with a low probability
a livelock may occur.
An unlucky process may never get to enter the
critical section  starvation
Process 1
  ...
L: c1=1;
  if c2=1 then
{ c1=0; go to L}
  < critical section>
  c1=0
Process 2
  ...
L: c2=1;
  if c1=1 then
{ c2=0; go to L}
  < critical section>
  c2=0

## Slide 16: A Protocol for Mutual Exclusion T. Dekker, 1966
Process 1
  ...
  c1=1;
  turn = 1;
L: if c2=1 & turn=1
    then go to L
  < critical section>
  c1=0;
A protocol based on 3 shared variables c1, c2 and turn.
Initially, both c1 and c2 are 0 (not busy)
turn = i ensures that only process i can wait
variables c1 and c2 ensure mutual exclusion
Solution for n processes was given by Dijkstra
and is quite tricky!
Process 2
  ...
  c2=1;
  turn = 2;
L: if c1=1 & turn=2
then go to L
  < critical section>
  c2=0;

## Slide 17: Analysis of Dekker’s Algorithm
  ... Process 1
  c1=1;
  turn = 1;
L: if c2=1 & turn=1
    then go to L
  < critical section>
  c1=0;
  ... Process 2
  c2=1;
  turn = 2;
L: if c1=1 & turn=2
then go to L
  < critical section>
  c2=0;
Scenario 1
  ... Process 1
  c1=1;
  turn = 1;
L: if c2=1 & turn=1
    then go to L
  < critical section>
  c1=0;
  ... Process 2
  c2=1;
  turn = 2;
L: if c1=1 & turn=2
then go to L
  < critical section>
  c2=0;
Scenario 2

## Slide 18: ISA Support for Mutual-Exclusion Locks
Regular loads and stores in SC model (plus fences in weaker model) sufficient to implement mutual exclusion, but inefficient and complex code
Therefore, atomic read-modify-write (RMW) instructions added to ISAs to support mutual exclusion
Many forms of atomic RMW instruction possible, some simple examples:
  Test and set (reg_x = M[a]; M[a]=1)
  Swap (reg_x=M[a]; M[a] = reg_y)

## Slide 19: Lock for Mutual-Exclusion Example
Release Lock
Acquire Lock
Critical Section
Memory
// Both threads execute:
li xone, 1
spin: amoswap xlock, xone, (xlockp)
bnez xlock, spin
ld xdata, (xdatap)
add xdata, 1
sd xdata, (xdatap)
sd x0, (xlockp)
data
Thread 1
Thread 2
xdatap
xdatap
lock
xlockp
xlockp
Assumes SC memory model

## Slide 20: Lock for Mutual-Exclusion with Relaxed MM
Release Lock
Acquire Lock
Critical Section
Memory
// Both threads execute:
li xone, 1
spin: amoswap xlock, xone, (xlockp)
bnez xlock, spin
fence.r.r
ld xdata, (xdatap)
add xdata, 1
sd xdata, (xdatap)
fence.w.w
sd x0, (xlockp)
data
Thread 1
Thread 2
xdatap
xdatap
lock
xlockp
xlockp

## Slide 21: Release Consistency
Observation that consistency only matters when processes communicate data
Only need to have consistent view when one process shares its updates to other processes
Other processes only need to ensure they receive updates after they acquire access to shared data
Release
Acquire
Critical
Release
Acquire
Critical
Other Code
Other Code
P1
P2
Ensure critical section updates visible before release visible
Ensure acquire happened before critical section reads data

## Slide 22: Release Consistency Adopted
Memory model for C/C++ and Java uses release consistency
Programmer has to identify sychronization operations, and if all data accesses are protected by synchronization, appears like SC to programmer
ARM v8 and RISC-V ISA adopt release consistency semantics on AMOs

## Slide 23: Nonblocking Synchronization
Compare&Swap(m), Rt, Rs:
if (Rt==M[m])
then M[m]=Rs;
Rs=Rt ;
status success;
else status fail;
try: Load Rhead, (head)
spin: Load Rtail, (tail)
if Rhead==Rtail goto spin
Load R, (Rhead)
Rnewhead = Rhead+1
Compare&Swap(head), Rhead, Rnewhead
if (status==fail) goto try
process(R)
status is an implicit argument

## Slide 24: Load-reserve & Store-conditional
Special register(s) to hold reservation flag and address,
and the outcome of store-conditional
try: Load-reserve Rhead, (head)
spin: Load Rtail, (tail)
if Rhead==Rtail goto spin
Load R, (Rhead)
Rhead = Rhead + 1
Store-conditional (head), Rhead
if (status==fail) goto try
process(R)
Load-reserve R, (m):
  <flag, adr>  <1, m>;
  R  M[m];
Store-conditional (m), R:
  if <flag, adr> == <1, m>
  then cancel other procs’
  reservation on m;
    M[m] R;
    status succeed;
  else status fail;

## Slide 25: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)