## Slide 1: Advanced Computer Graphics (Spring 2013)
CS 283, Lecture 24
Computational Imaging and Photography
Ravi Ramamoorthi
http://inst.eecs.berkeley.edu/~cs283/sp13
Many slides courtesy Ramesh Raskar, SIGGRAPH 2008 course

## Slide 2: Computational Imaging
Digital cameras now commonplace
Can we use computation for better images
  Many novel capabilities relative to film
And new ways of processing images
Is this computer graphics, optics, or image proc?
  All of the above; many rendering ideas apply
  Application shift. Computer aided design to movies/games to photography (big market)
Brief lecture. Subject of whole conference ICCP
  Industry: Light Field cameras, Google glass, …

## Slide 3: Outline
Image formation, basic lens-based camera
Light Field camera
Coded aperture depth of field
Flutter shutter (coded aperture shutter)
Many many more old, new innovations

## Slide 4: How do we see the world?
Let’s design a camera
  Idea 1: put a piece of film in front of an object
  Do we get a reasonable image?
Slide by Steve Seitz

## Slide 5: Pinhole camera
Add a barrier to block off most of the rays
  This reduces blurring
  The opening known as the aperture
  How does this transform the image?
Slide by Steve Seitz
Notes: It gets inverted

## Slide 6: Pinhole camera model
Pinhole model:
  Captures pencil of rays – all rays through a single point
  The point is called Center of Projection (COP)
  The image is formed on the Image Plane
  Effective focal length f is distance from COP to Image Plane
Slide by Steve Seitz

## Slide 7: Dimensionality Reduction Machine (3D to 2D)
Figures © Stephen E. Palmer, 2002
3D world
2D image
What have we lost?
  Angles
  Distances (lengths)

## Slide 8: Funny things happen…

## Slide 9: Parallel lines aren’t…
Figure by David Forsyth

## Slide 10: Lengths can’t be trusted...
Figure by David Forsyth
B’
C’
A’

## Slide 11: …but humans adapt!
http://www.michaelbach.de/ot/sze_muelue/index.html
Müller-Lyer Illusion
We don’t make measurements in the image plane

## Slide 12: Camera Obscura
The first camera
  Known to Aristotle
  Depth of the room is the effective focal length
Camera Obscura, Gemma Frisius, 1558

## Slide 13: From Pinhole to Lenses
Computer graphics assumes pinhole model
But making aperture narrow limits light
Making aperture large causes blurriness
Real cameras have lenses to collect more light, and focus it on the image plane
(Kolb et al. 95 simulates lens effects rendering)

## Slide 14: Home-made pinhole camera
http://www.debevec.org/Pinhole/
Why so
blurry?

## Slide 15: Shrinking the aperture
Why not make the aperture as small as possible?
  Less light gets through
  Diffraction effects…
Less light gets through
Slide by Steve Seitz

## Slide 16: The reason for lenses
Slide by Steve Seitz

## Slide 17: Focus and Defocus
A lens focuses light onto the film
  There is a specific distance at which objects are “in focus”
    other points project to a “circle of confusion” in the image
  Changing the shape/separation of lens changes this distance
“circle of
confusion”
Slide by Steve Seitz

## Slide 18: Thin lenses
Thin lens equation:
  Any object point satisfying this equation is in focus
  What is the shape of the focus region?
  How can we change the focus region?
  Thin lens applet: http://www.phy.ntnu.edu.tw/java/Lens/lens_e.html (by Fu-Kwun Hwang )
Slide by Steve Seitz

## Slide 19: Depth of Field
http://www.cambridgeincolour.com/tutorials/depth-of-field.htm

## Slide 20: Outline
Image formation, basic lens-based camera
Light Field camera
Coded aperture depth of field
Flutter shutter (coded aperture shutter)
Many many more old, new innovations

## Slide 21
Light Field Inside a Camera
Notes: 21

## Slide 22: Lenslet-based Light Field camera
[Adelson and Wang, 1992, Ng et al. 2005 ]
Light Field Inside a Camera
Notes: 22

## Slide 23: Stanford Plenoptic Camera [Ng et al 2005]
4000 × 4000 pixels ÷ 292 × 292 lenses = 14 × 14 pixels per lens
Contax medium format camera
Kodak 16-megapixel sensor
Adaptive Optics microlens array
125μ square-sided microlenses
Notes: 23

## Slide 24: Digital Refocusing
[Ng et al 2005]
Notes: 24

## Slide 25
Mask based Light Field Camera
Mask
Sensor
[Veeraraghavan, Raskar, Agrawal, Tumblin, Mohan, Siggraph 2007 ]
Notes: 25

## Slide 26
1/f0
Mask Tile
Cosine Mask Used

## Slide 27
Captured 2D Photo
Encoding due to Mask
[Veeraraghavan, Raskar, Agrawal, Tumblin, Mohan, Siggraph 2007 ]
Notes: 27

## Slide 28
2D FFT
Traditional Camera Photo
Heterodyne Camera Photo
Magnitude of 2D FFT
2D FFT
Magnitude of 2D FFT
Notes: 28

## Slide 29: Outline
Image formation, basic lens-based camera
Light Field camera
Coded aperture depth of field
Flutter shutter (coded aperture shutter)
Many many more old, new innovations

## Slide 30
Out of Focus Photo: Coded Aperture
Engineering the PSF when you cannot capture Lightfield
Notes: 30

## Slide 31
In Focus Photo
LED
2D Photo
Notes: 31

## Slide 32
Out of Focus Photo: Open Aperture
Notes: 32

## Slide 33
Out of Focus Photo: Coded Aperture
Notes: 33

## Slide 34: Captured Blurred Photo
[Veeraraghavan, Raskar, Agrawal, Tumblin, Mohan, Siggraph 2007 ]
Notes: 34
Reversibly encode all the information in this otherwise blurred photo

## Slide 35
Refocused on Person
Increase DoF + large aperture
Notes: 35
The glint out of focus shows the unusual pattern.

## Slide 36: Outline
Image formation, basic lens-based camera
Light Field camera
Coded aperture depth of field
Flutter shutter (coded aperture shutter)
Many many more old, new innovations

## Slide 37
Traditional Camera
Shutter is OPEN
Notes: How blurring happens in traditional camera

## Slide 38
Our Camera
Flutter Shutter
Notes: And in flutter shutter camera

## Slide 39
Shutter is OPEN and CLOSED

## Slide 40
Lab Setup

## Slide 41
Blurring
==
Convolution
Traditional Camera: Box Filter
Sync Function
Notes: How is the blurred image formed? It’s a convolution with box filter

## Slide 42
Flutter Shutter: Coded Filter
Preserves High Frequencies!!!
Notes: Coded exposure makes the filter broadband

## Slide 43
Comparison

## Slide 44
Inverse Filter Unstable
Inverse Filter stable

## Slide 45
Notes: Deblurring using the single photo. Blur is 60 pixels

## Slide 46
Input Image

## Slide 47
Rectified Crop
Deblurred Result
Notes: Result: Blur is 235 pixels, all text can be read