## Slide 1: CS 61C: Great Ideas in Computer Architecture (Machine Structures) Lecture 17 – Datacenters and Cloud Computing
Instructors:
Michael Franklin
Dan Garcia
http://inst.eecs.Berkeley.edu/~cs61c/fa11

## Slide 2: In the news
Google disclosed Thursday that it continuously uses enough electricity to power 200,000 homes, but it says that in doing so, it also makes the planet greener.
Search cost per day (per person) same as running a 60-watt bulb for 3 hours
Urs Hoelzle, Google SVP
Co-author of today’s reading
http://www.nytimes.com/2011/09/09/technology/google-details-and-defends-its-use-of-electricity.html

## Slide 3: Review
Great Ideas in Computer Architecture
  Layers of Representation/Interpretation
  Moore’s Law
  Principle of Locality/Memory Hierarchy
  Parallelism
  Performance Measurement and Improvement
  Dependability via Redundancy

## Slide 4: Computer Eras: Mainframe 1950s-60s
  “Big Iron”: IBM, UNIVAC, … build $1M computers for businesses => COBOL, Fortran, timesharing OS
Processor (CPU)
I/O

## Slide 5: Minicomputer Eras: 1970s
  Using integrated circuits, Digital, HP… build $10k computers for labs, universities => C, UNIX OS

## Slide 6: PC Era: Mid 1980s - Mid 2000s
  Using microprocessors, Apple, IBM, … build $1k computer for 1 person => Basic, Java, Windows OS

## Slide 7: PostPC Era: Late 2000s - ??
  Personal Mobile Devices (PMD): Relying on wireless networking, Apple, Nokia, … build $500 smartphone and tablet computers for individuals => Objective C, Android OS
  Cloud Computing: Using Local Area Networks, Amazon, Google, … build $200M Warehouse Scale Computers with 100,000 servers for Internet Services for PMDs
  => MapReduce, Ruby on Rails

## Slide 8: Why Cloud Computing Now?
“The Web Space Race”: Build-out of extremely large datacenters (10,000’s of commodity PCs)
  Build-out driven by growth in demand (more users)
  Infrastructure software and Operational expertise
Discovered economy of scale: 5-7x cheaper than provisioning a medium-sized (1000 servers) facility
More pervasive broadband Internet so can access remote computers efficiently
Commoditization of HW & SW
  Standardized software stacks

## Slide 9: January 2011 AWS Instances & Prices
Closest computer in WSC example is Standard Extra Large
@$0.11/hr, Amazon EC2 can make money!
  even if used only 50% of time
Instance | Per Hour | Ratio to Small | Compute Units | Virtual Cores | Compute Unit/ Core | Memory (GB) | Disk (GB) | Address
Standard Small | $0.085 | 1.0 | 1.0 | 1 | 1.00 | 1.7 | 160 | 32 bit
Standard Large | $0.340 | 4.0 | 4.0 | 2 | 2.00 | 7.5 | 850 | 64 bit
Standard Extra Large | $0.680 | 8.0 | 8.0 | 4 | 2.00 | 15.0 | 1690 | 64 bit
High-Memory Extra Large | $0.500 | 5.9 | 6.5 | 2 | 3.25 | 17.1 | 420 | 64 bit
High-Memory Double Extra Large | $1.000 | 11.8 | 13.0 | 4 | 3.25 | 34.2 | 850 | 64 bit
High-Memory Quadruple Extra Large | $2.000 | 23.5 | 26.0 | 8 | 3.25 | 68.4 | 1690 | 64 bit
High-CPU Medium | $0.170 | 2.0 | 5.0 | 2 | 2.50 | 1.7 | 350 | 32 bit
High-CPU Extra Large | $0.680 | 8.0 | 20.0 | 8 | 2.50 | 7.0 | 1690 | 64 bit
Cluster Quadruple Extra Large | $1.600 | 18.8 | 33.5 | 8 | 4.20 | 23.0 | 1690 | 64 bit

## Slide 10: Warehouse Scale Computers
Massive scale datacenters: 10,000 to 100,000 servers + networks to connect them together
  Emphasize cost-efficiency
  Attention to power: distribution and cooling
(relatively) homogeneous hardware/software
Offer very large applications (Internet services): search, social networking, video sharing
Very highly available: <1 hour down/year
  Must cope with failures common at scale
“…WSCs are no less worthy of the expertise of computer systems architects than any other class of machines” Barroso and Hoelzle 2009

## Slide 11: Design Goals of a WSC
Unique to Warehouse-scale
  Ample parallelism:
    Batch apps: large number independent data sets with independent processing. Also known as Data-Level Parallelism
  Scale and its Opportunities/Problems
    Relatively small number of these make design cost expensive and difficult to amortize
    But price breaks are possible from purchases of very large numbers of commodity servers
    Must also prepare for high component failures
  Operational Costs Count:
    Cost of equipment purchases << cost of ownership

## Slide 12: E.g., Google’s Oregon WSC

## Slide 13: Containers in WSCs
Inside WSC
Inside Container

## Slide 14: Equipment Inside a WSC
Server (in rack format):
1 ¾ inches high “1U”, x 19 inches x 16-20 inches: 8 cores, 16 GB DRAM, 4x1 TB disk
7 foot Rack: 40-80 servers + Ethernet local area network (1-10 Gbps) switch in middle (“rack switch”)
Array (aka cluster): 16-32 server racks + larger local area network switch (“array switch”) 10X faster => cost 100X: cost f(N2)

## Slide 15: Server, Rack, Array

## Slide 16: Google Server Internals
Google Server
Notes: Most companies buy servers from the likes of Dell, Hewlett-Packard, IBM, or Sun Microsystems. But Google, which has hundreds of thousands of servers and considers running them part of its core expertise, designs and builds its own. Ben Jai, who designed many of Google's servers, unveiled a modern Google server before the hungry eyes of a technically sophisticated audience.
Google's big surprise: each server has its own 12-volt battery to supply power if there's a problem with the main source of electricity. The company also revealed for the first time that since 2005, its data centers have been composed of standard shipping containers--each with 1,160 servers and a power consumption that can reach 250 kilowatts.
It may sound geeky, but a number of attendees--the kind of folks who run data centers packed with thousands of servers for a living--were surprised not only by Google's built-in battery approach, but by the fact that the company has kept it secret for years. Jai said in an interview that Google has been using the design since 2005 and now is in its sixth or seventh generation of design.
Read more: http://news.cnet.com/8301-1001_3-10209580-92.html#ixzz0yo8bhTOH

## Slide 17: Coping with Performance in Array
 | Local | Rack | Array
Racks | -- | 1 | 30
Servers | 1 | 80 | 2400
Cores (Processors) | 8 | 640 | 19,200
DRAM Capacity (GB) | 16 | 1,280 | 38,400
Disk Capacity (GB) | 4,000 | 320,000 | 9,600,000
DRAM Latency (microseconds) | 0.1 | 100 | 300
Disk Latency (microseconds) | 10,000 | 11,000 | 12,000
DRAM Bandwidth (MB/sec) | 20,000 | 100 | 10
Disk Bandwidth (MB/sec) | 200 | 100 | 10
Lower latency to DRAM in another server than local disk
Higher bandwidth to local disk than to DRAM in another server

## Slide 18: Coping with Workload Variation
Online service: Peak usage 2X off-peak
Midnight
Noon
Midnight
Workload
2X

## Slide 19: Impact of latency, bandwidth, failure, varying workload on WSC software?
WSC Software must take care where it places data within an array to get good performance
WSC Software must cope with failures gracefully
WSC Software must scale up and down gracefully in response to varying demand
More elaborate hierarchy of memories, failure tolerance, workload accommodation makes WSC software development more challenging than software for single computer

## Slide 20: Power vs. Server Utilization
Server power usage as load varies idle to 100%
Uses ½ peak power when idle!
Uses ⅔ peak power when 10% utilized! 90%@ 50%!
Most servers in WSC utilized 10% to 50%
Goal should be Energy-Proportionality: % peak load = % peak energy

## Slide 21: Power Usage Effectiveness
Overall WSC Energy Efficiency: amount of computational work performed divided by the total energy used in the process
Power Usage Effectiveness (PUE): Total building power / IT equipment power
  An power efficiency measure for WSC, not including efficiency of servers, networking gear
  1.0 = perfection

## Slide 22: PUE in the Wild (2007)

## Slide 23: High PUE: Where Does Power Go?
Computer
Room
Air Conditioner
Chiller cools warm
water from Air
Conditioner
Uninterruptable
Power Supply
(battery)
Servers + Networking
Power Distribution
Unit

## Slide 24: Google WSC A PUE: 1.24
Careful air flow handling
2. Elevated cold aisle temperatures
3. Use of free cooling
4. Per-server 12-V DC UPS
5. Measure vs. estimate PUE, publish PUE, and improve operation

## Slide 25: Google WSC A PUE: 1.24
Careful air flow handling
Don’t mix server hot air exhaust with cold air (separate warm aisle from cold aisle)
Short path to cooling so little energy spent moving cold or hot air long distances
Keeping servers inside containers helps control air flow

## Slide 26: Google WSC A PUE: 1.24
Elevated cold aisle temperatures
81°F instead of traditional 65°- 68°F
Found reliability OK if run servers hotter
Use of free cooling
Cool warm water outside by evaporation in cooling towers
Locate WSC in moderate climate so not too hot or too cold

## Slide 27: Google WSC A PUE: 1.24
Per-server 12-V DC UPS
Rather than WSC wide UPS, place single battery per server board
Increases WSC efficiency from 90% to 99%
Measure vs. estimate PUE, publish PUE, and improve operation

## Slide 28: Summary
Parallelism is one of the Great Ideas
  Applies at many levels of the system – from instructions to warehouse scale computers
Post PC Era: Parallel processing, smart phone to WSC
WSC SW must cope with failures, varying load, varying HW latency bandwidth
WSC HW sensitive to cost, energy efficiency
WSCs support many of the applications we have come to depend on