## Slide 1: 61C in the News0
Is organic computing finally here?
SPOTLIGHT | NOVEMBER 2, 2011
Today, computer chips can process data at 10 trillion (1013) bits per second. But, even though neurons in the human brain fire at a rate of 100 times per second, the brain still outperforms the best computers at various tasks. The main reason being that calculations done by computer chips happen in isolated pipelines one at a time.
Japanese scientists have made organic molecules perform parallel computations like neurons in the human brain. They created this promising new approach with a ring-like molecule called 2,3-dichloro-5,6-dicyano-p-benzoquinone, or DDQ.

## Slide 2: CS 61C: Great Ideas in Computer Architecture (Machine Structures) Lecture 30: Pipeline Parallelism 1
Instructors: Mike Franklin
Dan Garcia
http://inst.eecs.Berkeley.edu/~cs61c/fa11

## Slide 3: Datapath Control Signals
ExtOp: “zero”, “sign”
ALUsrc: 0  regB; 1  immed
ALUctr: “ADD”, “SUB”, “OR”
MemWr: 1  write memory
MemtoReg: 0  ALU; 1  Mem
nPC_sel: 0  “+4”; 1  “br”
RegDst: 0  “rt”; 1  “rd”
RegWr: 1  write register
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
clk
Data In
32
MemWr
0
1
0
1
ALU
0
1
WrEn
Adr
Data
Memory
5
imm16
clk
PC
00
4
nPC_sel & Equal
PC Ext
Adder
Adder
Mux
Inst Address
0
1

## Slide 4: Where Do Control Signals Come From?
ALUctr
RegDst
ALUSrc
ExtOp
MemtoReg
MemWr
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rs
Rt
nPC_sel
Adr
Inst
Memory
DATA PATH
Control
Op
<0:5>
Fun
RegWr
<26:31>

## Slide 5: P&H Figure 4.17

## Slide 6: Summary of the Control Signals (1/2)
inst Register Transfer
add R[rd]  R[rs] + R[rt]; PC  PC + 4
ALUsrc=RegB, ALUctr=“ADD”, RegDst=rd, RegWr, nPC_sel=“+4”
sub R[rd]  R[rs] – R[rt]; PC  PC + 4
ALUsrc=RegB, ALUctr=“SUB”, RegDst=rd, RegWr, nPC_sel=“+4”
ori R[rt]  R[rs] + zero_ext(Imm16); PC  PC + 4
ALUsrc=Im, Extop=“Z”, ALUctr=“OR”, RegDst=rt,RegWr, nPC_sel=“+4”
lw R[rt]  MEM[ R[rs] + sign_ext(Imm16)]; PC  PC + 4
ALUsrc=Im, Extop=“sn”, ALUctr=“ADD”, MemtoReg, RegDst=rt, RegWr, nPC_sel = “+4”
sw MEM[ R[rs] + sign_ext(Imm16)]  R[rs]; PC  PC + 4
ALUsrc=Im, Extop=“sn”, ALUctr = “ADD”, MemWr, nPC_sel = “+4”
beq if (R[rs] == R[rt]) then PC  PC + sign_ext(Imm16)] || 00 else PC  PC + 4
nPC_sel = “br”, ALUctr = “SUB”

## Slide 7: Summary of the Control Signals (2/2)
add
sub
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
nPCsel
Jump
ExtOp
ALUctr<2:0>
1
0
0
1
0
0
0
x
Add
1
0
0
1
0
0
0
x
Subtract
0
1
0
1
0
0
0
0
Or
0
1
1
1
0
0
0
1
Add
x
1
x
0
1
0
0
1
Add
x
0
x
0
0
1
0
x
Subtract
x
x
x
0
0
?
1
x
x
op
target address
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
op
rs
rt
immediate
R-type
I-type
J-type
add, sub
ori, lw, sw, beq
jump
func
op
00 0000
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010
Appendix A
10 0000
See
10 0010
We Don’t Care :-)
Notes: Here is a table summarizing the control signals setting for the seven (add, sub, ...) instructions we have looked at.
Instead of showing you the exact bit values for the ALU control (ALUctr), I have used the symbolic values here.
The first two columns are unique in the sense that they are R-type instrucions and in order to uniquely identify them, we need to look at BOTH the op field as well as the func fiels.
Ori, lw, sw, and branch on equal are I-type instructions and Jump is J-type. They all can be uniquely idetified by looking at the opcode field alone.
Now let’s take a more careful look at the first two columns. Notice that they are identical except the last row.
So we can combine these two rows here if we can “delay” the generation of ALUctr signals.
This lead us to something call “local decoding.”
+3 = 42 min. (Y:22)

## Slide 8: Boolean Exprs for Controller
rtype = ~op5  ~op4  ~op3  ~op2  ~op1  ~op0, ori = ~op5  ~op4  op3  op2  ~op1  op0 lw = op5  ~op4  ~op3  ~op2  op1  op0 sw = op5  ~op4  op3  ~op2  op1  op0 beq = ~op5  ~op4  ~op3  op2  ~op1  ~op0 jump = ~op5  ~op4  ~op3  ~op2  op1  ~op0
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rs
Rt
Adr
Inst
Memory
Op
<0:5>
Fun
<26:31>
Op 0-5 are really Instruction bits 26-31
Func 0-5 are really Instruction bits 0-5
How do we implement this in gates?
add = rtype  func5  ~func4  ~func3  ~func2  ~func1  ~func0 sub = rtype  func5  ~func4  ~func3  ~func2  func1  ~func0
Notes: ADD 0000 00ss ssst tttt dddd d000 0010 0000
SUB 0000 00ss ssst tttt dddd d000 0010 0010
ORI 0011 01ss ssst tttt iiii iiii iiii iiii
LW 1000 11ss ssst tttt iiii iiii iiii iiii
SW 1010 11ss ssst tttt iiii iiii iiii iiii
BEQ 0001 00ss ssst tttt iiii iiii iiii iiii
JUMP 0000 10ii iiii iiii iiii iiii iiii iiii

## Slide 9: Controller Implementation
add
sub
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
nPCsel
Jump
ExtOp
ALUctr[0]
ALUctr[1]
“AND” logic
“OR” logic
opcode
func

## Slide 10: Boolean Exprs for Controller
RegDst = add + sub ALUSrc = ori + lw + sw MemtoReg = lw RegWrite = add + sub + ori + lw MemWrite = sw nPCsel = beq Jump = jump ExtOp = lw + sw ALUctr[0] = sub + beq ALUctr[1] = ori
(assume ALUctr is 00 ADD, 01 SUB, 10 OR)
How do we implement this in gates?
Notes: ADD 0000 00ss ssst tttt dddd d000 0010 0000
SUB 0000 00ss ssst tttt dddd d000 0010 0010
ORI 0011 01ss ssst tttt iiii iiii iiii iiii
LW 1000 11ss ssst tttt iiii iiii iiii iiii
SW 1010 11ss ssst tttt iiii iiii iiii iiii
BEQ 0001 00ss ssst tttt iiii iiii iiii iiii
JUMP 0000 10ii iiii iiii iiii iiii iiii iiii

## Slide 11: Controller Implementation
add
sub
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
nPCsel
Jump
ExtOp
ALUctr[0]
ALUctr[1]
“AND” logic
“OR” logic
opcode
func

## Slide 12: Call home, we’ve made HW/SW contact!
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g.,MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation

## Slide 13: Administrivia
Due to time constraints – we can only allow the use of a maximum of 2 slip days on Project 4.
Thus, while we always encourage you to get your work done on time, if you still have 3 slip days left, you may want to consider using one prior to project 4

## Slide 14: Review: Single-cycle Processor
Five steps to design a processor:
  1. Analyze instruction set  datapath requirements
  2. Select set of datapath components & establish clock methodology
  3. Assemble datapath meeting the requirements
  4. Analyze implementation of each instruction to determine setting of control points that effects the register transfer.
  5. Assemble the control logic
    Formulate Logic Equations
    Design Circuits
Control
Datapath
Memory
Processor
Input
Output

## Slide 15: Single Cycle Performance
Assume time for actions are
  100ps for register read or write; 200ps for other events
Clock rate is?
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps
What can we do to improve clock rate?
Will this improve performance as well?
  Want increased clock rate to mean faster programs
Notes: 1.25 GHz

## Slide 16: Single Cycle Performance
Assume time for actions are
  100ps for register read or write; 200ps for other events
Clock rate is?
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps
What can we do to improve clock rate?
Will this improve performance as well?
  Want increased clock rate to mean faster programs
Notes: 1.25 GHz

## Slide 17: Gotta Do Laundry
Ann, Brian, Cathy, Dave each have one load of clothes to wash, dry, fold, and put away
  Washer takes 30 minutes
  Dryer takes 30 minutes
  “Folder” takes 30 minutes
  “Stasher” takes 30 minutes to put clothes into drawers
A
B
C
D

## Slide 18: Sequential Laundry
Sequential laundry takes 8 hours for 4 loads
T
a
s
k
O
r
d
e
r
B
C
D
A
30
Time
30
30
30
30
30
30
30
30
30
30
30
30
30
30
30
6 PM
7
8
9
10
11
12
1
2 AM

## Slide 19: Pipelined Laundry
Pipelined laundry takes 3.5 hours for 4 loads!
T
a
s
k
O
r
d
e
r
B
C
D
A
12
2 AM
6 PM
7
8
9
10
11
1
Time
30
30
30
30
30
30
30

## Slide 20: Pipelining Lessons (1/2)
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Multiple tasks operating simultaneously using different resources
Potential speedup = Number pipe stages
Time to “fill” pipeline and time to “drain” it reduces speedup: 2.3X v. 4X in this example
6 PM
7
8
9
Time
B
C
D
A
30
30
30
30
30
30
30
T
a
s
k
O
r
d
e
r

## Slide 21: Pipelining Lessons (2/2)
Suppose new Washer takes 20 minutes, new Stasher takes 20 minutes. How much faster is pipeline?
Pipeline rate limited by slowest pipeline stage
Unbalanced lengths of pipe stages reduces speedup
6 PM
7
8
9
Time
B
C
D
A
30
30
30
30
30
30
30
T
a
s
k
O
r
d
e
r

## Slide 22: Steps in Executing MIPS
1) IFtch: Instruction Fetch, Increment PC
2) Dcd: Instruction Decode, Read Registers
3) Exec: Mem-ref: Calculate Address Arith-log: Perform Operation
4) Mem: Load: Read Data from Memory Store: Write Data to Memory
5) WB: Write Data Back to Register

## Slide 23: Single Cycle Datapath
PC
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write Back

## Slide 24: Pipeline registers
PC
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write Back
Need registers between stages
  To hold information produced in previous cycle

## Slide 25: More Detailed Pipeline

## Slide 26: IF for Load, Store, …

## Slide 27: ID for Load, Store, …

## Slide 28: EX for Load

## Slide 29: MEM for Load

## Slide 30: WB for Load – Oops!
Wrong register number

## Slide 31: Corrected Datapath for Load

## Slide 32: So, in conclusion
You now know how to implement the control logic for the single-cycle CPU.
  (actually, you already knew it!)
Pipelining improves performance by increasing instruction throughput: exploits ILP
  Executes multiple instructions in parallel
  Each instruction has the same latency
Next: hazards in pipelining:
  Structure, data, control