## Slide 1: 61C In the News
Initially, when the iPhone 4S went on sale Oct. 14, many users couldn't get Siri to work because so many people were trying at the same time. Siri needs to go through Apple's cloud-based servers to work, and Siri's popularity caused a bit of a traffic jam.

## Slide 2: CS 61C: Great Ideas in Computer Architecture (Machine Structures) Lecture 31: Pipeline Parallelism 2
Instructors: Mike Franklin
Dan Garcia
http://inst.eecs.Berkeley.edu/~cs61c/fa11

## Slide 3: Instruction Level Parallelism (ILP)
Another parallelism form to go with Request Level Parallelism and Data Level Parallelism
RLP – e.g., Warehouse Scale Computing
DLP – e.g., SIMD, Map Reduce
ILP – e.g., Pipelined instruction Execution
5 stage pipeline => 5 instructions executing simultaneously, one at each pipeline stage

## Slide 4: You Are Here!
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates functioning in parallel at same time
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Main Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s Lecture

## Slide 5: Pipelined Execution Representation
Every instruction must take same number of steps, also called pipeline “stages”, so some will go idle sometimes
IFtch
Dcd
Exec
Mem
WB
IFtch
Dcd
Exec
Mem
WB
IFtch
Dcd
Exec
Mem
WB
IFtch
Dcd
Exec
Mem
WB
IFtch
Dcd
Exec
Mem
WB
IFtch
Dcd
Exec
Mem
WB
Time

## Slide 6: Graphical Pipeline Diagrams
PC
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write Back
Use datapath figure below to represent pipeline
IFtch
Dcd
Exec
Mem
WB
ALU
I$
Reg
D$
Reg

## Slide 7: Graphical Pipeline Representation
I
n
s
t
r.
O
r
d
e
r
Load
Add
Store
Sub
Or
I$
Time (clock cycles)
I$
ALU
Reg
Reg
I$
D$
ALU
ALU
Reg
D$
Reg
I$
D$
Reg
ALU
Reg
Reg
Reg
D$
Reg
D$
ALU
(In Reg, right half highlight read, left half write)
Reg
I$

## Slide 8: Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
What is pipelined clock rate?
  Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 9: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)

## Slide 10: Pipeline Speedup
If all stages are balanced
  i.e., all take the same time
  Time between instructionspipelined = Time between instructionsnonpipelined Number of stages
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease

## Slide 11: Hazards
Situations that prevent starting the next logical instruction in the next clock cycle
Structural hazards
  Required resource is busy (e.g., roommate studying)
Data hazard
  Need to wait for previous instruction to complete its data read/write (e.g., pair of socks in different loads)
Control hazard
  Deciding on control action depends on previous instruction (e.g., how much detergent based on how clean prior load turns out)

## Slide 12: 1. Structural Hazards
Conflict for use of a resource
In MIPS pipeline with a single memory
  Load/Store requires memory access for data
  Instruction fetch would have to stall for that cycle
    Causes a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  In reality, provide separate L1 I$ and L1 D$

## Slide 13: 1. Structural Hazard #1: Single Memory
Read same memory twice in same clock cycle
I$
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 14: 1. Structural Hazard #2: Registers (1/2)
Can we read and write to registers simultaneously?
I$
sw
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 15: 1. Structural Hazard #2: Registers (2/2)
Two different solutions have been used:
  1) RegFile access is VERY fast: takes less than half the time of ALU stage
    Write to Registers during first half of each clock cycle
    Read from Registers during second half of each clock cycle
  2) Build RegFile with independent read and write ports
Result: can perform Read and Write during same clock cycle

## Slide 16: Data Hazards (1/2)
Consider the following sequence of instructions
add $t0, $t1, $t2
sub $t4, $t0 ,$t3
and $t5, $t0 ,$t6
or $t7, $t0 ,$t8
xor $t9, $t0 ,$t10

## Slide 17: Data Hazards (2/2)
Data-flow backward in time are hazards
sub $t4,$t0,$t3
ALU
I$
Reg
D$
Reg
and $t5,$t0,$t6
ALU
I$
Reg
D$
Reg
or $t7,$t0,$t8
I$
ALU
Reg
D$
Reg
xor $t9,$t0,$t10
ALU
I$
Reg
D$
Reg
add $t0,$t1,$t2
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 18: Data Hazard Solution: Forwarding
Forward result from one stage to another
sub $t4,$t0,$t3
ALU
I$
Reg
D$
Reg
and $t5,$t0,$t6
ALU
I$
Reg
D$
Reg
or $t7,$t0,$t8
I$
ALU
Reg
D$
Reg
xor $t9,$t0,$t10
ALU
I$
Reg
D$
Reg
add $t0,$t1,$t2
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg
“or” hazard solved by register hardware

## Slide 19: Data Hazard: Load/Use (1/4)
Dataflow backwards in time are hazards
Can’t solve all cases with forwarding
Must stall instruction dependent on load, then forward (more hardware)
sub $t3,$t0,$t2
ALU
I$
Reg
D$
Reg
lw $t0,0($t1)
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg

## Slide 20: Data Hazard: Load/Use (2/4)
Hardware stalls pipeline (Called “interlock”)
sub $t3,$t0,$t2
ALU
I$
Reg
D$
Reg
bubble
and $t5,$t0,$t4
ALU
I$
Reg
D$
Reg
bubble
or $t7,$t0,$t6
I$
ALU
Reg
D$
bubble
lw $t0, 0($t1)
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg
Not in MIPS: (MIPS = Microprocessor without Interlocked Pipeline Stages)

## Slide 21: Data Hazard: Load/Use (3/4)
Instruction slot after a load is called “load delay slot”
If that instruction uses the result of the load, then the hardware interlock will stall it for one cycle.
Alternative: If the compiler puts an unrelated instruction in that slot, then no stall
Letting the hardware stall the instruction in the delay slot is equivalent to putting a nop in the slot (except the latter uses more code space)

## Slide 22: Data Hazard: Load/Use (4/4)
Stall is equivalent to nop
sub $t3,$t0,$t2
and $t5,$t0,$t4
or $t7,$t0,$t6
I$
ALU
Reg
D$
lw $t0, 0($t1)
ALU
I$
Reg
D$
Reg
bubble
bubble
bubble
bubble
bubble
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
nop

## Slide 23: Pipelining and ISA Design
MIPS Instruction Set designed for pipelining
All instructions are 32-bits
  Easier to fetch and decode in one cycle
  x86: 1- to 17-byte instructions
  (x86 HW actually translates to internal RISC instructions!)
Few and regular instruction formats, 2 source register fields always in same place
  Can decode and read registers in one step
Memory operands only in Loads and Stores
  Can calculate address 3rd stage, access memory 4th stage
Alignment of memory operands
  Memory access takes only one cycle

## Slide 24: 3. Control Hazards
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
BEQ, BNE in MIPS pipeline
Simple solution Option 1: Stall on every branch until have new PC value
  Would add 2 bubbles/clock cycles for every Branch! (~ 20% of instructions executed)

## Slide 25: Stall => 2 Bubbles/Clocks
Where do we do the compare for the branch?
I$
beq
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 26: Until next time …
Pipelining improves performance by increasing instruction throughput: exploits ILP
  Executes multiple instructions in parallel
  Each instruction has the same latency
Subject to hazards
  Structure, data, control
Stalls reduce performance
  But are required to get correct results
Compiler can arrange code to avoid hazards and stalls
  Requires knowledge of the pipeline structure
The BIG Picture