## Slide 1: CS 61C: Great Ideas in Computer Architecture Strings and Functions
Instructor:
Krste Asanovic, Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/sp12

## Slide 2: New-School Machine Structures (It’s a bit more complicated!)
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s Lecture

## Slide 3: Big Idea #1: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions

## Slide 4: Agenda
Review
Strings in C and MIPS
Administrivia
Functions
And in Conclusion, …

## Slide 5: Strings: C vs. Java
Recall: a string is just a long sequence of characters (i.e., array of chars)
C: 8-bit ASCII, define strings with end of string character NUL (0 in ASCII)
Java: 16-bit Unicode, first entry gives length of string

## Slide 6: Strings
“Cal” in ASCII in C; How many bytes?
Using 1 integer per byte, what does it look like?
Notes: Thus, the
string “Cal” is represented in C by the following 4 bytes, shown as decimal numbers:
67, 97, 108, 0.

## Slide 7: Strings
“Cal” in Unicode in Java; How many bytes?
Using 1 integer per byte, what does it look like? (For Latin alphabet, 1st byte is 0, 2nd byte is ASCII)
Notes: Thus, the
string “Cal” is represented in C by the following 10 bytes, shown as decimal numbers:
0, 0, 0, 3, 0, 67, 0, 97, 0, 108
(32 bit word contains string length)

## Slide 8: Pointers and Strings in C
char *p; # p is a pointer to a character
char x[] = “Randy Katz”; # x points to a literal string
p = x; # p points to the same place as x
p = &x[0]; # same as p = x
Cannot write x = “Randy Katz”;
Strings are not a primitive type in C (but character arrays are)
Element/character at a time processing possible, but whole string processing requires special routines
R A N D Y sp K A T Z 0
0 1 2 3 4 5 6 7 8 9 10
P
X
Notes: a[b] – Array subscript
*a -- Indirection ("object pointed to by a")
&a -- Reference ("address of a")
p = &x[0] is the same as “p gets the address of the 0th element pointed to by x

## Slide 9: Support for Characters and Strings
Load a word, use andi to isolate byte
lw $s0,0($s1)
andi $s0,$s0,255 # Zero everything but last 8 bits
RISC Design Principle: “Make the Common Case Fast”—Many programs use text: MIPS has load byte instruction (lb)
lb $s0,0($s1)
Also store byte instruction (sb)

## Slide 10: Support for Characters and Strings
Load a word, use andi to isolate half of word
lw $s0,0($s1)
andi $s0,$s0,65535 # Zero everything but last 16 bits
RISC Design Principle #3: “Make the Common Case Fast”—Many programs use text, MIPS has load halfword instruction (lh)
lh $s0,0($s1)
Also store halfword instruction (sh)

## Slide 11: Fast String Copy Code in C
Copy x[] to y[]
char *p, *q;
p = &x[0]; /* p = x */
/* set p to address of 1st char of x */
q = &y[0]; /* q = y also OK */
/* set q to address of 1st char of y */
while((*q++ = *p++) != ‘\0’) ;

## Slide 12: Fast String Copy in MIPS Assembly
Get addresses of x and y into $s1, $s2
p and q are assigned to these registers
# $t1 = &p (BA), q @ &p + 4
# $s1 = p
# $s2 = q
Loop: # $t2 = *p
# *q = $t2
# p = p + 1
# q = q + 1
# if *p == 0, go to Exit
j Loop # go to Loop
Exit: # N characters => N*6 + 3 instructions
P
Q
BA
BA+4

## Slide 13: Fast String Copy in MIPS Assembly
Get addresses of x and y into $s1, $s2
p and q are assigned to these registers
lw $t1, Base Address (e.g., BA)
lw $s1,0($t1) # $s1 = p
lw $s2,4($t1) # $s2 = q
Loop: lb $t2,0($s1) # $t2 = *p
sb $t2,0($s2) # *q = $t2
addi $s1,$s1,1 # p = p + 1
addi $s2,$s2,1 # q = q + 1
# if *p == 0, go to Exit
j Loop # go to Loop
Exit: # N characters => N*6 + 3 instructions
P
Q
BA
BA+4
Student Roulette?

## Slide 14: Fast String Copy in MIPS Assembly
Get addresses of x and y into $s1, $s2
p and q are assigned to these registers
lw $t1, Base Address (e.g., BA)
lw $s1,0($t1) # $s1 = p
lw $s2,4($t1) # $s2 = q
Loop: lb $t2,0($s1) # $t2 = *p
sb $t2,0($s2) # *q = $t2
addi $s1,$s1,1 # p = p + 1
addi $s2,$s2,1 # q = q + 1
beq $t2,$zero,Exit # if *p == 0, go to Exit
j Loop # go to Loop
Exit: # N characters => N*6 + 3 instructions
P
Q
BA
BA+4
Student Roulette?

## Slide 15
$s1 corresponds to p
$s1 corresponds to q
$s1 corresponds to *p
$t1 corresponds to p
☐
☐
☐
☐
Which statement is TRUE?
lw $t1, Base Address (e.g., BA)
lw $s1,0($t1) # $s1 = p
lw $s2,4($t1) # $s2 = q
Loop: lb $t2,0($s1) # $t2 = *p
sb $t2,0($s2) # *q = $t2
addi $s1,$s1,1 # p = p + 1
addi $s2,$s2,1 # q = q + 1
beq $t2,$zero,Exit # if *p == 0, go to Exit
j Loop # go to Loop
Exit:
char *p, *q;
p = &x[0]; q = &y[0];
while((*q++ = *p++) != ‘\0’) ;
Notes: VertLeftWhiteCheck1
Answer: B s1 corresponds to p,
($s2 corresponds to q)
($t1 corresponds to &x[0])
*p lb/sb $t2,0($s1) = value in $t2 at right point …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 16: Agenda
Review
Strings in C and MIPS
Administrivia
Functions
And in Conclusion, …

## Slide 17: Administrivia
Map-Reduce Project #1
  Two Parts, first part due Sunday
  Write-up posted last night (thanks Alan!)
Lab #3
  Hands on EC2, needed for Project #1, Part 2
HW #3
  C practice/numbers and strings
… Midterm is coming in < one month!
  Let us know special accommodation now …
  CS 188 students, ask your instructors to return my emails!

## Slide 18: Agenda
Review
Strings in C and MIPS
Administrivia
Functions
And in Conclusion, …

## Slide 19: Six Fundamental Steps in Calling a Function
Put parameters in a place where function can access them
Transfer control to function
Acquire (local) storage resources needed for function
Perform desired task of the function
Put result value in a place where calling program can access it and restore any registers you used
Return control to point of origin, since a function can be called from several points in a program

## Slide 20: MIPS Function Call Conventions
Registers faster than memory, so use them
$a0–$a3: four argument registers to pass parameters
$v0–$v1: two value registers to return values
$ra: one return address register to return to the point of origin
(7 + $zero +$at of 32, 23 left!)
Notes: $at – assembler temporary register, used for pseudo instructions

## Slide 21: MIPS Registers Assembly Language Conventions
$t0-$t9: 10 x temporaries (intermediates)
$s0-$s7: 8 x “saved” temporaries (program variables)
18 registers
32 – (18 + 9) = 5 left

## Slide 22: MIPS Function Call Instructions
Invoke function: jump and link instruction (jal)
  “link” means form an address or link that points to calling site to allow function to return to proper address
  Jumps to address and simultaneously saves the address of following instruction in register $ra
  jal ProcedureAddress
Return from function: jump register instruction (jr)
  Unconditional jump to address specified in register
  jr $ra

## Slide 23: Notes on Functions
Calling program (caller) puts parameters into registers $a0-$a3 and uses jal X to invoke X (callee)
Must have register in computer with address of currently executing instruction
  Instead of Instruction Address Register (better name), historically called Program Counter (PC)
  It’s a program’s counter; it doesn’t count programs!
jr $ra puts address inside $ra into PC
What value does jal X place into $ra? ????
Student Roulette?

## Slide 24: Notes on Functions
Calling program (caller) puts parameters into registers $a0-$a3 and uses jal X to invoke X (callee)
Must have register in computer with address of currently executing instruction
  Instead of Instruction Address Register (better name), historically called Program Counter (PC)
  It’s a program’s counter, it doesn’t count programs!
jr $ra puts address inside $ra into PC
What value does jal X place into $ra? Next PC
PC + 4

## Slide 25: Where Are Old Register Values Saved to Restore Them After Function Call
Need a place to save old values before call function, restore them when return, and delete
Ideal is stack: last-in-first-out queue (e.g., stack of plates)
  Push: placing data onto stack
  Pop: removing data from stack
Stack in memory, so need register to point to it
$sp is the stack pointer in MIPS
Convention is grow from high to low addresses
  Push decrements $sp, Pop increments $sp
(28 out of 32, 4 left!)

## Slide 26: Example
int leaf_example (int g, int h, int i, int j)
{
int f;
f = (g + h) – (i + j);
return f;
}
Parameter variables g, h, i, and j in argument registers $a0, $a1, $a2, and $a3, and f in $s0
Assume need one temporary register $t0

## Slide 27: Stack Before, During, After Function
Need to save old values of $s0 and $t0
Contents of $s0
Contents of $t0

## Slide 28: MIPS Code for leaf_example
leaf_example:
# adjust stack for 2 int items
# save $t0 for use afterwards
# save $s0 for use afterwards
# f = g + h
# t0 = i + j
# return value (g + h) – (i + j)
# restore $s0 for caller
# restore $t0 for caller
# delete 2 items from stack
# jump back to calling routine
Student Roulette?
Notes: addi $sp,$sp,-8 # adjust stack for 2 items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
add $t0,$a2,$a3 # t0 = i + j
sub $v0,$s0,$t0 # return value (g + h) – (i + j)
lw $s0, 0($sp) # restore register $s0 for caller
lw $t0, 4($sp) # restore register $t0 for caller
addi $sp,$sp,8 # adjust stack to delete 2 items
jr $ra # jump back to calling routine

## Slide 29
Print 4
a.out will crash
None of the above
Print -4
☐
☐
☐
☐
What will the printf output?
static int *p;
int leaf (int g, int h, int i, int j)
{
int f; p = &f;
f = (g + h) – (i + j);
return f;
}
int main(void) { int x;
x = leaf(1,2,3,4);
x = leaf(3,4,1,2);
…
printf(”%d\n”,*p);
}
Notes: VertLeftWhiteCheck1
B: Print 4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 30: What If a Function Calls a Function? Recursive Function Calls?
Would clobber values in $a0 to $a3 and $ra
What is the solution?
Student Roulette?
Notes: Save $ra on the stack

## Slide 31: Allocating Space on Stack
C has two storage classes: automatic and static
  Automatic variables are local to function and discarded when function exits
  Static variables exist across exits from and entries to procedures
Use stack for automatic (local) variables that don’t fit in registers
Procedure frame or activation record: segment of stack with saved registers and local variables
Some MIPS compilers use a frame pointer ($fp) to point to first word of frame
(29 of 32, 3 left!)

## Slide 32: Stack Before, During, After Call

## Slide 33: Recursive Function Factorial
int fact (int n)
{
if (n < 1) return (1);
else return (n * fact(n-1));
}

## Slide 34: Recursive Function Factorial
Fact: # adjust stack for 2 items
addi $sp,$sp,-8
# save return address
sw $ra, 4($sp) # save argument n
sw $a0, 0($sp) # test for n < 1
slti $t0,$a0,1
# if n >= 1, go to L1
beq $t0,$zero,L1 # Then part (n==1) return 1
addi $v0,$zero,1 # pop 2 items off stack
addi $sp,$sp,8 # return to caller
jr $ra
L1:
# Else part (n >= 1) # arg. gets (n – 1)
addi $a0,$a0,-1 # call fact with (n – 1)
jal fact
# return from jal: restore n
lw $a0, 0($sp) # restore return address
lw $ra, 4($sp) # adjust sp to pop 2 items
addi $sp, $sp,8 # return n * fact (n – 1)
mul $v0,$a0,$v0 # return to the caller
jr $ra
mul is a pseudo instruction
Notes: Slti: set dst to 1 if src is less than imm (signed immediate)

## Slide 35: Optimized Function Convention
To reduce expensive loads and stores from spilling and restoring registers, MIPS divides registers into two categories:
Preserved across function call
  Caller can rely on values being unchanged
  $ra, $sp, $gp, $fp, “saved registers” $s0- $s7
Not preserved across function call
  Caller cannot rely on values being unchanged
  Return value registers $v0,$v1, Argument registers $a0-$a3, “temporary registers” $t0-$t9

## Slide 36: Where is the Stack in Memory?
MIPS convention
Stack starts in high memory and grows down
  Hexadecimal (base 16) : 7fff fffchex
MIPS programs (text segment) in low end
  0040 0000hex
static data segment (constants and other static variables) above text for static variables
  MIPS convention global pointer ($gp) points to static
  (30 of 32, 2 left! – will see when talk about OS)
Heap above static for data structures that grow and shrink ; grows up to high addresses

## Slide 37: MIPS Memory Allocation

## Slide 38: Register Allocation and Numbering

## Slide 39
jal saves PC+1 in %ra
The callee can use temporary registers (%ti) without saving and restoring them
The caller can rely on save registers (%si) without fear of callee changing them
MIPS uses jal to invoke a function and jr to return from a function
☐
☐
☐
☐
Which statement is FALSE?
Notes: VertLeftWhiteCheck1
B: Print It saves PC+4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 40: And in Conclusion, …
C strings are char arrays, byte per character, null terminated
Distinguish pointers and the memory they point to
  * for dereference, & for address
C is function oriented; code reuse via functions
  Jump and link (jal) invokes, jump register (jr $ra) returns
  Registers $a0-$a3 for arguments, $v0-$v1 for return values
Stack for spilling registers, nested function calls, C local (automatic) variables