## Slide 1: CS 61C: Great Ideas in Computer Architecture Thread-Level Parallelism (TLP)
Instructor:
Krste Asanovic, Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa12

## Slide 2: Review
SIMD Parallelism via Intel SSE Instructions
Use of SSE intrinsics to get access to assembly instructions from C code
Restructuring data to provide aligned access for SSE loads and stores

## Slide 3: New-School Machine Structures (It’s a bit more complicated!)
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Project 3

## Slide 4: Simple Multiprocessor
Processor 0
Control
Datapath
PC
Registers
(ALU)
Memory
Input
Output
Bytes
I/O-Memory Interfaces
Processor 0 Memory Accesses
Processor 1
Control
Datapath
PC
Registers
(ALU)
Processor 1 Memory Accesses

## Slide 5: Multiprocessor Execution Model
Each processor has its own PC and executes an independent stream of instructions (MIMD)
Different processors can access the same memory space
  Processors can communicate via shared memory by storing/loading to/from common locations
Two ways to use a multiprocessor:
  Deliver high throughput for independent jobs via job-level parallelism
  Improve the run time of a single program that has been specially crafted to run on a multiprocessor - a parallel-processing program
  Now Use term core for processor (“Multicore”) because “Multiprocessor Microprocessor” too redundant

## Slide 6: Transition to Multicore
Sequential App Performance

## Slide 7: Parallelism Only Path to Higher Performance
Sequential processor performance not expected to increase much, and might go down
If want apps with more capability, have to embrace parallel processing (SIMD and MIMD)
In mobile systems, use multiple cores and GPUs
In warehouse-scale computers, use multiple nodes, and all the MIMD/SIMD capability of each node

## Slide 8: Multiprocessors and You
Only path to performance is parallelism
  Clock rates flat or declining
  SIMD: 2X width every 3-4 years
    128b wide now, 256b 2011, 512b in 2014?, 1024b in 2018?
  MIMD: Add 2 cores every 2 years: 2, 4, 6, 8, 10, …
A key challenge is to craft parallel programs that have high performance on multiprocessors as the number of processors increase – i.e., that scale
  Scheduling, load balancing, time for synchronization, overhead for communication
Project 3: fastest code on 8-core computers
  2 chips/computer, 4 cores/chip

## Slide 9: Potential Parallel Performance (assuming SW can use it)
Year | Cores | SIMD bits /Core | Core * SIMD bits | Peak DP FLOPs/Cycle
2003 | 2 | 128 | 256 | 4
2005 | 4 | 128 | 512 | 8
2007 | 6 | 128 | 768 | 12
2009 | 8 | 128 | 1024 | 16
2011 | 10 | 256 | 2560 | 40
2013 | 12 | 256 | 3072 | 48
2015 | 14 | 512 | 7168 | 112
2017 | 16 | 512 | 8192 | 128
2019 | 18 | 1024 | 18432 | 288
2021 | 20 | 1024 | 20480 | 320
2.5X
8X
20X
MIMD
SIMD
MIMD *SIMD
+2/
2yrs
2X/
4yrs

## Slide 10: Multiprocessor Caches
Memory is a performance bottleneck even with one processor
Use caches to reduce bandwidth demands on main memory
Each core has a local private cache holding data it has accessed recently
Only cache misses have to access the shared common memory
Processor
Processor
Processor
Cache
Cache
Cache
Interconnection Network
Memory
I/O
Notes: Power has become the overriding issue for both data centers and microprocessors. Power efficiency has joined scalable performance making the case for multiprocessors. Multiprocessors also improve availability.

## Slide 11: Shared Memory and Caches
What if?
  Processors 1 and 2 read Memory[1000] (value 20)
Processor
Processor
Processor
Cache
Cache
Cache
Interconnection Network
Memory
I/O
1000
20
1000
1000
1000
20
0
1
2

## Slide 12: Shared Memory and Caches
Now:
  Processor 0 writes Memory[1000] with 40
Processor
Processor
Processor
Cache
Cache
Cache
Interconnection Network
Memory
I/O
0
1
2
1000 20
1000 20
1000
1000 40
1000 40
Problem?

## Slide 13: Keeping Multiple Caches Coherent
Architect’s job: shared memory => keep cache values coherent
Idea: When any processor has cache miss or writes, notify other processors via interconnection network
  If only reading, many processors can have copies
  If a processor writes, invalidate any other copies
Write transactions from one processor “snoop” tags of other caches using common interconnect
  Invalidate any “hits” to same address in other caches
  If hit is to dirty line, other cache has to write back first!

## Slide 14: Shared Memory and Caches
Example, now with cache coherence
  Processors 1 and 2 read Memory[1000]
  Processor 0 writes Memory[1000] with 40
Processor
Processor
Processor
Cache
Cache
Cache
Interconnection Network
Memory
I/O
0
1
2
1000 20
1000 20
Processor 0
Write
Invalidates
Other Copies
1000
1000 40
1000 40

## Slide 15: Flashcard Quiz: Which statement is true?
Using write-through caches removes the need for cache coherence
Every processor store instruction must check contents of other caches
Most processor load and store accesses only need to check in local private cache
Only one processor can cache any memory location at one time

## Slide 16: Administrivia
Midterm Tuesday Oct 9, 8PM:
  Two rooms: 1 Pimentel and 2050 LSB
  Check your room assignment!
  Covers everything through lecture Wednesday 10/3
  Closed book, can bring one sheet notes, both sides
  Copy of Green card will be supplied
  No phones, calculators, …; just bring pencils & eraser
  TA Review: Sun. Oct. 7, 3-5pm, 2050 VLSB
NO LECTURE ON WEDNESDAY OCTOBER 10!!!

## Slide 17: Midterm Room Assignment by Login
1 Pimentel = logins ab – mk
2050 VLSB = logins mm - xm

## Slide 18: Cache Coherency Tracked by Block
Suppose block size is 32 bytes
Suppose Processor 0 reading and writing variable X, Processor 1 reading and writing variable Y
Suppose in X location 4000, Y in 4012
What will happen?
Processor 0
Processor 1
4000
4000
4004
4008
4012
4016
4028
Tag
32-Byte Data Block
Cache 0
Cache 1
Memory

## Slide 19: Coherency tracked by cache line
Block ping-pongs between two caches even though processors are accessing disjoint variables
Effect called false sharing
How can you prevent it?

## Slide 20: Fourth “C” of Cache Misses: Coherence Misses
Misses caused by coherence traffic with other processor
Also known as communication misses because represents data moving between processors working together on a parallel program
For some parallel programs, coherence misses can dominate total misses

## Slide 21: Threads
A thread is a unit of work described by a sequential flow of instructions
Each thread has a program counter and processor registers, and accesses the shared memory
Each processor provides one (or more) hardware threads that actively execute instructions
An operating system can multiplex multiple software threads onto the available hardware threads

## Slide 22: Operating System Threads
Give the illusion of many active threads by time-multiplexing hardware threads among software threads
Remove a software thread from a hardware thread by interrupting its execution and saving its registers and PC into memory
  Also if one thread is blocked waiting for network access or user input
Can make a different software thread active by loading its registers into processor and jumping to its saved PC

## Slide 23: Hardware Multithreading
Basic idea: Processor resources are expensive and should not be left idle
Long memory latency to memory on cache miss?
Hardware switches threads to bring in other useful work while waiting for cache miss
Cost of thread context switch must be much less than cache miss latency
Put in redundant hardware so don’t have to save context on every thread switch:
  PC, Registers
Attractive for apps with abundant TLP
  Commercial multi-user workloads

## Slide 24: Hardware Multithreading
Memory
Input
Output
Bytes
I/O-Memory Interfaces
Processor
Control
Datapath
PC 0
Registers 0
(ALU)
PC 1
Registers 1
Two copies of PC and Registers inside processor hardware
Looks like two processors to software (hardware thread 0, hardware thread 1)
Control logic decides which thread to execute an instruction from next

## Slide 25: Multithreading vs. Multicore
Multithreading => Better Utilization
  ≈1% more hardware, 1.10X better performance?
  Share integer adders, floating-point adders, caches (L1 I $, L1 D$, L2 cache, L3 cache), Memory Controller
Multicore => Duplicate Processors
  ≈50% more hardware, ≈2X better performance?
  Share outer caches (L2 cache, L3 cache), Memory Controller

## Slide 26: Machines in (old) 61C Lab
/usr/sbin/sysctl -a | grep hw\.
hw.model = MacPro4,1
…
hw.physicalcpu: 8
hw.logicalcpu: 16
…
hw.cpufrequency = 2,260,000,000
hw.physmem = 2,147,483,648
hw.cachelinesize = 64
hw.l1icachesize: 32,768
hw.l1dcachesize: 32,768
hw.l2cachesize: 262,144
hw.l3cachesize: 8,388,608
Therefore, should try up to 16 threads to see if performance gain even though only 8 cores

## Slide 27: And in Conclusion, …
Sequential software is slow software
  SIMD and MIMD only path to higher performance
Multiprocessor/Multicore uses Shared Memory
  Cache coherency implements shared memory even with multiple copies in multiple caches
  False sharing a concern; watch block size!
Multithreading increases utilization, Multicore more processors (MIMD)