## Slide 1: CS 61C: Great Ideas in Computer Architecture Timing and State
Instructors:
Krste Asanovic, Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa12

## Slide 2: You are Here!
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today

## Slide 3: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions

## Slide 4: Review
Real world voltages are analog, but are quantized to represent logic 0 and logic 1
Transistors are just switches, combined to form gates: AND, OR, NOT, NAND, NOR
Truth table can be mapped to gates for combinational logic design
Boolean algebra allows minimization of gates

## Slide 5: Agenda
State Elements
Finite State Machines
And in Conclusion, …

## Slide 6: Agenda
State Elements
Finite State Machines
And in Conclusion, …

## Slide 7: Type of Circuits
Synchronous Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL) circuits
    Output is a function of the inputs only, not the history of its execution
    E.g., circuits to add A, B (ALUs)
    Last lecture was CL
  Sequential Logic (SL)
    Circuits that “remember” or store information
    aka “State Elements”
    E.g., memories and registers (Registers)
    Today’s lecture is SL

## Slide 8: Design Hierarchy
system
datapath
control
state registers
combinational logic
multiplexer
comparator
code registers
register
logic
switching networks

## Slide 9: A Conceptual MIPS Datapath

## Slide 10: Uses for State Elements
Place to store values for later re-use:
  Register files (like $1-$31 on the MIPS)
  Memory (caches, and main memory)
Help control flow of information between combinational logic blocks
  State elements hold up the movement of information at input to combinational logic blocks to allow for orderly passage

## Slide 11: Accumulator Example
Want: S=0;
for (i=0;i<n;i++)
S = S + Xi
Why do we need to control the flow of information?
Assume:
  Each X value is applied in succession, one per cycle
  After n cycles the sum is present on S
SUM
Xi
S

## Slide 12: First Try: Does this work?
No!
Reason #1: How to control the next iteration of the ‘for’ loop?
Reason #2: How do we say: ‘S=0’?
Feedback

## Slide 13: Second Try: How About This?
Rough timing …
Register is used to hold up the transfer of data to adder
Time
High (1)
Low (0)
High (1)
Low (0)
Rounded Rectangle per clock means could be 1 or 0
Xi must be ready before clock edge due to adder delay
High (1)
Low (0)
Square wave clock sets when things change

## Slide 14: Model for Synchronous Systems
Collection of Combinational Logic blocks separated by registers
Feedback is optional
Clock signal(s) connects only to clock input of registers
Clock (CLK): steady square wave that synchronizes the system
Register: several bits of state that samples on rising edge of CLK (positive edge-triggered) or falling edge (negative edge-triggered)

## Slide 15: Register Internals
n instances of a “Flip-Flop”
Flip-flop name because the output flips and flops between 0 and 1
D is “data input”, Q is “data output”
Also called “D-type Flip-Flop”

## Slide 16: Camera Analogy Timing Terms
Want to take a portrait – timing right before and after taking picture
Set up time – don’t move since about to take picture (open camera shutter)
Hold time – need to hold still after shutter opens until camera shutter closes
Time click to data – time from open shutter until can see image on output (viewfinder)

## Slide 17: Hardware Timing Terms
Setup Time: when the input must be stable before the edge of the CLK
Hold Time: when the input must be stable after the edge of the CLK
“CLK-to-Q” Delay: how long it takes the output to change, measured from the edge of the CLK

## Slide 18: FSM Maximum Clock Frequency
What is the maximum frequency of this circuit?
Max Delay = Setup Time + CLK-to-Q Delay + CL Delay
Hint:
Frequency = 1/Period

## Slide 19: Pipelining to Improve Performance: BEFORE (1/2)
Timing…
Note: delay of 1 clock cycle from input to output.
Clock period limited by propagation delay of adder/shifter
High (1)
Low (0)
High (1)
Low (0)
High (1)
Low (0)
High (1)
Low (0)

## Slide 20: Pipelining to Improve Performance (2/2)
Timing…
Insertion of register allows higher clock frequency
More outputs per second
Ready before clock edge: setup time
Delay for Adder Combinational Logic
Delay for Setup + Clk to Q
Delay for Shifter Combinational Logic
Delay for Setup + Clk to Q

## Slide 21: Agenda
State Elements
Finite State Machines
And, in Conclusion, …

## Slide 22: Another Great (Theory) Idea: Finite State Machines (FSM)
You may have seen FSMs in other classes
Same basic idea
Function can be represented with a “state transition diagram”
With combinational logic and registers, any FSM can be implemented in hardware

## Slide 23: Example: 3 Ones FSM
Draw the FSM …
FSM to detect the occurrence of 3 consecutive 1’s in the Input
Assume state transitions are controlled by the clock: On each clock cycle the machine checks the inputs and moves to a new state and produces a new output …

## Slide 24: Hardware Implementation of FSM
=
+
Register needed to hold a representation of the machine’s state. Unique bit pattern for each state.
Combinational logic circuit is used to implement a function maps from present state (PS) and input to next state (NS) and output.
The register is used to break the feedback path between Next State (NS) and Prior State (PS), controlled by the clock

## Slide 25: Hardware for FSM: Combinational Logic
1
00
1
10
0
00
0
10
0
10
1
01
0
00
0
01
0
01
1
00
0
00
0
00
Output
NS
Input
PS
Truth table …
Can look at its functional specification, truth table form

## Slide 26: Hardware for FSM: Combinational Logic
1
00
1
10
0
00
0
10
0
10
1
01
0
00
0
01
0
01
1
00
0
00
0
00
Output
NS
Input
PS
Truth table …

## Slide 27: Hardware for FSM: Combinational Logic
1
00
1
10
0
00
0
10
0
10
1
01
0
00
0
01
0
01
1
00
0
00
0
00
Output
NS
Input
PS
Alternative Truth Table format: list only cases where value is a 1.Then restate as logic equations using PS1, PS0, Input
Truth table …

## Slide 28: Hardware for FSM: Combinational Logic
1
00
1
10
0
00
0
10
0
10
1
01
0
00
0
01
0
01
1
00
0
00
0
00
Output
NS
Input
PS
Alternative Truth Table format: list only cases where value is a 1.Then restate as logic equations using PS1, PS0, Input
Truth table …
1
10
Input
PS
Output is 1
1
00
Input
PS
NS bit 0 is 1
1
01
Input
PS
NS bit 1 is 1

## Slide 29: Hardware for FSM: Combinational Logic
1
00
1
10
0
00
0
10
0
10
1
01
0
00
0
01
0
01
1
00
0
00
0
00
Output
NS
Input
PS
Alternative Truth Table format: list only cases where value is a 1.Then restate as logic equations using PS1, PS0, Input
NS0 = PS1PS0Input
  NS0 = ~PS1~PS0Input
NS1 = PS1PS0Input
  NS1 = ~PS1PS0Input
Output= PS1PS0Input
  Output= PS1~PS0Input
Truth table …
1
10
Input
PS
Output is 1
1
00
Input
PS
NS bit 0 is 1
1
01
Input
PS
NS bit 1 is 1

## Slide 30: And, in Conclusion, …
Hardware systems made from Stateless Combinational Logic and Stateful “Memory” Logic (Registers)
Clocks tell us when D-flip-flops change
  Setup and Hold times important
We pipeline long-delay CL for faster clock cycle
  Split up the critical path
Finite State Machines extremely useful
Can implement FSM with register + logic