## Slide 1: CS 61C: Great Ideas in Computer Architecture Virtual Memory
Instructors:
Krste Asanovic, Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa12

## Slide 2: Review
Implementing precise interrupts in in-order pipelines:
  Save exceptions in pipeline until commit point
  Check for traps and interrupts before commit
  No architectural state overwritten before commit
Support multiprogramming with translation and protection
  Base and bound, simple scheme, suffers from memory fragmentation
  Paged systems remove external fragmentation but add indirection through page table

## Slide 3: You Are Here!
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Main Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s
Lecture

## Slide 4: Private Address Space per User
Each user has a page table
Page table contains an entry for each user page
VA1
User 1
Page Table
VA1
User 2
Page Table
VA1
User 3
Page Table
Physical Memory
free
OS
pages
Notes: OS ensures that the page tables are disjoint.

## Slide 5: A Problem in the Early Sixties
There were many applications whose data could not fit in the main memory, e.g., payroll
  Paged memory system reduced fragmentation but still required the whole program to be resident in the main memory

## Slide 6: Manual Overlays
Ferranti Mercury
1956
40k bits
main
640k bits
drum
Central Store
Assume an instruction can address all the storage on the drum
Method 1: programmer keeps track of addresses in the main memory and initiates an I/O transfer when required
  Difficult, error-prone!
Method 2: automatic initiation of I/O transfers by software address translation
  Brooker’s interpretive coding, 1960
  Inefficient!
Not just an ancient black art, e.g., IBM Cell microprocessor used in Playstation-3 has explicitly managed local store!
Notes: British Firm Ferranti, did Mercury and then Atlas
Method 1 too difficult for users
Method 2 too slow.

## Slide 7: Demand Paging in Atlas (1962)
Secondary
(Drum)
32x6 pages
Primary
32 Pages
512 words/page
Central
Memory
User sees 32 x 6 x 512 words
of storage
“A page from secondary
storage is brought into the primary storage whenever it is (implicitly) demanded by the processor.”
Tom Kilburn
Primary memory as a cache
for secondary memory
Notes: Single-level Store

## Slide 8: Hardware Organization of Atlas
Initial
Address
Decode
16 ROM pages
0.4 ~1 sec
2 subsidiary pages
1.4 sec
Main
32 pages
1.4 sec
Drum (4)
192 pages
8 Tape decks
88 sec/word
48-bit words
512-word pages
1 Page Address Register (PAR) per page frame
Compare the effective page address against all 32 PARs
match  normal access
no match  page fault
save the state of the partially executed
instruction
Effective
Address
system code
(not swapped)
system data
(not swapped)
0
31
PARs
<effective PN , status>

## Slide 9: Atlas Demand Paging Scheme
On a page fault:
  Input transfer into a free page is initiated
  The Page Address Register (PAR) is updated
  If no free page is left, a page is selected to be replaced (based on usage)
  The replaced page is written on the drum
    to minimize drum latency effect, the first empty page on the drum was selected
  The page table is updated to point to the new location of the page on the drum

## Slide 10: Recap: Typical Memory Hierarchy
Take advantage of the principle of locality to present the user with as much memory as is available in the cheapest technology at the speed offered by the fastest technology
Second
Level
Cache
(SRAM)
Control
Datapath
Secondary
Memory
(Disk)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
Speed (cycles): ½’s 1’s 10’s 100’s 10,000’s
Size (bytes): 100’s 10K’s M’s G’s T’s
Cost: highest lowest
Notes: Instead, the memory system of a modern computer consists of a series of black boxes ranging from the fastest to the slowest.
Besides variation in speed, these boxes also varies in size (smallest to biggest) and cost.
What makes this kind of arrangement work is one of the most important principle in computer design. The principle of locality. The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in detail in the next lectures on caches).

## Slide 11: Modern Virtual Memory Systems Illusion of a large, private, uniform store
Protection & Privacy
  several users, each with their private address space and one or more shared address spaces
page table  name space
Demand Paging
  Provides the ability to run programs larger than the primary memory
  Hides differences in machine configurations
The price is address translation on
each memory reference
OS
useri
Primary
Memory
Swapping
Store
VA
PA
mapping
TLB
Notes: Portability on machines with different memory configurations.

## Slide 12: Administrivia
Regrade request deadline Monday Nov 26
  For everything up to Project 4

## Slide 13: CS61C in the News “World's oldest digital computer successfully reboots”
Iain Thomson
The Register, 11/20/2012
“After three years of restoration by the National Museum of Computing (TNMOC) and staff at Bletchley Park, the world's oldest functioning digital computer has been successfully rebooted at a ceremony attended by two of its original developers. The 2.5 ton Harwell Dekatron, later renamed the Wolverhampton Instrument for Teaching Computation from Harwell (WITCH), was first constructed in 1949 and from 1951 ran at the USK's Harwell Atomic Energy Research Establishment, where it was used to process mathematical calculations for Britain's nuclear program.
The system uses 828 flashing Dekatron valves, each capable of holding a single digit, for volatile memory, plus 480 GPO 3000 type relays to shift calculations and six paper tape readers. It was very slow, taking a couple of seconds for each addition or subtraction, five seconds for multiplication and up to 15 for division.”

## Slide 14: Hierarchical Page Table
Level 1
Page Table
Level 2
Page Tables
Data Pages
page in primary memory
page in secondary memory
Root of the Current
Page Table
p1
offset
p2
Virtual Address
(Processor
Register)
PTE of a nonexistent page
p1 p2 offset
0
11
12
21
22
31
10-bit
L1 index
10-bit
L2 index
Physical Memory

## Slide 15: Two-Level Page Tables in Physical Memory
VA1
User 1
User1/VA1
User2/VA1
Level 1 PT User 1
Level 1 PT User 2
VA1
User 2
Level 2 PT User 2
Virtual Address Spaces
Physical Memory

## Slide 16: Address Translation & Protection
Every instruction and data access needs address
translation and protection checks
A good VM design needs to be fast (~ one cycle) and space efficient
Physical Address
Virtual Address
Address
Translation
Virtual Page No. (VPN)
offset
Physical Page No. (PPN)
offset
Protection
Check
Exception?
Kernel/User Mode
Read/Write

## Slide 17: Translation Lookaside Buffers (TLB)(really an Address Translation Cache!)
Address translation is very expensive!
  In a two-level page table, each reference becomes several memory accesses
Solution: Cache translations in TLB
TLB hit  Single-Cycle Translation
TLB miss  Page-Table Walk to refill
VPN offset
V R W D tag PPN
physical address
PPN offset
virtual address
hit?
(VPN = virtual page number)
(PPN = physical page number)
Notes: 3 memory references
2 page faults (disk accesses) + ..
Actually used in IBM before paged memory.

## Slide 18: TLB Designs
Typically 32-128 entries, usually fully associative
  Each entry maps a large page, hence less spatial locality across pages  more likely that two entries conflict
  Sometimes larger TLBs (256-512 entries) are 4-8 way set-associative
  Larger systems sometimes have multi-level (L1 and L2) TLBs
Random or FIFO replacement policy
No process information in TLB?
TLB Reach: Size of largest virtual address space that can be simultaneously mapped by TLB
  Example: 64 TLB entries, 4KB pages, one page per entry
  TLB Reach = _____________________________________________?

## Slide 19: TLB Designs
Typically 32-128 entries, usually fully associative
  Each entry maps a large page, hence less spatial locality across pages  more likely that two entries conflict
  Sometimes larger TLBs (256-512 entries) are 4-8 way set-associative
  Larger systems sometimes have multi-level (L1 and L2) TLBs
Random or FIFO replacement policy
No process information in TLB?
TLB Reach: Size of largest virtual address space that can be simultaneously mapped by TLB
  Example: 64 TLB entries, 4KB pages, one page per entry
  TLB Reach = _____________________________________________?
64 entries * 4 KB = 256 KB (if contiguous)

## Slide 20: Handling a TLB Miss
Software (MIPS, Alpha)
  TLB miss causes an exception and the operating system walks the page tables and reloads TLB. A privileged “untranslated” addressing mode used for walk
Hardware (SPARC v8, x86, PowerPC, RISC-V)
  A memory management unit (MMU) walks the page tables and reloads the TLB
  If a missing (data or PT) page is encountered during the TLB reloading, MMU gives up and signals a Page-Fault exception for the original instruction

## Slide 21: Flashcard Quiz: Which statement is false?
TLB miss is much faster than page fault
TLB exploits spatial locality
TLB hardware grows with larger page size
TLB exploits temporal locality

## Slide 22: Hierarchical Page Table Walk: SPARC v8
31 11 0
Virtual Address
Index 1 Index 2 Index 3 Offset
31 23 17 11 0
Context
Table
Register
Context
Register
root ptr
PTP
PTP
PTE
Context Table
L1 Table
L2 Table
L3 Table
Physical Address
PPN Offset
MMU does this table walk in hardware on a TLB miss

## Slide 23: Page-Based Virtual-Memory Machine (Hardware Page-Table Walk)
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Page Fault?
Protection violation?
Page Fault?
Protection violation?
Assumes page tables held in untranslated physical memory
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Physical Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?

## Slide 24: Address Translation: putting it all together
Virtual Address
TLB
Lookup
Page Table
Walk
Update TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
(to cache)
miss
hit
the page is
Ï memory Î memory
denied
permitted
Protection
Fault
hardware
hardware or software
software
SEGFAULT
Where?
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 25: Handling VM-related traps
Handling a TLB miss needs a hardware or software mechanism to refill TLB
Handling a page fault (e.g., page is on disk) needs a restartable trap so software handler can resume after retrieving page
  Precise exceptions are easy to restart
  Can be imprecise but restartable, but this complicates OS software
Handling protection violation may abort process
PC
Inst TLB
Inst. Cache
D
Decode
E
M
Data TLB
Data Cache
W
+
TLB miss? Page Fault?
Protection violation?
TLB miss? Page Fault?
Protection violation?

## Slide 26: Address Translation in CPU Pipeline
Need to cope with additional latency of TLB:
  slow down the clock?
  pipeline the TLB and cache access?
  virtual address caches (see CS152)
  parallel TLB/cache access
PC
Inst TLB
Inst. Cache
D
Decode
E
M
Data TLB
Data Cache
W
+
TLB miss? Page Fault?
Protection violation?
TLB miss? Page Fault?
Protection violation?

## Slide 27: Concurrent Access to TLB & Cache (Virtual Index/Physical Tag)
Index L is available without consulting the TLB
  cache and TLB accesses can begin simultaneously!
Tag comparison is made after both accesses are completed
Cases: L + b = k, L + b < k, L + b > k
VPN L b
TLB
Direct-map Cache
2L blocks
2b-byte block
PPN Page Offset
=
hit?
Data
Physical Tag
Tag
VA
PA
Virtual
Index
k

## Slide 28: Virtual-Index Physical-Tag Caches: Associative Organization
How does this scheme scale to larger caches?
VPN a L = k-b b
TLB
Direct-map
2L blocks
PPN Page Offset
=
hit?
Data
Phy.
Tag
Tag
VA
PA
Virtual
Index
k
Direct-map
2L blocks
2a
=
2a
After the PPN is known, 2a physical tags are compared
Notes:   Consider 4-Kbyte pages and caches with 32-byte blocks
  32-Kbyte cache  2a = 8
    4-Mbyte cache  2a =1024 No !

## Slide 29: VM features track historical uses:
Bare machine, only physical addresses
  One program owned entire machine
Batch-style multiprogramming
  Several programs sharing CPU while waiting for I/O
  Base & bound: translation and protection between programs (not virtual memory)
  Problem with external fragmentation (holes in memory), needed occasional memory defragmentation as new jobs arrived
Time sharing
  More interactive programs, waiting for user. Also, more jobs/second.
  Motivated move to fixed-size page translation and protection, no external fragmentation (but now internal fragmentation, wasted bytes in page)
  Motivated adoption of virtual memory to allow more jobs to share limited physical memory resources while holding working set in memory
Virtual Machine Monitors
  Run multiple operating systems on one machine
  Idea from 1970s IBM mainframes, now common on laptops
    e.g., run Windows on top of Mac OS X
  Hardware support for two levels of translation/protection
    Guest OS virtual -> Guest OS physical -> Host machine physical
  Also basis of Cloud Computing
    Virtual machine instances for Project 1

## Slide 30: Acknowledgements
These slides contain material developed and copyright by:
  Arvind (MIT)
  Krste Asanovic (MIT/UCB)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252