## Slide 1: CS 61C: Great Ideas in Computer Architecture Control and Pipelining
Instructor:
Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa13

## Slide 2: You Are Here!
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Today’s Lecture
Main Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0

## Slide 3: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions

## Slide 4: Instruction Level Parallelism (ILP)
Another parallelism form to go with Request Level Parallelism and Data Level Parallelism
  RLP – e.g., Warehouse Scale Computing
  DLP – e.g., SIMD, Map-Reduce
ILP – e.g., Pipelined Instruction Execution
  5 stage pipeline => 5 instructions executing simultaneously, one at each pipeline stage

## Slide 5: Agenda
Pipelined Execution
Pipelined Datapath
Structural and Data Hazards
Control Hazards

## Slide 6: Agenda
Pipelined Execution
Pipelined Datapath
Structural and Data Hazards
Control Hazards

## Slide 7: Review: Single-Cycle Processor
Five steps to design a processor:
  1. Analyze instruction set  datapath requirements
  2. Select set of datapath components & establish clock methodology
  3. Assemble datapath meeting the requirements: re-examine for pipelining
  4. Analyze implementation of each instruction to determine setting of control points that effects the register transfer.
  5. Assemble the control logic
    Formulate Logic Equations
    Design Circuits
Control
Datapath
Memory
Processor
Input
Output

## Slide 8: Pipeline Analogy: Doing Laundry
Ann, Brian, Cathy, Dave each have one load of clothes to wash, dry, fold, and put away
  Washer takes 30 minutes
  Dryer takes 30 minutes
  “Folder” takes 30 minutes
  “Stasher” takes 30 minutes to put clothes into drawers
A
B
C
D

## Slide 9: Sequential Laundry
Sequential laundry takes 8 hours for 4 loads
T
a
s
k
O
r
d
e
r
B
C
D
A
30
Time
30
30
30
30
30
30
30
30
30
30
30
30
30
30
30
6 PM
7
8
9
10
11
12
1
2 AM

## Slide 10: Pipelined Laundry
Pipelined laundry takes 3.5 hours for 4 loads!
T
a
s
k
O
r
d
e
r
B
C
D
A
12
2 AM
6 PM
7
8
9
10
11
1
Time
30
30
30
30
30
30
30

## Slide 11: Pipelining Lessons (1/2)
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Multiple tasks operating simultaneously using different resources
Potential speedup = Number pipe stages (4 in this case)
Time to fill pipeline and time to drain it reduces speedup: 8 hours/3.5 hours or 2.3X v. potential 4X in this example
6 PM
7
8
9
Time
B
C
D
A
30
30
30
30
30
30
30
T
a
s
k
O
r
d
e
r

## Slide 12: Pipelining Lessons (2/2)
Suppose new Washer takes 20 minutes, new Stasher takes 20 minutes. How much faster is pipeline?
Pipeline rate limited by slowest pipeline stage
Unbalanced lengths of pipe stages reduces speedup
6 PM
7
8
9
Time
B
C
D
A
30
30
30
30
30
30
30
T
a
s
k
O
r
d
e
r

## Slide 13: Agenda
Pipelined Execution
Pipelined Datapath
Structural and Data Hazards
Control Hazards

## Slide 14: Review: RISC Design Principles
“A simpler core is a faster core”
Reduction in the number and complexity of instructions in the ISA  simplifies pipelined implementation
Common RISC strategies:
  Fixed instruction length, generally a single word (MIPS = 32b); Simplifies process of fetching instructions from memory
  Simplified addressing modes; (MIPS just register + offset) Simplifies process of fetching operands from memory
  Fewer and simpler instructions in the instruction set; Simplifies process of executing instructions
  Simplified memory access: only load and store instructions access memory;
  Let the compiler do it. Use a good compiler to break complex high-level language statements into a number of simple assembly language statements

## Slide 15: Review: Single Cycle Datapath
op
rs
rt
immediate
0
16
21
26
31
Data Memory {R[rs] + SignExt[imm16]} = R[rt]
32
ALUctr=
clk
busW
RegWr=
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst=
Extender
32
16
imm16
ALUSrc=
ExtOp=
MemtoReg=
clk
Data In
32
MemWr=
zero
0
1
0
1
=
ALU
0
1
WrEn
Adr
Data
Memory
5
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
nPC_sel=
instr
fetch
unit
clk
Notes: The store instruction performs the inverse function of the load. Instead of loading data from memory, the store instruction sends the contents of register specified by Rt to data memory.
Similar to the load instruction, the store instruction needs to read the contents of register Rs (points to Ra port) and add it to the sign extended verion of the immediate filed (Imm16, ExtOp = 1, ALUSrc = 1) to form the data memory address (ALUctr = add).
However unlike the Load instructoion where busB is not used, the store instruction will use busB to send the data to the Data memory.
Consequently, the Rt field of the instruction has to be fed to the Rb port of the register file.
In order to write the Data Memory properly, the MemWr signal has to be set to 1.
Notice that the store instruction does not update the register file. Therefore, RegWr must be set to zero and consequently control signals RegDst and MemtoReg are don’t cares.
And once again we need to set the control signals Branch and Jump to zero to ensure proper Program Counter updataing.
Well, by now, you are probably tied of these boring stuff where Branch and Jump are zero so let’s look at something different--the bracnh instruction.
+3 = 31 min. (Y:11)

## Slide 16: Steps in Executing MIPS
1) IF: Instruction Fetch, Increment PC
2) ID: Instruction Decode, Read Registers
3) EX: Execution Mem-ref: Calculate Address Arith-log: Perform Operation
4) Mem: Load: Read Data from Memory Store: Write Data to Memory
5) WB: Write Data Back to Register

## Slide 17: Redrawn Single-Cycle Datapath
PC
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write Back

## Slide 18: Pipelined Datapath
PC
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write Back
Add registers between stages
  Hold information produced in previous cycle
5 stage pipeline; clock rate potential 5X faster

## Slide 19: More Detailed Pipeline
Registers named for adjacent stages, e.g., IF/ID

## Slide 20: IF for Load, Store, …
Highlight combinational logic components used + right half of state logic on read, left half on write

## Slide 21: ID for Load, Store, …

## Slide 22: EX for Load

## Slide 23: MEM for Load

## Slide 24: WB for Load
Wrong register number
Has Bug that was in 1st edition of textbook!

## Slide 25: Corrected Datapath for Load
Correct register number

## Slide 26: Pipelined Execution Representation
Every instruction must take same number of steps, also called pipeline stages, so some will go idle sometimes
IF
ID
EX
Mem
WB
IF
ID
EX
Mem
WB
IF
ID
EX
Mem
WB
IF
ID
EX
Mem
WB
IF
ID
EX
Mem
WB
IF
ID
EX
Mem
WB
Time

## Slide 27: Graphical Pipeline Diagrams
PC
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write Back
Use datapath figure below to represent pipeline
IF
ID
EX
Mem
WB
ALU
I$
Reg
D$
Reg

## Slide 28: Graphical Pipeline Representation
I
n
s
t
r.
O
r
d
e
r
Load
Add
Store
Sub
Or
I$
Time (clock cycles)
I$
ALU
Reg
Reg
I$
D$
ALU
ALU
Reg
D$
Reg
I$
D$
Reg
ALU
Reg
Reg
Reg
D$
Reg
D$
ALU
(In Reg, right half highlight read, left half write)
Reg
I$

## Slide 29: Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
What is pipelined clock rate?
  Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 30: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)

## Slide 31: Pipeline Speedup
If all stages are balanced
  i.e., all take the same time
  Time between instructionspipelined = Time between instructionsnonpipelined Number of stages
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease

## Slide 32: Agenda
Pipelined Execution
Pipelined Datapath
Structural and Data Hazards
Control Hazards

## Slide 33: Hazards
Situations that prevent starting the next logical instruction in the next clock cycle
Structural hazards
  Required resource is busy (e.g., stasher is studying)
Data hazard
  Need to wait for previous instruction to complete its data read/write (e.g., pair of socks in different loads)
Control hazard
  Deciding on control action depends on previous instruction (e.g., how much detergent based on how clean prior load turns out)

## Slide 34: 1. Structural Hazards
Conflict for use of a resource
In MIPS pipeline with a single memory
  Load/Store requires memory access for data
  Instruction fetch would have to stall for that cycle
    Causes a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  In reality, provide separate L1 instruction cache and L1 data cache

## Slide 35: 1. Structural Hazard #1: Single Memory
Read same memory twice in same clock cycle
I$
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 36: 1. Structural Hazard #2: Registers (1/2)
Can we read and write to registers simultaneously?
I$
sw
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 37: 1. Structural Hazard #2: Registers (2/2)
Two different solutions have been used:
  1) RegFile access is VERY fast: takes less than half the time of ALU stage
    Write to Registers during first half of each clock cycle
    Read from Registers during second half of each clock cycle
  2) Build RegFile with independent read and write ports
Result: can perform Read and Write during same clock cycle

## Slide 38: 2. Data Hazards
An instruction depends on completion of data access by a previous instruction
  add $s0, $t0, $t1 sub $t2, $s0, $t3

## Slide 39: Forwarding (aka Bypassing)
Use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra connections in the datapath

## Slide 40: Corrected Datapath for Forwarding?

## Slide 41: Forwarding Paths

## Slide 42: Load-Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!

## Slide 43: Stall/Bubble in the Pipeline
Stall inserted here

## Slide 44: Pipelining and ISA Design
MIPS Instruction Set designed for pipelining
All instructions are 32-bits
  Easier to fetch and decode in one cycle
  x86: 1- to 17-byte instructions
  (x86 HW actually translates to internal RISC instructions!)
Few and regular instruction formats, 2 source register fields always in same place
  Can decode and read registers in one step
Memory operands only in Loads and Stores
  Can calculate address 3rd stage, access memory 4th stage
Alignment of memory operands
  Memory access takes only one cycle

## Slide 45: Why Isn’t the Destination Register Always in the Same Field in MIPS ISA?
SPUR processor
(A project Dave Patterson and Randy worked on together)
Need to have 2 part immediate if 2 sources and 1 destination always in same place
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits

## Slide 46: 3. Control Hazards
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
BEQ, BNE in MIPS pipeline
Simple solution Option 1: Stall on every branch until have new PC value
  Would add 2 bubbles/clock cycles for every Branch! (~ 20% of instructions executed)

## Slide 47: Stall => 2 Bubbles/Clocks
Where do we do the compare for the branch?
I$
beq
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 48: 3. Control Hazard: Branching
Optimization #1:
  Insert special branch comparator in Stage 2
  As soon as instruction is decoded (Opcode identifies it as a branch), immediately make a decision and set the new value of the PC
  Benefit: since branch is complete in Stage 2, only one unnecessary instruction is fetched, so only one no-op is needed
  Side Note: means that branches are idle in Stages 3, 4 and 5

## Slide 49: Corrected Datapath for BEQ/BNE?

## Slide 50: One Clock Cycle Stall
Branch comparator moved to Decode stage.
I$
beq
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 51: Agenda
Pipelined Execution
Pipelined Datapath
Structural and Data Hazards
Control Hazards

## Slide 52: 3. Control Hazards
Option 2: Predict outcome of a branch, fix up if guess wrong
  Must cancel all instructions in pipeline that depended on guess that was wrong
Simplest hardware if we predict that all branches are NOT taken
  Why?

## Slide 53: 3. Control Hazard: Branching
Option #3: Redefine branches
  Old definition: if we take the branch, none of the instructions after the branch get executed by accident
  New definition: whether or not we take the branch, the single instruction immediately following the branch gets executed (the branch-delay slot)
Delayed Branch means we always execute inst after branch
This optimization is used with MIPS

## Slide 54: 3. Control Hazard: Branching
Notes on Branch-Delay Slot
  Worst-Case Scenario: put a no-op in the branch-delay slot
  Better Case: place some instruction preceding the branch in the branch-delay slot—as long as the changed doesn’t affect the logic of program
    Re-ordering instructions is common way to speed up programs
    Compiler usually finds such an instruction 50% of time
    Jumps also have a delay slot …

## Slide 55: Example: Nondelayed vs. Delayed Branch
add $1, $2, $3
sub $4, $5, $6
beq $1, $4, Exit
or $8, $9, $10
xor $10, $1, $11
Nondelayed Branch
add $1, $2, $3
sub $4, $5, $6
beq $1, $4, Exit
or $8, $9, $10
xor $10, $1, $11
Delayed Branch
Exit:
Exit:

## Slide 56: Delayed Branch/Jump and MIPS ISA?
Why does JAL put PC+8 in register 31?

## Slide 57: Delayed Branch/Jump and MIPS ISA?
Why does JAL put PC+8 in register 31?
JAL executes following instruction (PC+4) so should return to PC+8

## Slide 58: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction
C code for A = B + E; C = B + F;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
11 cycles
13 cycles

## Slide 59: Peer Instruction
Thanks to pipelining, I have reduced the time it took me to wash my one shirt.
Longer pipelines are always a win (since less work per stage & a faster clock).
A)(orange) I is True and II is True
B)(green) I is False and II is True
C)(pink) I is True and II is False
D)(yellow) I is False and II is False

## Slide 60: Peer Instruction Answer
Thanks to pipelining, I have reduced the time it took me to wash my one shirt.
Longer pipelines are always a win (since less work per stage & a faster clock).
F A L S E
F A L S E
Throughput better, not latency!
“…longer pipelines do usually mean faster clock rate, but hazards can cause problems!”
12
a) FF
b) FT
c) TF
d) TT

## Slide 61: And, in Conclusion, …
Pipelining improves performance by increasing instruction throughput: exploits ILP
  Executes multiple instructions in parallel
  Each instruction has the same latency
  Key enabler is placing registers between pipeline stages
Subject to hazards
  Structure, data, control
Stalls reduce performance
  But are required to get correct results
Compiler can arrange code to avoid hazards and stalls
  Requires knowledge of the pipeline structure