## Slide 1: CS 61C: Great Ideas in Computer Architecture Instruction Level Parallelism: Multiple Instruction Issue
Instructor:
Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa13

## Slide 2: You Are Here!
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Today’s Lecture
Main Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0

## Slide 3: Review: The Three Kinds of Hazards
Situations that prevent starting the next logical instruction in the next clock cycle
Structural hazards
  Required resource is busy (e.g., single memory)
Data hazard
  Need to wait for previous instruction to complete its data read/write (e.g., read before write)
Control hazard
  Deciding on control action depends on previous instruction (e.g., what to fetch after branch)

## Slide 4: Review: Control Hazard/Branching
Redefine branches
  Old definition: if we take the branch, none of the instructions after the branch get executed by accident
  New definition: whether or not we take the branch, the single instruction immediately following the branch gets executed (the branch-delay slot)
Delayed Branch means we always execute inst after branch
Optimization is used in MIPS

## Slide 5: Review: Control Hazard/Branching
Notes on Branch-Delay Slot
  Worst-Case Scenario: put a no-op in the branch-delay slot
  Better Case: place some instruction preceding the branch in the branch-delay slot—as long as the changed doesn’t affect the logic of program
    Re-ordering instructions is common way to speed up programs
    Compiler usually finds such an instruction 50% of time
    Jumps also have a delay slot …

## Slide 6: Note: Delayed Branch/Jump
Why does MIPS JAL put PC+8 in register 31?
JAL executes following instruction (PC+4) so should return to PC+8

## Slide 7: Compiler Assist to Minimize Hazards: Code Scheduling
Reorder code to avoid use of load result in the next instruction
C code for A = B + E; C = B + F;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
11 cycles
13 cycles

## Slide 8: Agenda
Higher Level ILP
Static Instruction Scheduling
Dynamic Instruction Scheduling
Out of Order Execution
Parallelism Big Picture
And, in Conclusion, …

## Slide 9: Agenda
Higher Level ILP
Static Instruction Scheduling
Dynamic Instruction Scheduling
Out of Order Execution
Parallelism Big Picture
And, in Conclusion, …

## Slide 10: Greater Instruction-Level Parallelism (ILP)
Deeper pipeline (5 => 10 => 15 stages)
  Less work per stage  shorter clock cycle
Multiple issue superscalar
  Replicate pipeline stages  multiple pipelines
  Start multiple instructions per clock cycle
CPI < 1, so can use Instructions Per Cycle (IPC)
  E.g., 4 GHz 4-way multiple-issue
    16 BIPS, peak CPI = 0.25, peak IPC = 4
  But dependencies reduce this in practice

## Slide 11: Multiple Issue
Static multiple issue
  Compiler groups instructions to be issued together
  Packages them into “issue slots”
  Compiler detects and avoids hazards
Dynamic multiple issue
  CPU examines instruction stream and chooses instructions to issue each cycle
  Compiler can help by reordering instructions
  CPU resolves hazards using advanced techniques at runtime

## Slide 12: Superscalar Laundry: Parallel per Stage
More resources, HW to match mix of parallel tasks?
T
a
s
k
O
r
d
e
r
12
2 AM
6 PM
7
8
9
10
11
1
Time
B
C
D
A
E
F
(light clothing)
(dark clothing)
(very dirty clothing)
(light clothing)
(dark clothing)
(very dirty clothing)
30
30
30
30
30

## Slide 13: Pipeline Depth and Issue Width
Intel Processors over Time
Microprocessor | Year | Clock Rate | Pipeline Stages | Issue width | Cores | Power
i486 | 1989 | 25 MHz | 5 | 1 | 1 | 5W
Pentium | 1993 | 66 MHz | 5 | 2 | 1 | 10W
Pentium Pro | 1997 | 200 MHz | 10 | 3 | 1 | 29W
P4 Willamette | 2001 | 2000 MHz | 22 | 3 | 1 | 75W
P4 Prescott | 2004 | 3600 MHz | 31 | 3 | 1 | 103W
Core 2 Conroe | 2006 | 2930 MHz | 14 | 4 | 2 | 75W
Core 2 Yorkfield | 2008 | 2930 MHz | 16 | 4 | 4 | 95W
Core i7 Gulftown | 2010 | 3460 MHz | 16 | 4 | 6 | 130W

## Slide 14: Pipeline Depth and Issue Width
Chart: 
| 1989.0 | 1993.0 | 1997.0 | 2001.0 | 2004.0 | 2006.0 | 2008.0 | 2010.0
Clock | 25 | 66 | 200 | 2000 | 3600 | 2930 | 2930 | 3460
Power | 5 | 10 | 29 | 75 | 103 | 75 | 95 | 130
Pipeline Stages | 5 | 5 | 10 | 22 | 31 | 14 | 16 | 16
Issue width | 1 | 2 | 3 | 3 | 3 | 4 | 4 | 4
Cores | 1 | 1 | 1 | 1 | 1 | 2 | 4 | 6

## Slide 15: Agenda
Higher Level ILP
Static Instruction Scheduling
Dynamic Instruction Scheduling
Out of Order Execution
Parallelism Big Picture
And, in Conclusion, …

## Slide 16: Static Multiple Issue
Compiler groups instructions into issue packets
  Group of instructions that can issue in a single cycle
  Determined by pipeline resources required
Think of issue packet as a “very long instruction”
  Specifies multiple concurrent operations
  Called VLIW for Very Long Instruction Word

## Slide 17: Scheduling Static Multiple Issue
Compiler must remove some/all hazards
  Reorder instructions into issue packets
  No dependencies with a packet
  Possibly some dependencies between packets
    Varies between ISAs; compiler must know!
  Pad with nop if necessary

## Slide 18: MIPS with Static Dual Issue
Dual-issue packets
  One ALU/branch instruction + One load/store instruction
  64-bit aligned
    ALU/branch, then load/store
    Pad an unused instruction with nop
Address | Instruction type | Pipeline Stages |  |  |  |  |  | 
n | ALU/branch | IF | ID | EX | MEM | WB |  | 
n + 4 | Load/store | IF | ID | EX | MEM | WB |  | 
n + 8 | ALU/branch |  | IF | ID | EX | MEM | WB | 
n + 12 | Load/store |  | IF | ID | EX | MEM | WB | 
n + 16 | ALU/branch |  |  | IF | ID | EX | MEM | WB
n + 20 | Load/store |  |  | IF | ID | EX | MEM | WB

## Slide 19: Datapath with Static Dual Issue
1 Extra ALU
1 Extra Sign Ext
2 Extra Reg Read Ports
1 Extra Write Port
1 Extra 32-bit instruction

## Slide 20: Hazards in the Dual-Issue MIPS
More instructions executing in parallel
EX data hazard
  Forwarding avoided stalls with single-issue
  Now can’t use ALU result for load/store in same packet
    add $t0, $s0, $s1 load $s2, 0($t0)
    Split into two packets, effectively a stall
Load-use hazard
  Still one cycle use latency, but now two instructions
More aggressive scheduling required

## Slide 21: Scheduling Example
Schedule this for dual-issue MIPS
Loop: lw $t0, 0($s1) # $t0=array element addu $t0, $t0, $s2 # add scalar in $s2 sw $t0, 0($s1) # store result addi $s1, $s1,–4 # decrement pointer bne $s1, $zero, Loop # branch $s1!=0
 | ALU/branch | Load/store | cycle
Loop: | nop | lw $t0, 0($s1) | 1
 | addi $s1, $s1,–4 | nop | 2
 | addu $t0, $t0, $s2 | nop | 3
 | bne $s1, $zero, Loop | sw $t0, 4($s1) | 4
  IPC = 5/4 = 1.25 (vs. peak IPC = 2)

## Slide 22: Loop Unrolling
Replicate loop body to expose more parallelism
  Reduces loop-control overhead
Use different registers per replication
  Called register renaming
  Avoid loop-carried anti-dependencies
    Store followed by a load of the same register
    Aka “name dependence”
      Reuse of a register name but no real dependency between instructions

## Slide 23: Loop Unrolling Example
IPC = 14/8 = 1.75
  Closer to 2, but at cost of more registers and bigger code
 | ALU/branch | Load/store | cycle
Loop: | addi $s1, $s1,–16 | lw $t0, 0($s1) | 1
 | nop | lw $t1, 12($s1) | 2
 | addu $t0, $t0, $s2 | lw $t2, 8($s1) | 3
 | addu $t1, $t1, $s2 | lw $t3, 4($s1) | 4
 | addu $t2, $t2, $s2 | sw $t0, 16($s1) | 5
 | addu $t3, $t3, $s2 | sw $t1, 12($s1) | 6
 | nop | sw $t2, 8($s1) | 7
 | bne $s1, $zero, Loop | sw $t3, 4($s1) | 8

## Slide 24: Administrivia
As of today, made 1 pass over all Big Ideas in Computer Architecture
Following lectures go into more depth on topics you’ve already seen while you work on projects
  1 Lecture on Memory + Caches
  2 Lectures on Dependability/Reliability/Redundancy
  1 Lecture on Virtual Memory + Virtual Machines
  1 on Programming Contest (Extra Credit Project 3)
  1 on Course Wrap-up and Review

## Slide 25: Administrivia
Final Exam
  Friday, December 20, 8-11 AM
  Room TBD
  Will be assigned by course account login
  Comprehensive, but concentrated on material since midterm examination
  Closed book/note, open crib sheet as before
  Special consideration students, please contact us

## Slide 26: Agenda
Higher Level ILP
Static Instruction Scheduling
Dynamic Instruction Scheduling
Out of Order Execution
Parallelism Big Picture
And, in Conclusion, …

## Slide 27: Dynamic Multiple Issue
“Superscalar” processors
CPU decides whether to issue 0, 1, 2, … instructions each cycle
  Avoiding structural and data hazards
Avoids need for compiler scheduling
  Though it may still help
  Code semantics ensured by the CPU

## Slide 28: Dynamic Pipeline Scheduling
Allow the CPU to execute instructions out of order to avoid stalls
  But commit result to registers in order
Example
  lw $t0, 20($s2) addu $t1, $t0, $t2 subu $s4, $s4, $t3 slti $t5, $s4, 20
  Can start subu while addu is waiting for lw
Especially if cache misses, can execute many instructions

## Slide 29: Why Do Dynamic Scheduling?
Why not just let the compiler schedule code?
Not all stalls are predicable
  e.g., cache misses
Can’t always schedule around branches
  Branch outcome is dynamically determined
Different implementations of an ISA have different latencies and hazards

## Slide 30: Speculation
“Guess” what to do with an instruction
  Start operation as soon as possible
  Check whether guess was right
    If so, complete the operation
    If not, roll-back and do the right thing
Examples
  Speculate on branch outcome (Branch Prediction)
    Roll back if path taken is different
  Speculate on load
    Roll back if location is updated
Can be done in hardware or by compiler
Common to static and dynamic multiple issue

## Slide 31: Pipeline Hazard: Matching socks in later load
A depends on D; stall since folder tied up;
T
a
s
k
O
r
d
e
r
B
C
D
A
E
F
bubble
12
2 AM
6 PM
7
8
9
10
11
1
Time
30
30
30
30
30
30
30

## Slide 32: Out-of-Order Laundry: Don’t Wait
A depends on D; rest continue; need more resources to allow out-of-order
T
a
s
k
O
r
d
e
r
12
2 AM
6 PM
7
8
9
10
11
1
Time
B
C
D
A
30
30
30
30
30
30
30
E
F
bubble

## Slide 33: Not a Simple Linear Pipeline
Three major units operating in parallel
One Instruction fetch and issue unit
  Issues instructions in program order
Many parallel functional (execution) units
  Each functional unit has input buffers called Reservation Stations
  Holds operands and records the operation
  Can execute instructions out-of-program-order (OOO)
One Commit unit
  Gets results from functional unit and saves in buffers called Reorder Buffer
  Stores results once branch resolved so OK to execute
  Commits results in program order

## Slide 34: Agenda
Higher Level ILP
Static Instruction Scheduling
Dynamic Instruction Scheduling
Out of Order Execution
Parallelism Big Picture
And, in Conclusion, …

## Slide 35: Out-of-Order Execution (1/2)
Basically, unroll loops in hardware
Fetch instructions in program order (≤4/clock)
Predict branches as taken/untaken
To avoid hazards on registers, rename registers using a set of internal registers (~80 registers)
Collection of renamed instructions might execute in a window (~60 instructions)
Execute instructions with ready operands in 1 of multiple functional units (ALUs, FPUs, Ld/St)

## Slide 36: Out-of-Order Execution (2/2)
Basically, unroll loops in hardware
Buffer results of executed instructions until predicted branches are resolved in reorder buffer
If predicted branch correctly, commit results in program order
If predicted branch incorrectly, discard all dependent results and start with correct PC

## Slide 37: Dynamically Scheduled CPU
Results also sent to any waiting reservation stations
Reorders buffer for register writes
Can supply operands for issued instructions
Preserves dependencies
Hold pending operands

## Slide 38: Out Of Order Intel
All use OOO since 2001
Microprocessor | Year | Clock Rate | Pipeline Stages | Issue width | Out-of-order/ Speculation | Cores | Power
i486 | 1989 | 25MHz | 5 | 1 | No | 1 | 5W
Pentium | 1993 | 66MHz | 5 | 2 | No | 1 | 10W
Pentium Pro | 1997 | 200MHz | 10 | 3 | Yes | 1 | 29W
P4 Willamette | 2001 | 2000MHz | 22 | 3 | Yes | 1 | 75W
P4 Prescott | 2004 | 3600MHz | 31 | 3 | Yes | 1 | 103W
Core | 2006 | 2930MHz | 14 | 4 | Yes | 2 | 75W
Core 2 Yorkfield | 2008 | 2930 MHz | 16 | 4 | Yes | 4 | 95W
Core i7 Gulftown | 2010 | 3460 MHz | 16 | 4 | Yes | 6 | 130W

## Slide 39: Does Multiple Issue Work?
Yes, but not as much as we’d like
Programs have real dependencies that limit ILP
Some dependencies are hard to eliminate
  e.g., pointer aliasing
Some parallelism is hard to expose
  Limited window size during instruction issue
Memory delays and limited bandwidth
  Hard to keep pipelines full
Speculation can help if done well

## Slide 40: Agenda
Higher Level ILP
Static Instruction Scheduling
Dynamic Instruction Scheduling
Out of Order Execution
Parallelism Big Picture
And, in Conclusion, …

## Slide 41: Big Picture on Parallelism
Two types of parallelism in applications
Data-Level Parallelism (DLP): arises because there are many data items that can be operated on at the same time
Task-Level Parallelism (TLP): arises because tasks of work are created that can operate largely in parallel

## Slide 42: Big Picture on Parallelism
Hardware can exploit app Data LP and Task LP in 4 ways:
Instruction-Level Parallelism: Hardware exploits application DLP using ideas like pipelining and speculative execution
SIMD architectures: exploit app DLP by applying a single instruction to a collection of data in parallel
Thread-Level Parallelism: exploits either app DLP or TLP in a tightly-coupled hardware model that allows for interaction among parallel threads
Request-Level Parallelism: exploits parallelism among largely decoupled tasks and is specified by the programmer of the operating system

## Slide 43: Peer Question
State if following techniques are associated primarily with a software- or hardware-based approach to exploiting ILP (in some cases, the answer may be both): Superscalar, Out-of-Order execution, Speculation, Register Renaming
 | Super-scalar | Out of Order | Specu-lation | Register Renaming
Orange | HW | HW | HW | HW
Green | HW | HW | Both | Both
Pink | HW | HW | HW | Both
Yellow | HW | HW | HW | SW

## Slide 44: Peer Question
State if following techniques are associated primarily with a software- or hardware-based approach to exploiting ILP (in some cases, the answer may be both): Superscalar, Out-of-Order execution, Speculation, Register Renaming
 | Super-scalar | Out of Order | Specu-lation | Register Renaming
Orange | HW | HW | HW | HW
Green | HW | HW | Both | Both
Pink | HW | HW | HW | Both
Yellow | HW | HW | HW | SW

## Slide 45: Peer Instruction
Instr LP, SIMD, Thread LP, Request LP are examples of
Parallelism above (∧) the Instruction Set Architecture
Parallelism explicitly at (=) the level of the ISA
Parallelism below (∨) the level of the ISA
 | Inst. LP | SIMD | Thr. LP | Req. LP
Orange | ∨ | = | = | ∧
Green | = | = | ∧ | ∧
Pink | ∨ | = | ∧ | ∧
Yellow | = | ∧ | ∧ | ∧
Notes: Pink

## Slide 46: Peer Instruction
Instr LP, SIMD, Thread LP, Request LP are examples of
Parallelism above (∧) the Instruction Set Architecture
Parallelism explicitly at (=) the level of the ISA
Parallelism below (∨) the level of the ISA
 | Inst. LP | SIMD | Thr. LP | Req. LP
Orange | ∨ | = | = | ∧
Green | = | = | ∧ | ∧
Pink | ∨ | = | ∧ | ∧
Yellow | = | ∧ | ∧ | ∧
Notes: Pink

## Slide 47: Peer Instruction
Thanks to pipelining, I have reduced the time it took me to wash my one shirt.
Longer pipelines are always a win (since less work per stage & a faster clock).
A)(orange) I is True and II is True
B)(green) I is False and II is True
C)(pink) I is True and II is False
D)(yellow) I is False and II is False

## Slide 48: Peer Answer
Thanks to pipelining, I have reduced the time it took me to wash my one shirt.
Longer pipelines are always a win (since less work per stage & a faster clock).
Red I is True and II is True
Orange I is False and II is True
Green I is True and II is False
Yellow I is False and II is False

## Slide 49: Peer Question
Not all instructions are active in every stage of the 5-stage pipeline. Ignoring the effects of hazards, which of the following is true?
1. Allowing jumps, branches, and ALU instructions to take fewer stages than the 5 required by the load instruction will increase pipeline performance for most programs.
2. You cannot make ALU instructions take fewer cycles because of the write back of the result, but branches and jumps can take fewer cycles, so there is some opportunity for improvement.
3. Instead of trying to make instructions take fewer cycles, we should explore making the pipeline longer, so that instructions take more cycles, but the cycles are shorter. This could improve performance.
4. The number of pipe stages per instruction affects throughput, not latency.
Orange: 1
Green: 2
Pink: 3
Yellow: 4
Notes: Pink: Statements 3 are correct; the rest are incorrect

## Slide 50: Peer Answer
Not all instructions are active in every stage of the 5-stage pipeline. Ignoring the effects of hazards, which of the following is true?
1. Allowing jumps, branches, and ALU instructions to take fewer stages than the 5 required by the load instruction will increase pipeline performance for most programs.
2. You cannot make ALU instructions take fewer cycles because of the write back of the result, but branches and jumps can take fewer cycles, so there is some opportunity for improvement.
3. Instead of trying to make instructions take fewer cycles, we should explore making the pipeline longer, so that instructions take more cycles, but the cycles are shorter. This could improve performance.
4. The number of pipe stages per instruction affects throughput, not latency.
Orange: 1
Green: 2
Pink: 3
Yellow: 4
Notes: Pink: Statements 3 are correct; the rest are incorrect

## Slide 51: “And in Conclusion, …”
Big Ideas of Instruction Level Parallelism
Pipelining, Hazards, and Stalls
Forwarding, Speculation to overcome Hazards
Multiple issue to increase performance
  IPC instead of CPI
Dynamic Execution: Superscalar in-order issue, branch prediction, register renaming, out-of-order execution, in-order commit
  “unroll loops in HW”, hide cache misses