## Slide 1: CS 61C: Great Ideas in Computer Architecture (Machine Structures) Dependability and RAID
Instructor: Randy H. Katz http://inst.eecs.Berkeley.edu/~cs61c/fa13

## Slide 2: Great Ideas in Computer Architecture
Layers of Representation/Interpretation
Moore’s Law
Principle of Locality/Memory Hierarchy
Parallelism
Performance Measurement & Improvement
Dependability via Redundancy

## Slide 3: Great Idea #6: Dependability via Redundancy
Redundancy so that a failing piece doesn’t make the whole system fail
1+1=2
1+1=2
1+1=1
1+1=2
2 of 3 agree
FAIL!
Increasing transistor density reduces the cost of redundancy

## Slide 4: Great Idea #6: Dependability via Redundancy
Applies to everything from datacenters to memory
  Redundant datacenters so that can lose 1 datacenter but Internet service stays online
  Redundant routes so can lose nodes but Internet doesn’t fail
  Redundant disks so that can lose 1 disk but not lose data (Redundant Arrays of Independent Disks/RAID)
  Redundant memory bits of so that can lose 1 bit but no data (Error Correcting Code/ECC Memory)

## Slide 5: Agenda
Dependability, Reliability, Availability metrics
Codes for Redundancy
Administrivia
Error Detection and Correction in Memory
RAID

## Slide 6: Agenda
Dependability, Reliability, Availability metrics
Codes for Redundancy
Administrivia
Error Detection and Correction in Memory
RAID

## Slide 7: Dependability
Fault: failure of a component
  May or may not lead to system failure
Service accomplishment
Service delivered as specified
Service interruption
Deviation from specified service
Failure
Restoration

## Slide 8: Dependability via Redundancy: Time vs. Space
Spatial Redundancy – replicated data or check information or hardware to handle hard and soft (transient) failures
Temporal Redundancy – redundancy in time (retry) to handle soft (transient) failures

## Slide 9: Dependability Measures
Reliability: Mean Time To Failure (MTTF)
Service interruption: Mean Time To Repair (MTTR)
Mean time between failures (MTBF)
  MTBF = MTTF + MTTR
Availability = MTTF / (MTTF + MTTR)
Improving Availability
  Increase MTTF: More reliable hardware/software + Fault Tolerance
  Reduce MTTR: improved tools and processes for diagnosis and repair

## Slide 10: Understanding MTTF
Probability of Failure
1
Time

## Slide 11: Understanding MTTF
Probability of Failure
1
Time
MTTF
1/3
2/3

## Slide 12: Availability Measures
Availability = MTTF / (MTTF + MTTR) as %
  MTTF, MTBF usually measured in hours
Since hope rarely down, shorthand is “number of 9s of availability per year”
1 nine: 90% => 36 days of repair/year
2 nines: 99% => 3.6 days of repair/year
3 nines: 99.9% => 526 minutes of repair/year
4 nines: 99.99% => 53 minutes of repair/year
5 nines: 99.999% => 5 minutes of repair/year

## Slide 13: Reliability Measures
Another is average number of failures per year: Annualized Failure Rate (AFR)
  E.g., 1000 disks with 100,000 hour MTTF
  365 days * 24 hours = 8760 hours
  (1000 disks * 8760 hrs/year) / 100,000 = 87.6 failed disks per year on average
  87.6/1000 = 8.76% annual failure rate
Google’s 2007 study* found that actual AFRs for individual drives ranged from 1.7% for first year drives to over 8.6% for three-year old drives
*research.google.com/archive/disk_failures.pdf

## Slide 14: Dependability Design Principle
Design Principle: No single points of failure
  “Chain is only as strong as its weakest link”
Dependability Corollary of Amdahl’s Law
  Doesn’t matter how dependable you make one portion of system
  Dependability limited by part you do not improve

## Slide 15: Agenda
Dependability, Reliability, Availability metrics
Codes for Redundancy
Administrivia
Error Detection and Correction in Memory
RAID

## Slide 16: Error Detection/Correction Codes
Memory systems generate errors (accidentally flipped-bits)
  DRAMs store very little charge per bit
  “Soft” errors occur occasionally when cells are struck by alpha particles or other environmental upsets
  “Hard” errors can occur when chips permanently fail.
  Problem gets worse as memories get denser and larger
Memories protected against failures with EDC/ECC
Extra bits are added to each data-word
  Used to detect and/or correct faults in the memory system
  Each data word value mapped to unique code word
  A fault changes valid code word to invalid one, which can be detected

## Slide 17: Detecting/Correcting Code Concept
Detection: bit pattern fails codeword check
Correction: map to nearest valid code word
Space of possible bit patterns (2N)
Sparse population of code words (2M << 2N)
- with identifiable signature
Error changes bit pattern to
non-code

## Slide 18: Hamming Distance: 8 code words

## Slide 19: Hamming Distance 2: Detection Detect Single Bit Errors
No 1 bit error goes to another valid code
½ codes are valid
Invalid
Codes

## Slide 20: Hamming Distance 3: Correction Correct Single Bit Errors, Detect Double Bit Errors
No 2 bit error goes to another valid code; 1 bit error near
1/8 codes are valid
Nearest 000
(one 1)
Nearest 111
(one 0)

## Slide 21: Agenda
Dependability, Reliability, Availability metrics
Codes for Redundancy
Administrivia
Error Detection and Correction in Memory
RAID

## Slide 22: Administrivia
Final Exam
  Friday, December 20, 8:00-11:00 TBD
  Short answer, fill in the blank, multiple choice, mix and match: 100 points/minutes
  Room 220/230/242 Hearst Gym (assigned by course account login)
  Comprehensive, but concentrated on material since midterm examination
  Closed book/note, open crib sheet as before, MIPS Green Card provided
  Special consideration students, please contact

## Slide 23: Administrivia
Topics for Final Exam
  Cache Aware Programming/Cache Blocking
  Data Level Parallelism: Intel SIMD SSE instructions and programming
  Thread Parallelism: Cache Coherency + Synchronization concepts
  OpenMP Programming
  Hardware: Transistors to Gates
  Hardware: Truth Tables to Boolean Algebra
  Hardware: Synchronous System Timing and Timing Diagrams
  Finite State Machines: State Diagrams and Implementation
  CPU Design: Data Path Design (ALUs, Shifters, Register Files, Muxes)
  CPU Design: Controller Design (FSMs for processor implementation)
  Instruction Level Parallelism/Instruction Pipelining
  Set Associative Caches
  Dependability: ECC + RAID
  Virtual Memory
  X-semester issues: Great Ideas in Computer Architecture

## Slide 24: Agenda
Dependability, Reliability, Availability metrics
Codes for Redundancy
Administrivia
Error Detection and Correction in Memory
RAID

## Slide 25: Block Code Principles
Hamming distance = difference in # of bits
p = 011011, q = 001111, Ham. distance (p,q) = 2
p = 011011, q = 110001, distance (p,q) = ?
Can think of extra bits as creating a code with the data
What if minimum distance between members of code is 2 and get a 1 bit error?
Richard Hamming, 1915-98
Turing Award Winner
Notes: Distance is 3 of second case

## Slide 26: Parity: Simple Error Detection Coding
Each data value, before it is written to memory is “tagged” with an extra bit to force the stored word to have even parity:
Each word, as it is read from memory is “checked” by finding its parity (including the parity bit).
b7b6b5b4b3b2b1b0p
+
b7b6b5b4b3b2b1b0p
+
c
Minimum Hamming distance of parity code is 2
A non-zero parity indicates an error occurred:
  2 errors (on different bits) are not detected
  nor any even number of errors, just odd numbers of errors are detected

## Slide 27: Parity Example
Data 0101 0101
4 ones, even parity now
Write to memory: 0101 0101 0 to keep parity even
Data 0101 0111
5 ones, odd parity now
Write to memory: 0101 0111 1 to make parity even
Read from memory 0101 0101 0
4 ones => even parity, so no error
Read from memory 1101 0101 0
5 ones => odd parity, so error
What if error in parity bit?

## Slide 28: Suppose Want to Correct 1 Error?
Richard Hamming came up with simple to understand mapping to allow Error Correction at minimum distance of 3
  Single error correction, double error detection
Called “Hamming ECC”
  Worked weekends on relay computer with unreliable card reader, frustrated with manual restarting
  Got interested in error correction; published 1950
  R. W. Hamming, “Error Detecting and Correcting Codes,” The Bell System Technical Journal, Vol. XXVI, No 2 (April 1950) pp 147-160.

## Slide 29: Hamming Error Correction Code
Use of extra parity bits to allow the position identification of a single error
Mark all bit positions that are powers of 2 as parity bits (positions 1, 2, 4, 8, 16, …)
  Start numbering bits at 1 at left (not at 0 on right)
2. All other bit positions are data bits (positions 3, 5, 6, 7, 9, 10, 11, 12, 13, 14, 15, …)
3. Each data bit is covered by 2 or more parity bits

## Slide 30: Hamming ECC
4. The position of parity bit determines sequence of data bits that it checks
Bit 1 (00012): checks bits (1,3,5,7,9,11,...)
  Bits with least significant bit of address = 1
Bit 2 (00102): checks bits (2,3,6,7,10,11,14,15,…)
  Bits with 2nd least significant bit of address = 1
Bit 4 (01002): checks bits (4-7, 12-15, 20-23, ...)
  Bits with 3rd least significant bit of address = 1
Bit 8 (10002): checks bits (8-15, 24-31, 40-47 ,...)
  Bits with 4th least significant bit of address = 1

## Slide 31: Graphic of Hamming Code
http://en.wikipedia.org/wiki/Hamming_code

## Slide 32: Hamming ECC
5. Set parity bits to create even parity for each group
A byte of data: 10011010
Create the coded word, leaving spaces for the parity bits:
_ _ 1 _ 0 0 1 _ 1 0 1 0
0 0 0 0 0 0 0 0 0 1 1 1 1 2 3 4 5 6 7 8 9 0 1 2
Calculate the parity bits
Notes: Do this on the white board

## Slide 33: Hamming ECC
Position 1 checks bits 1,3,5,7,9,11 (bold): ? _ 1 _ 0 0 1 _ 1 0 1 0. set position 1 to a _: _ _ 1 _ 0 0 1 _ 1 0 1 0
Position 2 checks bits 2,3,6,7,10,11 (bold): 0 ? 1 _ 0 0 1 _ 1 0 1 0. set position 2 to a _: 0 _ 1 _ 0 0 1 _ 1 0 1 0
Position 4 checks bits 4,5,6,7,12 (bold): 0 1 1 ? 0 0 1 _ 1 0 1 0. set position 4 to a _: 0 1 1 _ 0 0 1 _ 1 0 1 0
Position 8 checks bits 8,9,10,11,12: 0 1 1 1 0 0 1 ? 1 0 1 0. set position 8 to a _: 0 1 1 1 0 0 1 _ 1 0 1 0
Notes: Do this on white board.
Bit 1 is 0
Bit 2 is 1
Bit 4 is 1

## Slide 34: Hamming ECC
Position 1 checks bits 1,3,5,7,9,11: ? _ 1 _ 0 0 1 _ 1 0 1 0. set position 1 to a 0: 0 _ 1 _ 0 0 1 _ 1 0 1 0
Position 2 checks bits 2,3,6,7,10,11: 0 ? 1 _ 0 0 1 _ 1 0 1 0. set position 2 to a 1: 0 1 1 _ 0 0 1 _ 1 0 1 0
Position 4 checks bits 4,5,6,7,12: 0 1 1 ? 0 0 1 _ 1 0 1 0. set position 4 to a 1: 0 1 1 1 0 0 1 _ 1 0 1 0
Position 8 checks bits 8,9,10,11,12: 0 1 1 1 0 0 1 ? 1 0 1 0. set position 8 to a 0: 0 1 1 1 0 0 1 0 1 0 1 0

## Slide 35: Hamming ECC
Final code word: 011100101010
Data word: 1 001 1010
Notes: Bit 8 set to 0

## Slide 36: Hamming ECC Error Check
Suppose receive 011100101110 0 1 1 1 0 0 1 0 1 1 1 0

## Slide 37: Hamming ECC Error Check
Suppose receive 011100101110

## Slide 38: Hamming ECC Error Check
Suppose receive 011100101110 0 1 0 1 1 1 √ 11 01 11 X-Parity 2 in error 1001 0 √ 01110 X-Parity 8 in error
Implies position 8+2=10 is in error 011100101110

## Slide 39: Hamming ECC Error Correct
Flip the incorrect bit … 011100101010

## Slide 40: Hamming ECC Error Correct
Suppose receive 011100101010 0 1 0 1 1 1 √ 11 01 01 √ 1001 0 √ 01010 √

## Slide 41: Hamming ECC
Finding and fixing a corrupted bit:
Suppose receive 011100101110 123456789012
Parity 1_, Parity 2_, Parity 4_, Parity 8_
(Bits numbers xxx1two, xx1xtwo, x1xxtwo, 1xxxtwo)
Parity bits 2 and 8 incorrect. As 2 + 8 = 10, bit position 10 is location of bad bit: flip value!
Corrected value: 011100101010
Why does Hamming ECC work?
Notes: Do on the blackboard
Bit 8: 8, 9, 10, 11, 12 = 01110 => 1
Bit 4: 4, 5, 6, 7, 12 = 10010 => 0
Bit 2: 2,3, 6,7, 10,11 = 110111 => 1
Bit 1: 1, 3, 5, 7, 9, 11 = 010111 => 0
Bit with error is 1010two =10
Flipping bit 10 should make all groups 0 => no error
Bit 8: 8, 9, 10, 11, 12 = 01010 => 0
Bit 4: 4, 5, 6, 7, 12 = 10010 => 0
Bit 2: 2,3, 6,7, 10,11 = 110101 => 0
Bit 1: 1, 3, 5, 7, 9, 11 = 010111 => 0
Bit with error is 0000two = 0 => no bit has error (bits start at 1)

## Slide 42: Hamming Error Correcting Code
Overhead involved in single error correction code
Let p be total number of parity bits and d number of data bits in p + d bit word
If p error correction bits are to point to error bit (p + d cases) + indicate that no error exists (1 case), we need:
  2p >= p + d + 1,
  thus p >= log(p + d + 1)
  for large d, p approaches log(d)
8 bits data => d = 8, 2p = p + 8 + 1 => p = 4
16 data => 5 parity, 32 data => 6 parity, 64 data => 7 parity

## Slide 43: Hamming Single Error Correction, Double Error Detection (SEC/DED)
Adding extra parity bit covering the entire word provides double error detection as well as single error correction
1 2 3 4 5 6 7 8
p1 p2 d1 p3 d2 d3 d4 p4
Hamming parity bits H (p1 p2 p3) are computed (even parity as usual) plus the even parity over the entire word, p4:
H=0 p4=0, no error
H≠0 p4=1, correctable single error (odd parity if 1 error => p4=1)
H≠0 p4=0, double error occurred (even parity if 2 errors=> p4=0)
H=0 p4=1, single error occurred in p4 bit, not in rest of word
Typical modern codes in DRAM memory systems:
64-bit data blocks (8 bytes) with 72-bit code words (9 bytes).

## Slide 44: Hamming Single Error Correction + Double Error Detection
1 bit error (one 1) Nearest 0000
1 bit error (one 0) Nearest 1111
2 bit error (two 0s, two 1s) Halfway Between Both
Hamming Distance = 4
Notes: 1 bit error from 0000, all numbers with one 1
1 bit error from 1111, all numbers with one 0
2 bit error from 0000, all numbers with two 1s and two 0s
2 bit error from 1111, all numbers with two 1s and two 0s

## Slide 45: What if More Than 2 Bit Errors?
Network transmissions, disks, distributed storage common failure mode is bursts of bit errors, not just one or two bit errors
  Contiguous sequence of B bits in which first, last and any number of intermediate bits are in error
  Caused by impulse noise or by fading in wireless
  Effect is greater at higher data rates

## Slide 46: Cyclic Redundancy Check
For block of k bits, transmitter generates an n-k bit frame check sequence
Transmits n bits exactly divisible by some number
Receiver divides frame by that number
  If no remainder, assume no error
  Easy to calculate division for some binary numbers with shift register
Disks detect and correct blocks of 512 bytes with called Reed Solomon codes ≈ CRC

## Slide 47: (In More Depth: Code Types)
Linear Codes: Code is generated by G and in null-space of H
Hamming Codes: Design the H matrix
  d = 3  Columns nonzero, Distinct
  d = 4  Columns nonzero, Distinct, Odd-weight
Reed-solomon codes:
  Based on polynomials in GF(2k) (I.e. k-bit symbols)
  Data as coefficients, code space as values of polynomial:
  P(x)=a0+a1x1+… ak-1xk-1
  Coded: P(0),P(1),P(2)….,P(n-1)
  Can recover polynomial as long as get any k of n
  Alternatively: as long as no more than n-k coded symbols erased, can recover data.
Side note: Multiplication by constant in GF(2k) can be represented by kk matrix: ax
  Decompose unknown vector into k bits: x=x0+2x1+…+2k-1xk-1
  Each column is result of multiplying a by 2i

## Slide 48: Hamming ECC on your own
Test if these Hamming-code words are correct. If one is incorrect, indicate the correct code word. Also, indicate what the original data was.
110101100011
111110001100
000010001010

## Slide 49: Agenda
Dependability, Reliability, Availability metrics
Codes for Redundancy
Administrivia
Error Detection and Correction in Memory
RAID

## Slide 50: Evolution of the Disk Drive
IBM RAMAC 305, 1956
IBM 3390K, 1986
Apple SCSI, 1986

## Slide 51: Arrays of Small Disks
  Can smaller disks be used to close gap in performance between disks and CPUs?
14”
10”
5.25”
3.5”
3.5”
Disk Array: 1 disk design
Conventional: 4 disk designs
Low End
High End

## Slide 52: Replace Small Number of Large Disks with Large Number of Small Disks! (1988 Disks)
Capacity
Volume
Power
Data Rate
I/O Rate
MTTF
Cost
IBM 3390K
20 GBytes
97 cu. ft.
3 KW
15 MB/s
600 I/Os/s
250 KHrs
$250K
IBM 3.5" 0061
320 MBytes
0.1 cu. ft.
11 W
1.5 MB/s
55 I/Os/s
50 KHrs
$2K
x70
23 GBytes
11 cu. ft.
1 KW
120 MB/s
3900 IOs/s
??? Hrs
$150K
Disk Arrays have potential for large data and I/O rates, high MB per cu. ft., high MB per KW, but what about reliability?
9X
3X
8X
6X

## Slide 53: RAID: Redundant Arrays of (Inexpensive) Disks
Files are "striped" across multiple disks
Redundancy yields high data availability
  Availability: service still provided to user, even if some components failed
Disks will still fail
Contents reconstructed from data redundantly stored in the array
   Capacity penalty to store redundant info
   Bandwidth penalty to update redundant info

## Slide 54: Redundant Arrays of Inexpensive Disks RAID 1: Disk Mirroring/Shadowing
• Each disk is fully duplicated onto its “mirror”
Very high availability can be achieved
• Bandwidth sacrifice on write:
Logical write = two physical writes
  Reads may be optimized
• Most expensive solution: 100% capacity overhead
recovery
group

## Slide 55: Redundant Array of Inexpensive Disks RAID 3: Parity Disk
P
10010011
11001101
10010011
. . .
logical record
1
0
1
0
0
0
1
1
1
1
0
0
1
1
0
1
1
0
1
0
0
0
1
1
1
1
0
0
1
1
0
1
P contains sum of
other disks per stripe mod 2 (“parity”)
If disk fails, subtract
P from sum of other disks to find missing information
Striped physical
records

## Slide 56: Redundant Arrays of Inexpensive Disks RAID 4: High I/O Rate Parity
D0
D1
D2
D3
P
D4
D5
D6
P
D7
D8
D9
P
D10
D11
D12
P
D13
D14
D15
P
D16
D17
D18
D19
D20
D21
D22
D23
P
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
Disk Columns
Increasing
Logical
Disk
Address
Stripe
Insides of 5 disks
Example: small read D0 & D5, large write D12-D15

## Slide 57: Inspiration for RAID 5
RAID 4 works well for small reads
Small writes (write to one disk):
  Option 1: read other data disks, create new sum and write to Parity Disk
  Option 2: since P has old sum, compare old data to new data, add the difference to P
Small writes are limited by Parity Disk: Write to D0, D5 both also write to P disk
D0
D1
D2
D3
P
D4
D5
D6
P
D7

## Slide 58: RAID 5: High I/O Rate Interleaved Parity
Independent writes
possible because of
interleaved parity
D0
D1
D2
D3
P
D4
D5
D6
P
D7
D8
D9
P
D10
D11
D12
P
D13
D14
D15
P
D16
D17
D18
D19
D20
D21
D22
D23
P
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
Disk Columns
Increasing
Logical
Disk
Addresses
Example: write to D0, D5 uses disks 0, 1, 3, 4

## Slide 59: Problems of Disk Arrays: Small Writes
D0
D1
D2
D3
P
D0'
+
+
D0'
D1
D2
D3
P'
new
data
old
data
old
parity
XOR
XOR
(1. Read)
(2. Read)
(3. Write)
(4. Write)
RAID-5: Small Write Algorithm
1 Logical Write = 2 Physical Reads + 2 Physical Writes

## Slide 60: Tech Report Read ‘Round the World (December 1987)

## Slide 61: RAID-I
RAID-I (1989)
  Consisted of a Sun 4/280 workstation with 128 MB of DRAM, four dual-string SCSI controllers, 28 5.25-inch SCSI disks and specialized disk striping software

## Slide 62: RAID II
1990-1993
Early Network Attached Storage (NAS) System running a Log Structured File System (LFS)
Impact:
  $25 Billion/year in 2002
  Over $150 Billion in RAID device sold since 1990-2002
  200+ RAID companies (at the peak)
  Software RAID a standard component of modern OSs

## Slide 63: RAID II

## Slide 64: And, in Conclusion, …
Great Idea: Redundancy to Get Dependability
  Spatial (extra hardware) and Temporal (retry if error)
Reliability: MTTF & Annualized Failure Rate (AFR)
Availability: % uptime (MTTF-MTTR/MTTF)
Memory
  Hamming distance 2: Parity for Single Error Detect
  Hamming distance 3: Single Error Correction Code + encode bit position of error
Treat disks like memory, except you know when a disk has failed—erasure makes parity an Error Correcting Code
RAID-2, -3, -4, -5: Interleaved data and parity