## Slide 1
Lecturer SOE Dan Garcia
www.cs.berkeley.edu/~ddgarcia
inst.eecs.berkeley.edu/~cs61c CS61C : Machine Structures Lecture 20 Introduction to Synchronous Digital Systems 2010-03-08
What to call 1,000 yottas?  UC Davis physics student Austin
Sendek has earned his 15 min of
fame by suggesting that the next SI unit be (you guessed it) … “hella”. He wanted to pay homage to Northern California (UCB, UCD, Stanford, LBNL).
www.huffingtonpost.com/2010/03/02/hella-number-scientists-n_n_482260.html
Hello to Alejandro Torrijos listening from España!
Notes: Greet class

## Slide 2: Review
C program: foo.c
Assembly program: foo.s
Executable(mach lang pgm): a.out
Compiler
Assembler
Linker
Loader
Memory
Object(mach lang module): foo.o
lib.o

## Slide 3: What are “Machine Structures”?
61C
Coordination of many levels of abstraction
I/O system
Processor
Compiler
Operating
System
(MacOS X)
Application (Netscape)
Digital Design
Circuit Design
Instruction Set
Architecture
Datapath & Control
transistors
Memory
Hardware
Software
Assembler
ISA is an important abstraction level: contract between HW & SW

## Slide 4: Below the Program
High-level language program (in C)
  swap int v[], int k){
  int temp;
  temp = v[k];
  v[k] = v[k+1];
  v[k+1] = temp;
  }
Assembly language program (for MIPS)
  swap: sll $2, $5, 2
  add $2, $4,$2
  lw $15, 0($2)
  lw $16, 4($2)
  sw $16, 0($2)
  sw $15, 4($2)
  jr $31
Machine (object) code (for MIPS)
  000000 00000 00101 0001000010000000
  000000 00100 00010 0001000000100000 . . .
C compiler
assembler
?
Notes: For lecture
Computer only understands zeros and ones – instructions of 0’s and 1’s
Early programmers found representing machine instructions in a symbolic notation – assembly language
And developed programs that translate from assembler to machine code
Eventually, programmers found working even in assembler too tedious so migrated to higher-level languages and developed compilers that would translate from the higher-level languages to assembler

## Slide 5: Synchronous Digital Systems
Synchronous:
  Means all operations are coordinated by a central clock.
    It keeps the “heartbeat” of the system!
Digital:
  Mean all values are represented by discrete values
  Electrical signals are treated as 1’s and 0’s and grouped together to form words.
The hardware of a processor, such as the MIPS, is an example of a Synchronous Digital System

## Slide 6: Logic Design
Next 4 weeks: we’ll study how a modern processor is built; starting with basic elements as building blocks.
Why study hardware design?
  Understand capabilities and limitations of hardware in general and processors in particular.
  What processors can do fast and what they can’t do fast (avoid slow things if you want your code to run fast!)
  Background for more detailed hardware courses (CS 150, CS 152)
  There is just so much you can do with processors. At some point you may need to design your own custom hardware.

## Slide 7: PowerPC Die Photograph
Let’s look closer…

## Slide 8: Transistors 101
MOSFET
  Metal-Oxide-Semiconductor Field-Effect Transistor
  Come in two types:
    n-type NMOSFET
    p-type PMOSFET
For n-type (p-type opposite)
  If voltage not enough between G & S, transistor turns “off” (cut-off) and Drain-Source NOT connected
  If the G & S voltage is high enough, transistor turns “on” (saturation) and Drain-Source ARE connected
p-type
n-type
D
G
S
S
G
D
Side view
www.wikipedia.org/wiki/Mosfet

## Slide 9: Transistor Circuit Rep. vs. Block diagram
Chips is composed of nothing but transistors and wires.
Small groups of transistors form useful building blocks.
Block are organized in a hierarchy to build higher-level blocks: ex: adders.
a
b
c
0
0
1
0
1
1
1
0
1
1
1
0
“1” (voltage source)
“0” (ground)

## Slide 10: Signals and Waveforms: Clocks
Signals
  When digital is only treated as 1 or 0
  Is transmitted over wires continuously
  Transmission is effectively instant
    Implies that any wire only contains 1 value at a time

## Slide 11: Signals and Waveforms

## Slide 12: Signals and Waveforms: Grouping

## Slide 13: Signals and Waveforms: Circuit Delay
2
3
3
4
5
10
0
1
5
13
4
6

## Slide 14: Type of Circuits
Synchronous Digital Systems are made up of two basic types of circuits:
Combinational Logic (CL) circuits
  Our previous adder circuit is an example.
  Output is a function of the inputs only.
  Similar to a pure function in mathematics, y = f(x). (No way to store information from one invocation to the next. No side effects)
State Elements: circuits that store information.

## Slide 15: Circuits with STATE (e.g., register)

## Slide 16: Peer Instruction
SW can peek at HW (past ISA abstraction boundary) for optimizations
SW can depend on particular HW implementation of ISA
12
a) FF
b) FT
c) TF
d) TT
Notes: Answer: [correct=5, TFF] Individual (6, 3, 6, 3, 34, 37, 7, 4)% & Team (9, 4, 4, 4, 39, 34, 0, 7)%
A: T [18/82 & 25/75] (The game breaks up very quickly into separate, independent games -- big win to solve separated & put together)
B: F [80/20 & 86/14] (The game tree grows exponentially! A better static evaluator can make all the difference!)
C: F [53/57 & 52/48] (If you're just looking for the best move, just keep theBestMove around [ala memoizing max])

## Slide 17: And in conclusion…
ISA is very important abstraction layer
  Contract between HW and SW
Clocks control pulse of our circuits
Voltages are analog, quantized to 0/1
Circuit delays are fact of life
Two types of circuits:
  Stateless Combinational Logic (&,|,~)
  State circuits (e.g., registers)

## Slide 18: Sample Debugging Waveform