## Slide 1
Head TA Scott Beamer
www.cs.berkeley.edu/~sbeamer
inst.eecs.berkeley.edu/~cs61c UC Berkeley CS61C : Machine Structures Lecture 39 – Intra-machine Parallelism 2010-04-30
Old-Fashioned Mud-Slinging with Flash
Apple, Adobe, and Microsoft all pointing fingers at each other for Flash’s crashes. Apple and Microsoft will back HTML5.
Notes: Greet class

## Slide 2: Review
Parallelism is necessary for performance
  It looks like it’s the future of computing
  It is unlikely that serial computing will ever catch up with parallel computing
Software Parallelism
  Grids and clusters, networked computers
  MPI & MapReduce – two common ways to program
Parallelism is often difficult
  Speedup is limited by serial portion of the code and communication overhead

## Slide 3: Today
Superscalars
Power, Energy & Parallelism
Multicores
Vector Processors
Challenges for Parallelism

## Slide 4: Disclaimers
Please don’t let today’s material confuse what you have already learned about CPU’s and pipelining
When programmer is mentioned today, it means whoever is generating the assembly code (so it is probably a compiler)
Many of the concepts described today are difficult to implement, so if it sounds easy, think of possible hazards

## Slide 5: Superscalar
Add more functional units or pipelines to the CPU
Directly reduces CPI by doing more per cycle
Consider what if we:
  Added another ALU
  Added 2 more read ports to the RegFile
  Added 1 more write port to the RegFile

## Slide 6: Simple Superscalar MIPS CPU
clk
5
W0
Ra
Rb
Register
File
Rd
Data In
Data
Addr
Data
Memory
Inst0
Instruction
Address
Instruction
Memory
PC
5
Rs
5
Rt
32
32
32
32
A
B
Next Address
clk
clk
ALU
32
ALU
5
Rd
Inst1
5
Rs
5
Rt
W1
Rc
Rd
C
D
32
Can now do 2 instructions in 1 cycle!

## Slide 7: Simple Superscalar MIPS CPU (cont.)
Considerations
  ISA now has to be changed
  Forwarding for pipelining now harder
Limitations of our example
  Programmer must explicitly generate instruction parallel code
  Improvement only if other instructions can fill slots
  Doesn’t scale well

## Slide 8: Superscalars in Practice
Modern superscalar processors often hide behind a scalar ISA
  Gives the illusion of a scalar processor
  Dynamically schedules instructions
    Tries to fill all slots with useful instructions
    Detects hazards and avoids them
Instruction Level Parallelism (ILP)
  Multiple instructions from same instruction stream in flight at the same time
  Examples: pipelining and superscalars

## Slide 9: Scaling

## Slide 10: Scaling

## Slide 11: Energy & Power Considerations
Courtesy: Chris Batten

## Slide 12: Energy & Power Considerations
Courtesy: Chris Batten

## Slide 13: Parallel Helps Energy Efficiency
Power ~ CV2f
Circuit delay is roughly linear with V
William Holt, HOT Chips 2005

## Slide 14: Multicore
Put multiple CPU’s on the same die
Cost of multicore: complexity and slower single-thread execution
Task/Thread Level Parallelism (TLP)
  Multiple instructions streams in flight at the same time

## Slide 15: Cache Coherence Problem
CPU0
Cache | 
Addr | Value
CPU1
Shared Main Memory | 
Addr | Value
16 | 
Cache | 
Addr | Value
5
CPU0:
LW R2, 16(R0)
5
16
CPU1:
LW R2, 16(R0)
16
5
View of memory no longer “coherent”.
Loads of location 16 from CPU0 and CPU1 see different values!
CPU1:
SW R0,16(R0)
0
0
From: John Lazzaro

## Slide 16: Real World Example: IBM POWER7

## Slide 17: Administrivia
Proj3 due tonight at 11:59p
Performance Contest posted tonight
Office Hours Next Week
  Watch website for announcements
Final Exam Review – 5/9, 3-6p, 10 Evans
Final Exam – 5/14, 8-11a, 230 Hearst Gym
  You get to bring: two 8.5”x11” sheets of handwritten notes + MIPS Green sheet

## Slide 18: Flynn’s Taxonomy
Classification of Parallel Architectures
wwww.wikipedia.org
Single Data
Multiple Data
Single Instruction
Multiple Instruction

## Slide 19: Vector Processors
Vector Processors implement SIMD
  One operation applied to whole vector
    Not all program can easily fit into this
  Can get high performance and energy efficiency by amortizing instruction fetch
    Spends more silicon and power on ALUs
Data Level Parallelism (DLP)
  Compute on multiple pieces of data with the same instruction stream

## Slide 20: Vectors (continued)
Vector Extensions
  Extra instructions added to a scalar ISA to provide short vectors
  Examples: MMX, SSE, AltiVec
Graphics Processing Units (GPU)
  Also leverage SIMD
  Initially very fixed function for graphics, but now becoming more flexible to support general purpose computation

## Slide 21: Parallelism at Different Levels
Intra-Processor (within the core)
  Pipelining & superscalar (ILP)
  Vector extensions & GPU (DLP)
Intra-System (within the box)
  Multicore – multiple cores per socket (TLP)
  Multisocket – multiple sockets per system
Intra-Cluster (within the room)
  Multiple systems per rack and multiple racks per cluster

## Slide 22: Conventional Wisdom (CW) in Computer Architecture
Old CW: Power is free, but transistors expensive
New CW: Power wall Power expensive, transistors “free”
  Can put more transistors on a chip than have power to turn on
Old CW: Multiplies slow, but loads fast
New CW: Memory wall Loads slow, multiplies fast
  200 clocks to DRAM, but even FP multiplies only 4 clocks
Old CW: More ILP via compiler / architecture innovation
  Branch prediction, speculation, Out-of-order execution, VLIW, …
New CW: ILP wall Diminishing returns on more ILP
Old CW: 2X CPU Performance every 18 months
New CW is Power Wall + Memory Wall + ILP Wall = Brick Wall
Implication: We must go parallel!

## Slide 23: Parallelism again? What’s different this time?
“This shift toward increasing parallelism is not a triumphant stride forward based on breakthroughs in novel software and architectures for parallelism; instead, this plunge into parallelism is actually a retreat from even greater challenges that thwart efficient silicon implementation of traditional uniprocessor architectures.”
– Berkeley View, December 2006
HW/SW Industry bet its future that breakthroughs will appear before it’s too late
view.eecs.berkeley.edu

## Slide 24: Peer Instruction
All energy efficient systems are low power
My GPU at peak can do more FLOP/s than my CPU
12
a) FF
b) FT
c) TF
d) TT

## Slide 25: Peer Instruction Answer
12
a) FF
b) FT
c) TF
d) TT
All energy efficient systems are low power
My GPU at peak can do more FLOP/s than my CPU
An energy efficient system could peak with high power to get work done and then go to sleep … FALSE
Current GPUs tend to have more FPUs than current CPUs, they just aren’t as programmable … TRUE
Notes: False (explained above)
True

## Slide 26: “And In conclusion…”
Parallelism is all about energy efficiency
Types of Parallelism: ILP, TLP, DLP
Parallelism already at many levels
Great opportunity for change