## Slide 1: “so many gadgets, so many aches” - NYT
inst.eecs.berkeley.edu/~cs61c UCB CS61C : Machine Structures Lecture 08 MIPS Instruction Representation I 2012-02-08
TA/Guest Lecturer
Zachary Bush
www.nytimes.com/2010/02/19/technology/19china.html
Laptops “do not meet any of the ergonomic requirements for a computer system”. Touch screens “should not be used heavily for typing” Texting is a problem because thumb bones have two bones instead of three … “if you want to get injured, do a lot of texting”. Advice? Take a break

## Slide 2: Review
To help the conditional branches make decisions concerning inequalities, we introduce: “Set on Less Than” called slt, slti, sltu, sltiu
One can store and load (signed and unsigned) bytes as well as words with lb, lbu
Unsigned add/sub don’t cause overflow
New MIPS Instructions: sll, srl, lb, lbu slt, slti, sltu, sltiu addu, addiu, subu

## Slide 3: 61C Levels of Representation (abstractions)
High Level Language Program (e.g., C)
Assembly Language Program (e.g.,MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k]; v[k] = v[k+1]; v[k+1] = temp;
lw $t0, 0($s2)
lw $t1, 4($s2)
sw $t1, 0($s2)
sw $t0, 4($s2)
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Register File
ALU

## Slide 4: Overview – Instruction Representation
Big idea: stored program
  consequences of stored program
Instructions as numbers
Instruction encoding
MIPS instruction format for Add instructions
MIPS instruction format for Immediate, Data transfer instructions
Notes: credential:
bring a computer
die photo
wafer
:
This can be an hidden slide. I just want to use this to do my own planning.
I have rearranged Culler’s lecture slides slightly and add more slides. This covers everything he covers in his first lecture (and more) but may
We will save the fun part, “ Levels of Organization,” at the end (so student can stay awake): I will show the internal stricture of the SS10/20.
Notes to Patterson: You may want to edit the slides in your section or add extra slides to taylor your needs.

## Slide 5: Big Idea: Stored-Program Concept
Computers built on 2 key principles:
  Instructions are represented as bit patterns - can think of these as numbers.
  Therefore, entire programs can be stored in memory to be read or written just like data.
Simplifies SW/HW of computer systems:
  Memory technology for data also used for programs

## Slide 6: Consequence #1: Everything Addressed
Since all instructions and data are stored in memory, everything has a memory address: instructions, data words
  both branches and jumps use these
C pointers are just memory addresses: they can point to anything in memory
  Unconstrained use of addresses can lead to nasty bugs; up to you in C; limits in Java
One register keeps address of instruction being executed: “Program Counter” (PC)
  Basically a pointer to memory: Intel calls it Instruction Address Pointer, a better name

## Slide 7: Consequence #2: Binary Compatibility
Programs are distributed in binary form
  Programs bound to specific instruction set
  Different version for Macintoshes and PCs
New machines want to run old programs (“binaries”) as well as programs compiled to new instructions
Leads to “backward compatible” instruction set evolving over time
Selection of Intel 8086 in 1981 for 1st IBM PC is major reason latest PCs still use 80x86 instruction set (Pentium 4); could still run program from 1981 PC today

## Slide 8: Instructions as Numbers (1/2)
Currently all data we work with is in words (32-bit blocks):
  Each register is a word.
  lw and sw both access memory one word at a time.
So how do we represent instructions?
  Remember: Computer only understands 1s and 0s, so “add $t0,$0,$0” is meaningless.
  MIPS wants simplicity: since data is in words, make instructions be words too

## Slide 9: Instructions as Numbers (2/2)
One word is 32 bits, so divide instruction word into “fields”.
Each field tells processor something about instruction.
We could define different fields for each instruction, but MIPS is based on simplicity, so define 3 basic types of instruction formats:
  R-format
  I-format
  J-format

## Slide 10: Instruction Formats
I-format: used for instructions with immediates, lw and sw (since offset counts as an immediate), and branches (beq and bne),
  (but not the shift instructions; later)
J-format: used for j and jal
R-format: used for all other instructions
It will soon become clear why the instructions have been partitioned in this way.

## Slide 11: R-Format Instructions (1/5)
Define “fields” of the following number of bits each: 6 + 5 + 5 + 5 + 5 + 6 = 32
For simplicity, each field has a name:
Important: On these slides and in book, each field is viewed as a 5- or 6-bit unsigned integer, not as part of a 32-bit integer.
  Consequence: 5-bit fields can represent any number 0-31, while 6-bit fields can represent any number 0-63.
6
5
5
5
6
5
opcode
rs
rt
rd
funct
shamt

## Slide 12: R-Format Instructions (2/5)
What do these field integer values tell us?
  opcode: partially specifies what instruction it is
    Note: This number is equal to 0 for all R-Format instructions.
  funct: combined with opcode, this number exactly specifies the instruction
Question: Why aren’t opcode and funct a single 12-bit field?
  We’ll answer this later.

## Slide 13: R-Format Instructions (3/5)
More fields:
  rs (Source Register): generally used to specify register containing first operand
  rt (Target Register): generally used to specify register containing second operand (note that name is misleading)
  rd (Destination Register): generally used to specify register which will receive result of computation

## Slide 14: R-Format Instructions (4/5)
Notes about register fields:
  Each register field is exactly 5 bits, which means that it can specify any unsigned integer in the range 0-31. Each of these fields specifies one of the 32 registers by number.
  The word “generally” was used because there are exceptions that we’ll see later. E.g.,
    mult and div have nothing important in the rd field since the dest registers are hi and lo
    mfhi and mflo have nothing important in the rs and rt fields since the source is determined by the instruction (see COD)

## Slide 15: R-Format Instructions (5/5)
Final field:
  shamt: This field contains the amount a shift instruction will shift by. Shifting a 32-bit word by more than 31 is useless, so this field is only 5 bits (so it can represent the numbers 0-31).
  This field is set to 0 in all but the shift instructions.
For a detailed description of field usage for each instruction, see green insert in COD (You can bring with you to all exams)

## Slide 16: R-Format Example (1/2)
MIPS Instruction:
  add $8,$9,$10
  opcode = 0 (look up in table in book)
  funct = 32 (look up in table in book)
  rd = 8 (destination)
  rs = 9 (first operand)
  rt = 10 (second operand)
  shamt = 0 (not a shift)

## Slide 17: R-Format Example (2/2)
MIPS Instruction:
  add $8,$9,$10
  Decimal number per field representation:
  Binary number per field representation:
  hex representation: 012A 4020hex
  decimal representation: 19,546,144ten
  Called a Machine Language Instruction
0
9
10
8
32
0
000000
01001
01010
01000
100000
00000
hex

## Slide 18: Administrivia
Remember to look at Appendix A (also on SPIM website), for MIPS assembly language details, including “assembly directives”, etc.
Other administrivia, TAs?

## Slide 19: I-Format Instructions (1/4)
What about instructions with immediates?
  5-bit field only represents numbers up to the value 31: immediates may be much larger than this
  Ideally, MIPS would have only one instruction format (for simplicity): unfortunately, we need to compromise
Define new instruction format that is partially consistent with R-format:
  First notice that, if instruction has immediate, then it uses at most 2 registers.

## Slide 20: I-Format Instructions (2/4)
Define “fields” of the following number of bits each: 6 + 5 + 5 + 16 = 32 bits
  Again, each field has a name:
  Key Concept: Only one field is inconsistent with R-format. Most importantly, opcode is still in same location.
6
5
5
16
opcode
rs
rt
immediate

## Slide 21: I-Format Instructions (3/4)
What do these fields mean?
  opcode: same as before except that, since there’s no funct field, opcode uniquely specifies an instruction in I-format
  This also answers question of why R-format has two 6-bit fields to identify instruction instead of a single 12-bit field: in order to be consistent as possible with other formats while leaving as much space as possible for immediate field.
  rs: specifies a register operand (if there is one)
  rt: specifies register which will receive result of computation (this is why it’s called the target register “rt”) or other operand for some instructions.

## Slide 22: I-Format Instructions (4/4)
The Immediate Field:
  addi, slti, sltiu, the immediate is sign-extended to 32 bits. Thus, it’s treated as a signed integer.
  16 bits  can be used to represent immediate up to 216 different values
  This is large enough to handle the offset in a typical lw or sw, plus a vast majority of values that will be used in the slti instruction.
  We’ll see what to do when the number is too big in our next lecture…

## Slide 23: I-Format Example (1/2)
MIPS Instruction:
  addi $21,$22,-50
  opcode = 8 (look up in table in book)
  rs = 22 (register containing operand)
  rt = 21 (target register)
  immediate = -50 (by default, this is decimal)

## Slide 24: I-Format Example (2/2)
MIPS Instruction:
  addi $21,$22,-50
8
22
21
-50
001000
10110
10101
1111111111001110
  Decimal/field representation:
  Binary/field representation:
  hexadecimal representation: 22D5 FFCEhex
  decimal representation: 584,449,998ten

## Slide 25: Peer Instruction
Which instruction has same representation as 35ten?
  a) add $0, $0, $0
  b) subu $s0,$s0,$s0
  c) lw $0, 0($0)
  d) addi $0, $0, 35
  e) subu $0, $0, $0
  Registers numbers and names: 0: $0, .. 8: $t0, 9:$t1, ..15: $t7, 16: $s0, 17: $s1, .. 23: $s7
  Opcodes and function fields (if necessary)
  add: opcode = 0, funct = 32
  subu: opcode = 0, funct = 35
  addi: opcode = 8
  lw: opcode = 35
opcode
rs
rt
offset
rd
funct
shamt
opcode
rs
rt
opcode
rs
rt
immediate
rd
funct
shamt
opcode
rs
rt
rd
funct
shamt
opcode
rs
rt
Notes: 1 PERSON VOTE: Pink: 40%, Reed: 30%, Yellow: 20%, Blue: 20%
Afterwards: Pink 90%

## Slide 26: Peer Instruction Answer
Which instruction has same representation as 35ten?
  a) add $0, $0, $0
  b) subu $s0,$s0,$s0
  c) lw $0, 0($0)
  d) addi $0, $0, 35
  e) subu $0, $0, $0
  Registers numbers and names: 0: $0, .. 8: $t0, 9:$t1, ..15: $t7, 16: $s0, 17: $s1, .. 23: $s7
  Opcodes and function fields (if necessary)
  add: opcode = 0, funct = 32
  subu: opcode = 0, funct = 35
  addi: opcode = 8
  lw: opcode = 35
35
0
0
0
0
32
0
0
0
0
8
0
0
35
16
35
0
0
16
16
0
35
0
0
0
0
Notes: 1 PERSON VOTE: Pink: 40%, Reed: 30%, Yellow: 20%, Blue: 20%
Afterwards: Pink 90%

## Slide 27: In conclusion…
Simplifying MIPS: Define instructions to be same size as data word (one word) so that they can use the same memory (compiler can use lw and sw).
Computer actually stores programs as a series of these 32-bit numbers.
MIPS Machine Language Instruction: 32 bits representing a single instruction
opcode
rs
rt
immediate
opcode
rs
rt
rd
funct
shamt
R
I