## Slide 1: faculty “re-imagine” ugrad education
inst.eecs.berkeley.edu/~cs61c
UCB CS61C : Machine Structures
Lecture 16 – Running a Program (Compiling, Assembling, Linking, Loading)
2013-03-01
Highlights: Big Ideas courses, more team teaching, Academic Honor code, report avg and median grades to share context, meaning.
Head TA
Justin Hsia
ls.berkeley.edu/about-college/strategic-plan-UGR-Ed

## Slide 2: Administrivia…
Midterm Exam on Monday @ 7-9pm
  You’re responsible for all material up through today
  Find where to go on Piazza
You get to bring
  Your study sheet (2-sided!)
  Pens & Pencils
What you don’t need to bring
  Calculator, cell phone, pagers
  MIPS Green Sheet (attached to back of exam)
Conflicts? E-mail Justin (head TA)
Dan’s OH today are cancelled

## Slide 3: Interpretation
Scheme Interpreter is just a program that reads a scheme program and performs the functions of that scheme program.
Scheme program: foo.scm
Scheme interpreter

## Slide 4: Translation
Scheme Compiler is a translator from Scheme to machine language.
The processor is a hardware interpreter of machine language.
Scheme program: foo.scm
Scheme Compiler
Executable (mach lang pgm): a.out
Hardware

## Slide 5: Steps to Starting a Program (translation)
C program: foo.c
Compiler
Executable (mach lang pgm): a.out
Memory
Assembly program: foo.s
Assembler
Object (mach lang module): foo.o
Linker
Loader
lib.o

## Slide 6: Compiler
Input: High-Level Language Code (e.g., C, Java such as foo.c)
Output: Assembly Language Code (e.g., foo.s for MIPS)
Note: Output may contain pseudo-instructions
Pseudo-instructions: instructions that assembler understands but not in machine For example:
  move $s1,$s2 → add $s1,$s2,$zero

## Slide 7: Where Are We Now?
C program: foo.c
Compiler
Executable (mach lang pgm): a.out
Memory
Assembly program: foo.s
Assembler
Object (mach lang module): foo.o
Linker
Loader
lib.o
CS164

## Slide 8: Assembler
Input: Assembly Language Code (MAL) (e.g., foo.s for MIPS)
Output: Object Code, information tables (TAL) (e.g., foo.o for MIPS)
Reads and Uses Directives
Replace Pseudo-instructions
Produce Machine Language
Creates Object File

## Slide 9: Assembler Directives (p. A-51 to A-53)
Give directions to assembler, but do not produce machine instructions
  .text: Subsequent items put in user text segment (machine code)
  .data: Subsequent items put in user data segment (binary rep of data in source file)
  .globl sym: declares sym global and can be referenced from other files
  .asciiz str: Store the string str in memory and null-terminate it
  .word w1…wn: Store the n 32-bit quantities in successive memory words

## Slide 10: Pseudo-instruction Replacement
Asm. treats convenient variations of machine language instructions as if real instructions Pseudo: Real:
subu $sp,$sp,32 addiu $sp,$sp,-32
sd $a0, 32($sp) sw $a0, 32($sp) sw $a1, 36($sp)
mul $t7,$t6,$t5 mul $t6,$t5 mflo $t7
addu $t0,$t6,1 addiu $t0,$t6,1
ble $t0,100,loop slti $at,$t0,101 bne $at,$0,loop
la $a0, str lui $at,left(str) ori $a0,$at,right(str)

## Slide 11: Producing Machine Language (1/3)
Simple Case
  Arithmetic, Logical, Shifts, and so on.
  All necessary info is within the instruction already.
What about Branches?
  PC-Relative
  So once pseudo-instructions are replaced by real ones, we know by how many instructions to branch.
So these can be handled

## Slide 12: Producing Machine Language (2/3)
“Forward Reference” problem
  Branch instructions can refer to labels that are “forward” in the program:
  Solved by taking 2 passes over the program.
    First pass remembers position of labels
    Second pass uses label positions to generate code
or $v0, $0, $0 L1: slt $t0, $0, $a1 beq $t0, $0, L2 addi $a1, $a1, -1 j L1 L2: add $t1, $a0, $a1

## Slide 13: Producing Machine Language (3/3)
What about jumps (j and jal)?
  Jumps require absolute address.
  So, forward or not, still can’t generate machine instruction without knowing the position of instructions in memory.
What about references to data?
  la gets broken up into lui and ori
  These will require the full 32-bit address of the data.
These can’t be determined yet, so we create two tables…

## Slide 14: Symbol Table
List of “items” in this file that may be used by other files.
What are they?
  Labels: function calling
  Data: anything in the .data section; variables which may be accessed across files

## Slide 15: Relocation Table
List of “items” this file needs the address later.
What are they?
  Any label jumped to: j or jal
    internal
    external (including lib files)
  Any piece of data
    such as the la instruction

## Slide 16: Object File Format
object file header: size and position of the other pieces of the object file
text segment: the machine code
data segment: binary representation of the data in the source file
relocation information: identifies lines of code that need to be “handled”
symbol table: list of this file’s labels and data that can be referenced
debugging information
A standard format is ELF (except MS) http://www.skyfree.org/linux/references/ELF_Format.pdf

## Slide 17: Where Are We Now?
C program: foo.c
Compiler
Executable (mach lang pgm): a.out
Memory
Assembly program: foo.s
Assembler
Object (mach lang module): foo.o
Linker
Loader
lib.o

## Slide 18: Linker (1/3)
Input: Object Code files, information tables (e.g. foo.o, libc.o for MIPS)
Output: Executable Code (e.g. a.out for MIPS)
Combines several object (.o) files into a single executable (“linking”)
Enable Separate Compilation of files
  Changes to one file do not require recompilation of whole program
    Windows NT source was > 40 M lines of code!
  Old name “Link Editor” from editing the “links” in jump and link instructions

## Slide 19: Linker (2/3)
.o file 1
text 1
data 1
info 1
.o file 2
text 2
data 2
info 2
Linker
a.out
Relocated text 1
Relocated text 2
Relocated data 1
Relocated data 2

## Slide 20: Linker (3/3)
Step 1: Take text segment from each .o file and put them together.
Step 2: Take data segment from each .o file, put them together, and concatenate this onto end of text segments.
Step 3: Resolve References
  Go through Relocation Table; handle each entry
  That is, fill in all absolute addresses

## Slide 21: Four Types of Addresses we’ll discuss
PC-Relative Addressing (beq, bne)
  never relocate
Absolute Address (j, jal)
  always relocate
External Reference (usually jal)
  always relocate
Data Reference (often lui and ori)
  always relocate

## Slide 22: Absolute Addresses in MIPS
Which instructions need relocation editing?
  J-format: jump, jump and link
  Loads and stores to variables in static area, relative to global pointer
  What about conditional branches?
  PC-relative addressing preserved even if code moves
j/jal
xxxxx
lw/sw
$gp
$x
address
beq/bne
$rs
$rt
address

## Slide 23: Resolving References (1/2)
Linker assumes first word of first text segment is at address 0x00000000.
  (More later when we study “virtual memory”)
Linker knows:
  length of each text and data segment
  ordering of text and data segments
Linker calculates:
  absolute address of each label to be jumped to (internal or external) and each piece of data being referenced

## Slide 24: Resolving References (2/2)
To resolve references:
  search for reference (data or label) in all “user” symbol tables
  if not found, search library files (for example, for printf)
  once absolute address is determined, fill in the machine code appropriately
Output of linker: executable file containing text and data (plus header)

## Slide 25: Where Are We Now?
C program: foo.c
Compiler
Executable (mach lang pgm): a.out
Memory
Assembly program: foo.s
Assembler
Object (mach lang module): foo.o
Linker
Loader
lib.o
CS164

## Slide 26: Loader Basics
Input: Executable Code (e.g. a.out for MIPS)
Output: (program is run)
Executable files are stored on disk.
When one is run, loader’s job is to load it into memory and start it running.
In reality, loader is the operating system (OS)
  loading is one of the OS tasks

## Slide 27: Loader … what does it do?
Reads executable file’s header to determine size of text and data segments
Creates new address space for program large enough to hold text and data segments, along with a stack segment
Copies instructions and data from executable file into the new address space
Copies arguments passed to the program onto the stack
Initializes machine registers
  Most registers cleared, but stack pointer assigned address of 1st free stack location
Jumps to start-up routine that copies program’s arguments from stack to registers & sets the PC
  If main routine returns, start-up routine terminates program with the exit system call

## Slide 28: Conclusion
C program: foo.c
Compiler
Executable (mach lang pgm): a.out
Memory
Assembly program: foo.s
Assembler
Object (mach lang module): foo.o
Linker
Loader
lib.o
Compiler converts a single HLL file into a single assembly lang. file.
Assembler removes pseudo instructions, converts what it can to machine language, and creates a checklist for the linker (relocation table). A .s file becomes a .o file.
  Does 2 passes to resolve addresses, handling internal forward references
Linker combines several .o files and resolves absolute addresses.
  Enables separate compilation, libraries that need not be compiled, and resolves remaining addresses
Loader loads executable into memory and begins execution.
Stored Program concept is very powerful. It means that instructions sometimes act just like data. Therefore we can use programs to manipulate other programs!
  Compiler → Assembler → Linker (→ Loader)

## Slide 29: Peer Instruction
Which of the following instr. may need to be edited during link phase?
Loop: lui $at, 0xABCD ori $a0,$at, 0xFEDC bne $a0,$v0, Loop # 2
# 1
}
12
a) FF
b) FT
c) TF
d) TT

## Slide 30: Peer Instruction Answer
data reference; relocate
PC-relative branch; OK
Which of the following instr. may need to be edited during link phase?
Loop: lui $at, 0xABCD ori $a0,$at, 0xFEDC bne $a0,$v0, Loop # 2
# 1
}
12
a) FF
b) FT
c) TF
d) TT

## Slide 31: Peer Instruction
Assembler will ignore the instruction Loop:nop because it does nothing.
Java designers used a translater AND interpreter (rather than just a translater) mainly because of (at least 1 of): ease of writing, better error msgs, smaller object code.
12
a) FF
b) FT
c) TF
d) TT

## Slide 32: Peer Instruction Answer
Assembler keeps track of all labels in symbol table…F!
Java designers used both mainly because of code portability…F!
Assembler will ignore the instruction Loop:nop because it does nothing.
Java designers used a translater AND interpreter (rather than just a translater) mainly because of (at least 1 of): ease of writing, better error msgs, smaller object code.
12
a) FF
b) FT
c) TF
d) TT

## Slide 33: Bonus slides
These are extra slides that used to be included in lecture notes, but have been moved to this, the “bonus” area to serve as a supplement.
The slides will appear in the order they would have in the normal presentation
Bonus

## Slide 34: Language Execution Continuum
An Interpreter is a program that executes other programs.
Language translation gives us another option.
In general, we interpret a high level language when efficiency is not critical and translate to a lower level language to up performance
Easy to program
Inefficient to interpret
Difficult to program
Efficient to interpret
Scheme Java C++
C
Assembly
machine language
Java bytecode

## Slide 35: Interpretation vs Translation
How do we run a program written in a source language?
  Interpreter: Directly executes a program in the source language
  Translator: Converts a program from the source language to an equivalent program in another language
For example, consider a Scheme program foo.scm

## Slide 36: Interpretation
Any good reason to interpret machine language in software?
SPIM – useful for learning / debugging
Apple Macintosh conversion
  Switched from Motorola 680x0 instruction architecture to PowerPC.
    Similar issue with switch to x86.
  Could require all programs to be re-translated from high level language
  Instead, let executables contain old and/or new machine code, interpret old code in software if necessary (emulation)

## Slide 37: Interpretation vs. Translation? (1/2)
Generally easier to write interpreter
Interpreter closer to high-level, so can give better error messages (e.g., MARS, stk)
  Translator reaction: add extra information to help debugging (line numbers, names)
Interpreter slower (10x?), code smaller (2x?)
Interpreter provides instruction set independence: run on any machine

## Slide 38: Interpretation vs. Translation? (2/2)
Translated/compiled code almost always more efficient and therefore higher performance:
  Important for many applications, particularly operating systems.
Translation/compilation helps “hide” the program “source” from the users:
  One model for creating value in the marketplace (eg. Microsoft keeps all their source code secret)
  Alternative model, “open source”, creates value by publishing the source code and fostering a community of developers.

## Slide 39: Static vs Dynamically linked libraries
What we’ve described is the traditional way: statically-linked approach
  The library is now part of the executable, so if the library updates, we don’t get the fix (have to recompile if we have source)
  It includes the entire library even if not all of it will be used.
  Executable is self-contained.
An alternative is dynamically linked libraries (DLL), common on Windows & UNIX platforms

## Slide 40: Dynamically linked libraries
Space/time issues
  + Storing a program requires less disk space
  + Sending a program requires less time
  + Executing two programs requires less memory (if they share a library)
  – At runtime, there’s time overhead to do link
Upgrades
  + Replacing one file (libXYZ.so) upgrades every program that uses library “XYZ”
  – Having the executable isn’t enough anymore
Overall, dynamic linking adds quite a bit of complexity to the compiler, linker, and operating system. However, it provides many benefits that often outweigh these.
en.wikipedia.org/wiki/Dynamic_linking

## Slide 41: Dynamically linked libraries
The prevailing approach to dynamic linking uses machine code as the “lowest common denominator”
  The linker does not use information about how the program or library was compiled (i.e., what compiler or language)
  This can be described as “linking at the machine code level”
  This isn’t the only way to do it...

## Slide 42: Example: C → Asm → Obj → Exe → Run
#include <stdio.h>
int main (int argc, char *argv[]) {
int i, sum = 0;
for (i = 0; i <= 100; i++) sum = sum + i * i;
printf ("The sum of sq from 0 .. 100 is %d\n", sum);
}
C Program Source Code: prog.c
“printf” lives in “libc”

## Slide 43: Compilation: MAL
.text
.align 2
.globl main
main:
subu $sp,$sp,32
sw $ra, 20($sp)
sd $a0, 32($sp)
sw $0, 24($sp)
sw $0, 28($sp)
loop:
lw $t6, 28($sp)
mul $t7, $t6,$t6
lw $t8, 24($sp)
addu $t9,$t8,$t7
sw $t9, 24($sp)
addu $t0, $t6, 1
sw $t0, 28($sp)
ble $t0,100, loop
la $a0, str
lw $a1, 24($sp)
jal printf
move $v0, $0
lw $ra, 20($sp)
addiu $sp,$sp,32
jr $ra
.data
.align 0
str:
.asciiz "The sum of sq from 0 .. 100 is %d\n"
Where are
7 pseudo- instructions?

## Slide 44: Compilation: MAL
.text
.align 2
.globl main
main:
subu $sp,$sp,32
sw $ra, 20($sp)
sd $a0, 32($sp)
sw $0, 24($sp)
sw $0, 28($sp)
loop:
lw $t6, 28($sp)
mul $t7, $t6,$t6
lw $t8, 24($sp)
addu $t9,$t8,$t7
sw $t9, 24($sp)
addu $t0, $t6, 1
sw $t0, 28($sp)
ble $t0,100, loop
la $a0, str
lw $a1, 24($sp)
jal printf
move $v0, $0
lw $ra, 20($sp)
addiu $sp,$sp,32
jr $ra
.data
.align 0
str:
.asciiz "The sum of sq from 0 .. 100 is %d\n"
7 pseudo- instructions underlined

## Slide 45: Assembly step 1:
00 addiu $29,$29,-32
04 sw $31,20($29)
08 sw $4, 32($29)
0c sw $5, 36($29)
10 sw $0, 24($29)
14 sw $0, 28($29)
18 lw $14, 28($29)
1c multu $14, $14
20 mflo $15
24 lw $24, 24($29)
28 addu $25,$24,$15
2c sw $25, 24($29)
30 addiu $8,$14, 1
34 sw $8,28($29)
38 slti $1,$8, 101
3c bne $1,$0, loop
40 lui $4, l.str
44 ori $4,$4,r.str
48 lw $5,24($29)
4c jal printf
50 add $2, $0, $0
54 lw $31,20($29)
58 addiu $29,$29,32
5c jr $31
Remove pseudoinstructions, assign addresses

## Slide 46: Assembly step 2
Symbol Table
  Label address (in module) type
  main: 0x00000000 global text
  loop: 0x00000018 local text
  str: 0x00000000 local data
Relocation Information
  Address Instr. type Dependency 0x00000040 lui l.str 0x00000044 ori r.str 0x0000004c jal printf
Create relocation table and symbol table

## Slide 47: Assembly step 3
00 addiu $29,$29,-32
04 sw $31,20($29)
08 sw $4, 32($29)
0c sw $5, 36($29)
10 sw $0, 24($29)
14 sw $0, 28($29)
18 lw $14, 28($29)
1c multu $14, $14
20 mflo $15
24 lw $24, 24($29)
28 addu $25,$24,$15
2c sw $25, 24($29)
30 addiu $8,$14, 1
34 sw $8,28($29)
38 slti $1,$8, 101
3c bne $1,$0, -10
40 lui $4, l.str
44 ori $4,$4,r.str
48 lw $5,24($29)
4c jal printf
50 add $2, $0, $0
54 lw $31,20($29)
58 addiu $29,$29,32
5c jr $31
Resolve local PC-relative labels

## Slide 48: Assembly step 4
Generate object (.o) file:
  Output binary representation for
    ext segment (instructions),
    data segment (data),
    symbol and relocation tables.
  Using dummy “placeholders” for unresolved absolute and external references.

## Slide 49: Text segment in object file
0x000000 00100111101111011111111111100000
0x000004 10101111101111110000000000010100
0x000008 10101111101001000000000000100000
0x00000c 10101111101001010000000000100100
0x000010 10101111101000000000000000011000
0x000014 10101111101000000000000000011100
0x000018 10001111101011100000000000011100
0x00001c 10001111101110000000000000011000
0x000020 00000001110011100000000000011001
0x000024 00100101110010000000000000000001
0x000028 00101001000000010000000001100101
0x00002c 10101111101010000000000000011100
0x000030 00000000000000000111100000010010
0x000034 00000011000011111100100000100001
0x000038 00010100001000001111111111110111
0x00003c 10101111101110010000000000011000
0x000040 00111100000001000000000000000000
0x000044 10001111101001010000000000000000
0x000048 00001100000100000000000011101100
0x00004c 00100100000000000000000000000000
0x000050 10001111101111110000000000010100
0x000054 00100111101111010000000000100000
0x000058 00000011111000000000000000001000
0x00005c 00000000000000000001000000100001

## Slide 50: Link step 1: combine prog.o, libc.o
Merge text/data segments
Create absolute memory addresses
Modify & merge symbol and relocation tables
Symbol Table
  Label Address
  main: 0x00000000
  loop: 0x00000018
  str: 0x10000430
  printf: 0x000003b0 …
Relocation Information
  Address Instr. Type Dependency 0x00000040 lui l.str 0x00000044 ori r.str 0x0000004c jal printf …

## Slide 51: Link step 2:
00 addiu $29,$29,-32
04 sw $31,20($29)
08 sw $4, 32($29)
0c sw $5, 36($29)
10 sw $0, 24($29)
14 sw $0, 28($29)
18 lw $14, 28($29)
1c multu $14, $14
20 mflo $15
24 lw $24, 24($29)
28 addu $25,$24,$15
2c sw $25, 24($29)
30 addiu $8,$14, 1
34 sw $8,28($29)
38 slti $1,$8, 101
3c bne $1,$0, -10
40 lui $4, 4096
44 ori $4,$4,1072
48 lw $5,24($29)
4c jal 812
50 add $2, $0, $0
54 lw $31,20($29)
58 addiu $29,$29,32
5c jr $31
Edit Addresses in relocation table
  (shown in TAL for clarity, but done in binary )

## Slide 52: Link step 3:
Output executable of merged modules.
  Single text (instruction) segment
  Single data segment
  Header detailing size of each segment
NOTE:
  The preceeding example was a much simplified version of how ELF and other standard formats work, meant only to demonstrate the basic principles.

## Slide 53: Integer Multiplication (1/3)
Paper and pencil example (unsigned):
  Multiplicand 1000 8 Multiplier x1001 9 1000 0000 0000 +1000 01001000
m bits x n bits = m + n bit product

## Slide 54: Integer Multiplication (2/3)
In MIPS, we multiply registers, so:
  32-bit value x 32-bit value = 64-bit value
Syntax of Multiplication (signed):
  mult register1, register2
  Multiplies 32-bit values in those registers & puts 64-bit product in special result regs:
    puts product upper half in hi, lower half in lo
  hi and lo are 2 registers separate from the 32 general purpose registers
  Use mfhi register & mflo register to move from hi, lo to another register

## Slide 55: Integer Multiplication (3/3)
Example:
  in C: a = b * c;
  in MIPS:
    let b be $s2; let c be $s3; and let a be $s0 and $s1 (since it may be up to 64 bits)
  mult $s2,$s3 # b*c mfhi $s0 # upper half of # product into $s0 mflo $s1 # lower half of # product into $s1
Note: Often, we only care about the lower half of the product.

## Slide 56: Integer Division (1/2)
Paper and pencil example (unsigned):
  1001 Quotient Divisor 1000|1001010 Dividend -1000 10 101 1010 -1000 10 Remainder (or Modulo result)
Dividend = Quotient x Divisor + Remainder

## Slide 57: Integer Division (2/2)
Syntax of Division (signed):
  div register1, register2
  Divides 32-bit register 1 by 32-bit register 2:
  puts remainder of division in hi, quotient in lo
Implements C division (/) and modulo (%)
Example in C: a = c / d; b = c % d;
in MIPS: a$s0;b$s1;c$s2;d$s3
  div $s2,$s3 # lo=c/d, hi=c%d mflo $s0 # get quotient mfhi $s1 # get remainder

## Slide 58: Big Endian vs. Little Endian
Big-endian and little-endian derive from Jonathan Swift's Gulliver's Travels in which the Big Endians were a political faction that broke their eggs at the large end ("the primitive way") and rebelled against the Lilliputian King who required his subjects (the Little Endians) to break their eggs at the small end.
Big Endian
ADDR3 ADDR2 ADDR1 ADDR0 BYTE0 BYTE1 BYTE2 BYTE3 00000001 00000100 00000000 00000000
ADDR0 ADDR1 ADDR2 ADDR3 BYTE3 BYTE2 BYTE1 BYTE0 00000000 00000000 00000100 00000001
Little Endian
ADDR3 ADDR2 ADDR1 ADDR0 BYTE3 BYTE2 BYTE1 BYTE0 00000000 00000000 00000100 00000001
ADDR0 ADDR1 ADDR2 ADDR3 BYTE0 BYTE1 BYTE2 BYTE3 00000001 00000100 00000000 00000000
Consider the number 1025 as we normally write it: BYTE3 BYTE2 BYTE1 BYTE0 00000000 00000000 00000100 00000001
www.webopedia.com/TERM/b/big_endian.html searchnetworking.techtarget.com/sDefinition/0,,sid7_gci211659,00.html
www.noveltheory.com/TechPapers/endian.asp
en.wikipedia.org/wiki/Big_endian
The order in which BYTES are stored in memory
Bits always stored as usual. (E.g., 0xC2=0b 1100 0010)