## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
The Flynn Taxonomy,
Intel SIMD Instructions

## Slide 2: Review of Last Lecture
Amdahl’s Law limits benefits of parallelization
Request Level Parallelism
  Handle multiple requests in parallel (e.g. web search)
MapReduce Data Level Parallelism
  Framework to divide up data to be processed in parallel
  Mapper outputs intermediate key-value pairs
  Reducer “combines” intermediate values with same key

## Slide 3: Great Idea #4: Parallelism
Smart Phone
Warehouse Scale Computer
Leverage Parallelism &
Achieve High Performance
Core
…
Memory
Input/Output
Computer
Core
Parallel Requests
  Assigned to computer
  e.g. search “Garcia”
Parallel Threads
  Assigned to core
  e.g. lookup, ads
Parallel Instructions
  > 1 instruction @ one time
  e.g. 5 pipelined instructions
Parallel Data
  > 1 data item @ one time
  e.g. add of 4 pairs of words
Hardware descriptions
  All gates functioning in parallel at same time
Software Hardware
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A0+B0
A1+B1
A2+B2
A3+B3
Logic Gates
We are here

## Slide 4: Agenda
Flynn’s Taxonomy
Administrivia
Data Level Parallelism and SIMD
Bonus: Loop Unrolling

## Slide 5: Hardware vs. Software Parallelism
Choice of hardware and software parallelism are independent
  Concurrent software can also run on serial hardware
  Sequential software can also run on parallel hardware
Flynn’s Taxonomy is for parallel hardware

## Slide 6: Flynn’s Taxonomy
SIMD and MIMD most commonly encountered today
Most common parallel processing programming style: Single Program Multiple Data (“SPMD”)
  Single program that runs on all processors of an MIMD
  Cross-processor execution coordination through conditional expressions (will see later in Thread Level Parallelism)
SIMD: specialized function units (hardware), for handling lock-step calculations involving arrays
  Scientific computing, signal processing, multimedia (audio/video processing)

## Slide 7: Single Instruction/Single Data Stream
Sequential computer that exploits no parallelism in either the instruction or data streams
Examples of SISD architecture are traditional uniprocessor machines
Processing Unit

## Slide 8: Multiple Instruction/Single Data Stream
Exploits multiple instruction streams against a single data stream for data operations that can be naturally parallelized (e.g. certain kinds of array processors)
MISD no longer commonly encountered, mainly of historical interest only

## Slide 9: Single Instruction/Multiple Data Stream
Computer that applies a single instruction stream to multiple data streams for operations that may be naturally parallelized (e.g. SIMD instruction extensions or Graphics Processing Unit)

## Slide 10: Multiple Instruction/Multiple Data Stream
Multiple autonomous processors simultaneously executing different instructions on different data
MIMD architectures include multicore and Warehouse Scale Computers

## Slide 11: Agenda
Flynn’s Taxonomy
Administrivia
Data Level Parallelism and SIMD
Bonus: Loop Unrolling

## Slide 12: Administrivia
HW3 due Sunday
Proj2 (MapReduce) to be released soon
  Part 1 due 3/17
  Part 2 due 3/24
  Work in partners, preferably at least 1 knows Java
Midterms graded
  Collect after lecture today or from Lab TA next week

## Slide 14: Agenda
Flynn’s Taxonomy
Administrivia
Data Level Parallelism and SIMD
Bonus: Loop Unrolling

## Slide 15: SIMD Architectures
Data-Level Parallelism (DLP): Executing one operation on multiple data streams
Example: Multiplying a coefficient vector by a data vector (e.g. in filtering)
y[i] := c[i]  x[i], 0i<n
Sources of performance improvement:
  One instruction is fetched & decoded for entire operation
  Multiplications are known to be independent
  Pipelining/concurrency in memory access as well

## Slide 16: “Advanced Digital Media Boost”
To improve performance, Intel’s SIMD instructions
  Fetch one instruction, do the work of multiple instructions
  MMX (MultiMedia eXtension, Pentium II processor family)
  SSE (Streaming SIMD Extension, Pentium III and beyond)

## Slide 17: Example: SIMD Array Processing
for each f in array
f = sqrt(f)
for each f in array {
load f to the floating-point register
calculate the square root
write the result from the register to memory
}
for every 4 members in array {
load 4 members to the SSE register
calculate 4 square roots in one operation
write the result from the register to memory
}
pseudocode
SISD
SIMD

## Slide 18: SSE Instruction Categories for Multimedia Support
Intel processors are CISC (complicated instrs)
SSE-2+ supports wider data types to allow 16 × 8-bit and 8 × 16-bit operands
Notes: 64 bits operated on simultaneously!

## Slide 19: Intel Architecture SSE2+ 128-Bit SIMD Data Types
Note: in Intel Architecture (unlike MIPS) a word is 16 bits
  Single precision FP: Double word (32 bits)
  Double precision FP: Quad word (64 bits)
64 63
64 63
64 63
32 31
32 31
96 95
96 95
16 15
48 47
80 79
122 121
64 63
32 31
96 95
16 15
48 47
80 79
122 121
16 / 128 bits
8 / 128 bits
4 / 128 bits
2 / 128 bits

## Slide 20: XMM Registers
Architecture extended with eight 128-bit data registers
  64-bit address architecture: available as 16 64-bit registers (XMM8 – XMM15)
  e.g. 128-bit packed single-precision floating-point data type (doublewords), allows four single-precision operations to be performed simultaneously
XMM7
XMM6
XMM5
XMM4
XMM3
XMM2
XMM1
XMM0
127
0
Notes: Doublewords are the 32-bit chunks of data we’re used to working with.

## Slide 21: SSE/SSE2 Floating Point Instructions
{SS} Scalar Single precision FP: 1 32-bit operand in a 128-bit register
{PS} Packed Single precision FP: 4 32-bit operands in a 128-bit register
{SD} Scalar Double precision FP: 1 64-bit operand in a 128-bit register
{PD} Packed Double precision FP, or 2 64-bit operands in a 128-bit register

## Slide 22: SSE/SSE2 Floating Point Instructions
xmm: one operand is a 128-bit SSE2 register
mem/xmm: other operand is in memory or an SSE2 register
{A} 128-bit operand is aligned in memory
{U} means the 128-bit operand is unaligned in memory
{H} means move the high half of the 128-bit operand
{L} means move the low half of the 128-bit operand

## Slide 23: Example: Add Single Precision FP Vectors
add from mem to XMM register, packed single precision
move from XMM register to mem, memory aligned, packed single precision
move from mem to XMM register, memory aligned, packed single precision
Computation to be performed:
vec_res.x = v1.x + v2.x;
vec_res.y = v1.y + v2.y;
vec_res.z = v1.z + v2.z;
vec_res.w = v1.w + v2.w;
SSE Instruction Sequence:
movaps address-of-v1, %xmm0
// v1.w | v1.z | v1.y | v1.x -> xmm0
addps address-of-v2, %xmm0
// v1.w+v2.w | v1.z+v2.z | v1.y+v2.y | v1.x+v2.x -> xmm0
movaps %xmm0, address-of-vec_res

## Slide 24: Packed and Scalar Double-Precision Floating-Point Operations
Packed Double (PD)
Scalar Double (SD)

## Slide 25: Example: Image Converter (1/5)
Converts BMP (bitmap) image to a YUV (color space) image format:
  Read individual pixels from the BMP image, convert pixels into YUV format
  Can pack the pixels and operate on a set of pixels with a single instruction
Bitmap image consists of 8-bit monochrome pixels
  By packing these pixel values in a 128-bit register, we can operate on 128/8 = 16 values at a time
  Significant performance boost
Notes: BMP File Format, also known as Bitmap Image File
The BMP File Format is capable of storing 2D digital images of arbitrary width, height, and resolution, both monochrome and color, in various color depths, and optionally with data compression, alpha channels, and color profiles.
YUV is a color space typically used as part of a color image pipeline.
The Y'UV model defines a color space in terms of one luma (Y') and two chrominance (UV) components.

## Slide 26: Example: Image Converter (2/5)
FMADDPS – Multiply and add packed single precision floating point instruction
One of the typical operations computed in transformations (e.g. DFT or FFT)
P = ∑ f(n) × x(n)
N
n = 1
CISC Instr!

## Slide 27: Example: Image Converter (3/5)
FP numbers f(n) and x(n) in src1 and src2; p in dest;
C implementation for N = 4 (128 bits):
for (int i = 0; i < 4; i++)
p = p + src1[i] * src2[i];
Regular x86 instructions for the inner loop:
fmul […]
faddp […]
  Instructions executed: 4 * 2 = 8 (x86)
Notes: http://developer.amd.com/cpu/SSE5/Pages/default.aspx
"DE C0+i FADDP ST(i), ST(0) Add ST(0) to ST(i), store result in ST(i), and pop the register stack".
Destination on right called AT&T format

## Slide 28: Example: Image Converter (4/5)
FP numbers f(n) and x(n) in src1 and src2; p in dest;
C implementation for N = 4 (128 bits):
for (int i = 0; i < 4; i++)
p = p + src1[i] * src2[i];
SSE2 instructions for the inner loop:
//xmm0=p, xmm1=src1[i], xmm2=src2[i]
mulps %xmm1,%xmm2 // xmm2 * xmm1 -> xmm2
addps %xmm2,%xmm0 // xmm0 + xmm2 -> xmm0
  Instructions executed: 2 (SSE2)
Notes: http://developer.amd.com/cpu/SSE5/Pages/default.aspx
"DE C0+i FADDP ST(i), ST(0) Add ST(0) to ST(i), store result in ST(i), and pop the register stack".
Destination on right called AT&T format

## Slide 29: Example: Image Converter (5/5)
FP numbers f(n) and x(n) in src1 and src2; p in dest;
C implementation for N = 4 (128 bits):
for (int i = 0; i < 4; i++)
p = p + src1[i] * src2[i];
SSE5 accomplishes the same in one instruction:
fmaddps %xmm0, %xmm1, %xmm2, %xmm0
// xmm2 * xmm1 + xmm0 -> xmm0
// multiply xmm1 x xmm2 packed single, // then add product packed single to sum in xmm0
Notes: http://developer.amd.com/cpu/SSE5/Pages/default.aspx
"DE C0+i FADDP ST(i), ST(0) Add ST(0) to ST(i), store result in ST(i), and pop the register stack".
Destination on right called AT&T format

## Slide 30: Summary
Flynn Taxonomy of Parallel Architectures
  SIMD: Single Instruction Multiple Data
  MIMD: Multiple Instruction Multiple Data
  SISD: Single Instruction Single Data
  MISD: Multiple Instruction Single Data (unused)
Intel SSE SIMD Instructions
  One instruction fetch that operates on multiple operands simultaneously
  128/64 bit XMM registers

## Slide 31
You are responsible for the material contained on the following slides, though we may not have enough time to get to them in lecture.
They have been prepared in a way that should be easily readable and the material will be touched upon in the following lecture.
BONUS SLIDES

## Slide 32: Agenda
Flynn’s Taxonomy
Administrivia
Data Level Parallelism and SIMD
Bonus: Loop Unrolling

## Slide 33: Data Level Parallelism and SIMD
SIMD wants adjacent values in memory that can be operated in parallel
Usually specified in programs as loops
for(i=0; i<1000; i++)
x[i] = x[i] + s;
How can we reveal more data level parallelism than is available in a single iteration of a loop?
  Unroll the loop and adjust iteration rate

## Slide 34: Looping in MIPS
Assumptions:
$s0  initial address (beginning of array)
$s1  scalar value s
$s2  termination address (end of array)
Loop:
lw $t0,0($s0)
addu $t0,$t0,$s1 # add s to array element
sw $t0,0($s0) # store result
addiu $s0,$s0,4 # move to next element
bne $s0,$s2,Loop # repeat Loop if not done

## Slide 35: Loop Unrolled
Loop: lw $t0,0($s0)
addu $t0,$t0,$s1
sw $t0,0($s0)
lw $t1,4($s0)
addu $t1,$t1,$s1
sw $t1,4($s0)
lw $t2,8($s0)
addu $t2,$t2,$s1
sw $t2,8($s0)
lw $t3,12($s0)
addu $t3,$t3,$s1
sw $t3,12($s0)
addiu $s0,$s0,16
bne $s0,$s2,Loop
NOTE:
Using different registers eliminate stalls
Loop overhead encountered only once every 4 data iterations
This unrolling works if
loop_limit mod 4 = 0

## Slide 36: Loop Unrolled Scheduled
Loop: lwc1 $t0,0($s0)
lwc1 $t1,4($s0)
lwc1 $t2,8($s0)
lwc1 $t3,12($s0)
add.s $t0,$t0,$s1
add.s $t1,$t1,$s1
add.s $t2,$t2,$s1
add.s $t3,$t3,$s1
swc1 $t0,0($s0)
swc1 $t1,4($s0)
swc1 $t2,8($s0)
swc1 $t3,12($s0)
addiu $s0,$s0,16
bne $s0,$s2,Loop
4 Loads side-by-side:
Could replace with 4 wide SIMD Load
4 Adds side-by-side:
Could replace with 4 wide SIMD Add
4 Stores side-by-side:
Could replace with 4 wide SIMD Store
Note: We just switched from integer instructions to single-precision FP instructions!

## Slide 37: Loop Unrolling in C
Instead of compiler doing loop unrolling, could do it yourself in C:
for(i=0; i<1000; i++)
x[i] = x[i] + s;
for(i=0; i<1000; i=i+4) {
x[i] = x[i] + s;
x[i+1] = x[i+1] + s;
x[i+2] = x[i+2] + s;
x[i+3] = x[i+3] + s;
}
What is
downside of doing
this in C?
Loop Unroll

## Slide 38: Generalizing Loop Unrolling
Take a loop of n iterations and perform a k-fold unrolling of the body of the loop:
  First run the loop with k copies of the body floor(n/k) times
  To finish leftovers, then run the loop with 1 copy of the body n mod k times
(Will revisit loop unrolling again when get to pipelining later in semester)