## Slide 1
Guest Lecturer: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
Synchronization,
OpenMP

## Slide 2: Review of Last Lecture
Multiprocessor systems uses shared memory (single address space)
Cache coherence implements shared memory even with multiple copies in multiple caches
  Track state of blocks relative to other caches (e.g. MOESI protocol)
  False sharing a concern

## Slide 3: Great Idea #4: Parallelism
Smart Phone
Warehouse Scale Computer
Leverage Parallelism &
Achieve High Performance
Core
…
Memory
Input/Output
Computer
Core
Parallel Requests
  Assigned to computer
  e.g. search “Garcia”
Parallel Threads
  Assigned to core
  e.g. lookup, ads
Parallel Instructions
  > 1 instruction @ one time
  e.g. 5 pipelined instructions
Parallel Data
  > 1 data item @ one time
  e.g. add of 4 pairs of words
Hardware descriptions
  All gates functioning in parallel at same time
Software Hardware
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A0+B0
A1+B1
A2+B2
A3+B3
Logic Gates

## Slide 4: Agenda
Synchronization - A Crash Course
Administrivia
OpenMP Introduction
OpenMP Directives
  Workshare
  Synchronization
Bonus: Common OpenMP Pitfalls

## Slide 5: Data Races and Synchronization
Two memory accesses form a data race if different threads access the same location, and at least one is a write, and they occur one after another
  Means that the result of a program can vary depending on chance (which thread ran first?)
  Avoid data races by synchronizing writing and reading to get deterministic behavior
Synchronization done by user-level routines that rely on hardware synchronization instructions

## Slide 6: Analogy: Buying Milk
Your fridge has no milk. You and your roommate will return from classes at some point and check the fridge
Whoever gets home first will check the fridge, go and buy milk, and return
What if the other person gets back while the first person is buying milk?
  You’ve just bought twice as much milk as you need!
It would’ve helped to have left a note…

## Slide 7: Lock Synchronization (1/2)
Use a “Lock” to grant access to a region (critical section) so that only one thread can operate at a time
  Need all processors to be able to access the lock, so use a location in shared memory as the lock
Processors read lock and either wait (if locked) or set lock and go into critical section
  0 means lock is free / open / unlocked / lock off
  1 means lock is set / closed / locked / lock on

## Slide 8: Lock Synchronization (2/2)
Pseudocode:
Check lock
Set the lock
Critical section
(e.g. change shared variables)
Unset the lock
Can loop/idle here if locked

## Slide 9: Possible Lock Implementation
Lock (a.k.a. busy wait)
  Get_lock: # $s0 -> addr of lock
  addiu $t1,$zero,1 # t1 = Locked value
  Loop: lw $t0,0($s0) # load lock
  bne $t0,$zero,Loop # loop if locked
  Lock: sw $t1,0($s0) # Unlocked, so lock
Unlock
  Unlock:
sw $zero,0($s0)
Any problems with this?

## Slide 10: Possible Lock Problem
Thread 1
addiu $t1,$zero,1
Loop: lw $t0,0($s0)
bne $t0,$zero,Loop
Lock: sw $t1,0($s0)
Thread 2
addiu $t1,$zero,1
Loop: lw $t0,0($s0)
bne $t0,$zero,Loop
Lock: sw $t1,0($s0)
Time
Both threads think they have set the lock!
Exclusive access not guaranteed!

## Slide 11: Hardware Synchronization
Hardware support required to prevent an interloper (another thread) from changing the value
  Atomic read/write memory operation
  No other access to the location allowed between the read and write
How best to implement in software?
  Single instr? Atomic swap of register ↔ memory
  Pair of instr? One for read, one for write
Notes: Interloper thread can be from same core or another core.

## Slide 12: Synchronization in MIPS
Load linked: ll rt,off(rs)
Store conditional: sc rt,off(rs)
  Returns 1 (success) if location has not changed since the ll
  Returns 0 (failure) if location has changed
Note that sc clobbers the register value being stored (rt)!
  Need to have a copy elsewhere if you plan on repeating on failure or using value later
Notes: Here using the Green Sheet convention of rs and rt for source register and target register.

## Slide 13: Synchronization in MIPS Example
Atomic swap (to test/set lock variable)
Exchange contents of register and memory: $s4 ↔ Mem($s1)
  try: add $t0,$zero,$s4 #copy value
  ll $t1,0($s1) #load linked
  sc $t0,0($s1) #store conditional
  beq $t0,$zero,try #loop if sc fails
  add $s4,$zero,$t1 #load value in $s4
sc would fail if another threads executes sc here

## Slide 14: Test-and-Set
In a single atomic operation:
  Test to see if a memory location is set (contains a 1)
  Set it (to 1) if it isn’t (it contained a zero when tested)
  Otherwise indicate that the Set failed, so the program can try again
  While accessing, no other instruction can modify the memory location, including other Test-and-Set instructions
Useful for implementing lock operations

## Slide 15: Test-and-Set in MIPS
Example: MIPS sequence for implementing a T&S at ($s1)
  Try: addiu $t0,$zero,1
  ll $t1,0($s1)
  bne $t1,$zero,Try
  sc $t0,0($s1)
  beq $t0,$zero,try
  Locked:
  # critical section
  Unlock:
  sw $zero,0($s1)

## Slide 16
Question: Consider the following code when executed concurrently by two threads.
What possible values can result in *($s0)?
# *($s0) = 100
lw $t0,0($s0)
addi $t0,$t0,1
sw $t0,0($s0)
101 or 102
☐
100, 101, or 102
☐
100 or 101
☐
102
☐
Notes: - 102 if one thread starts executing after the other completely finishes.
- 101 if both threads execute the lw before either thread executes the sw. One thread will see “stale data”.

## Slide 17: Agenda
Synchronization - A Crash Course
Administrivia
OpenMP Introduction
OpenMP Directives
  Workshare
  Synchronization
Bonus: Common OpenMP Pitfalls

## Slide 18: Administrivia
Midterm re-grade requests due Tuesday (3/19)
Project 2: MapReduce
  Work in groups of two!
  Part 1: Due March 17 (this Sunday)
  Part 2: Due March 24 (part of Spring Break)
Homework 4 will be posted before Spring Break
  If you want to get a head start

## Slide 19: Agenda
Synchronization - A Crash Course
Administrivia
OpenMP Introduction
OpenMP Directives
  Workshare
  Synchronization
Bonus: Common OpenMP Pitfalls

## Slide 20: What is OpenMP?
API used for multi-threaded, shared memory parallelism
  Compiler Directives
  Runtime Library Routines
  Environment Variables
Portable
Standardized
Resources: http://www.openmp.org/ and http://computing.llnl.gov/tutorials/openMP/
Notes: API: Application Programming Interface

## Slide 21: OpenMP Specification

## Slide 22: Shared Memory Model with Explicit Thread-based Parallelism
Multiple threads in a shared memory environment, explicit programming model with full programmer control over parallelization
Pros:
  Takes advantage of shared memory, programmer need not worry (that much) about data placement
  Compiler directives are simple and easy to use
  Legacy serial code does not need to be rewritten
Cons:
  Code can only be run in shared memory environments
  Compiler must support OpenMP (e.g. gcc 4.2)

## Slide 23: OpenMP in CS61C
OpenMP is built on top of C, so you don’t have to learn a whole new programming language
  Make sure to add #include <omp.h>
  Compile with flag: gcc -fopenmp
  Mostly just a few lines of code to learn
You will NOT become experts at OpenMP
  Use slides as reference, will learn to use in lab
Key ideas:
  Shared vs. Private variables
  OpenMP directives for parallelization, work sharing, synchronization

## Slide 24: OpenMP Programming Model
Fork - Join Model:
OpenMP programs begin as single process (master thread) and executes sequentially until the first parallel region construct is encountered
  FORK: Master thread then creates a team of parallel threads
  Statements in program that are enclosed by the parallel region construct are executed in parallel among the various threads
  JOIN: When the team threads complete the statements in the parallel region construct, they synchronize and terminate, leaving only the master thread

## Slide 25: OpenMP Extends C with Pragmas
Pragmas are a preprocessor mechanism C provides for language extensions
Commonly implemented pragmas: structure packing, symbol aliasing, floating point exception modes (not covered in 61C)
Good mechanism for OpenMP because compilers that don't recognize a pragma are supposed to ignore them
  Runs on sequential computer even with embedded pragmas

## Slide 26: parallel Pragma and Scope
Basic OpenMP construct for parallelization:
#pragma omp parallel
{
/* code goes here */
}
  Each thread runs a copy of code within the block
  Thread scheduling is non-deterministic
OpenMP default is shared variables
  To make private, need to declare with pragma:
#pragma omp parallel private (x)
This is annoying, but curly brace MUST go on separate line from #pragma

## Slide 27: Thread Creation
How many threads will OpenMP create?
Defined by OMP_NUM_THREADS environment variable (or code procedure call)
  Set this variable to the maximum number of threads you want OpenMP to use
  Usually equals the number of cores in the underlying hardware on which the program is run

## Slide 28: OMP_NUM_THREADS
OpenMP intrinsic to set number of threads:
omp_set_num_threads(x);
OpenMP intrinsic to get number of threads:
num_th = omp_get_num_threads();
OpenMP intrinsic to get Thread ID number:
th_ID = omp_get_thread_num();

## Slide 29: Parallel Hello World
#include <stdio.h>
#include <omp.h>
int main () {
int nthreads, tid;
/* Fork team of threads with private var tid */
#pragma omp parallel private(tid)
{
tid = omp_get_thread_num(); /* get thread id */
printf("Hello World from thread = %d\n", tid);
/* Only master thread does this */
if (tid == 0) {
nthreads = omp_get_num_threads();
printf("Number of threads = %d\n", nthreads);
}
} /* All threads join master and terminate */
}

## Slide 30: Agenda
Synchronization - A Crash Course
Administrivia
OpenMP Introduction
OpenMP Directives
  Workshare
  Synchronization
Bonus: Common OpenMP Pitfalls

## Slide 31: OpenMP Directives (Work-Sharing)
Shares iterations of a loop across the threads
Each section is executed by a separate thread
Serializes the execution of a thread
These are defined within a parallel section
Notes: A work-sharing construct divides the execution of the enclosed code region among the members of the team that encounter it.

## Slide 32: Parallel Statement Shorthand
#pragma omp parallel
{
#pragma omp for
for(i=0;i<len;i++) { … }
}
can be shortened to:
#pragma omp parallel for
for(i=0;i<len;i++) { … }
Also works for sections
This is the only directive in the parallel section

## Slide 33: Building Block: for loop
for (i=0; i<max; i++) zero[i] = 0;
Break for loop into chunks, and allocate each to a separate thread
  e.g. if max = 100 with 2 threads: assign 0-49 to thread 0, and 50-99 to thread 1
Must have relatively simple “shape” for an OpenMP-aware compiler to be able to parallelize it
  Necessary for the run-time system to be able to determine how many of the loop iterations to assign to each thread
No premature exits from the loop allowed
  i.e. No break, return, exit, goto statements
In general, don’t jump outside of any pragma block
Notes: “Shape” restrictions: The FOR loop can not be a DO WHILE loop, or a loop without loop control. Also, the loop iteration variable must be an integer and the loop control parameters must be the same for all threads.

## Slide 34: Parallel for pragma
#pragma omp parallel for
for (i=0; i<max; i++) zero[i] = 0;
Master thread creates additional threads, each with a separate execution context
All variables declared outside for loop are shared by default, except for loop index which is private per thread (Why?)
Implicit synchronization at end of for loop
Divide index regions sequentially per thread
  Thread 0 gets 0, 1, …, (max/n)-1;
  Thread 1 gets max/n, max/n+1, …, 2*(max/n)-1
  Why?

## Slide 35: OpenMP Timing
Elapsed wall clock time:
double omp_get_wtime(void);
  Returns elapsed wall clock time in seconds
  Time is measured per thread, no guarantee can be made that two distinct threads measure the same time
  Time is measured from “some time in the past,” so subtract results of two calls to omp_get_wtime to get elapsed time

## Slide 36: Matrix Multiply in OpenMP
start_time = omp_get_wtime();
#pragma omp parallel for private(tmp, i, j, k)
for (i=0; i<Mdim; i++){
for (j=0; j<Ndim; j++){
tmp = 0.0;
for( k=0; k<Pdim; k++){
/* C(i,j) = sum(over k) A(i,k) * B(k,j)*/
tmp += *(A+(i*Pdim+k)) * *(B+(k*Ndim+j));
}
*(C+(i*Ndim+j)) = tmp;
}
}
run_time = omp_get_wtime() - start_time;
Outer loop spread across N threads; inner loops inside a single thread

## Slide 37: Notes on Matrix Multiply Example
More performance optimizations available:
  Higher compiler optimization (-O2, -O3) to reduce number of instructions executed
  Cache blocking to improve memory performance
  Using SIMD SSE instructions to raise floating point computation rate (DLP)

## Slide 38: OpenMP Directives (Synchronization)
These are defined within a parallel section
master
  Code block executed only by the master thread (all other threads skip)
critical
  Code block executed by only one thread at a time
atomic
  Specific memory location must be updated atomically (like a mini-critical section for writing to memory)
  Applies to single statement, not code block

## Slide 39: OpenMP Reduction
Reduction specifies that one or more private variables are the subject of a reduction operation at end of parallel region
  Clause reduction(operation:var)
  Operation: Operator to perform on the variables at the end of the parallel region
  Var: One or more variables on which to perform scalar reduction
#pragma omp for reduction(+:nSum)
for (i = START ; i <= END ; i++)
nSum += i;

## Slide 40: Summary
Data races lead to subtle parallel bugs
Synchronization via hardware primitives:
  MIPS does it with Load Linked + Store Conditional
OpenMP as simple parallel extension to C
  During parallel fork, be aware of which variables should be shared vs. private among threads
  Work-sharing accomplished with for/sections
  Synchronization accomplished with critical/atomic/reduction

## Slide 41
You are responsible for the material contained on the following slides, though we may not have enough time to get to them in lecture.
They have been prepared in a way that should be easily readable and the material will be touched upon in the following lecture.
BONUS SLIDES

## Slide 42: Agenda
Synchronization - A Crash Course
Administrivia
OpenMP Introduction
OpenMP Directives
  Workshare
  Synchronization
Bonus: Common OpenMP Pitfalls

## Slide 43: OpenMP Pitfall #1: Data Dependencies
Consider the following code:
  a[0] = 1;
  for(i=1; i<5000; i++)
  a[i] = i + a[i-1];
There are dependencies between loop iterations!
  Splitting this loop between threads does not guarantee in-order execution
  Out of order loop execution will result in undefined behavior (i.e. likely wrong result)

## Slide 44: Open MP Pitfall #2: Sharing Issues
Consider the following loop:
#pragma omp parallel for
for(i=0; i<n; i++){
temp = 2.0*a[i];
a[i] = temp;
b[i] = c[i]/temp;
}
temp is a shared variable!
#pragma omp parallel for private(temp)
for(i=0; i<n; i++){
temp = 2.0*a[i];
a[i] = temp;
b[i] = c[i]/temp;
}

## Slide 45: OpenMP Pitfall #3: Updating Shared Variables Simultaneously
Now consider a global sum:
for(i=0; i<n; i++)
sum = sum + a[i];
This can be done by surrounding the summation by a critical/atomic section or reduction clause:
#pragma omp parallel for reduction(+:sum)
{
for(i=0; i<n; i++)
sum = sum + a[i];
}
  Compiler can generate highly efficient code for reduction

## Slide 46: OpenMP Pitfall #4: Parallel Overhead
Spawning and releasing threads results in significant overhead
Better to have fewer but larger parallel regions
  Parallelize over the largest loop that you can (even though it will involve more work to declare all of the private variables and eliminate dependencies)

## Slide 47: OpenMP Pitfall #4: Parallel Overhead
start_time = omp_get_wtime();
for (i=0; i<Ndim; i++){
for (j=0; j<Mdim; j++){
tmp = 0.0;
#pragma omp parallel for reduction(+:tmp)
for( k=0; k<Pdim; k++){
/* C(i,j) = sum(over k) A(i,k) * B(k,j)*/
tmp += *(A+(i*Ndim+k)) * *(B+(k*Pdim+j));
}
*(C+(i*Ndim+j)) = tmp;
}
}
run_time = omp_get_wtime() - start_time;
Too much overhead in thread generation to have this statement run this frequently.
Poor choice of loop to parallelize.