## Slide 1
Guest Lecturer: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
Pipelining Hazards

## Slide 2: Great Idea #4: Parallelism
Smart Phone
Warehouse Scale Computer
Leverage Parallelism &
Achieve High Performance
Core
…
Memory
Input/Output
Computer
Core
Parallel Requests
  Assigned to computer
  e.g. search “Garcia”
Parallel Threads
  Assigned to core
  e.g. lookup, ads
Parallel Instructions
  > 1 instruction @ one time
  e.g. 5 pipelined instructions
Parallel Data
  > 1 data item @ one time
  e.g. add of 4 pairs of words
Hardware descriptions
  All gates functioning in parallel at same time
Software Hardware
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A0+B0
A1+B1
A2+B2
A3+B3
Logic Gates

## Slide 3: Review of Last Lecture
Implementing controller for your datapath
  Take decoded signals from instruction and generate control signals
  Use “AND” and “OR” Logic scheme
Pipelining improves performance by exploiting Instruction Level Parallelism
  5-stage pipeline for MIPS: IF, ID, EX, MEM, WB
  Executes multiple instructions in parallel
  What can go wrong???

## Slide 4: Agenda
Pipelining Performance
Structural Hazards
Administrivia
Data Hazards
  Forwarding
  Load Delay Slot
Control Hazards

## Slide 5: Review: Pipelined Datapath

## Slide 6: Pipelined Execution Representation
Every instruction must take same number of steps, so some stages will idle
  e.g. MEM stage for any arithmetic instruction
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Time
Notes: Each instruction has identical latency!

## Slide 7: Graphical Pipeline Diagrams
Use datapath figure below to represent pipeline:
IF
ID
EX
Mem
WB
ALU
I$
Reg
D$
Reg
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write
Back
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

## Slide 8: Graphical Pipeline Representation
I
n
s
t
r
O
r
d
e
r
Load
Add
Store
Sub
Or
I$
Time (clock cycles)
I$
ALU
Reg
Reg
I$
D$
ALU
ALU
Reg
D$
Reg
I$
D$
Reg
ALU
Reg
Reg
Reg
D$
Reg
D$
ALU
RegFile: left half is write, right half is read
Reg
I$

## Slide 9: Pipelining Performance (1/3)
Use Tc (“time between completion of instructions”) to measure speedup
  Equality only achieved if stages are balanced (i.e. take the same amount of time)
If not balanced, speedup is reduced
Speedup due to increased throughput
  Latency for each instruction does not decrease

## Slide 10: Pipelining Performance (2/3)
Assume time for stages is
  100ps for register read or write
  200ps for other stages
What is pipelined clock rate?
  Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 11: Pipelining Performance (3/3)
Single-cycle
Tc = 800 ps
Pipelined
Tc = 200 ps
Notes: Here using Tc as “time between completion of instructions.”

## Slide 12: Pipelining Hazards
A hazard is a situation that prevents starting the next instruction in the next clock cycle
Structural hazard
  A required resource is busy (e.g. needed in multiple stages)
Data hazard
  Data dependency between instructions
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Flow of execution depends on previous instruction

## Slide 13: Agenda
Pipelining Performance
Structural Hazards
Administrivia
Data Hazards
  Forwarding
  Load Delay Slot
Control Hazards

## Slide 14: 1. Structural Hazards
Conflict for use of a resource
MIPS pipeline with a single memory?
  Load/Store requires memory access for data
  Instruction fetch would have to stall for that cycle
    Causes a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Separate L1 I$ and L1 D$ take care of this

## Slide 15: Structural Hazard #1: Single Memory
I$
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
Trying to read same memory twice in same clock cycle

## Slide 16: Structural Hazard #2: Registers (1/2)
I$
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
Can we read and write to registers simultaneously?

## Slide 17: Structural Hazard #2: Registers (2/2)
Two different solutions have been used:
  Split RegFile access in two: Write during 1st half and Read during 2nd half of each clock cycle
    Possible because RegFile access is VERY fast (takes less than half the time of ALU stage)
  Build RegFile with independent read and write ports
Conclusion: Read and Write to registers during same clock cycle is okay

## Slide 18: Agenda
Pipelining Performance
Structural Hazards
Administrivia
Data Hazards
  Forwarding
  Load Delay Slot
Control Hazards

## Slide 19: Administrivia
Project 2: Performance Optimization
  Part 1 due Sunday (4/14)
  Part 2 released by Sunday night, due 4/21
  Built-in performance competition for Part 2!
Never too early to start looking at past exams!
Dan has moved his OH because of traveling
  See Piazza post @1492

## Slide 20: Agenda
Pipelining Performance
Structural Hazards
Administrivia
Data Hazards
  Forwarding
  Load Delay Slot
Control Hazards

## Slide 21: 2. Data Hazards (1/2)
Consider the following sequence of instructions:
add $t0, $t1, $t2
sub $t4, $t0, $t3
and $t5, $t0, $t6
or $t7, $t0, $t8
xor $t9, $t0, $t10

## Slide 22: 2. Data Hazards (2/2)
Data-flow backwards in time are hazards
sub $t4,$t0,$t3
ALU
I$
Reg
D$
Reg
and $t5,$t0,$t6
ALU
I$
Reg
D$
Reg
or $t7,$t0,$t8
I$
ALU
Reg
D$
Reg
xor $t9,$t0,$t10
ALU
I$
Reg
D$
Reg
add $t0,$t1,$t2
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)

## Slide 23: Data Hazard Solution: Forwarding
Forward result as soon as it is available
  OK that it’s not stored in RegFile yet
sub $t4,$t0,$t3
ALU
I$
Reg
D$
Reg
and $t5,$t0,$t6
ALU
I$
Reg
D$
Reg
or $t7,$t0,$t8
I$
ALU
Reg
D$
Reg
xor $t9,$t0,$t10
ALU
I$
Reg
D$
Reg
add $t0,$t1,$t2
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg

## Slide 24: Datapath for Forwarding (1/2)
What changes need to be made here?

## Slide 25: Datapath for Forwarding (2/2)
Handled by forwarding unit
Notes: Scan figure 4.54 on p. 368.

## Slide 26: Data Hazard: Loads (1/4)
Recall: Dataflow backwards in time are hazards
Can’t solve all cases with forwarding
  Must stall instruction dependent on load, then forward (more hardware)
sub $t3,$t0,$t2
ALU
I$
Reg
D$
Reg
lw $t0,0($t1)
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg

## Slide 27: Data Hazard: Loads (2/4)
Hardware stalls pipeline
  Called “hardware interlock”
sub $t3,$t0,$t2
ALU
I$
Reg
D$
Reg
bubble
and $t5,$t0,$t4
ALU
I$
Reg
D$
Reg
bubble
or $t7,$t0,$t6
I$
ALU
Reg
D$
bubble
lw $t0, 0($t1)
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg
Schematically, this is what we want, but in reality stalls done “horizontally”
How to stall just part of pipeline?

## Slide 28: Data Hazard: Loads (3/4)
Stall is equivalent to nop
sub $t3,$t0,$t2
and $t5,$t0,$t4
or $t7,$t0,$t6
I$
ALU
Reg
D$
lw $t0, 0($t1)
ALU
I$
Reg
D$
Reg
bubble
bubble
bubble
bubble
bubble
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
nop

## Slide 29: Data Hazard: Loads (4/4)
Slot after a load is called a load delay slot
  If that instruction uses the result of the load, then the hardware interlock will stall it for one cycle
  Letting the hardware stall the instruction in the delay slot is equivalent to putting a nop in the slot (except the latter uses more code space)
Idea: Let the compiler put an unrelated instruction in that slot  no stall!

## Slide 30: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction!
MIPS code for D=A+B; E=A+C;
# Method 1:
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
# Method 2:
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
Stall!
Stall!
13 cycles
11 cycles

## Slide 31: Agenda
More Pipelining
Structural Hazards
Administrivia
Data Hazards
  Forwarding
  Load Delay Slot
Control Hazards

## Slide 32: 3. Control Hazards
Branch (beq, bne) determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
Simple Solution: Stall on every branch until we have the new PC value
  How long must we stall?

## Slide 33: Branch Stall
When is comparison result available?
I$
beq
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
TWO bubbles required per branch!

## Slide 34: Summary
Hazards reduce effectiveness of pipelining
  Cause stalls/bubbles
Structural Hazards
  Conflict in use of datapath component
Data Hazards
  Need to wait for result of a previous instruction
Control Hazards
  Address of next instruction uncertain/unknown
  More to come next lecture!

## Slide 35
Question: For each code sequences below, choose one of the statements below:
No stalls as is
A)
No stalls with forwarding
B)
Must stall
C)
1: lw $t0,0($t0) add $t1,$t0,$t0 | 2: add $t1,$t0,$t0 addi $t2,$t0,5 addi $t4,$t1,5 | 3: addi $t1,$t0,1 addi $t2,$t0,2 addi $t3,$t0,2 addi $t3,$t0,4 addi $t5,$t1,5

## Slide 36: Code Sequence 1
I$
lw
add
instr
instr
instr
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
Must stall

## Slide 37: Code Sequence 2
I$
add
addi
addi
instr
instr
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
forwarding
no forwarding
No stalls with forwarding

## Slide 38: Code Sequence 3
I$
addi
addi
addi
addi
addi
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
No stalls as is