## Slide 1
Guest Lecturer: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
Virtual Memory II

## Slide 2: Agenda
Review of Last Lecture
  Goals of Virtual Memory
  Page Tables
  Translation Lookaside Buffer (TLB)
Administrivia
VM Performance

## Slide 3: Memory Hierarchy Requirements
Allow multiple processes to simultaneously occupy memory and provide protection
  Don’t let programs read from or write to each other’s memories
Give each program the illusion that it has its own private address space (via translation)
  Suppose code starts at address 0x00400000, then different processes each think their code resides at the same address
  Each program must have a different view of memory

## Slide 4: Goals of Virtual Memory
Next level in the memory hierarchy
  Provides illusion of very large main memory
  Working set of “pages” residing in main memory (subset of all pages residing on disk)
Main goal: Avoid reaching all the way back to disk as much as possible
Additional goals:
  Let OS share memory among many programs and protect them from each other
  Each process thinks it has all the memory to itself

## Slide 5: Review: Paging Terminology
Programs use virtual addresses (VAs)
  Space of all virtual addresses called virtual memory (VM)
  Divided into pages indexed by virtual page number (VPN)
Main memory indexed by physical addresses (PAs)
  Space of all physical addresses called physical memory (PM)
  Divided into pages indexed by physical page number (PPN)

## Slide 6: Virtual Memory Mapping Function
How large is main memory? Disk?
  Don’t know! Designed to be interchangeable components
  Need a system that works regardless of sizes
Use lookup table (page table) to deal with arbitrary mapping
  Index lookup table by # of pages in VM (not all entries will be used/valid)
  Size of PM will affect size of stored translation

## Slide 7: Address Mapping
Pages are aligned in memory
  Border address of each page has same lowest bits
  Page size is same in VM and PM, so denote lowest O = log2(page size/byte) bits as page offset
Use remaining upper address bits in mapping
  Tells you which page you want (similar to Tag)
Page Offset
Virtual Page #
Page Offset
Physical Page #
Same Size
Not necessarily the same size

## Slide 8: Address Mapping: Page Table
Page Table functionality:
  Incoming request is Virtual Address (VA), want Physical Address (PA)
  Physical Offset = Virtual Offset (page-aligned)
  So just swap Virtual Page Number (VPN) for Physical Page Number (PPN)
Implementation?
  Use VPN as index into PT
  Store PPN and management bits (Valid, Access Rights)
  Does NOT store actual data (the data sits in PM)
Page Offset
Virtual Page #
Physical Page #
Page Offset

## Slide 9: Page Table Layout
V | AR | PPN
X | XX | 
. . . |  | 
Virtual Address:
VPN
offset
Page Table
1) Index into PT using VPN
2) Check Valid and Access Rights bits
+
3) Combine PPN and offset
Physical
Address
4) Use PA to access memory

## Slide 10: Page Table Entry Format
Contains either PPN or indication not in main memory
Valid = Valid page table entry
  1  virtual page is in physical memory
  0  OS needs to fetch page from disk
Access Rights checked on every access to see if allowed (provides protection)
  Read Only: Can read, but not write page
  Read/Write: Read or write data on page
  Executable: Can fetch instructions from page

## Slide 11: Page Tables (1/2)
A page table (PT) contains the mapping of virtual addresses to physical addresses
Page tables located in main memory – Why?
  Too large to fit in registers (220 entries for 4 KiB pages)
  Faster to access than disk and can be shared by multiple processors
The OS maintains the PTs
  Each process has its own page table
    “State” of a process is PC, all registers, and PT
  OS stores address of the PT of the current process in the Page Table Base Register

## Slide 12: Page Tables (2/2)
Solves fragmentation problem: all pages are the same size, so can utilize all available slots
OS must reserve “swap space” on disk for each process
  Running programs requires hard drive space!
To grow a process, ask Operating System
  If unused pages in PM, OS uses them first
  If not, OS swaps some old pages (LRU) to disk

## Slide 13: Paging/Virtual Memory Multiple Processes
User B: Virtual Memory
¥
Code
Static
Heap
Stack
0
Code
Static
Heap
Stack
Page
Table A
Page
Table B
User A: Virtual Memory
¥
0
0
Physical
Memory
64 MB

## Slide 14
Question: How many bits wide are the following fields?
16 KiB pages
40-bit virtual addresses
64 GiB physical memory
26 26
A)
24 20
B)
22 22
C)
26 22
D)
VPN PPN

## Slide 15: Retrieving Data from Memory
VA1
User 1 Virtual Address Space
User 2 Virtual Address Space
PT User 1
PT User 2
VA2
1) Access page table for address translation
Physical Memory
2) Access correct physical address
Requires two accesses of physical memory!

## Slide 16: Virtual Memory Problem
2 physical memory accesses per data access = SLOW!
Build a separate cache for the Page Table
  For historical reasons, cache is called a Translation Lookaside Buffer (TLB)
  Notice that what is stored in the TLB is NOT data, but the VPN  PPN mapping translations

## Slide 17: TLBs vs. Caches
TLBs usually small, typically 16 – 512 entries
TLB access time comparable to cache (« main memory)
TLBs can have associativity
  Usually fully/highly associative
D$ / I$
Memory Address
Data at memory address
Access next cache level / main memory
On miss:
TLB
VPN
PPN
Access Page Table in main memory
On miss:

## Slide 18: Where Are TLBs Located?
Which should we check first: Cache or TLB?
  Can cache hold requested data if corresponding page is not in physical memory?
  With TLB first, does cache receive VA or PA?
No
PA
Cache
VA
PA
miss
hit
data
hit
miss
CPU
Main Memory
TLB
Page Table
Notice that it is now the TLB that does translation, not the Page Table!

## Slide 19: Address Translation Using TLB
TLB Tag
TLB Index
Page Offset
TLB Tag | PPN
(used just like in a cache) | 
. . . | 
TLB
VPN
PPN
Page Offset
Tag
Index
Offset
Virtual Address
Physical Address
 | Tag | Block Data
. . . |  | 
Data Cache
PA split two different ways!
Note: TIO for VA & PA unrelated

## Slide 20: Typical TLB Entry Format
Valid and Access Rights: Same usage as previously discussed for page tables
Dirty: Basically always use write-back, so indicates whether or not to write page to disk when replaced
Ref: Used to implement LRU
  Set when page is accessed, cleared periodically by OS
  If Ref = 1, then page was referenced recently
TLB Index: VPN mod (# TLB sets)
TLB Tag: VPN – TLB Index
Valid | Dirty | Ref | Access Rights | TLB Tag | PPN
X | X | X | XX |  | 

## Slide 21
Question: How many bits wide are the following?
16 KiB pages
40-bit virtual addresses
64 GiB physical memory
2-way set associative TLB with 512 entries
12 14 38
A)
18 8 45
B)
14 12 40
C)
17 9 43
D)
TLB Tag TLB Index TLB Entry
Valid | Dirty | Ref | Access Rights | TLB Tag | PPN
X | X | X | XX |  | 

## Slide 22: Agenda
Review of Last Lecture
  Goals of Virtual Memory
  Page Tables
  Translation Lookaside Buffer (TLB)
Administrivia
VM Performance

## Slide 23: Administrivia
Project 3 due Sunday 4/21
  Performance contest winners to be announced in class at end of semester
Project 4 (individual) coming soon!
Final – Tues 5/14, 3-6pm, 2050 VLSB
  MIPS Green Sheet provided again
  Two-sided handwritten cheat sheet
    Can use the back side of your midterm cheat sheet!

## Slide 24: Agenda
Review of Last Lecture
  Goals of Virtual Memory
  Page Tables
  Translation Lookaside Buffer (TLB)
Administrivia
VM Performance

## Slide 25: Fetching Data on a Memory Read
Check TLB (input: VPN, output: PPN)
  TLB Hit: Fetch translation, return PPN
  TLB Miss: Check page table (in memory)
    Page Table Hit: Load page table entry into TLB
    Page Table Miss (Page Fault): Fetch page from disk to memory, update corresponding page table entry, then load entry into TLB
Check cache (input: PPN, output: data)
  Cache Hit: Return data value to processor
  Cache Miss: Fetch data value from memory, store it in cache, return it to processor

## Slide 26: Page Faults
Load the page off the disk into a free page of memory
  Switch to some other process while we wait
Interrupt thrown when page loaded and the process' page table is updated
  When we switch back to the task, the desired data will be in memory
If memory full, replace page (LRU), writing back if necessary, and update both page table entries
  Continuous swapping between disk and memory called “thrashing”

## Slide 27: Performance Metrics
VM performance also uses Hit/Miss Rates and Miss Penalties
  TLB Miss Rate: Fraction of TLB accesses that result in a TLB Miss
  Page Table Miss Rate: Fraction of PT accesses that result in a page fault
Caching performance definitions remain the same
  Somewhat independent, as TLB will always pass PA to cache regardless of TLB hit or miss

## Slide 28: Data Fetch Scenarios
Are the following scenarios for a single data access possible?
  TLB Miss, Page Fault
  TLB Hit, Page Table Hit
  TLB Miss, Cache Hit
  Page Table Hit, Cache Miss
  Page Fault, Cache Hit
Yes
No
Yes
Yes
No
Cache
VA
PA
miss
hit
data
hit
miss
CPU
Main Memory
TLB
Page Table

## Slide 29
Question: A program tries to load a word at X that causes a TLB miss but not a page fault. Are the following statements TRUE or FALSE?
The page table does not contain a valid mapping for the virtual page corresponding to the address X
The word that the program is trying to load is present in physical memory
F F
A)
F T
B)
T F
C)
T T
D)
1 2

## Slide 30: VM Performance
Virtual Memory is the level of the memory hierarchy that sits below main memory
  TLB comes before cache, but affects transfer of data from disk to main memory
  Previously we assumed main memory was lowest level, now we just have to account for disk accesses
Same CPI, AMAT equations apply, but now treat main memory like a mid-level cache

## Slide 31: Typical Performance Stats
CPU
cache
primary
memory
secondary
memory
Caching Demand paging
  cache entry page frame
  cache block (≈32 bytes) page (≈4Ki bytes)
  cache miss rate (1% to 20%) page miss rate (<0.001%)
  cache hit (≈1 cycle) page hit (≈100 cycles)
  cache miss (≈100 cycles) page miss (≈5M cycles)
primary
memory
CPU

## Slide 32: Impact of Paging on AMAT (1/2)
Memory Parameters:
  L1 cache hit = 1 clock cycles, hit 95% of accesses
  L2 cache hit = 10 clock cycles, hit 60% of L1 misses
  DRAM = 200 clock cycles (≈100 nanoseconds)
  Disk = 20,000,000 clock cycles (≈10 milliseconds)
Average Memory Access Time (no paging):
  1 + 5%×10 + 5%×40%×200 = 5.5 clock cycles
Average Memory Access Time (with paging):
  5.5 (AMAT with no paging) + ?

## Slide 33: Impact of Paging on AMAT (2/2)
Average Memory Access Time (with paging) =
  5.5 + 5%×40%× (1-HRMem)×20,000,000
AMAT if HRMem = 99%?
  5.5 + 0.02×0.01×20,000,000 = 4005.5 (≈728x slower)
  1 in 20,000 memory accesses goes to disk: 10 sec program takes 2 hours!
AMAT if HRMem = 99.9%?
  5.5 + 0.02×0.001×20,000,000 = 405.5
AMAT if HRMem = 99.9999%
  5.5 + 0.02×0.000001×20,000,000 = 5.9

## Slide 34: Impact of TLBs on Performance
Each TLB miss to Page Table ~ L1 Cache miss
TLB Reach: Amount of virtual address space that can be simultaneously mapped by TLB:
  TLB typically has 128 entries of page size 4-8 KiB
  128 × 4 KiB = 512 KiB = just 0.5 MiB
What can you do to have better performance?
  Multi-level TLBs
  Variable page size (segments)
  Special situationally-used “superpages”
Conceptually same as multi-level caches
Not covered here

## Slide 35: Aside: Context Switching
How does a single processor run many programs at once?
Context switch: Changing of internal state of processor (switching between processes)
  Save register values (and PC) and change value in Page Table Base register
What happens to the TLB?
  Current entries are for different process
  Set all entries to invalid on context switch

## Slide 36: Virtual Memory Summary
User program view:
  Contiguous memory
  Start from some set VA
  “Infinitely” large
  Is the only running program
Reality:
  Non-contiguous memory
  Start wherever available memory is
  Finite size
  Many programs running simultaneously
Virtual memory provides:
  Illusion of contiguous memory
  All programs starting at same set address
  Illusion of ~ infinite memory (232 or 264 bytes)
  Protection , Sharing
Implementation:
  Divide memory into chunks (pages)
  OS controls page table that maps virtual into physical addresses
  memory as a cache for disk
  TLB is a cache for the page table