## Slide 1: CS 61C Great Ideas in Computer Architecture (a.k.a. Machine Structures) Lecture 1: Course Introduction
Instructors:
Professor Krste Asanovic (call me “Krste”) Professor Vladimir Stojanovic (call me “Vladimir”) (lots of help from TAs, esp Head TA Sagar Karandikar)
http://inst.eecs.berkeley.edu/~cs61c/

## Slide 2
3mm X 6mm Chip Fabricated in 45nm SOI 75m+ transistors
Dual-Core RISC-V Processor with Vector Accelerators
1MB SRAM Memory Structure for Testing
Monolithically-Integrated Silicon Photonic Links
About Us, Our Joint Project: Integrated Silicon Photonics
Notes: On the transmit cell, a resonant ring modulator is driven by an integrated driver circuit, with optical IO facilitated by two vertical grating couplers.
On the receiver cell, an input coupler being fed into an absorption-type photodetector. The receiver circuit is located nearby to minimize the wiring capacitance.

## Slide 3: Agenda
Thinking about Machine Structures
Great Ideas in Computer Architecture
What you need to know about this class
Everything is a Number

## Slide 4: Agenda
Thinking about Machine Structures
Great Ideas in Computer Architecture
What you need to know about this class
Everything is a Number

## Slide 5: CS61C is NOT really about C Programming
It is about the hardware-software interface
  What does the programmer need to know to achieve the highest possible performance
C is closer to the underlying hardware, unlike languages like Scheme, Python, Java!
  Allows us to talk about key hardware features in higher level terms
  Allows programmer to explicitly harness underlying hardware parallelism for high performance

## Slide 6: Old School CS61C
Notes: This image is a fake!
Although the photograph displayed could represent what some people in the early 1950s contemplated a "home computer" might look like (based on the technology of the day), it isn't, as the accompanying text claims, a RAND Corporation illustration from 1954 of a prototype "home computer." The picture is actually an entry submitted to a Fark.com image modification competition, taken from an original photo of a <A HREF="http://home.att.net/~jeff1_satobserve/photo17.htm" TARGET=sub>submarine</A> submarine maneuvering room console found on the U.S. Navy web site, converted to grayscale, and modified to replace a modern display panel and TV screen with pictures of a decades-old teletype/printer and television (as well as to add the gray-suited man to the left-hand side of the photo):

## Slide 7: New School CS61C (1/2)
Personal Mobile Devices

## Slide 8: New School CS61C (2/3)

## Slide 9: New School CS61C (3/3)

## Slide 10: Old School Machine Structures
CS61C
I/O system
Processor
Compiler
Operating
System
(Mac OSX)
Application (ex: browser)
Digital Design
Circuit Design
Instruction Set
Architecture
Datapath & Control
transistors
Memory
Hardware
Software
Assembler

## Slide 11: New-School Machine Structures (It’s a bit more complicated!)
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates functioning in parallel at same time
Smart Phone
Warehouse-Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Main Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Project 1
Project 4
Project 3
Project 2

## Slide 12: Agenda
Thinking about Machine Structures
Great Ideas in Computer Architecture
What you need to know about this class
Everything is a Number

## Slide 13: 6 Great Ideas in Computer Architecture
Abstraction (Layers of Representation/Interpretation)
Moore’s Law (Designing through trends)
Principle of Locality (Memory Hierarchy)
Parallelism
Performance Measurement & Improvement
Dependability via Redundancy

## Slide 14: Great Idea #1: Abstraction (Levels of Representation/Interpretation)
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions

## Slide 15: #2: Moore’s Law
Gordon Moore Intel Cofounder B.S. Cal 1950!
# of transistors on an integrated circuit (IC)
Year
Predicts:
2X Transistors / chip every 2 years

## Slide 16: Interesting Times
Moore’s Law
1965-2020?
Moore’s Law was based on how many transistors/chip at cheapest cost/transistor as technology scaled.
BUT newest, smallest fabrication processes <14nm, might have greater cost/transistor !!!!
So, why shrink????

## Slide 17: Jim Gray’s Storage Latency Analogy: How Far Away is the Data?
Registers
On Chip Cache
On Board Cache
Memory
Disk
1
2
10
100
Tape /Optical
Robot
10
9
10
6
Sacramento
This Campus
This Room
My Head
10 min
1.5 hr
2 Years
1 min
Pluto
2,000 Years
Andromeda
(ns)
Jim Gray Turing Award
B.S. Cal 1966
Ph.D. Cal 1969!

## Slide 18: Great Idea #3: Principle of Locality/ Memory Hierarchy

## Slide 19: Great Idea #4: Parallelism

## Slide 20
Caveat: Amdahl’s Law
Gene Amdahl
Computer Pioneer

## Slide 21: Great Idea #5: Performance Measurement and Improvement
Tuning application to underlying hardware to exploit:
  Locality
  Parallelism
  Special hardware features, like specialized instructions (e.g., matrix manipulation)
Latency
  How long to set the problem up
  How much faster does it execute once it gets going
  It is all about time to finish

## Slide 22: Coping with Failures
4 disks/server, 50,000 servers
Failure rate of disks: 2% to 10% / year
  Assume 4% annual failure rate
On average, how often does a disk fail?
  1 / month
  1 / week
  1 / day
  1 / hour

## Slide 23: Coping with Failures
4 disks/server, 50,000 servers
Failure rate of disks: 2% to 10% / year
  Assume 4% annual failure rate
On average, how often does a disk fail?
  1 / month
  1 / week
  1 / day
  1 / hour
50,000 x 4 = 200,000 disks
200,000 x 4% = 8000 disks fail
365 days x 24 hours = 8760 hours

## Slide 24: NASA Fixing Rover’s Flash Memory
Opportunity still active on Mars after >10 years
But flash memory worn out
New software update will avoid using worn out memory banks
http://www.engadget.com/2014/12/30/nasa-opportunity-rover-flash-fix/

## Slide 25: Great Idea #6: Dependability via Redundancy
Redundancy so that a failing piece doesn’t make the whole system fail
1+1=2
1+1=2
1+1=1
1+1=2
2 of 3 agree
FAIL!
Increasing transistor density reduces the cost of redundancy

## Slide 26: Great Idea #6: Dependability via Redundancy
Applies to everything from datacenters to storage to memory to instructors
  Redundant datacenters so that can lose 1 datacenter but Internet service stays online
  Redundant disks so that can lose 1 disk but not lose data (Redundant Arrays of Independent Disks/RAID)
  Redundant memory bits of so that can lose 1 bit but no data (Error Correcting Code/ECC Memory)

## Slide 27: Agenda
Thinking about Machine Structures
Great Ideas in Computer Architecture
What you need to know about this class
Everything is a Number

## Slide 28: Yoda says…
“Always in motion, the future is…”
Our schedule may change slightly depending on some factors. This includes lectures, assignments & labs…

## Slide 29: Weekly Schedule
Tuesday lecture starts new weekly cycle

## Slide 30: Course Information
Course Web: http://inst.eecs.Berkeley.edu/~cs61c/
Instructors:
  Krste Asanovic & Vladimir Stojanovic
Teaching Assistants: (see webpage)
Textbooks: Average 15 pages of reading/week (can rent!)
  Patterson & Hennessey, Computer Organization and Design, 5/e (we’ll try to provide 4th Ed pages, not Asian version 4th edition)
  Kernighan & Ritchie, The C Programming Language, 2nd Edition
  Barroso & Holzle, The Datacenter as a Computer, 2nd Edition
Piazza:
  Every announcement, discussion, clarification happens there

## Slide 31: Course Grading
EPA: Effort, Participation and Altruism (5%)
Homework (10%)
Labs (5%)
Projects (20%)
  Non-Parallel Application (MIPS & C)
  Computer Processor Design (Logisim)
  Parallelize for Performance, SIMD, MIMD
  Massive Data Parallelism (Spark on Amazon EC2)
Two midterms (15% each): 6th & 12th week in class, can be clobbered!
Final (30%): 2015/5/15 @ 7-10pm
Performance Competition for honor (and EPA)

## Slide 32: Tried-and-True Technique: Peer Instruction
Increase real-time learning in lecture, test understanding of concepts vs. details
As complete a “segment” ask multiple-choice question
  1-2 minutes to decide yourself
  2 minutes in pairs/triples to reach consensus.
  Teach others!
  2 minute discussion of answers, questions, clarifications
You can get transmitters from the ASUC bookstore
  We’ll start this next week
  No web-based clickers, sorry!

## Slide 33: EECS Grading Policy
http://www.eecs.berkeley.edu/Policies/ugrad.grading.shtml
“A typical GPA for courses in the lower division is 2.7. This GPA would result, for example, from 17% A's, 50% B's, 20% C's, 10% D's, and 3% F's. A class whose GPA falls outside the range 2.5 - 2.9 should be considered atypical.”
Fall 2010: GPA 2.81 26% A's, 47% B's, 17% C's, 3% D's, 6% F's
Job/Intern Interviews: They grill you with technical questions, so it’s what you say, not your GPA
(New 61C gives good stuff to say)
 | Fall | Spring
2010 | 2.81 | 2.81
2009 | 2.71 | 2.81
2008 | 2.95 | 2.74
2007 | 2.67 | 2.76

## Slide 34: Our goal as instructors
To make your experience in CS61C as enjoyable & informative as possible
  Humor, enthusiasm & technology-in-the-news in lecture
  Fun, challenging projects & HW
  Pro-student policies (exam clobbering)
To maintain Cal & EECS standards of excellence
  Projects & exams will be as rigorous as every year.
Score 7.0 on HKN:
  Please give feedback so we can improve! Why are we not 7.0 for you? We will listen!!

## Slide 35: EPA!
Effort
  Attending prof and TA office hours, completing all assignments, turning in HW0, doing reading quizzes
Participation
  Attending lecture and voting using the clickers
  Asking great questions in discussion and lecture and making it more interactive
Altruism
  Helping others in lab or on Piazza
EPA! points have the potential to bump students up to the next grade level! (but actual EPA! scores are internal)

## Slide 36: Late Policy … Slip Days!
Assignments due at 11:59:59 PM
You have 3 slip day tokens (NOT hour or min)
Every day your project or homework is late (even by a minute) we deduct a token
After you’ve used up all tokens, it’s 33% deducted per day.
  No credit if more than 3 days late
  Save your tokens for projects, worth more!!
No need for sob stories, just use a slip day!

## Slide 37: Policy on Assignments and Independent Work
ALL PROJECTS WILL BE DONE WITH A PARTNER
With the exception of laboratories and assignments that explicitly permit you to work in groups, all homework and projects are to be YOUR work and your work ALONE.
PARTNER TEAMS MAY NOT WORK WITH OTHER PARTNER TEAMS
You are encouraged to discuss your assignments with other students, and extra credit will be assigned to students who help others, particularly by answering questions on Piazza, but we expect that what you hand in is yours.
It is NOT acceptable to copy solutions from other students.
It is NOT acceptable to copy (or start your) solutions from the Web.
It is NOT acceptable to use PUBLIC github archives (giving your answers away)
We have tools and methods, developed over many years, for detecting this. You WILL be caught, and the penalties WILL be severe.
At the minimum F in the course, and a letter to your university record documenting the incidence of cheating.
(We’ve caught people in recent semesters!)
Both Giver and Receiver are equally culpable and suffer equal penalties

## Slide 38: Architecture of a typical Lecture
Attention
Time (minutes)
10
35
60
78
90
Clickers Administrivia
“And in conclusion…”
Full
Clickers
Fun/News

## Slide 39: Agenda
Thinking about Machine Structures
Great Ideas in Computer Architecture
What you need to know about this class
Everything is a Number

## Slide 40: Key Concepts
Inside computers, everything is a number
But numbers usually stored with a fixed size
  8-bit bytes, 16-bit half words, 32-bit words, 64-bit double words, …
Integer and floating-point operations can lead to results too big to store within their representations: overflow/underflow

## Slide 41: Number Representation
Value of i-th digit is d × Basei where i starts at 0 and increases from right to left:
12310 = 110 x 10102 + 210 x 10101 + 310 x 10100
= 1x10010 + 2x1010 + 3x110 = 10010 + 2010 + 310
= 12310
Binary (Base 2), Hexadecimal (Base 16), Decimal (Base 10) different ways to represent an integer
  We use 1two, 5ten, 10hex to be clearer (vs. 12, 48, 510, 1016 )

## Slide 42: Number Representation
Hexadecimal digits: 0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F
FFFhex = 15tenx 16ten2 + 15tenx 16ten1 + 15tenx 16ten0 = 3840ten + 240ten + 15ten = 4095ten
1111 1111 1111two = FFFhex = 4095ten
May put blanks every group of binary, octal, or hexadecimal digits to make it easier to parse, like commas in decimal

## Slide 43: Signed and Unsigned Integers
C, C++, and Java have signed integers, e.g., 7, -255:
  int x, y, z;
C, C++ also have unsigned integers, which are used for addresses
32-bit word can represent 232 binary numbers
Unsigned integers in 32 bit word represent 0 to 232-1 (4,294,967,295)

## Slide 44: Unsigned Integers
0000 0000 0000 0000 0000 0000 0000 0000two = 0ten
0000 0000 0000 0000 0000 0000 0000 0001two = 1ten
0000 0000 0000 0000 0000 0000 0000 0010two = 2ten
... ...
0111 1111 1111 1111 1111 1111 1111 1101two = 2,147,483,645ten
0111 1111 1111 1111 1111 1111 1111 1110two = 2,147,483,646ten
0111 1111 1111 1111 1111 1111 1111 1111two = 2,147,483,647ten
1000 0000 0000 0000 0000 0000 0000 0000two = 2,147,483,648ten
1000 0000 0000 0000 0000 0000 0000 0001two = 2,147,483,649ten
1000 0000 0000 0000 0000 0000 0000 0010two = 2,147,483,650ten
... ...
1111 1111 1111 1111 1111 1111 1111 1101two = 4,294,967,293ten
1111 1111 1111 1111 1111 1111 1111 1110two = 4,294,967,294ten
1111 1111 1111 1111 1111 1111 1111 1111two = 4,294,967,295ten

## Slide 45: Signed Integers and Two’s-Complement Representation
Signed integers in C; want ½ numbers <0, want ½ numbers >0, and want one 0
Two’s complement treats 0 as positive, so 32-bit word represents 232 integers from -231 (–2,147,483,648) to 231-1 (2,147,483,647)
  Note: one negative number with no positive version
  Book lists some other options, all of which are worse
  Every computer uses two’s complement today
Most-significant bit (leftmost) is the sign bit, since 0 means positive (including 0), 1 means negative
  Bit 31 is most significant, bit 0 is least significant

## Slide 46: Two’s-Complement Integers
0000 0000 0000 0000 0000 0000 0000 0000two = 0ten
0000 0000 0000 0000 0000 0000 0000 0001two = 1ten
0000 0000 0000 0000 0000 0000 0000 0010two = 2ten
... ...
0111 1111 1111 1111 1111 1111 1111 1101two = 2,147,483,645ten
0111 1111 1111 1111 1111 1111 1111 1110two = 2,147,483,646ten
0111 1111 1111 1111 1111 1111 1111 1111two = 2,147,483,647ten
1000 0000 0000 0000 0000 0000 0000 0000two = –2,147,483,648ten
1000 0000 0000 0000 0000 0000 0000 0001two = –2,147,483,647ten
1000 0000 0000 0000 0000 0000 0000 0010two = –2,147,483,646ten
... ...
1111 1111 1111 1111 1111 1111 1111 1101two = –3ten
1111 1111 1111 1111 1111 1111 1111 1110two = –2ten
1111 1111 1111 1111 1111 1111 1111 1111two = –1ten
Sign Bit

## Slide 47: Ways to Make Two’s Complement
For N-bit word, complement to 2tenN
  For 4 bit number 3ten=0011two, two’s complement (i.e. -3ten) would be 16ten-3ten=13ten or 10000two – 0011two = 1101two
Here is an easier way:
  Invert all bits and add 1
  Computers actually do it like this, too
0011two
1100two
+ 1two
3ten
1101two
Bitwise complement
-3ten

## Slide 48: Two’s-Complement Examples
Assume for simplicity 4 bit width, -8 to +7 represented
0011
0010
3
+2
5
0101
0011
1110
3
+ (-2)
1
1 0001
0111
0001
7
+1
-8
1000
Overflow!
1101
1110
-3
+ (-2)
-5
1 1011
1000
1111
-8
+ (-1)
+7
1 0111
Carry into MSB =
Carry Out MSB
Carry into MSB =
Carry Out MSB
Overflow!

## Slide 49
0 to +31
-16 to +15
-15 to +16
-32 to +31
☐
☐
☐
☐
Suppose we had a 5-bit word. What integers can be represented in two’s complement?
Notes: VertLeftWhiteCheck1
B: Print 4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 50: Summary
CS61C: Learn 6 great ideas in computer architecture to enable high performance programming via parallelism, not just learn C
  Abstraction (Layers of Representation/Interpretation)
  Moore’s Law
  Principle of Locality/Memory Hierarchy
  Parallelism
  Performance Measurement and Improvement
  Dependability via Redundancy
Everything is a Number!