## Slide 1: CS 61C: Great Ideas in Computer Architecture (Machine Structures) Thread-Level Parallelism (TLP) and OpenMP Intro
Instructors:
Krste Asanovic & Vladimir Stojanovic
http://inst.eecs.berkeley.edu/~cs61c/

## Slide 2: Review
Amdahl’s Law: Serial sections limit speedup
Flynn Taxonomy
Intel SSE SIMD Instructions
  Exploit data-level parallelism in loops
  One instruction fetch that operates on multiple operands simultaneously
  128-bit XMM registers
SSE Instructions in C
  Embed the SSE machine instructions directly into C programs through use of intrinsics
  Achieve efficiency beyond that of optimizing compiler

## Slide 3: New-School Machine Structures (It’s a bit more complicated!)
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Project 3

## Slide 4: Simple Multiprocessor
Processor 0
Control
Datapath
PC
Registers
(ALU)
Memory
Input
Output
Bytes
I/O-Memory Interfaces
Processor 0 Memory Accesses
Processor 1
Control
Datapath
PC
Registers
(ALU)
Processor 1 Memory Accesses

## Slide 5: Multiprocessor Execution Model
Each processor has its own PC and executes an independent stream of instructions (MIMD)
Different processors can access the same memory space
  Processors can communicate via shared memory by storing/loading to/from common locations
Two ways to use a multiprocessor:
  Deliver high throughput for independent jobs via job-level parallelism
  Improve the run time of a single program that has been specially crafted to run on a multiprocessor - a parallel-processing program
Use term core for processor (“Multicore”) because “Multiprocessor Microprocessor” too redundant

## Slide 6: Transition to Multicore
Sequential App Performance

## Slide 7: Parallelism Only Path to Higher Performance
Sequential processor performance not expected to increase much, and might go down
If want apps with more capability, have to embrace parallel processing (SIMD and MIMD)
In mobile systems, use multiple cores and GPUs
In warehouse-scale computers, use multiple nodes, and all the MIMD/SIMD capability of each node

## Slide 8: Multiprocessors and You
Only path to performance is parallelism
  Clock rates flat or declining
  SIMD: 2X width every 3-4 years
    128b wide now, 256b 2011, 512b in 2014, 1024b in 2018?
  MIMD: Add 2 cores every 2 years: 2, 4, 6, 8, 10, …
Key challenge is to craft parallel programs that have high performance on multiprocessors as the number of processors increase – i.e., that scale
  Scheduling, load balancing, time for synchronization, overhead for communication
Project 3: fastest code on 8-core computers
  2 chips/computer, 4 cores/chip

## Slide 9: Potential Parallel Performance (assuming SW can use it)
Year | Cores | SIMD bits /Core | Core * SIMD bits | Peak DP FLOPs/Cycle
2003 | 2 | 128 | 256 | 4
2005 | 4 | 128 | 512 | 8
2007 | 6 | 128 | 768 | 12
2009 | 8 | 128 | 1024 | 16
2011 | 10 | 256 | 2560 | 40
2013 | 12 | 256 | 3072 | 48
2015 | 14 | 512 | 7168 | 112
2017 | 16 | 512 | 8192 | 128
2019 | 18 | 1024 | 18432 | 288
2021 | 20 | 1024 | 20480 | 320
2.5X
8X
20X
MIMD
SIMD
MIMD *SIMD
+2/
2yrs
2X/
4yrs

## Slide 10: Threads
Thread: a sequential flow of instructions that performs some task
Each thread has a PC + processor registers and accesses the shared memory
Each processor provides one (or more) hardware threads (or harts) that actively execute instructions
Operating system multiplexes multiple software threads onto the available hardware threads

## Slide 11: Operating System Threads
Give the illusion of many active threads by time-multiplexing software threads onto hardware threads
Remove a software thread from a hardware thread by interrupting its execution and saving its registers and PC into memory
  Also if one thread is blocked waiting for network access or user input
Can make a different software thread active by loading its registers into a hardware thread’s registers and jumping to its saved PC

## Slide 12: Hardware Multithreading
Basic idea: Processor resources are expensive and should not be left idle
Long memory latency to memory on cache miss?
Hardware switches threads to bring in other useful work while waiting for cache miss
Cost of thread context switch must be much less than cache miss latency
Put in redundant hardware so don’t have to save context on every thread switch:
  PC, Registers
Attractive for apps with abundant TLP
  Commercial multi-user workloads

## Slide 13: Hardware Multithreading
Memory
Input
Output
Bytes
I/O-Memory Interfaces
Processor
Control
Datapath
PC 0
Registers 0
(ALU)
PC 1
Registers 1
Two copies of PC and Registers inside processor hardware
Looks like two processors to software (hardware thread 0, hardware thread 1)
Control logic decides which thread to execute an instruction from next

## Slide 14: Multithreading vs. Multicore
Multithreading => Better Utilization
  ≈1% more hardware, 1.10X better performance?
  Share integer adders, floating-point units, all caches (L1 I$, L1 D$, L2$, L3$), Memory Controller
Multicore => Duplicate Processors
  ≈50% more hardware, ≈2X better performance?
  Share outer caches (L2$, L3$), Memory Controller
Modern machines do both
  Multiple cores with multiple threads per core

## Slide 15: Krste’s MacBook Air
/usr/sbin/sysctl -a | grep hw\.
hw.model = MacBookAir5,1
…
hw.physicalcpu: 2
hw.logicalcpu: 4
…
hw.cpufrequency = 2,000,000,000
hw.memsize = 8,589,934,592
hw.cachelinesize = 64
hw.l1icachesize: 32,768
hw.l1dcachesize: 32,768
hw.l2cachesize: 262,144
hw.l3cachesize: 4,194,304

## Slide 16: Machines in (old) 61C Lab
/usr/sbin/sysctl -a | grep hw\.
hw.model = MacPro4,1
…
hw.physicalcpu: 8
hw.logicalcpu: 16
…
hw.cpufrequency = 2,260,000,000
hw.physmem = 2,147,483,648
hw.cachelinesize = 64
hw.l1icachesize: 32,768
hw.l1dcachesize: 32,768
hw.l2cachesize: 262,144
hw.l3cachesize: 8,388,608
Therefore, should try up to 16 threads to see if performance gain even though only 8 cores

## Slide 17: Administrivia

## Slide 18: 100s of (Mostly Dead) Parallel Programming Languages
ActorScript | Concurrent Pascal | JoCaml | Orc
Ada | Concurrent ML | Join | Oz
Afnix | Concurrent Haskell | Java | Pict
Alef | Curry | Joule | Reia
Alice | CUDA | Joyce | SALSA
APL | E | LabVIEW | Scala
Axum | Eiffel | Limbo | SISAL
Chapel | Erlang | Linda | SR
Cilk | Fortan 90 | MultiLisp | Stackless Python
Clean | Go | Modula-3 | SuperPascal
Clojure | Io | Occam | VHDL
Concurrent C | Janus | occam-π | XC

## Slide 19: OpenMP
OpenMP is a language extension used for multi-threaded, shared-memory parallelism
  Compiler Directives (inserted into source code)
  Runtime Library Routines (called from your code)
  Environment Variables (set in your shell)
Portable
Standardized
Easy to compile: cc –fopenmp name.c

## Slide 20: Shared Memory Model with Explicit Thread-based Parallelism
Multiple threads in a shared memory environment, explicit programming model with full programmer control over parallelization
Pros:
  Takes advantage of shared memory, programmer need not worry (that much) about data placement
  Compiler directives are simple and easy to use
  Legacy serial code does not need to be rewritten
Cons:
  Code can only be run in shared memory environments
  Compiler must support OpenMP (e.g. gcc 4.2)

## Slide 21: OpenMP in CS61C
OpenMP is built on top of C, so you don’t have to learn a whole new programming language
  Make sure to add #include <omp.h>
  Compile with flag: gcc -fopenmp
  Mostly just a few lines of code to learn
You will NOT become experts at OpenMP
  Use slides as reference, will learn to use in lab
Key ideas:
  Shared vs. Private variables
  OpenMP directives for parallelization, work sharing, synchronization

## Slide 22: OpenMP Programming Model
Fork - Join Model:
OpenMP programs begin as single process (master thread) and executes sequentially until the first parallel region construct is encountered
  FORK: Master thread then creates a team of parallel threads
  Statements in program that are enclosed by the parallel region construct are executed in parallel among the various threads
  JOIN: When the team threads complete the statements in the parallel region construct, they synchronize and terminate, leaving only the master thread

## Slide 23: OpenMP Extends C with Pragmas
Pragmas are a preprocessor mechanism C provides for language extensions
Commonly implemented pragmas: structure packing, symbol aliasing, floating point exception modes (not covered in 61C)
Good mechanism for OpenMP because compilers that don't recognize a pragma are supposed to ignore them
  Runs on sequential computer even with embedded pragmas

## Slide 24: parallel Pragma and Scope
Basic OpenMP construct for parallelization:
#pragma omp parallel
{
/* code goes here */
}
  Each thread runs a copy of code within the block
  Thread scheduling is non-deterministic
OpenMP default is shared variables
  To make private, need to declare with pragma:
#pragma omp parallel private (x)
This is annoying, but curly brace MUST go on separate line from #pragma

## Slide 25: Thread Creation
How many threads will OpenMP create?
Defined by OMP_NUM_THREADS environment variable (or code procedure call)
  Set this variable to the maximum number of threads you want OpenMP to use
  Usually equals the number of cores in the underlying hardware on which the program is run

## Slide 26: What Kind of Threads?
OpenMP threads are operating system (software) threads.
OS will multiplex requested OpenMP threads onto available hardware threads.
Hopefully each gets a real hardware thread to run on, so no OS-level time-multiplexing.
But other tasks on machine can also use hardware threads!
Be careful when timing results for project 3!

## Slide 27: OMP_NUM_THREADS
OpenMP intrinsic to set number of threads:
omp_set_num_threads(x);
OpenMP intrinsic to get number of threads:
num_th = omp_get_num_threads();
OpenMP intrinsic to get Thread ID number:
th_ID = omp_get_thread_num();

## Slide 28: Parallel Hello World
#include <stdio.h>
#include <omp.h>
int main () {
int nthreads, tid;
/* Fork team of threads with private var tid */
#pragma omp parallel private(tid)
{
tid = omp_get_thread_num(); /* get thread id */
printf("Hello World from thread = %d\n", tid);
/* Only master thread does this */
if (tid == 0) {
nthreads = omp_get_num_threads();
printf("Number of threads = %d\n", nthreads);
}
} /* All threads join master and terminate */
}

## Slide 29: Data Races and Synchronization
Two memory accesses form a data race if from different threads to same location, and at least one is a write, and they occur one after another
If there is a data race, result of program can vary depending on chance (which thread first?)
Avoid data races by synchronizing writing and reading to get deterministic behavior
Synchronization done by user-level routines that rely on hardware synchronization instructions
(more later)

## Slide 30: Analogy: Buying Milk
Your fridge has no milk. You and your roommate will return from classes at some point and check the fridge
Whoever gets home first will check the fridge, go and buy milk, and return
What if the other person gets back while the first person is buying milk?
  You’ve just bought twice as much milk as you need!
It would’ve helped to have left a note…

## Slide 31: Lock Synchronization (1/2)
Use a “Lock” to grant access to a region (critical section) so that only one thread can operate at a time
  Need all processors to be able to access the lock, so use a location in shared memory as the lock
Processors read lock and either wait (if locked) or set lock and go into critical section
  0 means lock is free / open / unlocked / lock off
  1 means lock is set / closed / locked / lock on

## Slide 32: Lock Synchronization (2/2)
Pseudocode:
Check lock
Set the lock
Critical section
(e.g. change shared variables)
Unset the lock
Can loop/idle here if locked

## Slide 33: Possible Lock Implementation
Lock (a.k.a. busy wait)
  Get_lock: # $s0 -> addr of lock
  addiu $t1,$zero,1 # t1 = Locked value
  Loop: lw $t0,0($s0) # load lock
  bne $t0,$zero,Loop # loop if locked
  Lock: sw $t1,0($s0) # Unlocked, so lock
Unlock
  Unlock:
sw $zero,0($s0)
Any problems with this?

## Slide 34: Possible Lock Problem
Thread 1
addiu $t1,$zero,1
Loop: lw $t0,0($s0)
bne $t0,$zero,Loop
Lock: sw $t1,0($s0)
Thread 2
addiu $t1,$zero,1
Loop: lw $t0,0($s0)
bne $t0,$zero,Loop
Lock: sw $t1,0($s0)
Time
Both threads think they have set the lock!
Exclusive access not guaranteed!

## Slide 35: Hardware Synchronization
Hardware support required to prevent an interloper (another thread) from changing the value
  Atomic read/write memory operation
  No other access to the location allowed between the read and write
How best to implement in software?
  Single instr? Atomic swap of register ↔ memory
  Pair of instr? One for read, one for write
Notes: Interloper thread can be from same core or another core.

## Slide 36: Synchronization in MIPS
Load linked: ll rt,off(rs)
Store conditional: sc rt,off(rs)
  Returns 1 (success) if location has not changed since the ll
  Returns 0 (failure) if location has changed
Note that sc clobbers the register value being stored (rt)!
  Need to have a copy elsewhere if you plan on repeating on failure or using value later
Notes: Here using the Green Sheet convention of rs and rt for source register and target register.

## Slide 37: Synchronization in MIPS Example
Atomic swap (to test/set lock variable)
Exchange contents of register and memory: $s4 ↔ Mem($s1)
  try: add $t0,$zero,$s4 #copy value
  ll $t1,0($s1) #load linked
  sc $t0,0($s1) #store conditional
  beq $t0,$zero,try #loop if sc fails
  add $s4,$zero,$t1 #load value in $s4
sc would fail if another threads executes sc here

## Slide 38: Test-and-Set
In a single atomic operation:
  Test to see if a memory location is set (contains a 1)
  Set it (to 1) if it isn’t (it contained a zero when tested)
  Otherwise indicate that the Set failed, so the program can try again
  While accessing, no other instruction can modify the memory location, including other Test-and-Set instructions
Useful for implementing lock operations

## Slide 39: Test-and-Set in MIPS
Example: MIPS sequence for implementing a T&S at ($s1)
  Try: addiu $t0,$zero,1
  ll $t1,0($s1)
  bne $t1,$zero,Try
  sc $t0,0($s1)
  beq $t0,$zero,try
  Locked:
  # critical section
  Unlock:
  sw $zero,0($s1)
  Idea is that not for programmers to use this directly, but as a tool for enabling implementation of parallel libraries

## Slide 40
Clickers: Consider the following code when executed concurrently by two threads.
What possible values can result in *($s0)?
# *($s0) = 100
lw $t0,0($s0)
addi $t0,$t0,1
sw $t0,0($s0)
A: 101 or 102
B: 100, 101, or 102
C: 100 or 101
D: 102
Notes: - 102 if one thread starts executing after the other completely finishes.
- 101 if both threads execute the lw before either thread executes the sw. One thread will see “stale data”.

## Slide 41: OpenMP Directives (Work-Sharing)
Shares iterations of a loop across the threads
Each section is executed by a separate thread
Serializes the execution of a thread
These are defined within a parallel section
Notes: A work-sharing construct divides the execution of the enclosed code region among the members of the team that encounter it.

## Slide 42: Parallel Statement Shorthand
#pragma omp parallel
{
#pragma omp for
for(i=0;i<len;i++) { … }
}
can be shortened to:
#pragma omp parallel for
for(i=0;i<len;i++) { … }
Also works for sections
This is the only directive in the parallel section

## Slide 43: Building Block: for loop
for (i=0; i<max; i++) zero[i] = 0;
Break for loop into chunks, and allocate each to a separate thread
  e.g. if max = 100 with 2 threads: assign 0-49 to thread 0, and 50-99 to thread 1
Must have relatively simple “shape” for an OpenMP-aware compiler to be able to parallelize it
  Necessary for the run-time system to be able to determine how many of the loop iterations to assign to each thread
No premature exits from the loop allowed
  i.e. No break, return, exit, goto statements
In general, don’t jump outside of any pragma block
Notes: “Shape” restrictions: The FOR loop can not be a DO WHILE loop, or a loop without loop control. Also, the loop iteration variable must be an integer and the loop control parameters must be the same for all threads.

## Slide 44: Parallel for pragma
#pragma omp parallel for
for (i=0; i<max; i++) zero[i] = 0;
Master thread creates additional threads, each with a separate execution context
All variables declared outside for loop are shared by default, except for loop index which is private per thread (Why?)
Implicit synchronization at end of for loop
Divide index regions sequentially per thread
  Thread 0 gets 0, 1, …, (max/n)-1;
  Thread 1 gets max/n, max/n+1, …, 2*(max/n)-1
  Why?

## Slide 45: OpenMP Timing
Elapsed wall clock time:
double omp_get_wtime(void);
  Returns elapsed wall clock time in seconds
  Time is measured per thread, no guarantee can be made that two distinct threads measure the same time
  Time is measured from “some time in the past,” so subtract results of two calls to omp_get_wtime to get elapsed time

## Slide 46: Matrix Multiply in OpenMP
start_time = omp_get_wtime();
#pragma omp parallel for private(tmp, i, j, k)
for (i=0; i<Mdim; i++){
for (j=0; j<Ndim; j++){
tmp = 0.0;
for( k=0; k<Pdim; k++){
/* C(i,j) = sum(over k) A(i,k) * B(k,j)*/
tmp += *(A+(i*Pdim+k)) * *(B+(k*Ndim+j));
}
*(C+(i*Ndim+j)) = tmp;
}
}
run_time = omp_get_wtime() - start_time;
Outer loop spread across N threads; inner loops inside a single thread

## Slide 47: Notes on Matrix Multiply Example
More performance optimizations available:
  Higher compiler optimization (-O2, -O3) to reduce number of instructions executed
  Cache blocking to improve memory performance
  Using SIMD SSE instructions to raise floating point computation rate (DLP)

## Slide 48: And in Conclusion, …
Sequential software is slow software
  SIMD and MIMD only path to higher performance
Multithreading increases utilization, Multicore more processors (MIMD)
OpenMP as simple parallel extension to C
  Threads, Parallel for, private, critical sections, …
  ≈ C: small so easy to learn, but not very high level and it’s easy to get into trouble