## Slide 1: CS 61C: Great Ideas in Computer Architecture Virtual Memory
Instructors:
Krste Asanovic & Vladimir Stojanovic
http://inst.eecs.berkeley.edu/~cs61c/

## Slide 2: Review
Programmed I/O
Polling versus Interrupts
Asynchronous interrupts versus synchronous traps
Precise interrupt looks like execution stopped at exactly one instruction, every instruction before finished, no instruction after started.
  Simplify software view of interrupted state

## Slide 3: You Are Here!
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Main Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s
Lecture

## Slide 4: Traps/Interrupts/Execeptions: altering the normal flow of control
Ii-1
HI1
HI2
HIn
Ii
Ii+1
program
trap
handler
An external or internal event that needs to be processed by another (system) program. The event is usually unexpected or rare from program’s point of view.

## Slide 5: Terminology
In CS61C (you’ll see other definitions in use elsewhere):
Interrupt – caused by an event external to current running program (e.g. key press, mouse activity)
  Asynchronous to current program, can handle interrupt on any convenient instruction
Exception – caused by some event during execution of one instruction of current running program (e.g., page fault, illegal instruction)
  Synchronous, must handle exception on instruction that causes exception
Trap – action of servicing interrupt or exception by hardware jump to “trap handler” code

## Slide 6: Precise Traps
Trap handler’s view of machine state is that every instruction prior to the trapped one has completed, and no instruction after the trap has executed.
Implies that handler can return from an interrupt by restoring user registers and jumping to EPC
  Interrupt handler software doesn’t need to understand the pipeline of the machine, or what program was doing!
  More complex to handle trap caused by an exception
Providing precise traps is tricky in a pipelined superscalar out-of-order processor!
  But handling imprecise interrupts in software is even worse.

## Slide 7: Trap Handling in 5-Stage Pipeline
How to handle multiple simultaneous exceptions in different pipeline stages?
How and where to handle external asynchronous interrupts?
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
Asynchronous Interrupts

## Slide 8: Save Exceptions Until Commit
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
Asynchronous
Interrupts
Exc
D
PC
D
Exc
E
PC
E
Exc
M
PC
M
Cause
EPC
Kill D Stage
Kill F Stage
Kill E Stage
Select Handler PC
Kill Writeback
Commit Point

## Slide 9: Handling Traps in In-Order Pipeline
Hold exception flags in pipeline until commit point (M stage)
Exceptions in earlier pipe stages override later exceptions for a given instruction
Inject external interrupts at commit point (override others)
If exception/interrupt at commit: update Cause and EPC registers, kill all stages, inject handler PC into fetch stage

## Slide 10: Trap Pipeline Diagram
      time
      t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) 096: ADD IF1 ID1 EX1 MA1 - overflow!
(I2) 100: XOR IF2 ID2 EX2 - -
(I3) 104: SUB IF3 ID3 - - -
(I4) 108: ADD IF4 - - - -
(I5) Trap Handler code IF5 ID5 EX5 MA5 WB5

## Slide 11: Virtual Memory

## Slide 12: “Bare” 5-Stage Pipeline
In a bare machine, the only kind of address is a physical address
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Physical Address

## Slide 13: Dynamic Address Translation
Motivation
  In early machines, I/O operations were slow and each word transferred involved the CPU
  Higher throughput if CPU and I/O of 2 or more programs were overlapped.
  How?multiprogramming with DMA I/O devices, interrupts
Location-independent programs
  Programming and storage management ease
 need for a base register
Protection
  Independent programs should not affect
  each other inadvertently
 need for a bound register
Multiprogramming drives requirement for resident supervisor (operating system) software to manage context switches between multiple programs
prog1
prog2
Physical Memory
OS

## Slide 14: Simple Base and Bound Translation
Load X
Program
Address
Space
Bound
Register

Bounds
Violation?
Physical Memory
current
segment
Base
Register
+
Physical
Address
Logical
Address
Base and bounds registers are visible/accessible only when processor is running in supervisor mode
Base Physical Address
Segment Length

## Slide 15: Separate Areas for Program and Data
Physical Address
Physical Address
Load X
Program
Address
Space
Main Memory
data
segment
Data Bound Register
Mem. Address Register
Data Base Register

+
Bounds
Violation?
Program Bound Register
Program Counter
Program Base Register

+
Bounds
Violation?
program
segment
Logical Address
Logical Address
What is an advantage of this separation?
(Scheme used on all Cray vector supercomputers prior to X1, 2002)
Notes: Permits sharing of program segments.

## Slide 16: Base and Bound Machine
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Data Bound Register
Data Base Register

+
[ Can fold addition of base register into (register+immediate) address calculation using a carry-save adder (sums three numbers with only a few gate delays more than adding two numbers) ]
Logical Address
Bounds Violation?
Physical Address
Prog. Bound Register
Program Base Register

+
Logical Address
Bounds Violation?

## Slide 17: Memory Fragmentation
As users come and go, the storage is “fragmented”.
Therefore, at some stage programs have to be moved
around to compact the storage.
OS
Space
16K
24K
24K
32K
24K
user 1
user 2
user 3
OS
Space
16K
24K
16K
32K
24K
user 1
user 2
user 3
user 5
user 4
8K
Users 4 & 5
arrive
Users 2 & 5
leave
OS
Space
16K
24K
16K
32K
24K
user 1
user 4
8K
user 3
free
Notes: Called Burping the memory.

## Slide 18: Paged Memory Systems
Processor-generated address can be split into:
Page tables make it possible to store the pages of a program non-contiguously.
0
1
2
3
0
1
2
3
Address Space
of User-1
Page Table
of User-1
1
0
2
3
page number offset
A page table contains the physical address of the base of each page:
Physical Memory
Notes: Relaxes the contiguous allocation requirement.

## Slide 19: Private Address Space per User
Each user has a page table
Page table contains an entry for each user page
VA1
User 1
Page Table
VA1
User 2
Page Table
VA1
User 3
Page Table
Physical Memory
free
OS
pages
Notes: OS ensures that the page tables are disjoint.

## Slide 20: Where Should Page Tables Reside?
Space required by the page tables (PT) is proportional to the address space, number of users, ...
    Too large to keep in registers inside CPU
Idea: Keep PTs in the main memory
  needs one reference to retrieve the page base address and another to access the data word
   doubles the number of memory references!

## Slide 21: Page Tables in Physical Memory
VA1
User 1 Virtual Address Space
User 2 Virtual Address Space
PT User 1
PT User 2
VA1
Physical Memory

## Slide 22: Administrivia
Midterm 2 scores up:
  Regrade request deadline is 23:59:59 on Sunday April 26th
Clobber Policy:
  Final composed of MT1, MT2, post-MT2 sections
  z-scores on MT1/MT2 sections of Final compared to MT1/MT2 grades, will replace if better
Proj4-1 due date extended to Wed, April 29

## Slide 23: Midterm 2 Distribution

## Slide 24: CS61C In the News: “Moore’s Law 50 Years Anniversary!”
Gordon Moore’s paper appeared in 19 April 1965 issue of Electronics.
“With unit cost falling as the number of components per circuit rises, by 1975 economics may dictate squeezing as many as 65,000 components on a single silicon chip.”

## Slide 25: Demand Paging in Atlas (1962)
Secondary
(Drum)
32x6 pages
Primary
32 Pages
512 words/page
Central
Memory
User sees 32 x 6 x 512 words
of storage
“A page from secondary
storage is brought into the primary storage whenever it is (implicitly) demanded by the processor.”
Tom Kilburn
Primary memory as a cache
for secondary memory
Notes: Single-level Store

## Slide 26: Hardware Organization of Atlas
Initial
Address
Decode
16 ROM pages
0.4 ~1 sec
2 subsidiary pages
1.4 sec
Main
32 pages
1.4 sec
Drum (4)
192 pages
8 Tape decks
88 sec/word
48-bit words
512-word pages
1 Page Address Register (PAR) per page frame
Compare the effective page address against all 32 PARs
match  normal access
no match  page fault
save the state of the partially executed
instruction
Effective
Address
system code
(not swapped)
system data
(not swapped)
0
31
PARs
<effective PN , status>

## Slide 27: Atlas Demand Paging Scheme
On a page fault:
  Input transfer into a free page is initiated
  The Page Address Register (PAR) is updated
  If no free page is left, a page is selected to be replaced (based on usage)
  The replaced page is written on the drum
    to minimize drum latency effect, the first empty page on the drum was selected
  The page table is updated to point to the new location of the page on the drum

## Slide 28: Linear Page Table
VPN
Offset
Virtual address
PT Base Register
VPN
Data word
Data Pages
Offset
PPN
PPN
DPN
PPN
PPN
PPN
Page Table
DPN
PPN
DPN
DPN
DPN
PPN
Page Table Entry (PTE) contains:
  A bit to indicate if a page exists
  PPN (physical page number) for a memory-resident page
  DPN (disk page number) for a page on the disk
  Status bits for protection and usage
OS sets the Page Table Base Register whenever active user process changes

## Slide 29: Size of Linear Page Table
With 32-bit addresses, 4-KB pages & 4-byte PTEs:
  220 PTEs, i.e, 4 MB page table per user
  4 GB of swap needed to back up full virtual address space
Larger pages?
  Internal fragmentation (Not all memory in page is used)
  Larger page fault penalty (more time to read from disk)
What about 64-bit virtual address space???
  Even 1MB pages would require 244 8-byte PTEs (35 TB!)
What is the “saving grace” ?
Notes: Virtual address space is large but only a small fraction of the
pages are populated. So we can use a sparse representation
of the table.

## Slide 30: Hierarchical Page Table
Level 1
Page Table
Level 2
Page Tables
Data Pages
page in primary memory
page in secondary memory
Root of the Current
Page Table
p1
offset
p2
Virtual Address
(Processor
Register)
PTE of a nonexistent page
p1 p2 offset
0
11
12
21
22
31
10-bit
L1 index
10-bit
L2 index
Physical Memory

## Slide 31: Two-Level Page Tables in Physical Memory
VA1
User 1
User1/VA1
User2/VA1
Level 1 PT User 1
Level 1 PT User 2
VA1
User 2
Level 2 PT User 2
Virtual Address Spaces
Physical Memory

## Slide 32: Address Translation & Protection
Every instruction and data access needs address
translation and protection checks
A good VM design needs to be fast (~ one cycle) and space efficient
Physical Address
Virtual Address
Address
Translation
Virtual Page No. (VPN)
offset
Physical Page No. (PPN)
offset
Protection
Check
Exception?
Kernel/User Mode
Read/Write

## Slide 33: Translation Lookaside Buffers (TLB)
Address translation is very expensive!
  In a two-level page table, each reference becomes several memory accesses
Solution: Cache translations in TLB
TLB hit  Single-Cycle Translation
TLB miss  Page-Table Walk to refill
VPN offset
V R W D tag PPN
physical address
PPN offset
virtual address
hit?
(VPN = virtual page number)
(PPN = physical page number)
Notes: 3 memory references
2 page faults (disk accesses) + ..
Actually used in IBM before paged memory.

## Slide 34: TLB Designs
Typically 32-128 entries, usually fully associative
  Each entry maps a large page, hence less spatial locality across pages  more likely that two entries conflict
  Sometimes larger TLBs (256-512 entries) are 4-8 way set-associative
  Larger systems sometimes have multi-level (L1 and L2) TLBs
Random or FIFO replacement policy
No process information in TLB?
TLB Reach: Size of largest virtual address space that can be simultaneously mapped by TLB
  Example: 64 TLB entries, 4KB pages, one page per entry
  TLB Reach = _____________________________________________?

## Slide 35: VM-related events in pipeline
Handling a TLB miss needs a hardware or software mechanism to refill TLB
  usually done in hardware now
Handling a page fault (e.g., page is on disk) needs a precise trap so software handler can easily resume after retrieving page
Handling protection violation may abort process
PC
Inst TLB
Inst. Cache
D
Decode
E
M
Data TLB
Data Cache
W
+
TLB miss? Page Fault?
Protection violation?
TLB miss? Page Fault?
Protection violation?

## Slide 36: Hierarchical Page Table Walk: SPARC v8
31 11 0
Virtual Address
Index 1 Index 2 Index 3 Offset
31 23 17 11 0
Context
Table
Register
Context
Register
root ptr
PTP
PTP
PTE
Context Table
L1 Table
L2 Table
L3 Table
Physical Address
PPN Offset
MMU does this table walk in hardware on a TLB miss

## Slide 37: Page-Based Virtual-Memory Machine (Hardware Page-Table Walk)
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Page Fault?
Protection violation?
Page Fault?
Protection violation?
Assumes page tables held in untranslated physical memory
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Physical Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?

## Slide 38: Address Translation: putting it all together
Virtual Address
TLB
Lookup
Page Table
Walk
Update TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
(to cache)
miss
hit
the page is
Ï memory Î memory
denied
permitted
Protection
Fault
hardware
hardware or software
software
SEGFAULT
Where?
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 39: Modern Virtual Memory Systems Illusion of a large, private, uniform store
Protection & Privacy
  several users, each with their private address space and one or more shared address spaces
page table  name space
Demand Paging
  Provides the ability to run programs larger than the primary memory
  Hides differences in machine configurations
The price is address translation on
each memory reference
OS
useri
Primary
Memory
Swapping
Store
VA
PA
mapping
TLB
Notes: Portability on machines with different memory configurations.

## Slide 40: VM features track historical uses:
Bare machine, only physical addresses
  One program owned entire machine
Batch-style multiprogramming
  Several programs sharing CPU while waiting for I/O
  Base & bound: translation and protection between programs (not virtual memory)
  Problem with external fragmentation (holes in memory), needed occasional memory defragmentation as new jobs arrived
Time sharing
  More interactive programs, waiting for user. Also, more jobs/second.
  Motivated move to fixed-size page translation and protection, no external fragmentation (but now internal fragmentation, wasted bytes in page)
  Motivated adoption of virtual memory to allow more jobs to share limited physical memory resources while holding working set in memory
Virtual Machine Monitors
  Run multiple operating systems on one machine
  Idea from 1970s IBM mainframes, now common on laptops
    e.g., run Windows on top of Mac OS X
  Hardware support for two levels of translation/protection
    Guest OS virtual -> Guest OS physical -> Host machine physical
  Also basis of Cloud Computing
    Virtual machine instances for Project 4