## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
Floating Point,
Performance

## Slide 2: Code on Piazza
Most questions on Piazza can be asked without posting code
Show only relevant lines of code
  Posting an entire function is BAD
Lecture examples, provided code, & output/error messages OK
Why do we care?
  Giving away answers prevents learning
  If copied, you are culpable as the enabler
  We are keeping track; could affect your P&A grade

## Slide 3: Review of Last Lecture
Compiler converts a single HLL file into a single assembly file .c  .s
Assembler removes pseudo-instructions, converts what it can to machine language, and creates a checklist for linker (relocation table) .s  .o
  Resolves addresses by making 2 passes (for internal forward references)
Linker combines several object files and resolves absolute addresses .o  .out
  Enable separate compilation and use of libraries
Loader loads executable into memory and begins execution

## Slide 4
Discuss with Neighbors: (previous midterm question)
In one word each, name the most common producer and consumer of the following items.
Choose from: Linker, Loader, Compiler, Assembler, Programmer
(item) | This is the output of: | This is the input to:
bne $t0,$s0,done | Compiler | Assembler
char *s = “hello world”; |  | 
app.o string.o |  | 
firefox |  | 

## Slide 5
Discuss with Neighbors: (previous midterm question)
In one word each, name the most common producer and consumer of the following items.
Choose from: Linker, Loader, Compiler, Assembler, Programmer
(item) | This is the output of: | This is the input to:
bne $t0,$s0,done | Compiler | Assembler
char *s = “hello world”; | Programmer | Compiler
app.o string.o | Assembler | Linker
firefox | Linker | Loader

## Slide 6: Great Idea #1: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
Higher-Level Language Program (e.g. C)
Assembly Language Program (e.g. MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g. block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
We__
are__
here._

## Slide 7: Agenda
Floating Point
Administrivia
Floating Point Special Cases
Performance
Bonus: FP Conversion Practice
Bonus: FP Casting Concerns

## Slide 8: Number Rep Revisited
Given one word (32 bits), what can we represent so far?
  Signed and Unsigned Integers
  Characters (ASCII)
  Instructions
How do we encode the following:
  Real numbers (e.g. 3.14159)
  Very large numbers (e.g. 6.02×1023)
  Very small numbers (e.g. 6.626×10-34)
Floating
Point
Notes: Avagadro’s Number and Planck’s Constant

## Slide 9: Goals of Floating Point
Support a wide range of values
  Both the very small and the very large
Keep as much precision as possible
Help programmer with errors in real arithmetic
  Support +∞, -∞, Not-A-Number (NaN), exponent overflow and underflow
Keep encoding that is somewhat compatible with two’s complement
  e.g. 0 in FP is same as 0 in two’s complement
  Make it possible to sort without needing to do a special floating point comparison

## Slide 10: Representation of Fractions
“Binary Point” like decimal point signifies boundary between integer and fractional parts:
Example 6-bit representation:
Example: 10.1010two = 1×21 + 1×2-1 + 1×2-3 = 2.625ten
Binary point numbers that match the 6-bit format above range from 0 (00.0000two) to 3.9375 (11.1111two)
xx.yyyy
21
20
2-1
2-2
2-3
2-4

## Slide 11: Scientific Notation (Decimal)
Normalized form: no leadings 0s (exactly one digit to left of decimal point)
Alternatives to representing 1/1,000,000,000
  Normalized: 1.0×10-9
  Not normalized: 0.1×10-8,10.0×10-10
6.02ten × 1023
radix (base)
decimal point
mantissa
exponent

## Slide 12: Scientific Notation (Binary)
Computer arithmetic that supports this called floating point due to the “floating” of the binary point
  Declare such variable in C as float
1.01two × 2-1
radix (base)
binary point
exponent
mantissa

## Slide 13: Translating To and From Scientific Notation
Consider the number 1.011two×24
To convert to ordinary number, shift the decimal to the right by 4
  Result: 10110two = 22ten
For negative exponents, shift decimal to the left
  1.011two×2-2 => 0.01011two = 0.34375ten
Go from ordinary number to scientific notation by shifting until in normalized form
  1101.001two => 1.101001two×23

## Slide 14: Floating Point Encoding
Use normalized, Base 2 scientific notation: +1.xxx…xtwo×2yyy…ytwo
Split a 32-bit word into 3 fields:
  S represents Sign (1 is negative, 0 positive)
  Exponent represents y’s
  Significand represents x’s
S
Exponent
Significand
31 30
23 22
0
1 bit
8 bits
23 bits

## Slide 15: Exponent Comparison
Which is smaller? (i.e. closer to -∞)
  0 or 1 x 10-127 ?
  1 x 10-126 or 1 x 10-127 ?
  -1 x 10-127 or 0 ?
  -1 x 10-126 or -1 x 10-127 ?
Which is smaller? (i.e. closer to -∞)
  0 or 1 x 10-127 ?
  1 x 10-126 or 1 x 10-127 ?
  -1 x 10-127 or 0 ?
  -1 x 10-126 or -1 x 10-127 ?

## Slide 16: The Exponent Field
Want to reuse integer comparison hardware, so examine top 9 bits (sign + exponent):
A: 0b 0 0000 0000 = 0
AB
B: 0b 0 1111 1111 = 255
C: 0b 1 0000 0000 = -256
CD
D: 0b 1 1111 1111 = -1
Need a signed exponent to represent both large and small numbers
  Can’t just use unsigned
Increasing
Numeral
For exponent we want: 0x00 to be the smallest 0xFF to be the largest

## Slide 17: The Exponent Field
Use biased notation
  Read exponent as unsigned, but with bias of -127
  Defines -127 through 128 as 00000000two through 11111111two
  Exponent 0 is represented as 01111111two = 127ten
To encode in biased notation, subtract the bias (add 127) then encode in unsigned:
  1 => 128 => 10000000two
  127 => 254 => 11111110two

## Slide 18: Bias Notation (-127)
∞, NaN
Zero
Closer to zero
How it is encoded
How it is interpreted

## Slide 19: Floating Point Encoding
Note the implicit 1 in front of the Significand
  Ex: 0011 1111 1100 0000 0000 0000 0000 0000two is read as 1.1two = 1.5ten, NOT 0.1two = 0.5ten
  Gives us an extra bit of precision
(-1)S x (1 . Significand) x 2(Exponent-127)
S
Exponent
Significand
31 30
23 22
0
1 bit
8 bits
23 bits

## Slide 20: Agenda
Floating Point
Administrivia
Floating Point Special Cases
Performance
Bonus: FP Conversion Practice
Bonus: FP Casting Concerns

## Slide 21: Administrivia
I will be sitting in on discussions today
  For TA critiques, so don’t mind me
Project 1 due Sunday 7/8
Midterm next Friday 7/13
  9am-12pm in 245 Li Ka Shing
  One-sided, handwritten cheat sheet
  We will supply you with a Green Sheet
Catch-up Lecture tomorrow

## Slide 22: Agenda
Floating Point
Administrivia
Floating Point Special Cases
Performance
Bonus: FP Conversion Practice
Bonus: FP Casting Concerns

## Slide 23: Representing Very Small Numbers
But wait… what happened to zero?
  Using standard encoding 0x00000000 is 1.0×2-127≠0
  Special case: Exp and Sig all zeros = 0
  Two zeros! But at least 0x00000000 = 0 like integers
Numbers closest to 0:
  a = 1.0…0two×2-126 = 2-126
  b = 1.0…01two×2-126 = 2-126 + 2-149
  Normalization and implicit 1 are to blame
  Special case: Exp = 0, Sig ≠ 0 are denorm numbers
b
a
0
+∞
-∞
Gaps!

## Slide 24: Denorm Numbers
Short for “denormalized numbers”
  No leading 1
  Careful! Implicit exponent is -126 even though Exp = 0x00 (not -127)
Now what do the gaps look like?
  Smallest norm: ± 1.0…0two×2-126 = ± 2-126
  Largest denorm: ± 0.1…1two×2-126 = ± (2-126 – 2-149)
  Smallest denorm: ± 0.0…01two×2-126 = ± 2-149
No gap
So much closer to 0

## Slide 25: Other Special Cases
Exp = 0xFF, Sig = 0: ± ∞
  e.g. division by 0
  Still work in comparisons
Exp = 0xFF, Sig ≠ 0: Not a Number (NaN)
  e.g. square root of negative number, 0/0, ∞–∞
  NaN proprogates through computations
  Value of Sig can be useful in debugging
Largest value (besides ∞)?
  Exp = 0xFF has now been taken! Exp = 0xFE has largest: 1.1…1two×2127 = 2128 – 2104

## Slide 26: Floating Point Numbers Summary
Exponent | Significand | Meaning
0 | 0 | ± 0
0 | non-zero | Denorm Num
1-254 | anything | ± FP Num
255 | 0 | ± ∞
255 | non-zero | NaN

## Slide 27: Floating Point Limitations (1/2)
What if result x is too large? (abs(x)> 2128)
  Overflow: Exponent is larger than can be represented
What if result x too small? (0 < abs(x)< 2-149)
  Underflow: Negative exponent is larger than can be represented
What if result runs off the end of the significand?
  Rounding occurs and can lead to unexpected results
  FP has different rounding modes (covered in discussion)
0
2-149
2128
1
-1
-2-149
-2128
underflow
overflow
overflow

## Slide 28: Floating Point Limitations (2/2)
FP addition is NOT associative!
  You can find Big and Small numbers such that: Small + Big + Small ≠ Small + Small + Big
  This is due to rounding errors: FP approximates results because it only has 23 bits for Significand
  You will examine this in lab
Despite being seemingly “more accurate,” FP cannot represent all integers
  e.g. 224 + 223 + 1 = 25165825 (try it!)
  Be careful when casting between int and float
Notes: Information can get lost when casting between int and float (in both directions!)
Some optimizations change the ordering of FP operations, which can lead to errors.

## Slide 29: Double Precision FP Encoding
Next multiple of word size (64 bits)
Double Precision (vs. Single Precision)
  C variable declared as double
  Exponent bias is 210-1 = 1023
  Smallest denorm: 2-1074 , Largest (not ∞): 21024 – 2971
  Primary advantage is greater precision due to larger significand
S
Exponent (11)
Significand (20 of 52)
63 62
52 51
32
Significand (32 of 52)
31
0

## Slide 30: MIPS Floating Point Instructions
MIPS instructions: .s for single, .d for double
  FP addition: add.s (single) and add.d (double)
  Similar instruction naming scheme for subtraction, multiplication, and division
  Comparison and branching a little different; see Green Sheet
MIPS has 32 separate registers for floating point operations ($f#)
  Use adjacent pairs (e.g. $f1 and $f2) for double
  lwc1 (load word), swc1 (store word)
Notes: The “c1” in the instructions refers to Co-processor 1, which is the separate floating point unit (FPU).
For doubles, must used TWO lwc1/swc1 each time, or ldc1/sdc1.

## Slide 31
Question:
Let FP(1,2) = # of floats between 1 and 2
Let FP(2,3) = # of floats between 2 and 3
Which of the following statements is true?
FP(1,2) > FP(2,3)
☐
FP(1,2) = FP(2,3)
☐
FP(1,2) < FP(2,3)
☐
It depends
☐

## Slide 32
Question: Suppose we have the following floats in C:
Big = 1017, Tiny = 10-15, BigNeg = -Big
What will the following conditionals evaluate to?
(Big * Tiny) * BigNeg == (Big * BigNeg) * Tiny
(Big + Tiny) + BigNeg == (Big + BigNeg) + Tiny
F F
☐
F T
☐
T F
☐
T T
☐
1 2
In general:
(1) is TRUE as long as Big * BigNeg doesn’t overflow.
(2) evaluates to 0 != Tiny, which is FALSE as long as Tiny is at least 224 times smaller than Big.

## Slide 33: Get to Know Your Staff
Category: Music

## Slide 34: Agenda
Floating Point
Administrivia
Floating Point Special Cases
Performance
Bonus: FP Conversion Practice
Bonus: FP Casting Concerns

## Slide 35: Six Great Ideas in Computer Architecture
Layers of Representation/Interpretation
Moore’s Law
Principle of Locality/Memory Hierarchy
Parallelism
Performance Measurement & Improvement
Dependability via Redundancy

## Slide 36: Defining CPU Performance
What does it mean to say X is faster than Y?
Ferrari vs. School Bus:
2009 Ferrari 599 GTB
  2 passengers, 11.1 secs in quarter mile
2009 Type D school bus
  54 passengers, quarter mile time?
http://www.youtube.com/watch?v=KwyCoQuhUNA
Response Time
Throughput

## Slide 37: Measurements of Performance
Latency (or response time or execution time)
  Time to complete one task
Bandwidth (or throughput)
  Tasks completed per unit time

## Slide 38: Cloud Performance: Why Application Latency Matters
Key figure of merit: application responsiveness
  Longer the delay, the fewer the user clicks, the less the user happiness, and the lower the revenue per user

## Slide 39: Defining Relative Performance
Compare performance (perf) of X vs. Y
  Latency in this case

“Computer X is N times faster than Y”:

## Slide 40: Measuring CPU Performance
Computers use a clock to determine when events take place within hardware
Clock cycles: discrete time intervals
  a.k.a. clocks, cycles, clock periods, clock ticks
Clock rate or clock frequency: clock cycles per second (inverse of clock cycle time)
Example: 3 GigaHertz clock rate means clock cycle time = 1/(3x109) seconds = 333 picoseconds (ps)

## Slide 41: CPU Performance Factors
To distinguish between processor time and I/O, CPU time is time spent in processor

## Slide 42: CPU Performance Factors
But a program executes instructions!
  Let’s reformate this equation, then:
Instruction Count
CPI: Clock Cycles Per Instruction
Clock Cycle Time

## Slide 43: CPU Performance Equation
For a given program:
CPU Time

## Slide 44: Components That Affect Performance Factors
Component (HW/SW) | Perf Factors Affected
Algorithm | 
Programming Language | 
Compiler | 
Instruction Set Architecture | 
See P&H p.38 for more detailed explanations
Component (HW/SW) | Perf Factors Affected
Algorithm | Instruction Count, (CPI)
Programming Language | Instruction Count, CPI
Compiler | Instruction Count, CPI
Instruction Set Architecture | Instruction Count, CPI Clock Rate
Notes: Algorithm [Instruction count, possibly CPI]
The algorithm determines the number of source program instructions executed and hence the number of processor instructions executed. The algorithm may also affect the CPI, by favoring slower or faster instructions. For example, if the algorithm uses more floating-point operations, it will tend to have a higher CPI.
Programming language
[Instruction count, CPI]
The programming language certainly affects the instruction count, since statements in the language are translated to processor instructions, which determine instruction count. The language may also affect the CPI because of its features; for example, a language with heavy support for data abstraction (e.g., Java) will require indirect calls, which will use higher CPI instructions.
Compiler
[Instruction count, CPI]
The efficiency of the compiler affects both the instruction count and average cycles per instruction, since the compiler determines the translation of the source language instructions into computer instructions. The compiler’s role can be very complex and affect the CPI in complex ways.
Instruction set architecture
[Instruction count, clock rate, CPI]
The instruction set architecture affects all three aspects of CPU performance, since it affects the instructions needed for a function, the cost in cycles of each instruction, and the overall clock rate of the processor

## Slide 45
Computer A is ≈ 1.2 times faster than B
☐
Computer A is ≈ 4.0 times faster than B
☐
Computer B is ≈ 1.7 times faster than A
☐
Computer B is ≈ 3.4 times faster than A
☐
Question: Which statement is TRUE?
Computer A clock cycle time 250 ps, CPIA = 2
Computer B clock cycle time 500 ps, CPIB = 1.2
Assume A and B have same instruction set

## Slide 46: Summary
Floating point approximates real numbers:
  Largest magnitude: 2128 – 2104 (Exp = 0xFE) Smallest magnitude: 2-149 (denorm)
  Also has encodings for 0, ±∞, NaN
Performance measured in latency or bandwidth
Latency measurement:
  Affected by different components of the computer
S
Exponent (8)
Significand (23)
31 30
23 22
0

## Slide 47
You are responsible for the material contained on the following slides, though we may not have enough time to get to them in lecture.
They have been prepared in a way that should be easily readable and the material will be touched upon in the following lecture.
BONUS SLIDES

## Slide 48: Precision and Accuracy
Precision is a count of the number of bits in a computer word used to represent a value
Accuracy is a measure of the difference between the actual value of a number and its computer representation
High precision permits high accuracy but doesn’t guarantee it. It is possible to have high precision but low accuracy.
Example: float pi = 3.14;
  pi will be represented using all 24 bits of the significand (highly precise), but is only an approximation (not accurate)
Don’t confuse these two terms!

## Slide 49: “Father” of the Floating Point Standard
IEEE Standard 754 for Binary Floating-Point Arithmetic.
www.cs.berkeley.edu/~wkahan/ieee754status/754story.html
Prof. Kahan
1989 ACM Turing Award Winner!
Notes: 1:30 in

## Slide 50: Agenda
Floating Point
Administrivia
Floating Point Special Cases
Performance
Bonus: FP Conversion Practice
Bonus: FP Casting Concerns

## Slide 51: Example: Convert FP to Decimal
Sign: 0 means positive
Exponent:
  0110 1000two = 104ten
  Bias adjustment: 104 - 127 = -23
Significand:
  1 . 10101010100001101000010
  = 1 + 1x2-1+ 0x2-2 + 1x2-3 + 0x2-4 + 1x2-5 +... = 1 + 2-1 + 2-3 + 2-5 + 2-7 + 2-9 + 2-14 + 2-15 + 2-17 + 2-22 = 1.0 + 0.666115
Represents: 1.666115ten×2-23 ≈ 1.986*10-7
0
0110 1000
101 0101 0100 0011 0100 0010

## Slide 52: Example: Scientific Notation to FP
-2.340625 x 101
Denormalize: -23.40625
Convert integer part:
  23 = 16 + 4 + 2 + 1 = 10111two
Convert fractional part:
  .40625 = .25 + .125 + .03125 = 0.01101two
Put parts together and normalize:
  10111.01101 = 1.011101101×24
Convert exponent: 4 + 127 = 10000011two
1
1000 0011
011 1011 0100 0000 0000 0000

## Slide 53: Example: Convert to FP
1/3
  = 0.33333…ten
  = 0.25 + 0.0625 + 0.015625 + 0.00390625 + …
  = 1/4 + 1/16 + 1/64 + 1/256 + …
  = 2-2 + 2-4 + 2-6 + 2-8 + …
  = 0.0101010101… two × 20
  = 1.0101010101… two × 2-2
  Sign: 0
  Exponent = -2 + 127 = 125 = 01111101two
  Significand = 0101010101…two
0
0111 1101
010 1010 1010 1010 1010 1010

## Slide 54: Agenda
Floating Point
Administrivia
Floating Point Special Cases
Performance
Bonus: FP Conversion Practice
Bonus: FP Casting Concerns

## Slide 55: Casting floats to ints and vice versa
(int) floating_point_expression
  Coerces and converts it to the nearest integer (C uses truncation)
  i = (int) (3.14159 * f);
(float) integer_expression
  Converts integer to nearest floating point
  f = f + (float) i;

## Slide 56: float  int  float
if (f == (float)((int) f)) {
printf(“true”);
}
Will not always print “true”
  Small floating point numbers (< 1) don’t have integer representations
For other numbers, often will be rounding errors

## Slide 57: int  float  int
if (i == (int)((float) i)) {
printf(“true”);
}
Will not always print “true”
  Many large values of integers don’t have exact floating point representations
What about double?
  Significand is now 52 bits, which can hold all of 32-bit integer, so will always print “true”