## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
Direct-Mapped Caches

## Slide 2: Review of Last Lecture
Floating point (single and double precision) approximates real numbers
  Exponent field uses biased notation
  Special cases: 0, ±∞, NaN, denorm
  MIPS has special instructions and registers
Performance measured in latency or bandwidth
Latency measurement:
  Affected by different components of the computer

## Slide 3: Great Idea #3: Principle of Locality/ Memory Hierarchy

## Slide 4: Agenda
Memory Hierarchy Overview
Administrivia
Direct-Mapped Caches
Direct-Mapped Cache Example
Cache Reads and Writes

## Slide 5: Storage in a Computer
Processor
  Holds data in register files (~ 100 bytes)
  Registers accessed on sub-nanosecond timescale
Memory (“main memory”)
  More capacity than registers (~ Gbytes)
  Access time ~ 50-100 ns
Hundreds of clock cycles per memory access?!

## Slide 6: Processor-Memory Gap
Chart: Year
| 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005
uProc | 1 | 1.35 | 1.82 | 2.46 | 3.32 | 4.48 | 6.05 | 8.17 | 12.67 | 19.63 | 30.43 | 47.17 | 73.11 | 113.32 | 175.65 | 272.26 | 422.01 | 654.11 | 1013.88 | 1571.51 | 2435.84 | 3775.55 | 5852.1 | 9070.75 | 9500 | 10000
DRAM | 1 | 1.07 | 1.15 | 1.23 | 1.31 | 1.4 | 1.5 | 1.61 | 1.72 | 1.84 | 1.97 | 2.1 | 2.25 | 2.41 | 2.58 | 2.76 | 2.95 | 3.16 | 3.38 | 3.62 | 3.87 | 4.14 | 4.43 | 4.74 | 5.07 | 5.43
“Moore’s Law”
Processor-Memory
Performance Gap (grows 50%/year)
1989 first Intel CPU with cache on chip
1998 Pentium III has two cache levels on chip
µProc
55%/year
(2X/1.5yr)
DRAM
7%/year
(2X/10yrs)

## Slide 7: Library Analogy
Writing a report on a specific topic
  e.g. the works of J.D. Salinger
While at library, check out books and keep them on desk
If need more, check them out and bring to desk
  Don’t return earlier books since might still need them
  Limited space on desk; which books do we keep?
You hope this collection of ~10 books on desk enough to write report, despite 10 being only 0.00001% of the books in UC Berkeley libraries

## Slide 8: Principle of Locality (1/3)
Principle of Locality: Programs access only a small portion of the full address space at any instant of time
  Recall: Address space holds both code and data
  Loops and sequential instruction execution mean generally localized code access
  Stack and Heap try to keep your data together
  Arrays and structs naturally group data you would access together

## Slide 9: Principle of Locality (2/3)
Temporal Locality (locality in time)
  Go back to the same book on desk multiple times
  If a memory location is referenced then it will tend to be referenced again soon
Spatial Locality (locality in space)
  When go to book shelf, grab many books on J.D. Salinger since library stores related books together
  If a memory location is referenced, the locations with nearby addresses will tend to be referenced soon
Notes: How does the memory hierarchy work? Well it is rather simple, at least in principle.
In order to take advantage of the temporal locality, that is the locality in time, the memory hierarchy will keep those more recently accessed data items closer to the processor because chances are (points to the principle), the processor will access them again soon.
In order to take advantage of the spatial locality, not ONLY do we move the item that has just been accessed to the upper level, but we ALSO move the data items that are adjacent to it.
+1 = 15 min. (X:55)

## Slide 10: Principle of Locality (3/3)
We exploit the principle of locality in hardware via a memory hierarchy where:
  Levels closer to processor are faster (and more expensive per bit so smaller)
  Levels farther from processor are larger (and less expensive per bit so slower)
Goal: Create the illusion of memory being almost as fast as fastest memory and almost as large as biggest memory of the hierarchy

## Slide 11: Memory Hierarchy Schematic
Smaller,
Faster, More expensive
Bigger,
Slower, Cheaper
Processor
Level 1
Level 2
Level n
Level 3
. . .
Lower Higher
Notes: The Processor accesses data out of the highest levels.
Lowest level (usually disk) contains all available data.

## Slide 12: Cache Concept
Introduce intermediate hierarchy level: memory cache, which holds a copy of a subset of main memory
  As a pun, often use $ (“cash”) to abbreviate cache (e.g. D$ = Data Cache, L1$ = Level 1 Cache)
Modern processors have separate caches for instructions and data, as well as several levels of caches implemented in different sizes
Implemented with same IC processing technology as CPU and integrated on-chip – faster but more expensive than main memory

## Slide 13: Memory Hierarchy Technologies
Caches use static RAM (SRAM)
  Fast (typical access times of 0.5 to 2.5 ns)
  Low density (6 transistor cells), higher power, expensive ($2000 to $4000 per GB in 2011)
  Static: content will last as long as power is on
Main memory uses dynamic RAM (DRAM)
  High density (1 transistor cells), lower power, cheaper ($20 to $40 per GB in 2011)
  Slower (typical access times of 50 to 70 ns)
  Dynamic: needs to be “refreshed” regularly (~ every 8 ms)
Notes: In case you didn’t know, RAM stands for Random Access Memory.
Size comparison: DRAM/SRAM is 4 to 8 times
Cost/cycle time comparison SRAM/DRAM is 8 to 16 times
http://parts.digikey.com/1/parts/1211303-ic-sram-1mbit-10ns-32soj-cy7c109d-10vxi.html
Quantity discount 10ns 1MBit SRAM $2.24, $17/Mbyte, $1700/100 Mbyte, $17000/GByte
http://www.frys.com/template/harddrives
DRAM: 4GB @ $70 or $17.50 per GB
24GB@$800 = $33/Gbyte
http://www.frys.com/category/Outpost/Hard+Drives+&+Memory/Memory/Notebook+Memory/Apple+-+Mac++Memory/
DDR2 1GB @ $25 per
DDR3 1 GB @ $37.5 per
FLASH Media
Approx. $2 per Gbyte

## Slide 14: Memory Transfer in the Hierarchy
Inclusive: data in L1$ ⊂ data in L2$ ⊂ data in MM ⊂ data in SM
Processor
L1$
L2$
Secondary Memory
Main Memory
Block: Unit of transfer between memory and cache
4-8 bytes (word)
16-128 bytes (block)
4,096+ bytes (page)
8-32 bytes (block)
Notes: Symbol ⊂ means “is a subset of”

## Slide 15: Managing the Hierarchy
registers  memory
  By compiler (or assembly level programmer)
cache  main memory
  By the cache controller hardware
main memory  disks (secondary storage)
  By the OS (virtual memory, which is a later topic)
  Virtual to physical address mapping assisted by the hardware (TLB)
  By the programmer (files)
We are here

## Slide 16: Typical Memory Hierarchy
On-Chip Components
Second
Level
Cache
(SRAM)
Control
Datapath
Secondary
Memory
(Disk
or Flash)
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
Cost/bit: highest lowest
Speed: ½’s 1’s 10’s 100’s 1,000,000’s
(cycles)
Size: 100’s 10K’s M’s G’s T’s
(bytes)
Notes: Instead, the memory system of a modern computer consists of a series of black boxes ranging from the fastest to the slowest.
Besides variation in speed, these boxes also varies in size (smallest to biggest) and cost.
What makes this kind of arrangement work is one of the most important principle in computer design. The principle of locality. The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in detail in the next lectures on caches).

## Slide 17: Review So Far
Goal: present the programmer with ≈ as much memory as the largest memory at ≈ the speed of the fastest memory
Approach: Memory Hierarchy
  Successively higher levels contain “most used” data from lower levels
  Exploits temporal and spatial locality
  We will start by studying caches

## Slide 18: Agenda
Memory Hierarchy Overview
Administrivia
Direct-Mapped Caches
Direct-Mapped Cache Example
Cache Reads and Writes

## Slide 19: Administrivia
Midterm
  Friday 7/13, 9am-12pm, 245 Li Ka Shing
  How to study:
    Studying in groups can help
    Take old exams for practice
    Look at lectures, section notes, projects, hw, labs, etc.
  Will cover material through caches
Project 1 due Sunday
  Brandon extra OHs Sat, 3-5pm in lab

## Slide 20: Agenda
Memory Hierarchy Overview
Administrivia
Direct-Mapped Caches
Direct-Mapped Cache Example
Cache Reads and Writes

## Slide 21: Cache Management
Library analogy: organization is necessary!
What is the overall organization of blocks we impose on our cache?
  Where do we put a block of data from memory?
  How do we know if a block is already in cache?
  How do we quickly find a block when we need it?
  When do we replace something in the cache?
Notes: Library analogy: How do we sort the books on our desk? If we throw them everywhere, then we have to scan through all of them to find what we want – so inefficient! After you’ve gone through enough books, you might not remember which ones you put back.

## Slide 22: General Notes on Caches
Recall: Memory is byte-addressed
We haven’t specified the size of our “blocks,” but will be multiple of word size (32-bits)
  How do we access individual words or bytes within a block?
Cache is smaller than memory
  Can’t fit all blocks at once, so multiple blocks in memory map to the same cache slot (row)
  Need some way of identifying which memory block is currently in the row
OFFSET
INDEX
TAG

## Slide 23: Direct-Mapped Caches (1/3)
Each memory block is mapped to exactly one row in the cache (direct-mapped)
  Use simple hash function
Effect of block size:
  Spatial locality dictates our blocks consist of adjacent bytes, which differ in address by 1
  Offset field: Lowest bits of memory address can be used to index to specific bytes within a block
    Block size needs to be a power of two (in bytes)
Notes:   Check just one location to see if block is in cache.

## Slide 24: Direct-Mapped Caches (2/3)
Effect of cache size: (total stored data)
  Determines number of blocks cache holds
  If could hold all of memory, would use remaining bits (minus offset bits) to select appropriate row of cache
  Index field: Apply hash function to remaining bits to determine which row the block goes in
    (block address) modulo (# of blocks in the cache)
  Tag field: Leftover upper bits of memory address determine which portion of memory the block came from (identifier)

## Slide 25: TIO Address Breakdown
Memory address fields:
Meaning of the field sizes:
  O bits ↔ 2O bytes/block = 2O-2 words/block
  I bits ↔ 2I rows in cache = cache size / block size
  T bits = A – I – O, where A = # of address bits (A = 32 here)
Tag
Index
Offset
31
0
T bits
I bits
O bits

## Slide 26: Direct-Mapped Caches (3/3)
What’s actually in the cache?
  Each row contains the actual data block to store (B bits = 8 × 2O bits)
  In addition, must save Tag field of address as identifier (T bits)
  Valid bit: Indicates whether the block in that row is valid or not
Total bits in cache = # rows × (B + T + 1) = 2I × (8×2O + T + 1) bits
Notes: Data can be invalid at start of new program or memory updated at other levels of the memory hierarchy (more on this later in the course).

## Slide 27: Cache Example (1/2)
Cache parameters:
  Address space of 64B, block size of 1 word, cache size of 4 words
TIO Breakdown:
  1 word = 4 bytes, so O = log2(4) = 2
  Cache size / block size = 4, so I = log2(4) = 2
  A = log2(64) = 6 bits, so T = 6 – 2 – 2 = 2
Bits in cache = 22 × (8×22 + 2 + 1) = 140 bits
XX
XX
XX
Memory Addresses:
Block address

## Slide 28: Cache Example (2/2)
Main Memory:
Which blocks map to each row of the cache?
(see colors)
On a memory request: (let’s say 001011two)
1) Take Index field (10)
2) Check if Valid bit is true in that row of cache
3) If valid, then check if Tag matches
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
00
01
10
11
Cache:
Tag
Data
Valid
Index
Cache rows exactly match the Index field
Which blocks map to each row of the cache?
(see colors)
Main Memory shown in blocks, so offset bits not shown (x’s)

## Slide 29: Direct-Mapped Cache Internals
Four words/block, cache size = 1 Ki words
8
Index
Data (words)
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11 . . . 4 3 2 1 0
Byte offset
20
20
Tag
Hit
Data
32
Block offset
and
Notes: To take advantage of spatial locality, want a cache block that is larger than a word in size.
Careful: Offset field is the combination of the Byte and Block offsets shown here.

## Slide 30: Caching Terminology (1/2)
When reading memory, 3 things can happen:
  Cache hit: Cache block is valid and contains the proper address, so read the desired word
  Cache miss: Nothing in that row of the cache (not valid), so fetch from memory
  Cache miss with block replacement: Wrong block is in the row, so discard it and fetch desired data from memory

## Slide 31: Caching Terminology (2/2)
How effective is your cache?
  Want to max cache hits and min cache misses
  Hit rate (HR): Percentage of memory accesses in a program or set of instructions that result in a cache hit
  Miss rate (MR): Like hit rate, but for cache misses MR = 1 – HR
How fast is your cache?
  Hit time (HT): Time to access cache (including Tag comparison)
  Miss penalty (MP): Time to replace a block in the cache from a lower level in the memory hierarchy

## Slide 32: Sources of Cache Misses: The 3Cs
Compulsory: (cold start or process migration, 1st reference)
  First access to block impossible to avoid; Effect is small for long running programs
Capacity:
  Cache cannot contain all blocks accessed by the program
Conflict: (collision)
  Multiple memory locations mapped to the same cache location

## Slide 33: Get To Know Your Instructor

## Slide 34: Agenda
Memory Hierarchy Overview
Administrivia
Direct-Mapped Caches
Direct-Mapped Cache Example
Cache Reads and Writes

## Slide 35: Direct-Mapped Cache Example
Consider the sequence of memory address accesses
  0 1 2 3 4 3 4 15
0
1
2
3
4
3
4
15
00 Mem(0)
00 Mem(0)
00 Mem(1)
00 Mem(0)
00 Mem(0)
00 Mem(1)
00 Mem(2)
miss
miss
miss
miss
miss
miss
hit
hit
00 Mem(0)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01
4
11
15
00 Mem(1)
00 Mem(2)
00 Mem(3)
Start with an empty cache - all blocks initially marked as not valid
  8 requests, 6 misses (HR = 0.25, MR = 0.75)
Time
0000 0001 0010 0011 0100 0011 0100 1111
Notes: For lecture
Reference string is word addresses (or block number since we are using one word blocks) – i.e., the low order two bits used to selected the byte in the 32-bit word are ignored

## Slide 36: Taking Advantage of Spatial Locality
Let cache block hold more than one byte
  0 1 2 3 4 3 4 15
0
1
2
3
4
3
4
15
00 Mem(1) Mem(0)
miss
00 Mem(1) Mem(0)
hit
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
miss
hit
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
miss
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
01
5
4
hit
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
hit
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
miss
11
15
14
Start with an empty cache - all blocks initially marked as not valid
  8 requests, 4 misses (HR = 0.5, MR = 0.5)
0000 0001 0010 0011 0100 0011 0100 1111
Notes: For lecture
Show the 4-bit address mapping – 2-bits of tag, 1-bit of set address (index), 1-bit of word-in-block select

## Slide 37: Effect of Block and Cache Sizes on Miss Rate
Chart: Block size (bytes)
| 16 | 32 | 64 | 128 | 256
4 KB | 8.5 | 7.5 | 7.25 | 7.75 | 9.5
16 KB | 4 | 2.75 | 2.75 | 3 | 3.5
64 KB | 2 | 1.7 | 1.55 | 1.4 | 1.4
256 KB | 1 | 0.7 | 0.5 | 0.5 | 0.6
Miss rate goes up if the block size becomes a significant fraction of the cache size because the number of blocks that can be held in the same size cache is smaller (increasing capacity misses)
Notes: Increasing the block size usually decreases the miss rate.
A more serious problem is that the miss penalty goes up since it is primarily determined by the time to fetch the block from the next lower level of the hierarchy and load it into the cache.

## Slide 38: Agenda
Memory Hierarchy Overview
Administrivia
Direct-Mapped Caches
Direct-Mapped Cache Example
Cache Reads and Writes

## Slide 39: Cache Reads and Writes
Want to handle reads and writes quickly while maintaining consistency between cache and memory (i.e. both know about all updates)
  Policies for cache hits and misses are independent
Here we assume the use of separate instruction and data caches (I$ and D$)
  Read from both
  Write only to D$ (assume no self-modifying code)

## Slide 40: Handling Cache Hits
Read hits (I$ and D$)
  Fastest possible scenario, so want more of these
Write hits (D$)
  Write-Through Policy: Always write data to cache and to memory (through cache)
    Forces cache and memory to always be consistent
    Slow! (every memory access is long)
    Include a Write Buffer that updates memory in parallel with processor
Assume present in all schemes when writing to memory
Notes: In a write-back cache, because we cannot overwrite the block (since we may not have a backup copy anywhere), stores either require two cycles (one to check for a hit, followed by one to actually do the write) or require a write buffer to hold that data (essentially pipelining the write).
By comparison, a write-through cache can always be done in one cycle assuming there is room in the write buffer. Read the tag and write the data in parallel. If the tag doesn’t match, the generate a write miss to fetch the rest of that block from the next level in the hierarchy (and update the tag field).

## Slide 41: Handling Cache Hits
Read hits (I$ and D$)
  Fastest possible scenario, so want more of these
Write hits (D$)
  Write-Back Policy: Write data only to cache, then update memory when block is removed
    Allows cache and memory to be inconsistent
    Multiple writes collected in cache; single write to memory per block
    Dirty bit: Extra bit per cache row that is set if block was written to (is “dirty”) and needs to be written back

## Slide 42: Handling Cache Misses
Miss penalty grows as block size does
Read misses (I$ and D$)
  Stall execution, fetch block from memory, put in cache, send requested word to processor, resume
Write misses (D$)
  Write allocate: Fetch block from memory, put in cache, execute a write hit
    Works with either write-through or write-back
    Ensures cache is up-to-date after write miss
Notes: Write allocate almost always paired with write-back.

## Slide 43: Handling Cache Misses
Miss penalty grows as block size does
Read misses (I$ and D$)
  Stall execution, fetch block from memory, put in cache, send requested word to processor, resume
Write misses (D$)
  No-write allocate: Skip cache altogether and write directly to memory
    Cache is never up-to-date after write miss
    Ensures memory is always up-to-date
Notes: No-write allocate almost always paired with write-through.

## Slide 44: Improvements
  Nonblocking cache: allows for multiple loads, so the processor can continue to access cache while cache is handling an earlier miss
Early restart: Processor resumes as soon as requested portion of block is available
Critical word first: Always load requested portion of block first
  Early restart and critical word first can be used together

## Slide 45: Summary
Memory hierarchy exploits principle of locality to deliver lots of memory at fast speeds
Direct-Mapped Cache: Each block in memory maps to exactly one row in the cache
  Index to determine which row
  Offset to determine which byte within block
  Tag to identify if it’s the block you want
Cache read and write policies:
  Write-back and write-through for hits
  Write allocate and no-write allocate for misses