## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
Pipelining Hazards

## Slide 2: Great Idea #4: Parallelism
Smart Phone
Warehouse Scale Computer
Leverage Parallelism &
Achieve High Performance
Core
…
Memory
Input/Output
Computer
Core
Parallel Requests
  Assigned to computer
  e.g. search “Katz”
Parallel Threads
  Assigned to core
  e.g. lookup, ads
Parallel Instructions
  > 1 instruction @ one time
  e.g. 5 pipelined instructions
Parallel Data
  > 1 data item @ one time
  e.g. add of 4 pairs of words
Hardware descriptions
  All gates functioning in parallel at same time
Software Hardware
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A0+B0
A1+B1
A2+B2
A3+B3
Logic Gates

## Slide 3: Review of Last Lecture
Implementing controller for your datapath
  Take decoded signals from instruction and generate control signals
  Use “AND” and “OR” Logic scheme
Pipelining improves performance by exploiting Instruction Level Parallelism
  5-stage pipeline for MIPS: IF, ID, EX, MEM, WB
  Executes multiple instructions in parallel
  Each instruction has the same latency
  What can go wrong???

## Slide 4
Question: Are the following statement TRUE or FALSE?
Adding a new instruction will NOT require changing any of your existing control logic.
Adding a new control signal will NOT require changing any of your existing control logic.
F F
☐
F T
☐
T F
☐
T T
☐
1 2

## Slide 5: Review: Pipelined Datapath

## Slide 6: Graphical Pipeline Representation
I
n
s
t
r
O
r
d
e
r
Load
Add
Store
Sub
Or
I$
Time (clock cycles)
I$
ALU
Reg
Reg
I$
D$
ALU
ALU
Reg
D$
Reg
I$
D$
Reg
ALU
Reg
Reg
Reg
D$
Reg
D$
ALU
RegFile: right half is read, left half is write
Reg
I$

## Slide 7
Question: Which of the following signals (buses or control signals) for MIPS-lite does NOT need to be passed into the EX pipeline stage?
PC + 4
☐
MemWr
☐
RegWr
☐
imm16
☐
IF
ID
EX
Mem
WB
ALU
I$
Reg
D$
Reg

## Slide 8: Pipelining Hazards
A hazard is a situation that prevents starting the next instruction in the next clock cycle
Structural hazard
  A required resource is busy (e.g. needed in multiple stages)
Data hazard
  Data dependency between instructions
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Flow of execution depends on previous instruction

## Slide 9: Agenda
Structural Hazards
Data Hazards
  Forwarding
Administrivia
Data Hazards (Continued)
  Load Delay Slot
Control Hazards
  Branch and Jump Delay Slots
  Branch Prediction

## Slide 10: 1. Structural Hazards
Conflict for use of a resource
MIPS pipeline with a single memory?
  Load/Store requires memory access for data
  Instruction fetch would have to stall for that cycle
    Causes a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Separate L1 I$ and L1 D$ take care of this

## Slide 11: Structural Hazard #1: Single Memory
I$
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
Trying to read same memory twice in same clock cycle

## Slide 12: Structural Hazard #2: Registers (1/2)
I$
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
Can we read and write to registers simultaneously?

## Slide 13: Structural Hazard #2: Registers (2/2)
Two different solutions have been used:
  Split RegFile access in two: Write during 1st half and Read during 2nd half of each clock cycle
    Possible because RegFile access is VERY fast (takes less than half the time of ALU stage)
  Build RegFile with independent read and write ports
Conclusion: Read and Write to registers during same clock cycle is okay

## Slide 14: Agenda
Structural Hazards
Data Hazards
  Forwarding
Administrivia
Data Hazards (Continued)
  Load Delay Slot
Control Hazards
  Branch and Jump Delay Slots
  Branch Prediction

## Slide 15: 2. Data Hazards (1/2)
Consider the following sequence of instructions:
add $t0, $t1, $t2
sub $t4, $t0, $t3
and $t5, $t0, $t6
or $t7, $t0, $t8
xor $t9, $t0, $t10

## Slide 16: 2. Data Hazards (2/2)
Data-flow backward in time are hazards
sub $t4,$t0,$t3
ALU
I$
Reg
D$
Reg
and $t5,$t0,$t6
ALU
I$
Reg
D$
Reg
or $t7,$t0,$t8
I$
ALU
Reg
D$
Reg
xor $t9,$t0,$t10
ALU
I$
Reg
D$
Reg
add $t0,$t1,$t2
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)

## Slide 17: Data Hazard Solution: Forwarding
Forward result as soon as it is available
  OK that it’s not stored in RegFile yet
sub $t4,$t0,$t3
ALU
I$
Reg
D$
Reg
and $t5,$t0,$t6
ALU
I$
Reg
D$
Reg
or $t7,$t0,$t8
I$
ALU
Reg
D$
Reg
xor $t9,$t0,$t10
ALU
I$
Reg
D$
Reg
add $t0,$t1,$t2
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg

## Slide 18: Datapath for Forwarding (1/2)
What changes need to be made here?

## Slide 19: Datapath for Forwarding (2/2)
Handled by forwarding unit
Notes: Scan figure 4.54 on p. 368.

## Slide 20: Agenda
Structural Hazards
Data Hazards
  Forwarding
Administrivia
Data Hazards (Continued)
  Load Delay Slot
Control Hazards
  Branch and Jump Delay Slots
  Branch Prediction

## Slide 21: Administrivia
HW 4 due tonight
Project 2 Part 2 due Sunday
Project 3 will be released Thursday or Friday

## Slide 22: Agenda
Structural Hazards
Data Hazards
  Forwarding
Administrivia
Data Hazards (Continued)
  Load Delay Slot
Control Hazards
  Branch and Jump Delay Slots
  Branch Prediction

## Slide 23: Data Hazard: Loads (1/4)
Recall: Dataflow backwards in time are hazards
Can’t solve all cases with forwarding
  Must stall instruction dependent on load, then forward (more hardware)
sub $t3,$t0,$t2
ALU
I$
Reg
D$
Reg
lw $t0,0($t1)
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg

## Slide 24: Data Hazard: Loads (2/4)
Hardware stalls pipeline
  Called “hardware interlock”
sub $t3,$t0,$t2
ALU
I$
Reg
D$
Reg
bubble
and $t5,$t0,$t4
ALU
I$
Reg
D$
Reg
bubble
or $t7,$t0,$t6
I$
ALU
Reg
D$
bubble
lw $t0, 0($t1)
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg
Schematically, this is what we want, but in reality stalls done “horizontally”
How to stall just part of pipeline?

## Slide 25: Data Hazard: Loads (3/4)
Stall is equivalent to nop
sub $t3,$t0,$t2
and $t5,$t0,$t4
or $t7,$t0,$t6
I$
ALU
Reg
D$
lw $t0, 0($t1)
ALU
I$
Reg
D$
Reg
bubble
bubble
bubble
bubble
bubble
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
nop

## Slide 26: Data Hazard: Loads (4/4)
Slot after a load is called a load delay slot
  If that instruction uses the result of the load, then the hardware interlock will stall it for one cycle
  Letting the hardware stall the instruction in the delay slot is equivalent to putting a nop in the slot (except the latter uses more code space)
Idea: Let the compiler put an unrelated instruction in that slot  no stall!

## Slide 27: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction!
MIPS code for A=B+E; C=B+F;
# Method 1:
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
# Method 2:
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
Stall!
Stall!
13 cycles
11 cycles

## Slide 28: Agenda
Structural Hazards
Data Hazards
  Forwarding
Administrivia
Data Hazards (Continued)
  Load Delay Slot
Control Hazards
  Branch and Jump Delay Slots
  Branch Prediction

## Slide 29: 3. Control Hazards
Branch (beq, bne) determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
Simple Solution: Stall on every branch until we have the new PC value
  How long must we stall?

## Slide 30: Branch Stall
When is comparison result available?
I$
beq
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
TWO bubbles required per branch!

## Slide 31: 3. Control Hazard: Branching
Option #1: Insert special branch comparator in ID stage
  As soon as instruction is decoded, immediately make a decision and set the new value of the PC
  Benefit: Branch decision made in 2nd stage, so only one nop is needed instead of two
  Side Note: This means that branches are idle in EX, MEM, and WB

## Slide 32: Improved Branch Stall
When is comparison result available?
I$
beq
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
Only one bubble required now

## Slide 33: Datapath for ID Branch Comparator
What changes need to be made here?

## Slide 34: Datapath for ID Branch Comparator
Handled by hazard detection unit
Notes: Scan figure 4.54 on p. 368.

## Slide 35: 3. Control Hazard: Branching
Option #2: Branch Prediction – guess outcome of a branch, fix afterwards if necessary
  Must cancel (flush) all instructions in pipeline that depended on guess that was wrong
  How many instructions do we end up flushing?
Achieve simplest hardware if we predict that all branches are NOT taken

## Slide 36: 3. Control Hazard: Branching
Option #3: Branch delay slot
  Whether or not we take the branch, always execute the instruction immediately following the branch
  Worst-Case: Put a nop in the branch-delay slot
  Better Case: Move an instruction from before the branch into the branch-delay slot
    Must not affect the logic of program

## Slide 37: 3. Control Hazard: Branching
MIPS uses this delayed branch concept
  Re-ordering instructions is a common way to speed up programs
  Compiler finds an instruction to put in the branch delay slot ≈ 50% of the time
Jumps also have a delay slot
  Why is one needed?

## Slide 38: Delayed Branch Example
add $1, $2, $3
sub $4, $5, $6
beq $1, $4, Exit
or $8, $9, $10
xor $10, $1, $11
Nondelayed Branch
add $1, $2,$3
sub $4, $5, $6
beq $1, $4, Exit
or $8, $9, $10
xor $10, $1, $11
Delayed Branch
Exit:
Exit:
Why not any of the other instructions?

## Slide 39: Delayed Jump in MIPS
MIPS Green Sheet for jal: R[31]=PC+8; PC=JumpAddr
  PC+8 because of jump delay slot!
  Instruction at PC+4 always gets executed before jal jumps to label, so return to PC+8

## Slide 40: Get To Know Your Staff
Category: Movies

## Slide 41: Agenda
Structural Hazards
Data Hazards
  Forwarding
Administrivia
Data Hazards (Continued)
  Load Delay Slot
Control Hazards
  Branch and Jump Delay Slots
  Branch Prediction

## Slide 42: Dynamic Branch Prediction
Branch penalty is more significant in deeper pipelines
  Also superscalar pipelines (discussed tomorrow)
Use dynamic branch prediction
  Have branch prediction buffer (a.k.a. branch history table) that stores outcomes (taken/not taken) indexed by recent branch instruction addresses
  To execute a branch
    Check table and predict the same outcome for next fetch
    If wrong, flush pipeline and flip prediction

## Slide 43: 1-Bit Predictor: Shortcoming
Examine the code below, assuming both loops will be executed multiple times:
outer: … … inner: …
…
beq …, …, inner … beq …, …, outer
Inner loop branches are predicted wrong twice!
  Predict as taken on last iteration of inner loop
  Then predict as not taken on first iteration of inner loop next time around

## Slide 44: 2-Bit Predictor
Only change prediction after two successive incorrect predictions

## Slide 45
Question: Are the following statement TRUE or FALSE?
Thanks to pipelining, I have reduced the time it took me to wash my one shirt
Longer pipelines are always a win (since less work per stage & a faster clock)
F F
☐
F T
☐
T F
☐
T T
☐
1 2

## Slide 46
Question: For each code sequences below, choose one of the statements below:
No stalls as is
☐
No stalls with forwarding
☐
Must stall
☐
1: lw $t0,0($t0) add $t1,$t0,$t0 | 2: add $t1,$t0,$t0 addi $t2,$t0,5 addi $t4,$t1,5 | 3: addi $t1,$t0,1 addi $t2,$t0,2 addi $t3,$t0,2 addi $t3,$t0,4 addi $t5,$t1,5

## Slide 47: Code Sequence 1
I$
lw
add
instr
instr
instr
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
Must stall

## Slide 48: Code Sequence 2
I$
add
addi
addi
instr
instr
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
forwarding
no forwarding
No stalls with forwarding

## Slide 49: Code Sequence 3
I$
addi
addi
addi
addi
addi
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
No stalls as is

## Slide 50: Summary
Hazards reduce effectiveness of pipelining
  Cause stalls/bubbles
Structural Hazards
  Conflict in use of datapath component
Data Hazards
  Need to wait for result of a previous instruction
Control Hazards
  Address of next instruction uncertain/unknown
  Branch and jump delay slots