## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
Amdahl’s Law,
Thread Level Parallelism

## Slide 2: 1st Half in Review
Write bigger, talk slower
Students afraid/too lost to respond
  Don’t be afraid/ashamed of being lost/wrong
Peer instruction grading
  Answers will be added to slides after lecture
2nd half material is “clean slate”
Found copied code! Will be dealt with at end.
  Don’t dig yourself into a deeper hole…

## Slide 3: Review of Last Lecture
Flynn Taxonomy of Parallel Architectures
  SIMD: Single Instruction Multiple Data
  MIMD: Multiple Instruction Multiple Data
Intel SSE SIMD Instructions
  One instruction fetch that operates on multiple operands simultaneously
  128/64 bit XMM registers
  Embed the SSE machine instructions directly into C programs through use of intrinsics
Loop Unrolling: Access more of array in each iteration of a loop

## Slide 4: Agenda
Amdahl’s Law
Administrivia
Multiprocessor Systems
Multiprocessor Cache Coherence
Synchronization - A Crash Course

## Slide 5: Amdahl’s (Heartbreaking) Law
Speedup due to enhancement E:
Example: Suppose that enhancement E accelerates a fraction F (F<1) of the task by a factor S (S>1) and the remainder of the task is unaffected
Exec time w/E =
Speedup w/E =
F
Exec Time w/o E  [ (1-F) + F/S]
1 / [ (1-F) + F/S ]

## Slide 6: Amdahl’s Law
Speedup = 1
Example: the execution time of half of the program can be accelerated by a factor of 2. What is the program speed-up overall?
(1 - F) + F
S
Non-speed-up part
Speed-up part
1
0.5 + 0.5
2
1
0.5 + 0.25
=
=
1.33

## Slide 7: Consequence of Amdahl’s Law
The amount of speedup that can be achieved through parallelism is limited by the non-parallel portion of your program!
Parallel
portion
Serial
portion
Time
Number of Processors
1
2
3
4
5
Speedup
Number of Processors

## Slide 8: Parallel Speed-up Examples (1/3)
Consider an enhancement which runs 20 times faster but which is only usable 15% of the time
Speedup = 1/(.85 + .15/20) = 1.166
What if it’s usable 25% of the time?
Speedup = 1/(.75 + .25/20) = 1.311
Amdahl’s Law tells us that to achieve linear speedup with more processors, none of the original computation can be scalar (non-parallelizable)
To get a speedup of 90 from 100 processors, the percentage of the original program that could be scalar would have to be 0.1% or less
Speedup = 1/(.001 + .999/100) = 90.99
Speedup w/ E = 1 / [ (1-F) + F/S ]
Nowhere near
20x speedup!
Notes: For last part, can solve for max percentage:
1/(x + (1-x)/100) = 90
1/90 = x + (1-x)/100
10/9 – 1 = 99x
x = 1/891 = 0.112233%!!!  so small!

## Slide 9: Parallel Speed-up Examples (2/3)
10 “scalar” operations (non-parallelizable)
100 parallelizable operations
  Say, element-wise addition of two 10x10 matrices.
110 operations
  100/110 = .909 Parallelizable, 10/110 = 0.091 Scalar
Z1 + Z2 + … + Z10
X1,1
X1,10
X10,1
X10,10
Y1,1
Y1,10
Y10,1
Y10,10
+
Non-parallel part
Parallel part
Partition 10 ways and perform on 10 parallel processing units
.
.
.
.
.
.

## Slide 10: Parallel Speed-up Examples (3/3)
Consider summing 10 scalar variables and two 10 by 10 matrices (matrix sum) on 10 processors
Speedup = 1/(.091 + .909/10) = 1/0.1819 = 5.5
What if there are 100 processors ?
Speedup = 1/(.091 + .909/100) = 1/0.10009 = 10.0
What if the matrices are 100 by 100 (or 10,010 adds in total) on 10 processors?
Speedup = 1/(.001 + .999/10) = 1/0.1009 = 9.9
What if there are 100 processors ?
Speedup = 1/(.001 + .999/100) = 1/0.01099 = 91
Speedup w/ E = 1 / [ (1-F) + F/S ]

## Slide 11: Strong and Weak Scaling
To get good speedup on a multiprocessor while keeping the problem size fixed is harder than getting good speedup by increasing the size of the problem
  Strong scaling: When speedup is achieved on a parallel processor without increasing the size of the problem
  Weak scaling: When speedup is achieved on a parallel processor by increasing the size of the problem proportionally to the increase in the number of processors
Load balancing is another important factor: every processor doing same amount of work
  Just 1 unit with twice the load of others cuts speedup almost in half (bottleneck!)
Notes: Add load balancing example here – page 638

## Slide 12
Question: Suppose a program spends 80% of its time in a square root routine. How much must you speed up square root to make the program run 5 times faster?
10
(A)
20
(B)
100
(C)
None of the above
(D)
Speedup w/ E = 1 / [ (1-F) + F/S ]

## Slide 13: Agenda
Amdahl’s Law
Administrivia
Multiprocessor Systems
Multiprocessor Cache Coherence
Synchronization - A Crash Course

## Slide 14: Administrivia (1/2)
Midterm Re-grade Policy
  Rubric posted
  Any questions? Ask in discussion section
  Written appeal process
    Explain rationale for re-grade request
    Attach rationale to exam & submit to your TA by the end of Thursday’s lab
    ENTIRE test will be re-graded (is possible to end up with a lower grade)

## Slide 15: Administrivia (2/2)
Project 2: Matrix Multiply Performance Improvement
  Work in groups of two!
  Part 1: Due July 28 (this Sunday)
  Part 2: Due August 4 (posted by Thu)
HW 5 also due July 31 (posted Thu)
Closely packed due dates, try to get ahead of schedule for the project

## Slide 16: Agenda
Amdahl’s Law
Administrivia
Multiprocessor Systems
Multiprocessor Cache Coherence
Synchronization - A Crash Course

## Slide 17: Great Idea #4: Parallelism
Smart Phone
Warehouse Scale Computer
Leverage Parallelism &
Achieve High Performance
Core
…
Memory
Input/Output
Computer
Core
Parallel Requests
  Assigned to computer
  e.g. search “Garcia”
Parallel Threads
  Assigned to core
  e.g. lookup, ads
Parallel Instructions
  > 1 instruction @ one time
  e.g. 5 pipelined instructions
Parallel Data
  > 1 data item @ one time
  e.g. add of 4 pairs of words
Hardware descriptions
  All gates functioning in parallel at same time
Software Hardware
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A0+B0
A1+B1
A2+B2
A3+B3
Logic Gates

## Slide 18: Parallel Processing: Multiprocessor Systems (MIMD)
Multiprocessor (MIMD): a computer system with at least 2 processors
  Use term core for processor (“multicore”)
Deliver high throughput for independent jobs via request-level or task-level parallelism
Processor
Processor
Processor
Cache
Cache
Cache
Interconnection Network
Memory
I/O
Notes: Power has become the overriding issue for both data centers and microprocessors. Power efficiency has joined scalable performance making the case for multiprocessors. Multiprocessors also improve availability.

## Slide 19: Parallel Processing: Multiprocessor Systems (MIMD)
Multiprocessor (MIMD): a computer system with at least 2 processors
  Use term core for processor (“multicore”)
Improve the run time of a single program that has been specially crafted to run on a multiprocessor - a parallel processing program
Processor
Processor
Processor
Cache
Cache
Cache
Interconnection Network
Memory
I/O
Notes: Power has become the overriding issue for both data centers and microprocessors. Power efficiency has joined scalable performance making the case for multiprocessors. Multiprocessors also improve availability.

## Slide 20: Shared Memory Multiprocessor (SMP)
Single address space shared by all processors
Processors coordinate/communicate through shared variables in memory (via loads and stores)
  Use of shared data must be coordinated via synchronization primitives (locks) that allow access to data to only one processor at a time
All multicore computers today are SMP

## Slide 21: Memory Model for Multi-threading
Can be specified in a language with MIMD support – such as OpenMP

## Slide 22: Example: Sum Reduction (1/2)
Sum 100,000 numbers on 100 processor SMP
  Each processor has ID: 0 ≤ Pn ≤ 99
  Partition 1000 numbers per processor
Step 1: Initial summation on each processor
    sum[Pn] = 0;
    for (i=1000*Pn; i<1000*(Pn+1); i++) sum[Pn] = sum[Pn] + A[i];
Step 2: Now need to add these partial sums
  Reduction: divide and conquer approach to sum
  Half the processors add pairs, then quarter, …
  Need to synchronize between reduction steps

## Slide 23: Example: Sum Reduction (2/2)
half = 100;
repeat
synch();
if (half%2 != 0 && Pn == 0)
sum[0] = sum[0] + sum[half-1];
/* When half is odd, P0 gets extra element */
half = half/2; /* dividing line on who sums */
if (Pn < half) sum[Pn] = sum[Pn] + sum[Pn+half];
until (half == 1);
This is Step 2, after all “local” sums computed.
This code runs simultaneously on all processors.
Notes: “barrier synchronization” – wait until everyone reaches that point.
% is modulus operator in C
Round 1 in repeat loop: 8/2  4, p0 = p0 + p4, p1 = p1 + p5; p2 = p2 + p6; p3 = p3 + p7;
Round 2 in repeat loop: 4/2  2, p0 = p0 + p2: p1 = p1 + p3;
Round 3 in repeat loop: 2/2  1, p0 = p0 + p1;

## Slide 24: Sum Reduction with 10 Processors
P0
P1
P2
P3
P4
P5
P6
P7
P8
P9
sum[P0]
sum[P1]
sum[P2]
sum[P3]
sum[P4]
sum[P5]
sum[P6]
sum[P7]
sum[P8]
sum[P9]
P0
P0
P1
P2
P3
P4
half = 10
half = 5
P1
half = 2
P0
half = 1
Notes: For lecture
So load balancing issue at second reduction (when half = 2)

## Slide 25
Question: Given the Sum Reduction code, are the given variables Shared data or Private data?
half = 100;
repeat
synch();
... /* handle odd elements */
half = half/2; /* dividing line */
if (Pn < half)
sum[Pn] = sum[Pn] + sum[Pn+half];
until (half == 1);
Shared Shared Shared
(A)
Shared Shared Private
(B)
Private Shared Private
(C)
Private Private Shared
(D)
half sum Pn
Notes: Reason we need half to be private is because EVERY processor is running the “half = half/2” instruction. If Shared, would hit < 1 in one pass!

## Slide 26: Agenda
Amdahl’s Law
Administrivia
Multiprocessor Systems
Multiprocessor Cache Coherence
Synchronization - A Crash Course

## Slide 27: Shared Memory and Caches
How many processors can be supported?
  Key bottleneck in an SMP is the memory system
  Caches can effectively increase memory bandwidth/open the bottleneck
But what happens to the memory being actively shared among the processors through the caches?

## Slide 28: Shared Memory and Caches (1/2)
What if?
  Processors 1 and 2 read Memory[1000] (value 20)
Processor
Processor
Processor
Cache
Cache
Cache
Interconnection Network
Memory
I/O
1000
20
1000
1000
1000
20
0
1
2

## Slide 29: Shared Memory and Caches (2/2)
What if?
  Processors 1 and 2 read Memory[1000]
  Processor 0 writes Memory[1000] with 40
Processor
Processor
Processor
Cache
Cache
Cache
Interconnection Network
Memory
I/O
0
1
2
1000 20
1000 20
Processor 0
Write
Invalidates
Other Copies
1000
1000 40
1000 40

## Slide 30: Cache Coherence (1/2)
Cache Coherence: When multiple caches access the same memory, ensure data is consistent in each local cache
  Main goal is to ensure no cache incorrectly uses an outdated value of memory
Many different implementations
  We will focus on snooping, where every cache monitors a bus (the interconnection network) that is used to broadcast activity among the caches

## Slide 31: Cache Coherence (2/2)
Snooping Idea: When any processor has a cache miss or writes to memory, notify the other processors via the bus
  If reading, multiple processors are allowed to have the most up-to-date copy
  If a processor writes, invalidate all other copies (those copies are now old)
What if many processors use the same block?
  Block can “ping-pong” between caches

## Slide 32: Implementing Cache Coherence
Cache write policies still apply
  For coherence between cache and memory
  Write-through/write-back
  Write allocate/no-write allocate
What does each cache need?
  Valid bit? Definitely!
  Dirty bit? Depends…
  New: Assign each block of a cache a state, indicating its status relative to the other caches

## Slide 33: Cache Coherence States (1/3)
The following state should be familiar to you:
Invalid: Data is not in cache
  Valid bit is set to 0
  Could still be empty or invalidated by another cache; data is not up-to-date
  This is the only state that indicates that data is NOT up-to-date

## Slide 34: Cache Coherence States (2/3)
The following states indicate sole ownership
  No other cache has a copy of the data
Modified: Data is dirty (mem is out-of-date)
  Can write to block without updating memory
Exclusive: Cache and memory both have up-to-date copy
Notes: Modified indicates a write-back policy

## Slide 35: Cache Coherence States (3/3)
The following states indicate that multiple caches have a copy of the data
Shared: One of multiple copies in caches
  Not necessarily consistent with memory
  Does not have to write to memory if block replaced (other copies in other caches)
Owned: “Main” copy of multiple in caches
  Same as Shared, but can supply data on a read instead of going to memory (can only be 1 owner)

## Slide 36: Cache Coherence Protocols
Common protocols called by the subset of caches states that they use:
  Modified
  Owned
  Exclusive
  Shared
  Invalid
e.g. MOESI, MESI, MSI, MOSI, etc.
Snooping/Snoopy Protocols
e.g. the Berkeley Ownership Protocol
See http://en.wikipedia.org/wiki/Cache_coherence

## Slide 37: Example: MOESI Transitions
You’ll see more in discussion

## Slide 38: False Sharing
One block contains both variables x and y
What happens if Processor 0 reads and writes to x and Processor 1 reads and writes to y?
  Cache invalidations even though not using the same data!
This effect is known as false sharing
How can you prevent it?
  e.g. different block size, ordering of variables in memory, processor access patterns

## Slide 39: Get To Know Your Staff
Category: Television

## Slide 40: Agenda
Amdahl’s Law
Administrivia
Multiprocessor Systems
Multiprocessor Cache Consistency
Synchronization - A Crash Course

## Slide 41: Threads
Thread of execution: Smallest unit of processing scheduled by operating system
On uniprocessor, multithreading occurs by time-division multiplexing
  Processor switches between different threads
  Context switching happens frequently enough user perceives threads as running at the same time
On a multiprocessor, threads run at the same time, with each processor running a thread

## Slide 42: Multithreading vs. Multicore (1/2)
Basic idea: Processor resources are expensive and should not be left idle
Long memory latency to memory on cache miss?
  Hardware switches threads to bring in other useful work while waiting for cache miss
  Cost of thread context switch must be much less than cache miss latency
Put in redundant hardware so don’t have to save context on every thread switch:
  PC, Registers, L1 caches?

## Slide 43: Multithreading vs. Multicore (2/2)
Multithreading => Better Utilization
  ≈1% more hardware, 1.10X better performance?
  Share integer adders, floating point adders, caches (L1 I $, L1 D$, L2 cache, L3 cache), Memory Controller
Multicore => Duplicate Processors
  ≈50% more hardware, ≈2X better performance?
  Share lower caches (L2 cache, L3 cache), Memory Controller

## Slide 44: Data Races and Synchronization
Two memory accesses form a data race if different threads access the same location, and at least one is a write, and they occur one after another
  Means that the result of a program can vary depending on chance (which thread ran first?)
  Avoid data races by synchronizing writing and reading to get deterministic behavior
Synchronization done by user-level routines that rely on hardware synchronization instructions

## Slide 45: Analogy: Buying Milk
Your fridge has no milk. You and your roommate will return from classes at some point and check the fridge
Whoever gets home first will check the fridge, go and buy milk, and return
What if the other person gets back while the first person is buying milk?
  You’ve just bought twice as much milk as you need!
It would’ve helped to have left a note…

## Slide 46: Lock Synchronization (1/2)
Use a “Lock” to grant access to a region (critical section) so that only one thread can operate at a time
  Need all processors to be able to access the lock, so use a location in shared memory as the lock
Processors read lock and either wait (if locked) or set lock and go into critical section
  0 means lock is free / open / unlocked / lock off
  1 means lock is set / closed / locked / lock on

## Slide 47: Lock Synchronization (2/2)
Pseudocode:
Check lock
Set the lock
Critical section
(e.g. change shared variables)
Unset the lock
Can loop/idle here if locked

## Slide 48: Possible Lock Implementation
Lock (a.k.a. busy wait)
  Get_lock: # $s0 -> address of lock
  addiu $t1,$zero,1 # t1 = Locked value
  Loop: lw $t0,0($s0) # load lock
  bne $t0,$zero,Loop # loop if locked
  Lock: sw $t1,0($s0) # Unlocked, so lock
Unlock
  Unlock:
sw $zero,0($s0)
Any problems with this?

## Slide 49: Possible Lock Problem
Thread 1
addiu $t1,$zero,1
Loop: lw $t0,0($s0)
bne $t0,$zero,Loop
Lock: sw $t1,0($s0)
Thread 2
addiu $t1,$zero,1
Loop: lw $t0,0($s0)
bne $t0,$zero,Loop
Lock: sw $t1,0($s0)
Time
Both threads think they have set the lock!
Exclusive access not guaranteed!

## Slide 50: Hardware Synchronization
Hardware support required to prevent an interloper (another thread) from changing the value
  Atomic read/write memory operation
  No other access to the location allowed between the read and write
How best to implement?
  Single instr? Atomic swap of register ↔ memory
  Pair of instr? One for read, one for write
Notes: Interloper thread can be from same core or another core.

## Slide 51: Synchronization in MIPS
Load linked: ll rt,off(rs)
Store conditional: sc rt,off(rs)
  Returns 1 (success) if location has not changed since the ll
  Returns 0 (failure) if location has changed
Note that sc clobbers the register value being stored (rt)!
  Need to have a copy elsewhere if you plan on repeating on failure or using value later
Notes: Here using the Green Sheet convention of rs and rt for source register and target register.

## Slide 52: Synchronization in MIPS Example
Atomic swap (to test/set lock variable)
Exchange contents of register and memory: $s4 ↔ Mem($s1)
  try: add $t0,$zero,$s4 #copy value
  ll $t1,0($s1) #load linked
  sc $t0,0($s1) #store conditional
  beq $t0,$zero,try #loop if sc fails
  add $s4,$zero,$t1 #load value in $s4
sc would fail if another threads executes sc here

## Slide 53: Test-and-Set
In a single atomic operation:
  Test to see if a memory location is set (contains a 1)
  Set it (to 1) if it isn’t (it contained a zero when tested)
  Otherwise indicate that the Set failed, so the program can try again
  While accessing, no other instruction can modify the memory location, including other Test-and-Set instructions
Useful for implementing lock operations

## Slide 54: Test-and-Set in MIPS
Example: MIPS sequence for implementing a T&S at ($s1)
  Try: addiu $t0,$zero,1
  ll $t1,0($s1)
  bne $t1,$zero,Try
  sc $t0,0($s1)
  beq $t0,$zero,try
  Locked:
  # critical section
  Unlock:
  sw $zero,0($s1)

## Slide 55: Summary
Amdahl’s Law limits benefits of parallelization
Multiprocessor systems uses shared memory (single address space)
Cache coherence implements shared memory even with multiple copies in multiple caches
  Track state of blocks relative to other caches (e.g. MOESI protocol)
  False sharing a concern
Synchronization via hardware primitives:
  MIPS does it with Load Linked + Store Conditional