## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
Combinational and Sequential Logic,
Boolean Algebra

## Slide 2: Review of Last Lecture
OpenMP as simple parallel extension to C
  During parallel fork, be aware of which variables should be shared vs. private among threads
  Work-sharing accomplished with for/sections
  Synchronization accomplished with critical/atomic/reduction
Hardware is made up of transistors and wires
  Transistors are voltage-controlled switches
  Building blocks of all higher-level blocks

## Slide 3: Great Idea #1: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
Higher-Level Language Program (e.g. C)
Assembly Language Program (e.g. MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g. block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
We are here

## Slide 4: Synchronous Digital Systems
Synchronous:
  All operations coordinated by a central clock
    “Heartbeat” of the system!
Digital:
  Represent all values with two discrete values
  Electrical signals are treated as 1’s and 0’s
    1 and 0 are complements of each other
  High/Low voltage for True/False, 1/0
Hardware of a processor, such as the MIPS, is an example of a Synchronous Digital System

## Slide 5: Signals and Waveforms: Clocks
Signals transmitted over wires continuously
Transmission is effectively instantaneous
  Implies that any wire only contains one value at any given time
Rising Edge
Falling Edge
Clock period (CPU cycle time)

## Slide 6: Signals and Waveforms
  All signals change after clock “triggers”
Stack signals on top of each other

## Slide 7: Signals and Waveforms: Grouping
A group of wires when interpreted as a bit field is called a bus
X
Clock triggers

## Slide 8: Hardware Design Hierarchy
system
datapath
control
state registers
combinational logic
multiplexer
comparator
code registers
register
logic
switching networks
Today

## Slide 9: Agenda
Combinational Logic
  Truth Tables and Logic Gates
Administrivia
Boolean Algebra
Sequential Logic
  State Elements
  Bonus: Karnaugh Maps (Optional)

## Slide 10: Type of Circuits
Synchronous Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL)
    Output is a function of the inputs only, not the history of its execution
    e.g. circuits to add A, B (ALUs)
  Sequential Logic (SL)
    Circuits that “remember” or store information
    a.k.a. “State Elements”
    e.g. memory and registers (Registers)

## Slide 11: Representations of Combinational Logic
Circuit Diagram
  Transistors and wires (Lec 17)
  Logic Gates (Lec 18)
Truth Table (Lec 18)
Boolean Expression (Lec 18)
All are equivalent
Right Now!

## Slide 12: Truth Tables
Table that relates the inputs to a CL circuit to its output
  Output only depends on current inputs
  Use abstraction of 0/1 instead of high/low V
  Shows output for every possible combination of inputs
How big?
  0 or 1 for each of N inputs
, so 2N rows

## Slide 13: CL: General Form
F
Y
A
B
C
D
0
If N inputs, how many distinct functions F do we have?
Function maps each row to 0 or 1, so 2^(2N) possible functions

## Slide 14: CL: Multiple Outputs
For 3 outputs, just three separate functions: X(A,B,C,D), Y(A,B,C,D), and Z(A,B,C,D)
  Can show functions in separate columns without adding any rows!
F
Y
A
B
C
D
X
Z

## Slide 15: Logic Gates (1/2)
Special names and symbols:
NOT
AND
OR
a | b | c
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
a | b | c
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
a | c
0 | 1
1 | 0
Circle means NOT!

## Slide 16: Logic Gates (2/2)
Special names and symbols:
NAND
NOR
XOR
a | b | c
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
a | b | c
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
a | b | c
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 17: More Complicated Truth Tables
3-Input Majority
a | b | c | y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
2-bit Adder
A |  | B |  | C |  | 
a1 | a0 | b1 | b0 | c2 | c1 | c0
 |  |  | . |  |  | 
 |  |  | . |  |  | 
 |  |  | . |  |  | 
+
c1
a1
a0
b1
b0
c2
c0
How many
rows?
3 separate functions

## Slide 18
Question: Convert the following statements into a Truth Table assuming the output is whether Justin is comfortable (1) or uncomfortable (0).
Input X: Justin wears light (0) or heavy (1) clothing
Input Y: It is cold (0) or hot (1) outside
Input Z: Justin spends the day indoors (0) or outdoors (1)
X | Y | Z | (A) | (B) | (C) | (D)
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 1 | 0 | 1 | 1

## Slide 19: My Hand Hurts…
Truth tables are huge
  Write out EVERY combination of inputs and outputs (thorough, but inefficient)
  Finding a particular combination of inputs involves scanning a large portion of the table
There must be a shorter way to represent combinational logic
  Boolean Algebra to the rescue!

## Slide 20: Agenda
Combinational Logic
  Truth Tables and Logic Gates
Administrivia
Boolean Algebra
Sequential Logic
  State Elements
Bonus: Karnaugh Maps (Optional)

## Slide 21: Administrivia
Midterm re-grade requests due tomorrow
Project 2: Matrix Multiply Performance Improvement
  Part 0: pick partner, due tonight
  Part 1: Due July 28 (this Sunday)
  Part 2: Due August 4
HW 5 also due July 31

## Slide 22: Agenda
Combinational Logic
  Truth Tables and Logic Gates
Administrivia
Boolean Algebra
Sequential Logic
  State Elements
  Bonus: Karnaugh Maps (Optional)

## Slide 23: Boolean Algebra
Represent inputs and outputs as variables
  Each variable can only take on the value 0 or 1
Overbar is NOT: “logical complement”
  e.g. if A is 0, then`A is 1 and vice-versa
Plus (+) is 2-input OR: “logical sum”
Product (·) is 2-input AND: “logical product”
  All other gates and logical expressions can be built from combinations of these (e.g. A XOR B = `AB +`BA = A’B + AB’)
For slides, will also use A’ for`A

## Slide 24: Truth Table to Boolean Expression
We can show that these are equivalent!
Read off of table
  For 1, write variable name
  For 0, write complement of variable
Sum of Products (SoP)
  Take rows with 1’s in output column, sum products of inputs
  c =`ab +`ba
Product of Sums (PoS)
  Take rows with 0’s in output column, product the sum of the complements of the inputs
  c = ( a + b ) · (`a +`b )
a | b | c
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Notes: Choice between the two generally comes down to whether the output function has more 0’s or 1’s. Choosing the conversion (SoP/PoS) with less items will result in a shorter expression!
(This example happens to be balanced: 2 0’s and 2 1’s)

## Slide 25: Manipulating Boolean Algebra
SoP and PoS expressions can still be long
  We wanted to have shorter representation than a truth table!
Boolean algebra follows a set of rules that allow for simplification
  Goal will be to arrive at the simplest equivalent expression
  Allows us to build simpler (and faster) hardware

## Slide 26: Faster Hardware?
Recall: Everything we are dealing with is just an abstraction of transistors and wires
  Inputs propagating to the outputs are voltage signals passing through transistor networks
  There is always some delay before a CL’s output updates to reflect the inputs
Simpler Boolean expressions ↔ smaller transistor networks ↔ smaller circuit delays ↔ faster hardware

## Slide 27: Combinational Logic Circuit Delay
2
3
3
4
5
10
0
1
5
13
4
6
Symbol for a bus (and width)
Combinational Logic delay

## Slide 28: Laws of Boolean Algebra
These laws allow us to perform simplification:

## Slide 29: Boolean Algebraic Simplification Example
Notes: Do on black board
From distribution: a(b +1) + c
Froms laws of 0s and 1s: b+1 = b
= ab + c
Truth Table
a b c y
0 0 0 0
0 0 1 1
0 0 1 1

## Slide 30: Circuit Simplification
(Transistors and/or Gates)
1)
2)
3)
4)

## Slide 31: Converting Combinational Logic
Circuit
Diagram
Truth
Table
Boolean
Expression
This is difficult to do efficiently!
Try all input combinations
SoP or PoS
Wire inputs to proper gates
(easiest to use AND, OR, and NOT)
Try all input
combinations
Propagate signals through gates

## Slide 32: Circuit Simplification Example (1/4)
Simplify the following circuit:
Options:
  Test all combinations of the inputs and build the Truth Table, then use SoP or PoS
  Write out expressions for signals based on gates
    Will show this method here
A
B
C
D

## Slide 33: Circuit Simplification Example (2/4)
Simplify the following circuit:
Start from left, propagate signals to the right
Arrive at D = (AB)’(A + B’C)
A
B
C
D
A
C
B’
B
A
AB
B’C
(AB)’
A+B’C

## Slide 34: Circuit Simplification Example (3/4)
Simplify Expression:
D = (AB)’(A + B’C)
= (A’ + B’)(A + B’C) DeMorgan’s
= A’A + A’B’C + B’A + B’B’C Distribution
= 0 + A’B’C + B’A + B’B’C Complementarity
= A’B’C + B’A + B’C Idempotent Law
= (A’ + 1)B’C + AB’ Distribution
= B’C + AB’ Law of 1’s
= B’(A + C) Distribution
Which of these is “simpler”?

## Slide 35: Circuit Simplification Example (4/4)
Draw out final circuit:
  D = B’C + AB’ = B’(A + C)
Simplified Circuit:
  Reduction from 6 gates to 3!
How many gates do we need for each?
4
3
A
B
C
D
Notes: Also only has to go through 2 “stages” worth of gates as opposed to 4 previously.
Longest path here is B  NOT  AND  D. Before one of the longest paths was B  NOT  AND  OR  AND  D.

## Slide 36: Karnaugh Maps (Optional)
Lots of Boolean Algebra laws for simplification
  Difficult to memorize and spot applications
  When do you know if in simplest form?
Karnaugh Maps (K-maps) are an alternate way to simplify Boolean Algebra
  This technique is normally taught in CS150
  We will never ask you to use a K-map to solve a problem, but you may find it faster/easier if you choose to learn how to use it (see Bonus Slides)

## Slide 37
Question: What is the MOST simplified Boolean Algebra expression for the following circuit?
B (A + C)
(A)
B + AC
(B)
AB + B + C
(C)
A + C
(D)

## Slide 38: Get To Know Your Staff
Category: Television

## Slide 39: Agenda
Combinational Logic
  Truth Tables and Logic Gates
Administrivia
Boolean Algebra
Sequential Logic
  State Elements
  Bonus: Karnaugh Maps (Optional)

## Slide 40: Type of Circuits
Synchronous Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL)
    Output is a function of the inputs only, not the history of its execution
    e.g. circuits to add A, B (ALUs)
  Sequential Logic (SL)
    Circuits that “remember” or store information
    a.k.a. “State Elements”
    e.g. memory and registers (Registers)

## Slide 41: Uses for State Elements
Place to store values for some amount of time:
  Register files (like in MIPS)
  Memory (caches and main memory)
Help control flow of information between combinational logic blocks
  State elements are used to hold up the movement of information at the inputs to combinational logic blocks and allow for orderly passage

## Slide 42: Accumulator Example
Want: S=0;
for X1,X2,X3 over time...
S = S + Xi
An example of why we would need to control the flow of information.
Assume:
  Each X value is applied in succession, one per cycle
  The sum since time 1 (cycle) is present on S
SUM
Xi
S

## Slide 43: First Try: Does this work?
No!
How to control the next iteration of the ‘for’ loop?
How do we say: ‘S=0’?
Feedback
X

## Slide 44: Second Try: How About This?
Rough timing …
Time
A Register is the state element that is used here to hold up the transfer of data to the adder
Delay through Register and Adder

## Slide 45: Register Internals
n instances of a “Flip-Flop”
  Output flips and flops between 0 and 1
Specifically this is a “D-type Flip-Flop”
  D is “data input”, Q is “data output”
  In reality, has 2 outputs (Q and`Q), but we only care about 1
http://en.wikibooks.org/wiki/Practical_Electronics/Flip-flops
Notes: Can see Wikipedia page for gate internals and other types of flip-flops.

## Slide 46: Flip-Flop Timing Behavior (1/2)
Edge-triggered D-type flip-flop
  This one is “positive edge-triggered”
“On the rising edge of the clock, input d is sampled and transferred to the output. At other times, the input d is ignored and the previously sampled value is retained.”
Example waveforms:

## Slide 47: Flip-Flop Timing Terminology (1/2)
Camera Analogy: Taking a photo
  Setup time: don’t move since about to take picture (open camera shutter)
  Hold time: need to hold still after shutter opens until camera shutter closes
  Time to data: time from open shutter until image appears on the output (viewfinder)

## Slide 48: Flip-Flop Timing Terminology (2/2)
Now applied to hardware:
  Setup Time: how long the input must be stable before the CLK trigger for proper input read
  Hold Time: how long the input must be stable after the CLK trigger for proper input read
  “CLK-to-Q” Delay: how long it takes the output to change, measured from the CLK trigger

## Slide 49: Flip-Flop Timing Behavior (2/2)
Edge-triggered d-type flip-flop
  This one is “positive edge-triggered”
“On the rising edge of the clock, input d is sampled and transferred to the output. At other times, the input d is ignored and the previously sampled value is retained.”

## Slide 50: Accumulator Revisited Proper Timing (2/2)
reset signal shown
Also, in practice Xi might not arrive to the adder at the same time as Si-1
Si temporarily is wrong, but register always captures correct value
In good circuits, instability never happens around rising edge of CLK
“Undefined” (unknown) signal

## Slide 51: Summary
Hardware systems are constructed from Stateless Combinational Logic and Stateful “Memory” Logic (registers)
Voltages are analog, but quantized to represent logical 0’s and 1’s
Combinational Logic: equivalent circuit diagrams, truth tables, and Boolean expressions
  Boolean Algebra allows minimization of gates
State registers implemented from Flip-flops

## Slide 52
Special Bonus Slides: You are NOT responsible for the material contained on the following slides!!! You may, however, find it useful to read anyway.
BONUS SLIDES

## Slide 53: Agenda
Combinational Logic
  Truth Tables and Logic Gates
Administrivia
Boolean Algebra
Sequential Logic
  State Elements
  Bonus: Karnaugh Maps (Optional)

## Slide 54: Karnaugh Maps (Optional)
Again, this is completely OPTIONAL material
  Recommended you use .pptx to view animations
Karnaugh Maps (K-maps) are an alternate way to simplify Boolean Algebra
  This technique is normally taught in CS150
  We will never ask you to use a K-map to solve a problem, but you may find it faster/easier if you choose to learn how to use it
For more info, see: http://en.wikipedia.org/wiki/Karnaugh_map

## Slide 55: Underlying Idea
Using Sum of Products, “neighboring” input combinations simplify
  “Neighboring”: inputs that differ by a single signal
  e.g. ab + a’b = b, a’bc + a’bc’ = a’b, etc.
  Recall: Each product only appears where there is a 1 in the output column
Idea: Let’s write out our Truth Table such that the neighbors become apparent!
  Need a Karnaugh map for EACH output

## Slide 56: Reorganizing the Truth Table
Split inputs into 2 evenly-sized groups
  One group will have an extra if an odd # of inputs
Write out all combinations of one group horizontally and all combinations of the other group vertically
  Group of n inputs → 2n combinations
  Successive combinations change only 1 input
2 Inputs: 3 Inputs:
 | 00 | 01 | 11 | 10
0 |  |  |  | 
1 |  |  |  | 
 | 0 | 1
0 |  | 
1 |  | 
A
B
AB
C
Notes: Choice of split is not essential (changes order of how you fill in values from the Truth Table).

## Slide 57: K-map: Majority Circuit (1/2)
a | b | c | y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 | 00 | 01 | 11 | 10
0 |  |  |  | 
1 |  |  |  | 
0
0
0
1
0
1
1
1
ab
c
0
0
0
0
0
1
0
1
1
1
1
1
0
1
0
1
Each row of truth table corresponds to ONE cell of Karnaugh map
Recommended you view the animation on this slide on the Powerpoint (pptx)
Note the funny jump when you go from input 011 to 100 (most mistakes made here)
Filling in the Karnaugh map:

## Slide 58: K-map: Majority Circuit (2/2)
Group neighboring 1’s so all are accounted for:
  Each group of neighbors becomes a product term in output
y =
Larger groups become smaller terms
  The single 1 in top row  abc’
  Vertical group of two 1’s  ab
  If entire lower row was 1’s  c
bc
 | 00 | 01 | 11 | 10
0 |  |  |  | 
1 |  |  |  | 
ab
c
0
0
0
1
1
1
0
1
bc
+ ab
+ ac
+ ab
+ ac
Single cell can be part of many groups

## Slide 59: General K-map Rules
Only group in powers of 2
  Grouping should be of size 2i × 2j
  Applies for both directions
Wraps around in all directions
  “Corners” case is extreme example
Always choose largest groupings possible
  Avoid single cells whenever possible
y =
 | 00 | 01 | 11 | 10
00 | 1 | 0 | 0 | 1
01 | 0 | 1 | 1 | 0
11 | 0 | 1 | 1 | 1
10 | 1 | 0 | 0 | 1
ab
cd
NOT a valid group
IS a valid group
IS a valid group
“Corners” case
1 of 2 good choices here (spot the other?)
bd
+ b’d’
+ acd