## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
MIPS CPU Datapath,
Control Introduction

## Slide 2: Review of Last Lecture
Critical path constrains clock rate
  Timing constants: setup, hold, and clk-to-q times
  Can adjust with extra registers (pipelining)
Finite State Machines examples of sequential logic circuits
  Can implement systems with Register + CL
Use MUXes to select among input
  S input bits selects one of 2S inputs
Build n-bit adder out of chained 1-bit adders
  Can also do subtraction and overflow detection!

## Slide 3: Hardware Design Hierarchy
system
datapath
control
state registers
combinational logic
multiplexer
comparator
code registers
register
logic
switching networks
Today

## Slide 4: Agenda
Processor Design
Administrivia
Datapath Overview
Assembling the Datapath
Control Introduction

## Slide 5: Five Components of a Computer
Components a computer needs to work
  Control
  Datapath
  Memory
  Input
  Output
Processor
Computer
Control
(“brain”)
Datapath
(“brawn”)
Memory
Devices
Input
Output
Notes: That is, any computer, no matter how primitive or advance, can be divided into five parts:
1) The input devices bring the data from the outside world into the computer.
2) These data are kept in the computer’s memory until...
3) The datapath request and process them.
4) The operation of the datapath is controlled by the computer’s controller.
All the work done by the computer will NOT do us any good unless we can get the data back to the outside world, so…
5) Getting the data back to the outside world is the job of the output devices.
The most COMMON way to connect these 5 components together is to use a network of busses.

## Slide 6: The Processor
Processor (CPU): Implements the instructions of the Instruction Set Architecture (ISA)
  Datapath: part of the processor that contains the hardware necessary to perform operations required by the processor (“the brawn”)
  Control: part of the processor (also in hardware) which tells the datapath what needs to be done (“the brain”)

## Slide 7: Processor Design Process
Five steps to design a processor:
  1. Analyze instruction set  datapath requirements
  2. Select set of datapath components & establish clock methodology
  3. Assemble datapath meeting the requirements
  4. Analyze implementation of each instruction to determine setting of control points that effects the register transfer
  5. Assemble the control logic
    Formulate Logic Equations
    Design Circuits
Control
Datapath
Memory
Processor
Input
Output
Now

## Slide 8: The MIPS-lite Instruction Subset
ADDU and SUBU
  addu rd,rs,rt
  subu rd,rs,rt
OR Immediate:
  ori rt,rs,imm16
LOAD and STORE Word
  lw rt,rs,imm16
  sw rt,rs,imm16
BRANCH:
  beq rs,rt,imm16
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits

## Slide 9: Register Transfer Language (RTL)
All start by fetching the instruction:
RTL gives the meaning of the instructions:
R-format: {op, rs, rt, rd, shamt, funct}  MEM[ PC ]
I-format: {op, rs, rt, imm16}  MEM[ PC ]
Inst Register Transfers
ADDU R[rd]R[rs]+R[rt]; PCPC+4
SUBU R[rd]R[rs]–R[rt]; PCPC+4
ORI R[rt]R[rs]|zero_ext(imm16); PCPC+4
LOAD R[rt]MEM[R[rs]+sign_ext(imm16)]; PCPC+4
STORE MEM[R[rs]+sign_ext(imm16)]R[rt]; PCPC+4
BEQ if ( R[rs] == R[rt] ) then PCPC+4 + (sign_ext(imm16) || 00) else PCPC+4

## Slide 10: Step 1: Requirements of the Instruction Set
Memory (MEM)
  Instructions & data (separate: in reality just caches)
  Load from and store to
Registers (32 32-bit regs)
  Read rs and rt
  Write rt or rd
PC
  Add 4 (+ maybe extended immediate)
Extender (sign/zero extend)
Add/Sub/OR unit for operation on register(s) or extended immediate
  Compare if registers equal?

## Slide 11: Generic Datapath Layout
Break up the process of “executing an instruction”
  Smaller phases easier to design and modify independently
Proj1 had 3 phases: Fetch, Decode, Execute
  Now expand Execute
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Register
Write
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

## Slide 12: Step 2: Components of the Datapath
Combinational Elements
  Gates and wires
State Elements + Clock
Building Blocks:
32
A
B
32
Y
32
Select
MUX
Multiplexer
ALU
32
32
A
B
32
Result
OP
ALU
32
32
A
B
32
Sum
CarryOut
CarryIn
Adder
Adder

## Slide 13: ALU Requirements
MIPS-lite: add, sub, OR, equality
  ADDU R[rd] = R[rs] + R[rt]; ...
  SUBU R[rd] = R[rs] – R[rt]; ...
  ORI R[rt] = R[rs] | zero_ext(Imm16)...
  BEQ if ( R[rs] == R[rt] )...
Equality test: Use subtraction and implement output to indicate if result is 0
P&H also adds AND, Set Less Than (1 if A < B, 0 otherwise)
Can see ALU from P&H C.5 (on CD)

## Slide 14: Storage Element: Idealized Memory
Memory (idealized)
  One input bus: Data In
  One output bus: Data Out
Memory access:
  Read: Write Enable = 0, data at Address is placed on Data Out
  Write: Write Enable = 1, Data In written to Address
Clock input (CLK)
  CLK input is a factor ONLY during write operation
  During read, behaves as a combinational logic block: Address valid  Data Out valid after “access time”
CLK
Data In
Write Enable
32
32
DataOut
Address

## Slide 15: Storage Element: Register
As seen in Logisim intro
  N-bit input and output buses
  Write Enable input
Write Enable:
  De-asserted (0): Data Out will not change
  Asserted (1): Data In value placed onto Data Out after CLK trigger
CLK
Data In
Write Enable
N
N
Data Out

## Slide 16: Storage Element: Register File
Register File consists of 32 registers:
  Output buses busA and busB
  Input bus busW
Register selection
  Place data of register RA (number) onto busA
  Place data of register RB (number) onto busB
  Store data on busW into register RW (number) when Write Enable is 1
Clock input (CLK)
  CLK input is a factor ONLY during write operation
  During read, behaves as a combinational logic block: RA or RB valid  busA or busB valid after “access time”
Clk
busW
Write Enable
32
32
busA
32
busB
5
5
5
RW
RA
RB
32 x 32-bit
Registers

## Slide 17: Agenda
Processor Design
Administrivia
Datapath Overview
Assembling the Datapath
Control Introduction

## Slide 18: Administrivia
HW 5 due Thursday
Project 2, Part 2 due Sunday 8/4
  Extra Credit (released tonight) also due 8/4
No lab on Thursday – work on HW/project

## Slide 19: Agenda
Processor Design
Administrivia
Datapath Overview
Assembling the Datapath
Control Introduction
Clocking Methodology

## Slide 20: Datapath Overview (1/5)
Phase 1: Instruction Fetch (IF)
  Fetch 32-bit instruction from memory
  Increment PC (PC = PC + 4)
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Register
Write
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

## Slide 21: Datapath Overview (2/5)
Phase 2: Instruction Decode (ID)
  Read the opcode and appropriate fields from the instruction
  Gather all necessary registers values from Register File
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Register
Write
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

## Slide 22: Datapath Overview (3/5)
Phase 3: Execute (EX)
  ALU performs operations: arithmetic (+,-,*,/), shifting, logical (&,|), comparisons (slt,==)
  Also calculates addresses for loads and stores
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Register
Write
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

## Slide 23: Datapath Overview (4/5)
Phase 4: Memory Access (MEM)
  Only load and store instructions do anything during this phase; the others remain idle or skip this phase
  Should hopefully be fast due to caches
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Register
Write
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

## Slide 24: Datapath Overview (5/5)
Phase 5: Register Write (WB for “write back”)
  Write the instruction result back into the Register File
  Those that don’t (e.g. sw, j, beq) remain idle or skip this phase
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Register
Write
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

## Slide 25: Why Five Stages?
Could we have a different number of stages?
  Yes, and other architectures do
So why does MIPS have five if instructions tend to idle for at least one stage?
  The five stages are the union of all the operations needed by all the instructions
  There is one instruction that uses all five stages: load (lw/lb)

## Slide 26: Agenda
Processor Design
Administrivia
Datapath Overview
Assembling the Datapath
Control Introduction

## Slide 27: Step 3: Assembling the Datapath
Assemble datapath to meet RTL requirements
  Exact requirements will change based on ISA
  Here we will examine each instruction of MIPS-lite
The datapath is all of the hardware components and wiring necessary to carry out ALL of the different instructions
  Make sure all components (e.g. RegFile, ALU) have access to all necessary signals and buses
  Control will make sure instructions are properly executed (the decision making)

## Slide 28: Datapath by Instruction
All instructions: Instruction Fetch (IF)
  Fetch the Instruction: Mem[PC]
  Update the program counter:
    Sequential Code: PC  PC + 4
    Branch and Jump: PC  “something else”
Next Address
Logic
32
Instruction
Address
Instruction
Memory
PC
CLK

## Slide 29: Datapath by Instruction
All instructions: Instruction Decode (ID)
  Pull off all relevant fields from instruction to make available to other parts of datapath
    MIPS-lite only has R-format and I-format
    Control will sort out the proper routing (discussed later)
Wires and
Splitters
32
Instr
5
5
5
5
6
16
6
opcode
rs
rt
rd
shamt
funct
imm

## Slide 30: Step 3: Add & Subtract
ADDU R[rd]R[rs]+R[rt];
Hardware needed:
  Instruction Mem and PC (already shown)
  Register File (RegFile) for read and write
  ALU for add/subtract
CLK
busW
32
32
busA
32
busB
5
5
5
RW
RA
RB
32 x 32-bit
Registers
32
Result
ALU
32
A
32
B

## Slide 31: Step 3: Add & Subtract
ADDU R[rd]R[rs]+R[rt];
Connections:
  RegFile and ALU Inputs
  Connect RegFile and ALU
  RegWr (1) and ALUctr (ADD/SUB) set by control in ID
32
Result
CLK
busW
32
32
busA
32
busB
5
5
5
RW
RA
RB
32 x 32-bit
Registers
ALUctr
RegWr
rs
rt
rd
ALU
32
A
32
B

## Slide 32: Step 3: Or Immediate
ORI R[rt]R[rs]|zero_ext(Imm16);
Is the hardware below sufficient?
  Zero extend imm16?
  Pass imm16 to input of ALU?
  Write result to rt?
32
Result
CLK
busW
32
32
busA
32
busB
5
5
5
RW
RA
RB
32 x 32-bit
Registers
ALUctr
RegWr
rs
rt
rd
ALU

## Slide 33: Step 3: Or Immediate
ORI R[rt]R[rs]|zero_ext(Imm16);
Add new hardware:
  Still support add/sub
  New control signals: RegDst, ALUSrc
32
ALUctr
CLK
RegWr
32
32
busA
32
busB
5
5
RW
RA
RB
RegFile
rs
rt
rt
rd
ZeroExt
32
16
imm16
ALUSrc
0
1
0
1
ALU
5
RegDst
2:1 MUX
How to implement this?

## Slide 34: Step 3: Load
LOAD R[rt]MEM[R[rs]+sign_ext(Imm16)];
Hardware sufficient?
  Sign extend imm16?
  Where’s MEM?
32
ALUctr
CLK
RegWr
32
32
busA
32
busB
5
5
RW
RA
RB
RegFile
rs
rt
rt
rd
ZeroExt
32
16
imm16
ALUSrc
0
1
0
1
ALU
5
RegDst

## Slide 35: Step 3: Load
LOAD R[rt]MEM[R[rs]+sign_ext(Imm16)];
New control signals: ExtOp, MemWr, MemtoReg
32
ALUctr
CLK
busW
RegWr
32
32
busA
32
busB
5
5
RW
RA
RB
RegFile
rs
rt
rt
rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
CLK
Data In
32
MemWr
0
1
0
1
ALU
0
1
WrEn
Addr
Data
Memory
5
???
Must now also handle sign extension
What goes here during a store?

## Slide 36: Step 3: Store
STORE MEM[R[rs]+sign_ext(Imm16)]R[rt];
Connect busB to Data In (no extra control needed!)
32
ALUctr
CLK
busW
RegWr
32
32
busA
32
busB
5
5
RW
RA
RB
RegFile
rs
rt
rt
rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
CLK
Data In
32
MemWr
0
1
0
1
ALU
0
1
WrEn
Addr
Data
Memory
5

## Slide 37: Step 3: Branch If Equal
BEQ if(R[rs]==R[rt]) then PCPC+4 + (sign_ext(Imm16) || 00)
Need comparison output from ALU
32
ALUctr
CLK
busW
RegWr
32
32
busA
32
busB
5
5
RW
RA
RB
RegFile
rs
rt
rt
rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
CLK
Data In
32
MemWr
0
1
0
1
ALU
0
1
WrEn
Addr
Data
Memory
5
zero
=

## Slide 38: Step 3: Branch If Equal
Next Address
Logic
32
Instruction
Address
Instruction
Memory
PC
CLK
BEQ if(R[rs]==R[rt]) then PCPC+4 + (sign_ext(Imm16) || 00)
Revisit “next address logic”:
imm16
CLK
PC
4
PC Ext
Adder
Adder
MUX
0
1
32
Instruction
Addr
Instruction
Memory
Instr Fetch Unit
???
nPC_sel
zero
How to hook these up?
Sign extend and ×4

## Slide 39: Step 3: Branch If Equal
BEQ if(R[rs]==R[rt]) then PCPC+4 + (sign_ext(Imm16) || 00)
Revisit “next address logic”:
  nPC_sel should be 1 if branch, 0 otherwise
nPC_sel
MUX
0
1
zero
MUX
PC+4
PC+4 + branchAddr
nextPC (nPC)
nPC_sel | zero | MUX
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
How does this change if we add bne?

## Slide 40: Step 3: Branch If Equal
BEQ if(R[rs]==R[rt]) then PCPC+4 + (sign_ext(Imm16) || 00)
Revisit “next address logic”:
imm16
CLK
PC
4
PC Ext
Adder
Adder
MUX
0
1
32
Instruction
Addr
Instruction
Memory
Instr Fetch Unit
nPC_sel
zero

## Slide 41: Get To Know Your Staff
Category: Movies

## Slide 42: Agenda
Processor Design
Administrivia
Datapath Overview
Assembling the Datapath
Control Introduction

## Slide 43: Processor Design Process
Five steps to design a processor:
  1. Analyze instruction set  datapath requirements
  2. Select set of datapath components & establish clock methodology
  3. Assemble datapath meeting the requirements
  4. Analyze implementation of each instruction to determine setting of control points that effects the register transfer
  5. Assemble the control logic
    Formulate Logic Equations
    Design Circuits
Control
Datapath
Memory
Processor
Input
Output
Now

## Slide 44: Control
Need to make sure that correct parts of the datapath are being used for each instruction
  Have seen control signals in datapath used to select inputs and operations
  For now, focus on what value each control signal should be for each instruction in the ISA
    Next lecture, we will see how to implement the proper combinational logic to implement the control

## Slide 45: Desired Datapath For addu
32
ALUctr=?
CLK
busW
RegWr=?
32
32
busA
32
busB
5
5
RW
RA
RB
rs
rt
rt
rd
RegDst=?
Extender
32
16
imm16
ALUSrc=?
ExtOp=?
MemtoReg=?
CLK
Data In
32
MemWr=?
0
1
RegFile
0
1
ALU
0
1
Data
Memory
WrEn
Addr
5
zero
=
Instruction <31:0>
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rt
rs
nPC_sel=?
Instr
Fetch
Unit
CLK
R[rd]R[rs]+R[rt];
32
ALUctr=?
CLK
busW
RegWr=?
32
32
busA
32
busB
5
5
RW
RA
RB
rs
rt
rt
rd
RegDst=?
Extender
32
16
imm16
ALUSrc=?
ExtOp=?
MemtoReg=?
CLK
Data In
32
MemWr=?
0
1
RegFile
0
1
ALU
0
1
Data
Memory
WrEn
Addr
5
zero
=
Instruction <31:0>
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rt
rs
nPC_sel=?
Instr
Fetch
Unit
CLK
nPC_sel=?
RegDst=?
RegWr=?
ExtOp=?
ALUSrc=?
ALUctr=?
MemWr=?
MemtoReg=?
+4
1
1
ADD
0
0
0
X

## Slide 46: Desired Datapath For ori
R[rt]R[rs]|ZeroExt(imm16);
32
ALUctr=?
CLK
busW
RegWr=?
32
32
busA
32
busB
5
5
RW
RA
RB
rs
rt
rt
rd
RegDst=?
Extender
32
16
imm16
ALUSrc=?
ExtOp=?
MemtoReg=?
CLK
Data In
32
MemWr=?
0
1
RegFile
0
1
ALU
0
1
Data
Memory
WrEn
Addr
5
zero
=
Instruction <31:0>
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rt
rs
nPC_sel=?
Instr
Fetch
Unit
CLK
32
ALUctr=?
CLK
busW
RegWr=?
32
32
busA
32
busB
5
5
RW
RA
RB
rs
rt
rt
rd
RegDst=?
Extender
32
16
imm16
ALUSrc=?
ExtOp=?
MemtoReg=?
CLK
Data In
32
MemWr=?
0
1
RegFile
0
1
ALU
0
1
Data
Memory
WrEn
Addr
5
zero
=
Instruction <31:0>
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rt
rs
nPC_sel=?
Instr
Fetch
Unit
CLK
+4
0
1
OR
0
0
1
Zero

## Slide 47: Desired Datapath For load
R[rt]MEM{R[rs]+SignExt[imm16]};
32
ALUctr=?
CLK
busW
RegWr=?
32
32
busA
32
busB
5
5
RW
RA
RB
rs
rt
rt
rd
RegDst=?
Extender
32
16
imm16
ALUSrc=?
ExtOp=?
MemtoReg=?
CLK
Data In
32
MemWr=?
0
1
RegFile
0
1
ALU
0
1
Data
Memory
WrEn
Addr
5
zero
=
Instruction <31:0>
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rt
rs
nPC_sel=?
Instr
Fetch
Unit
CLK
32
ALUctr=?
CLK
busW
RegWr=?
32
32
busA
32
busB
5
5
RW
RA
RB
rs
rt
rt
rd
RegDst=?
Extender
32
16
imm16
ALUSrc=?
ExtOp=?
MemtoReg=?
CLK
Data In
32
MemWr=?
0
1
RegFile
0
1
ALU
0
1
Data
Memory
WrEn
Addr
5
zero
=
Instruction <31:0>
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rt
rs
nPC_sel=?
Instr
Fetch
Unit
CLK
+4
0
1
ADD
1
0
1
Sign

## Slide 48: Desired Datapath For store
MEM{R[rs]+SignExt[imm16]}R[rt];
32
ALUctr=?
CLK
busW
RegWr=?
32
32
busA
32
busB
5
5
RW
RA
RB
rs
rt
rt
rd
RegDst=?
Extender
32
16
imm16
ALUSrc=?
ExtOp=?
MemtoReg=?
CLK
Data In
32
MemWr=?
0
1
RegFile
0
1
ALU
0
1
Data
Memory
WrEn
Addr
5
zero
=
Instruction <31:0>
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rt
rs
nPC_sel=?
Instr
Fetch
Unit
CLK
32
ALUctr=?
CLK
busW
RegWr=?
32
32
busA
32
busB
5
5
RW
RA
RB
rs
rt
rt
rd
RegDst=?
Extender
32
16
imm16
ALUSrc=?
ExtOp=?
MemtoReg=?
CLK
Data In
32
MemWr=?
0
1
RegFile
0
1
ALU
0
1
Data
Memory
WrEn
Addr
5
zero
=
Instruction <31:0>
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rt
rs
nPC_sel=?
Instr
Fetch
Unit
CLK
+4
X
0
ADD
X
1
1
Sign

## Slide 49: Desired Datapath For beq
BEQ if(R[rs]==R[rt]) then PCPC+4 + (sign_ext(Imm16) || 00)
32
ALUctr=?
CLK
busW
RegWr=?
32
32
busA
32
busB
5
5
RW
RA
RB
rs
rt
rt
rd
RegDst=?
Extender
32
16
imm16
ALUSrc=?
ExtOp=?
MemtoReg=?
CLK
Data In
32
MemWr=?
0
1
RegFile
0
1
ALU
0
1
Data
Memory
WrEn
Addr
5
zero
=
Instruction <31:0>
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rt
rs
nPC_sel=?
Instr
Fetch
Unit
CLK
32
ALUctr=?
CLK
busW
RegWr=?
32
32
busA
32
busB
5
5
RW
RA
RB
rs
rt
rt
rd
RegDst=?
Extender
32
16
imm16
ALUSrc=?
ExtOp=?
MemtoReg=?
CLK
Data In
32
MemWr=?
0
1
RegFile
0
1
ALU
0
1
Data
Memory
WrEn
Addr
5
zero
=
Instruction <31:0>
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rt
rs
nPC_sel=?
Instr
Fetch
Unit
CLK
Br
X
0
SUB
X
0
0
X

## Slide 50: MIPS-lite Datapath Control Signals
ExtOp: 0  “zero”; 1  “sign”
ALUsrc: 0  busB; 1  imm16
ALUctr: “ADD”, “SUB”, “OR”
nPC_sel: 0  +4; 1  branch
MemWr: 1  write memory
MemtoReg: 0  ALU; 1  Mem
RegDst: 0  “rt”; 1  “rd”
RegWr: 1  write register
32
ALUctr
CLK
busW
RegWr
32
32
busA
32
busB
5
5
RW
RA
RB
rs
rt
rt
rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
CLK
Data In
32
MemWr
0
1
RegFile
0
1
ALU
0
1
Data
Memory
WrEn
Addr
5
zero
=
nPC_sel
Instr
Fetch
Unit
CLK

## Slide 51
When not in use, parts of the datapath cease to carry a value.
(A)
Adding the instruction jr will not change the datapath.
(B)
All control signals will be don’t care (‘X’) in at least one instruction.
(C)
Adding the instruction addiu will not change the datapath.
(D)
Question: Which statement is TRUE about the MIPS-lite ISA?

## Slide 52: Summary (1/2)
Five steps to design a processor:
  Analyze instruction set  datapath requirements
  Select set of datapath components & establish clock methodology
  Assemble datapath meeting the requirements
  Analyze implementation of each instruction to determine setting of control points that effects the register transfer
  Assemble the control logic
    Formulate Logic Equations
    Design Circuits
Control
Datapath
Memory
Processor
Input
Output

## Slide 53: Summary (2/2)
Determining control signals
  Any time a datapath element has an input that changes behavior, it requires a control signal (e.g. ALU operation, read/write)
  Any time you need to pass a different input based on the instruction, add a MUX with a control signal as the selector (e.g. next PC, ALU input, register to write to)
Your datapath and control signals will change based on your ISA