## Slide 1: CS 61C: Great Ideas in Computer Architecture Lecture 10: Finite State Machines, Functional Units
Instructor: Sagar Karandikar
sagark@eecs.berkeley.edu
http://inst.eecs.berkeley.edu/~cs61c

## Slide 2: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions

## Slide 3: Type of Circuits
Synchronous Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL) circuits
    Output is a function of the inputs only, not the history of its execution
    E.g., circuits to add A, B (ALUs)
  Sequential Logic (SL)
    Circuits that “remember” or store information
    aka “State Elements”
    E.g., memories and registers (Registers)

## Slide 4: Uses for State Elements
Place to store values for later re-use:
  Register files (like $1-$31 in MIPS)
  Memory (caches and main memory)
Help control flow of information between combinational logic blocks
  State elements hold up the movement of information at input to combinational logic blocks to allow for orderly passage

## Slide 5: Accumulator Example
Want: S=0;
for (i=0;i<n;i++)
S = S + Xi
Why do we need to control the flow of information?
Assume:
  Each X value is applied in succession, one per cycle
  After n cycles the sum is present on S
SUM
Xi
S

## Slide 6: First Try: Does this work?
No!
Reason #1: How to control the next iteration of the ‘for’ loop?
Reason #2: How do we say: ‘S=0’?
We’ll go through a working version in more detail today
Feedback
Notes: Like if you write y = y + 1 as a math formula (NOT an assignment in C)

## Slide 7: Model for Synchronous Systems
Collection of Combinational Logic blocks separated by registers
Feedback is optional
Clock signal(s) connects only to clock input of registers
Clock (CLK): steady square wave that synchronizes the system
Register: several bits of state that samples on rising edge of CLK (positive edge-triggered) or falling edge (negative edge-triggered)

## Slide 8: Register Internals
n instances of a “Flip-Flop”
Flip-flop name because the output flips and flops between 0 and 1
D is “data input”, Q is “data output”
Also called “D-type Flip-Flop”

## Slide 9: Flip-Flop Operation
Edge-triggered d-type flip-flop
  This one is “positive edge-triggered”
“On the rising edge of the clock, the input d is sampled and transferred to the output. At all other times, the input d is ignored.”
Example waveforms:

## Slide 10: Flip-Flop Timing
Edge-triggered d-type flip-flop
  This one is “positive edge-triggered”
“On the rising edge of the clock, the input d is sampled and transferred to the output. At all other times, the input d is ignored.”
Example waveforms (more detail):

## Slide 11: Camera Analogy Timing Terms
Want to take a portrait – timing right before and after taking picture
Set up time – don’t move since about to take picture (open camera shutter)
Hold time – need to hold still after shutter opens until camera shutter closes
Time click to data – time from open shutter until can see image on output (viewscreen)

## Slide 12: Hardware Timing Terms
Setup Time: when the input must be stable before the edge of the CLK
Hold Time: when the input must be stable after the edge of the CLK
“CLK-to-Q” Delay: how long it takes the output to change, measured from the edge of the CLK

## Slide 13: Accumulator Timing 1/2
Reset input to register is used to force it to all zeros (takes priority over D input).
Si-1 holds the result of the ith-1 iteration.
Analyze circuit timing starting at the output of the register.

## Slide 14: Accumulator Timing 2/2
Reset signal shown
Also, in practice X might not arrive to the adder at the same time as Si-1
Si temporarily is wrong, but register always captures correct value.
In good circuits, instability never happens around rising edge of clk.

## Slide 15: Accumulator Logisim Demo

## Slide 16: Maximum Clock Frequency
What is the maximum frequency of this circuit?
Max Delay = CLK-to-Q Delay + CL Delay + Setup Time
Hint:
Frequency = 1/Period

## Slide 17: Critical Paths
Timing…
Note: delay of 1 clock cycle from input to output.
Clock period limited by propagation delay of adder/shifter.

## Slide 18: Pipelining to improve performance
Timing…
Insertion of register allows higher clock frequency.
More outputs per second (higher bandwidth)
But each individual result takes longer (greater latency)

## Slide 19: Recap of Timing Terms
Clock (CLK) - steady square wave that synchronizes system
Setup Time - when the input must be stable before the rising edge of the CLK
Hold Time - when the input must be stable after the rising edge of the CLK
“CLK-to-Q” Delay - how long it takes the output to change, measured from the rising edge of the CLK
Flip-flop - one bit of state that samples every rising edge of the CLK (positive edge-triggered)
Register - several bits of state that samples on rising edge of CLK or on LOAD (positive edge-triggered)

## Slide 20: Clickers/Peer Instruction
What is maximum clock frequency? (assume all unconnected inputs come from some register)
A: 5 GHz
B: 200 MHz
C: 500 MHz
D: 1/7 GHz
E: 1/6 GHz
Clock->Q 1ns
Setup 1ns
Hold 1ns
AND delay 1ns

## Slide 21: Administrivia
HW2 out
  We recommend doing this before the midterm
Proj 2-1 out
  Make sure you test your code on hive machines, that’s where we’ll grade them
  Team registration problems? Email Jay

## Slide 22: Administrivia
Midterm this Thursday
  In this room, at this time
  One 8.5”x11” handwritten cheatsheet
  We’ll provide a MIPS green sheet
  No electronics
  Covers up to and including the 07/02 lecture
  Review session slides posted on Piazza

## Slide 23: Break

## Slide 24: Finite State Machines (FSM) Intro
A convenient way to conceptualize computation over time
We start at a state and given an input, we follow some edge to another (or the same) state
The function can be represented with a “state transition diagram”.
With combinational logic and registers, any FSM can be implemented in hardware.

## Slide 25: FSM Example: 3 ones…
Draw the FSM…
FSM to detect the occurrence of 3 consecutive 1’s in the input.
Assume state transitions are controlled by the clock:
on each clock cycle the machine checks the inputs and moves to a new state and produces a new output…

## Slide 26: Hardware Implementation of FSM
+
=
?
… Therefore a register is needed to hold the a representation of which state the machine is in. Use a unique bit pattern for each state.
Combinational logic circuit is used to implement a function maps from present state and input to next state and output.

## Slide 27: FSM Combinational Logic
1
00
1
10
0
00
0
10
0
10
1
01
0
00
0
01
0
01
1
00
0
00
0
00
Output
NS
Input
PS
Truth table…
Specify CL using a truth table.

## Slide 28: Moving between Representations
Truth Table
Gate Diagram
Boolean Expression
Sum of Products,
Product of Sums Methods
Enumerate Inputs
Enumerate Inputs
Use Equivalency between boolean operators and gates
Use this table and techniques we learned last time (and later in discussion) to transform between alternative views of same logic function

## Slide 29: Building Standard Functional Units
Data multiplexers
Arithmetic and Logic Unit
Adder/Subtractor

## Slide 30: Data Multiplexer (“Mux”) (here 2-to-1, n-bit-wide)
Notes: draw the truth table

## Slide 31: N instances of 1-bit-wide mux
How many rows in TT?

## Slide 32: How do we build a 1-bit-wide mux?

## Slide 33: 4-to-1 multiplexer?
How many rows in TT?

## Slide 34: Another way to build 4-1 mux?
Hint: NCAA tourney!
Ans: Hierarchically!

## Slide 35: Arithmetic and Logic Unit
Most processors contain a special logic block called the “Arithmetic and Logic Unit” (ALU)
We’ll show you an easy one that does ADD, SUB, bitwise AND, bitwise OR

## Slide 36: Our simple ALU

## Slide 37: Clicker Question
Convert the truth table to a boolean expression using sum of products (no need to simplify):
A: F = xy + x(~y)
B: F = xy + (~x)y + (~x)(~y)
C: F = xy + (~x)y
D: F = (~x)y + x(~y)
x | y | F(x,y)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 38: In the News: Microsoft, Google beat Humans at Image Recognition (EE Times)
On ImageNet benchmark image database, systems from Microsoft and Google performed better than humans at recognizing images
Both companies used deep artificial neural networks to train on image database
NVIDIA is a sponsor of the annual ImageNet Challenge, and supplies access to arrays of its graphic processing units (GPUs) to all contestants. Microsoft did use Nvidia GPUs, but bought and configured their own supercomputer using them to simulate parametric rectified linear neural units to become the "1st to beat a human" at image classification.

## Slide 39: Break

## Slide 40: How to design Adder/Subtractor?
Truth-table, then determine canonical form, then minimize and implement as we’ve seen before
Look at breaking the problem down into smaller pieces that we can cascade or hierarchically layer

## Slide 41: Adder/Subtractor – One-bit adder LSB…

## Slide 42: Adder/Subtractor – One-bit adder (1/2)…

## Slide 43: Adder/Subtractor – One-bit adder (2/2)

## Slide 44: N 1-bit adders  1 N-bit adder
What about overflow?
Overflow = cn?
+
+
+
b0

## Slide 45: Extremely Clever Subtractor
x | y | XOR(x,y)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
+
+
+
XOR serves as conditional inverter!

## Slide 46: Clicker Question pt. 2
Convert the truth table to a boolean expression using product of sums (no need to simplify):
A: F = (x+y)(~x+y)
B: F = (x+y)(~x+~y)
C: F = (~x+y)(x+y)(~x+~y)
D: F = (~x+~y)(~x+y)(x+~y)(x+y)
x | y | F(x,y)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 47: In Conclusion
Finite State Machines have clocked state elements plus combinational logic to describe transition between states
Standard combinational functional unit blocks built hierarchically from subcomponents
Tomorrow: We’ll build a CPU