## Slide 1: CS 61C: Great Ideas in Computer Architecture Lecture 20: Thread-Level Parallelism (TLP) and OpenMP Part 2
Instructor: Sagar Karandikar
sagark@eecs.berkeley.edu
http://inst.eecs.berkeley.edu/~cs61c

## Slide 2: Review: Symmetric Multiprocessing
Processor 0
Control
Datapath
PC
Registers
(ALU)
Memory
Input
Output
Bytes
I/O-Memory Interfaces
Processor 0 Memory Accesses
Processor 1
Control
Datapath
PC
Registers
(ALU)
Processor 1 Memory Accesses

## Slide 3: Review
Sequential software is slow software
  SIMD and MIMD only path to higher performance
Multithreading increases utilization, Multicore more processors (MIMD)
Synchronization
  atomic read-modify-write using load-linked/store-conditional
OpenMP as simple parallel extension to C
  Threads, Parallel for, private, critical sections, …
  ≈ C: small so easy to learn, but not very high level and it’s easy to get into trouble

## Slide 4: Review: OpenMP Directives (Work-Sharing)
Shares iterations of a loop across the threads
Each section is executed by a separate thread
Serializes the execution of a thread
These are defined within a parallel section
Notes: A work-sharing construct divides the execution of the enclosed code region among the members of the team that encounter it.

## Slide 5: Review: Parallel Statement Shorthand
#pragma omp parallel
{
#pragma omp for
for(i=0;i<len;i++) { … }
}
can be shortened to:
#pragma omp parallel for
for(i = 0; i < len; i++) { … }
This is the only directive in the parallel section

## Slide 6: Review: Building Block: for loop
for (i=0; i<max; i++) zero[i] = 0;
Break for loop into chunks, and allocate each chunk to a separate thread
  e.g. if max = 100 with 2 threads: assign 0-49 to thread 0, and 50-99 to thread 1
Must have relatively simple “shape” for an OpenMP-aware compiler to be able to parallelize it
  Necessary for the run-time system to be able to determine how many of the loop iterations to assign to each thread
No premature exits from the loop allowed
  i.e. No break, return, exit, goto statements
In general, don’t jump outside of any pragma block
Notes: “Shape” restrictions: The FOR loop can not be a DO WHILE loop, or a loop without loop control. Also, the loop iteration variable must be an integer and the loop control parameters must be the same for all threads.

## Slide 7: Review: Parallel for pragma
#pragma omp parallel for
for (i=0; i<max; i++) zero[i] = 0;
Master thread creates additional threads, each with a separate execution context
All variables declared outside for loop are shared by default, except for loop index which is private per thread (Why?)
Implicit synchronization at end of for loop
Divide index regions sequentially per thread
  Thread 0 gets 0, 1, …, (max/n)-1;
  Thread 1 gets max/n, max/n+1, …, 2*(max/n)-1
  Why?

## Slide 8: Review: Matrix Multiply in OpenMP
start_time = omp_get_wtime();
#pragma omp parallel for private(tmp, i, j, k)
for (i = 0; i < Mdim; i++){
for (j = 0; j < Ndim; j++){
tmp = 0.0;
for(k = 0; k < Pdim; k++){
/* C(i,j) = sum(over k) A(i,k) * B(k,j)*/
tmp += A[i*Pdim + k] * B[k*Ndim + j];
}
C[i*Ndim + j] = tmp;
}
}
run_time = omp_get_wtime() - start_time;
Outer loop spread across N threads; inner loops inside a single thread

## Slide 9: Review: Synchronization in MIPS
Load linked: ll rt,off(rs)
Store conditional: sc rt,off(rs)
  Returns 1 (success) if location has not changed since the ll
  Returns 0 (failure) if location has changed
Note that sc clobbers the register value being stored (rt)!
  Need to have a copy elsewhere if you plan on repeating on failure or using value later
Notes: Here using the Green Sheet convention of rs and rt for source register and target register.

## Slide 10: New: OpenMP Directives (Synchronization)
These are defined within a parallel section
master
  Code block executed only by the master thread (all other threads skip)
critical
  Code block executed by only one thread at a time
atomic
  Specific memory location must be updated atomically (like a mini-critical section for writing to memory)
  Applies to single statement, not code block

## Slide 11: What’s wrong with this code?
double compute_sum(double *a, int a_len) {
double sum = 0.0;
#pragma omp parallel for
for (int i = 0; i < a_len; i++) {
sum += a[i];
}
return sum;
}

## Slide 12: Sample use of critical
double compute_sum(double *a, int a_len) {
double sum = 0.0;
#pragma omp parallel for
for (int i = 0; i < a_len; i++) {
#pragma omp critical
sum += a[i];
}
return sum;
}
Notes: but we’ve essentially serialized the computation!

## Slide 13: Where are the caches?
Processor 0
Control
Datapath
PC
Registers
(ALU)
Memory
Input
Output
Bytes
I/O-Memory Interfaces
Processor 0 Memory Accesses
Processor 1
Control
Datapath
PC
Registers
(ALU)
Processor 1 Memory Accesses

## Slide 14: Multiprocessor Caches
Memory is a performance bottleneck even with one processor
Use caches to reduce bandwidth demands on main memory
Each core has a local private cache holding data it has accessed recently
Only cache misses have to access the shared common memory
Processor
Processor
Processor
Cache
Cache
Cache
Interconnection Network
Memory
I/O
Notes: Power has become the overriding issue for both data centers and microprocessors. Power efficiency has joined scalable performance making the case for multiprocessors. Multiprocessors also improve availability.

## Slide 15: Shared Memory and Caches
What if?
  Processors 1 and 2 read Memory[1000] (value 20)
Processor
Processor
Processor
Cache
Cache
Cache
Interconnection Network
Memory
I/O
1000
20
1000
1000
1000
20
0
1
2

## Slide 16: Shared Memory and Caches
Now:
  Processor 0 writes Memory[1000] with 40
Processor
Processor
Processor
Cache
Cache
Cache
Interconnection Network
Memory
I/O
0
1
2
1000 20
1000 20
1000
1000 40
1000 40
Problem?

## Slide 17: Keeping Multiple Caches Coherent
Architect’s job: shared memory => keep cache values coherent
Idea: When any processor has cache miss or writes, notify other processors via interconnection network
  If only reading, many processors can have copies
  If a processor writes, invalidate any other copies
Write transactions from one processor “snoop” tags of other caches using common interconnect
  Invalidate any “hits” to same address in other caches
  If hit is to dirty line, other cache has to write back first!

## Slide 18: Shared Memory and Caches
Example, now with cache coherence
  Processors 1 and 2 read Memory[1000]
  Processor 0 writes Memory[1000] with 40
Processor
Processor
Processor
Cache
Cache
Cache
Interconnection Network
Memory
I/O
0
1
2
1000 20
1000 20
Processor 0
Write
Invalidates
Other Copies
1000
1000 40
1000 40

## Slide 19: Clickers/Peer Instruction: Which statement is true?
A: Using write-through caches removes the need for cache coherence
B: Every processor store instruction must check contents of other caches
C: Most processor load and store accesses only need to check in local private cache
D: Only one processor can cache any memory location at one time

## Slide 20: Administrivia
Project 3-2 Out
HW5 Out – Performance Programming
Guerrilla Section on Performance Programming on Thursday, 5-7pm, Woz

## Slide 21: Administrivia
Midterm 2 is tomorrow!
  In this room, at this time
  Two double-sided 8.5”x11” handwritten cheatsheets
  We’ll provide a MIPS green sheet
  No electronics
  Covers up to and including 07/21 lecture
  Review session slides on Piazza

## Slide 22: Break

## Slide 23: Cache Coherency Tracked by Block
Suppose block size is 32 bytes
Suppose Processor 0 reading and writing variable X, Processor 1 reading and writing variable Y
Suppose in X location 4000, Y in 4012
What will happen?
Processor 0
Processor 1
4000
4000
4004
4008
4012
4016
4028
Tag
32-Byte Data Block
Cache 0
Cache 1
Memory

## Slide 24: Coherency Tracked by Cache Line
Block ping-pongs between two caches even though processors are accessing disjoint variables
Effect called false sharing
How can you prevent it?

## Slide 25: Understanding Cache Misses: The 3Cs
Compulsory (cold start or process migration, 1st reference):
  First access to a block in memory impossible to avoid; small effect for long running programs
  Solution: increase block size (increases miss penalty; very large blocks could increase miss rate)
Capacity:
  Cache cannot contain all blocks accessed by the program
  Solution: increase cache size (may increase access time)
Conflict (collision):
  Multiple memory locations mapped to the same cache location
  Solution 1: increase cache size
  Solution 2: increase associativity (may increase access time)
Notes: (Capacity miss) That is the cache misses are due to the fact that the cache is simply not large enough to contain all the blocks that are accessed by the program.
The solution to reduce the Capacity miss rate is simple: increase the cache size.
Here is a summary of other types of cache miss we talked about.
First is the Compulsory misses. These are the misses that we cannot avoid. They are caused when we first start the program.
Then we talked about the conflict misses. They are the misses that caused by multiple memory locations being mapped to the same cache location.
There are two solutions to reduce conflict misses. The first one is, once again, increase the cache size. The second one is to increase the associativity.
For example, say using a 2-way set associative cache instead of directed mapped cache.
But keep in mind that cache miss rate is only one part of the equation. You also have to worry about cache access time and miss penalty. Do NOT optimize miss rate alone.
Finally, there is another source of cache miss we will not cover today. Those are referred to as invalidation misses caused by another process, such as IO , update the main memory so you have to flush the cache to avoid inconsistency between memory and cache.
+2 = 43 min. (Y:23)

## Slide 26: Rules for Determining Miss Type for a Given Access Pattern in 61C
1) Compulsory: A miss is compulsory if and only if it results from accessing the data for the first time. If you have ever brought the data you are accessing into the cache before, it's not a compulsory miss, otherwise it is.
2) Conflict: A conflict miss is a miss that's not compulsory and that would have been avoided if the cache was fully associative. Imagine you had a cache with the same parameters but fully-associative (with LRU). If that would've avoided the miss, it's a conflict miss.
3) Capacity: This is a miss that would not have happened with an infinitely large cache. If your miss is not a compulsory or conflict miss, it's a capacity miss.
Notes: In order to determine what kind of miss you are dealing with, you can first check 1, then 2 and then 3. The type of your miss is the first of these definitions that applies. Note that making the capacity infinitely large also eliminates conflict misses, which is why you should check whether it is a conflict miss first.

## Slide 27: Fourth “C” of Cache Misses: Coherence Misses
Misses caused by coherence traffic with other processor
Also known as communication misses because represents data moving between processors working together on a parallel program
For some parallel programs, coherence misses can dominate total misses

## Slide 28: π
3. 141592653589793238462643383279502884197169399375105820974944592307816406286208998628034825342117067982148086513282306647093844609550582231725359408128481117450284102…

## Slide 29: Calculating π

## Slide 30: Sequential Calculation of π in C
#include <stdio.h> /* Serial Code */
static long num_steps = 100000;
double step;
void main () {
int i;
double x, pi, sum = 0.0;
step = 1.0/(double)num_steps;
for (i = 1; i <= num_steps; i++) {
x = (i - 0.5) * step;
sum = sum + 4.0 / (1.0 + x*x);
}
pi = sum / num_steps;
printf ("pi = %6.12f\n", pi);
}

## Slide 31: OpenMP Version (with bug)
#include <omp.h>
#define NUM_THREADS 2
static long num_steps = 100000; double step;
void main () {
int i; double x, pi, sum[NUM_THREADS];
step = 1.0/(double) num_steps;
#pragma omp parallel private (x)
{
int id = omp_get_thread_num();
for (i=id, sum[id]=0.0; i< num_steps; i=i+NUM_THREADS)
{
x = (i+0.5)*step;
sum[id] += 4.0/(1.0+x*x);
}
}
for(i=0, pi=0.0; i<NUM_THREADS; i++)
pi += sum[i];
printf ("pi = %6.12f\n", pi / num_steps);
}

## Slide 32: Experiment
Run with NUM_THREADS = 1 multiple times
Run with NUM_THREADS = 2 multiple times
What happens?

## Slide 33: OpenMP Version (with bug)
#include <omp.h>
#define NUM_THREADS 2
static long num_steps = 100000; double step;
void main () {
int i; double x, pi, sum[NUM_THREADS];
step = 1.0/(double) num_steps;
#pragma omp parallel private (x)
{
int id = omp_get_thread_num();
for (i=id, sum[id]=0.0; i< num_steps; i=i+NUM_THREADS)
{
x = (i+0.5)*step;
sum[id] += 4.0/(1.0+x*x);
}
}
for(i=0, pi=0.0; i<NUM_THREADS; i++)
pi += sum[i];
printf ("pi = %6.12f\n", pi / num_steps);
}
Note: loop index variable i is shared between threads

## Slide 34: Sum Reduction
Sum 100,000 numbers on 100 processor SMP
  Each processor has ID: 0 ≤ Pn ≤ 99
  Partition 1000 numbers per processor
  Initial summation on each processor [Phase I]
  Aka, “the map phase”
  sum[Pn] = 0;
  for (i = 1000*Pn; i < 1000*(Pn+1); i = i + 1) sum[Pn] = sum[Pn] + A[i];
Now need to add these partial sums [Phase II]
  Reduction: divide and conquer in “the reduce phase”
  Half the processors add pairs, then quarter, …
  Need to synchronize between reduction steps

## Slide 35: Example: Sum Reduction
Second Phase:
After each processor has computed its “local” sum
This code runs simultaneously on each core
half = 100;
repeat
synch();
/* Proc 0 sums extra element if there is one */
if (half%2 != 0 && Pn == 0)
sum[0] = sum[0] + sum[half-1];
half = half/2; /* dividing line on who sums */
if (Pn < half) sum[Pn] = sum[Pn] + sum[Pn+half];
until (half == 1);

## Slide 36: An Example with 10 Processors
P0
P1
P2
P3
P4
P5
P6
P7
P8
P9
sum[P0]
sum[P1]
sum[P2]
sum[P3]
sum[P4]
sum[P5]
sum[P6]
sum[P7]
sum[P8]
sum[P9]
half = 10
Notes: For class handout

## Slide 37: An Example with 10 Processors
P0
P1
P2
P3
P4
P5
P6
P7
P8
P9
sum[P0]
sum[P1]
sum[P2]
sum[P3]
sum[P4]
sum[P5]
sum[P6]
sum[P7]
sum[P8]
sum[P9]
P0
P0
P1
P2
P3
P4
half = 10
half = 5
P1
half = 2
P0
half = 1
if (half%2 != 0 && Pn == 0)
sum[0] = sum[0] + sum[half-1];
Notes: For lecture
So load balancing issue at second reduction (when half = 2)

## Slide 38: OpenMP Reduction
Reduction: specifies that 1 or more variables that are private to each thread are subject of reduction operation at end of parallel region: reduction(operation:var) where
  Operation: operator to perform on the variables (var) at the end of the parallel region
  Var: One or more variables on which to perform scalar reduction.
#pragma omp for reduction(+ : nSum)
for (i = START ; i <= END ; ++i) nSum += i;

## Slide 39: OpenMP Reduction Version
#include <omp.h>
#include <stdio.h>
static long num_steps = 100000;
double step;
void main () {
int i; double x, pi, sum = 0.0;
step = 1.0/(double) num_steps;
#pragma omp parallel for private(x) reduction(+:sum)
for (i = 1; i <= num_steps; i++){
x = (i-0.5)*step;
sum = sum + 4.0/(1.0+x*x);
}
pi = sum / num_steps;
printf ("pi = %6.8f\n", pi);
}
Note: Don’t have to declare for loop index variable i private, since that is default

## Slide 40: OpenMP Pitfalls
Unfortunately, we can’t just throw pragmas on everything 
  Data dependencies
  Sharing issues (incorrectly marking private vars as non-private)
  Updating shared values
  Parallel Overhead

## Slide 41: OpenMP Pitfall #1: Data Dependencies
Consider the following code:
  a[0] = 1;
  for(i=1; i<5000; i++)
  a[i] = i + a[i-1];
There are dependencies between loop iterations!
  Splitting this loop between threads does not guarantee in-order execution
  Out of order loop execution will result in undefined behavior (i.e. likely wrong result)

## Slide 42: Open MP Pitfall #2: Sharing Issues
Consider the following loop:
#pragma omp parallel for
for(i=0; i<n; i++){
temp = 2.0*a[i];
a[i] = temp;
b[i] = c[i]/temp;
}
temp is a shared variable!
#pragma omp parallel for private(temp)
for(i=0; i<n; i++){
temp = 2.0*a[i];
a[i] = temp;
b[i] = c[i]/temp;
}

## Slide 43: OpenMP Pitfall #3: Updating Shared Variables Simultaneously
Now consider a global sum:
for(i=0; i<n; i++)
sum = sum + a[i];
This can be done by surrounding the summation by a critical/atomic section or reduction clause:
#pragma omp parallel for reduction(+:sum)
{
for(i=0; i<n; i++)
sum = sum + a[i];
}
  Compiler can generate highly efficient code for reduction

## Slide 44: OpenMP Pitfall #4: Parallel Overhead
Spawning and releasing threads results in significant overhead
Better to have fewer but larger parallel regions
  Parallelize over the largest loop that you can (even though it will involve more work to declare all of the private variables and eliminate dependencies)

## Slide 45: OpenMP Pitfall #4: Parallel Overhead
start_time = omp_get_wtime();
for (i=0; i<Ndim; i++){
for (j=0; j<Mdim; j++){
tmp = 0.0;
#pragma omp parallel for reduction(+:tmp)
for( k=0; k<Pdim; k++){
/* C(i,j) = sum(over k) A(i,k) * B(k,j)*/
tmp += *(A+(i*Ndim+k)) * *(B+(k*Pdim+j));
}
*(C+(i*Ndim+j)) = tmp;
}
}
run_time = omp_get_wtime() - start_time;
Too much overhead in thread generation to have this statement run this frequently.
Poor choice of loop to parallelize.

## Slide 46: And in Conclusion:
Multiprocessor/Multicore uses Shared Memory
  Cache coherency implements shared memory even with multiple copies in multiple caches
  False sharing a concern; watch block size!
OpenMP as simple parallel extension to C
  Threads, Parallel for, private, critical sections, reductions …
  ≈ C: small so easy to learn, but not very high level and it’s easy to get into trouble