## Slide 1: CS 61C: Great Ideas in Computer Architecture Lecture 28: Course Summary and Wrap-Up
Instructor: Sagar Karandikar
sagark@eecs.berkeley.edu
http://inst.eecs.berkeley.edu/~cs61c

## Slide 2: New School CS61C (1/3)
Personal Mobile Devices

## Slide 3: New School CS61C (2/3)

## Slide 4: New School CS61C (3/3)

## Slide 5: Old Machine Structures
CS61C
I/O system
Processor
Compiler
Operating
System
(Mac OSX)
Application (ex: browser)
Digital Design
Circuit Design
Instruction Set
Architecture
Datapath & Control
transistors
Memory
Hardware
Software
Assembler

## Slide 6: New-School Machine Structures (It’s a bit more complicated!)
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates functioning in parallel at same time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Leverage Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Project 1, 2
Lab 13
Project 4
Project 3

## Slide 7: CS61c is NOT about C Programming
It’s about the hardware-software interface
  What does the programmer need to know to achieve the highest possible performance
Languages like C are closer to the underlying hardware, unlike languages like Python!
  Allows us to talk about key hardware features in higher level terms
  Allows programmer to explicitly harness underlying hardware parallelism for high performance: “programming for performance”

## Slide 8: Great Ideas in Computer Architecture
Design for Moore’s Law
Abstraction to Simplify Design
Make the Common Case Fast
Dependability via Redundancy
Memory Hierarchy
Performance via Parallelism/Pipelining/Prediction

## Slide 9: Powers of Ten inspired 61C Overview
Going Top Down cover 3 Views
Architecture (when possible)
Physical Implementation of that architecture
Programming system for that architecture and implementation (when possible)
See http://www.powersof10.com/film

## Slide 10: Earth
107 meters

## Slide 11: The Dalles, Oregon
104 meters

## Slide 12: The Dalles, Oregon
104 meters

## Slide 13: Google’s Oregon WSC
103 meters

## Slide 14: Google’s Oregon WSC
104 meters
103 meters
102 meters
10 kilometers

## Slide 15: Google Warehouse
90 meters by 75 meters, 10 Megawatts
Contains 40,000 servers, 190,000 disks
Power Utilization Effectiveness: 1.23
  85% of 0.23 overhead goes to cooling losses
  15% of 0.23 overhead goes to power losses
Contains 45, 40-foot long containers
  8 feet x 9.5 feet x 40 feet
30 stacked as double layer, 15 as single layer

## Slide 16: Containers in WSCs
102 meters
100 meters

## Slide 17: Google Container
101 meters

## Slide 18: Google Container
2 long rows, each with 29 racks
Cooling below raised floor
Hot air returned behind racks
100 meters
10 meters

## Slide 19: Equipment Inside a Container
Server (in rack format):
7 foot Rack: servers + Ethernet local area network switch in middle (“rack switch”)
Array (aka cluster): server racks + larger local area network switch (“array switch”) 10X faster => cost 100X: cost f(N2)

## Slide 20: Google Rack
Google rack with 20 servers + Network Switch in the middle
48-port 1 Gigabit/sec Ethernet switch every other rack
Array switches connect to racks via multiple 1 Gbit/s links
2 datacenter routers connect to array switches over 10 Gbit/s links
100 meters
1 meter

## Slide 21: Programming WSC: Word Count in Spark’s Python API
// RDD: primary abstraction of a distributed collection of items
file = sc.textFile(“hdfs://…”)
// Two kinds of operations:
// Actions: RDD  Value
// Transformations: RDD  RDD
// e.g. flatMap, Map, reduceByKey
file.flatMap(lambda line: line.split())
.map(lambda word: (word, 1))
.reduceByKey(lambda a, b: a + b)

## Slide 22: Great Ideas in Computer Architecture
Design for Moore’s Law
  -- WSC, Container, Rack
Abstraction to Simplify Design
Make the Common Case Fast
Dependability via Redundancy
  -- Multiple WSCs, Multiple Racks, Multiple Switches
Memory Hierarchy
Performance via Parallelism/Pipelining/Prediction
  -- Task level Parallelism, Data Level Parallelism

## Slide 23: Google Server Internals
Google Server
10-1 meters
10 centimeters
Notes: Most companies buy servers from the likes of Dell, Hewlett-Packard, IBM, or Sun Microsystems. But Google, which has hundreds of thousands of servers and considers running them part of its core expertise, designs and builds its own. Ben Jai, who designed many of Google's servers, unveiled a modern Google server before the hungry eyes of a technically sophisticated audience.
Google's big surprise: each server has its own 12-volt battery to supply power if there's a problem with the main source of electricity. The company also revealed for the first time that since 2005, its data centers have been composed of standard shipping containers--each with 1,160 servers and a power consumption that can reach 250 kilowatts.
It may sound geeky, but a number of attendees--the kind of folks who run data centers packed with thousands of servers for a living--were surprised not only by Google's built-in battery approach, but by the fact that the company has kept it secret for years. Jai said in an interview that Google has been using the design since 2005 and now is in its sixth or seventh generation of design.
Read more: http://news.cnet.com/8301-1001_3-10209580-92.html#ixzz0yo8bhTOH

## Slide 24: Google Board Details
Supplies only 12 volts
Battery per board vs. large battery room
  Improves PUE: 99.99% efficient local battery vs 94% for battery room
2 SATA Disk Drives
  1 Terabyte capacity each
  3.5 inch disk drive
  7200 RPM
2 AMD Opteron Microprocessors
  Dual Core, 2.2 GHz
8 DIMMs
  8 GB DDR2 DRAM
1 Gbit/sec Ethernet Network Interface Card

## Slide 25: Programming Multicore Microprocessor: OpenMP
#include <omp.h>
#include <stdio.h>
static long num_steps = 100000;
int value[num_steps];
int reduce()
{ int i; int sum = 0;
#pragma omp parallel for private(x) reduction(+:sum)
for (i=1; i<= num_steps; i++){
sum = sum + value[i];
}
}

## Slide 26: Great Ideas in Computer Architecture
Design for Moore’s Law
-- More transistors = Multicore + SIMD
2. Abstraction to Simplify Design
3. Make the Common Case Fast
Dependability via Redundancy
Memory Hierarchy
  -- More transistors = Cache Memories
6. Performance via Parallelism/Pipelining/ Prediction
  -- Thread-level Parallelism

## Slide 27: AMD Opteron Microprocessor
10-2 meters
centimeters

## Slide 28: AMD Opteron Microarchitecture
72 physical registers

## Slide 29: AMD Opteron Pipeline Flow
For integer operations
  12 stages (Floating Point is 17 stages)
  Up to 106 RISC-ops in progress

## Slide 30: AMD Opteron Block Diagram
AGU
AGU
Int Decode & Rename
FADD
FMISC
FMUL
44-entry
Load/Store
Queue
36-entry FP scheduler
FP Decode & Rename
ALU
AGU
ALU
MULT
ALU
Res
Res
Res
L1
Icache
64B
L1
Dcache
64KB
Fetch
Branch
Prediction
Instruction Control Unit (72 entries)
Fastpath
Microcode Engine
Scan/Align/Decode
µops
Notes: AGU = Address Generation Unit specialized for that for power, area, etc.

## Slide 31: AMD Opteron Microprocessor
10-2 meters
centimeters

## Slide 32: AMD Opteron Core
10-3 meters
millimeters

## Slide 33: Programming One Core: C with Intrinsics
void mmult(int n, float *A, float *B, float *C)
{
for ( int i = 0; i < n; i+=4 )
for ( int j = 0; j < n; j++ )
{
__m128 c0 = _mm_load_ps(C+i+j*n);
for( int k = 0; k < n; k++ )
c0 = _mm_add_ps(c0, _mm_mul_ps(_mm_load_ps(A+i+k*n), _mm_load1_ps(B+k+j*n)));
_mm_store_ps(C+i+j*n, c0);
}
}

## Slide 34: Inner loop from gcc –O -S
Assembly snippet from innermost loop:
          movaps (%rax), %xmm9
          mulps %xmm0, %xmm9
          addps %xmm9, %xmm8
          movaps 16(%rax), %xmm9
          mulps %xmm0, %xmm9
          addps %xmm9, %xmm7
          movaps 32(%rax), %xmm9
          mulps %xmm0, %xmm9
          addps %xmm9, %xmm6
          movaps 48(%rax), %xmm9
          mulps %xmm0, %xmm9
          addps %xmm9, %xmm5

## Slide 35: Great Ideas in Computer Architecture
Design for Moore’s Law
Abstraction to Simplify Design
  -- Instruction Set Architecture, Micro-operations
Make the Common Case Fast
Dependability via Redundancy
Memory Hierarchy
Performance via Parallelism/Pipelining/Prediction
  -- Instruction-level Parallelism (superscalar, pipelining)
  -- Data-level Parallelism

## Slide 36: SIMD Adder
Four 32-bit adders that operate in parallel
  Data Level Parallelism

## Slide 37: One 32-bit Adder

## Slide 38: 1 bit of 32-bit Adder

## Slide 39: Complementary MOS Transistors (NMOS and PMOS) of NAND Gate
3v
X
Y
0v
Z
x
y
z
0 volts
3 volts
0 volts
3 volts
0 volts
0 volts
3 volts
3 volts
3 volts
3 volts
3 volts
0 volts
NAND gate
Notes: Bottom
X = 0v Y = 0V both closed on top in series, so Z = 3v
X = 0v Y = 0V both open bottom
X = 0v Y = 3V 1st open on top,
X = 0v Y = 3V 2nd in series closed, so Z = 0v
X = 3v Y = 0V 2nd open on top
X = 3v Y = 0V 2nd in series closed, so Z = 0v
X = 3v Y = 3V both open on top
X = 3v Y = 3V both closed, so Z = 0v

## Slide 40: Physical Layout of NAND Gate
10-7 meters
100 nanometers

## Slide 41: Scanning Electron Microscope
10-7 meters
Cross Section
Top View
100 nanometers

## Slide 42: Block Diagram of Static RAM
10-6 meters

## Slide 43: 1 Bit SRAM in 6 Transistors
Notes: The core of this cell is formed by the four transistors M1 to M4 which form two cross-coupled inverters. They have two stable states, representing 0 and 1 respectively. The state is stable as long as power on Vdd is available.
If access to the state of the cell is needed the word access line WL is raised. This makes the state of the cell immediately available for reading on BL and BL. If the cell state must be overwritten the BL and BL lines are first set to the desired values and then WL is raised. Since the outside drivers are stronger than the four transistors (M1 through M4) this allows the old state to be overwritten.

## Slide 44: Physical Layout of SRAM Bit
10-7 meters
100 nanometers

## Slide 45: SRAM Cross Section
10-7 meters
100 nanometers

## Slide 46: DIMM Module
DDR = Double Data Rate
  Transfers bits on Falling AND Rising Clock Edge
Has Single Error Correcting, Double Error Detecting Redundancy (SEC/DED)
  72 bits to store 64 bits of data
  Uses “Chip kill” organization so that if single DRAM chip fails can still detect failure
Average server has 22,000 correctable errors and 1 uncorrectable error per year

## Slide 47: DRAM Bits
10-6 meters
1 micron

## Slide 48: DRAM Cell in Transistors

## Slide 49: Physical Layout of DRAM Bit

## Slide 50: Cross Section of DRAM Bits
10-7 meters
100 nanometers

## Slide 51: AMD Dependability
• L1 cache data is SEC/DED protected
• L2 cache and tags are SEC/DED protected
• DRAM is SEC/DED protected with chipkill
• On-chip and off-chip ECC protected arrays include autonomous, background hardware scrubbers
• Remaining arrays are parity protected
– Instruction cache, tags and TLBs
– Data tags and TLBs
– Generally read only data that can be recovered from lower levels

## Slide 52: Programming Memory Hierarchy: Cache Blocked Algorithm
The blocked version of the i-j-k algorithm is written simply as (A,B,C are submatricies of a, b, c)
for (i=0;i<N/r;i++)
for (j=0;j<N/r;j++)
for (k=0;k<N/r;k++)
C[i][j] += A[i][k]*B[k][j]
  r = block (sub-matrix) size (Assume r divides N)
  X[i][j] = a sub-matrix of X, defined by block row i and block column j

## Slide 53: Great Ideas in Computer Architecture
Design for Moore’s Law
  -- Higher capacities caches and DRAM
Abstraction to Simplify Design
Make the Common Case Fast
Dependability via Redundancy
-- Parity, SEC/DEC
5. Memory Hierarchy
  -- Caches, TLBs
Performance via Parallelism/Pipelining/Prediction
-- Data-level Parallelism

## Slide 54: Course Summary
As the field changes, cs61c had to change too!
It is still about the software-hardware interface
  Programming for performance!
  Parallelism: Task-, Thread-, Instruction-, and Data- MapReduce, OpenMP, C, SSE instrinsics
  Understanding the memory hierarchy and its impact on application performance
Interviewers ask what you did this semester!

## Slide 55: Administrivia
No more assignments!
Upcoming Lecture Schedule
  8/11: Summary, What’s Next? (+ HKN reviews)
    Project 4 Competition Winners Announced
    (Today)
  8/12: No Lecture, I’ll have OH in this room
Notes: disc/lab next week

## Slide 56: Administrivia
Final Exam is this Thursday (8/13)
  9am-12pm, 10 Evans
  Three 8.5”x11”, double-sided, handwritten cheat-sheets
  Broken into MT1 section, MT2 section, and post-MT2 section (so that the clobber can be applied)
  Review slides posted on Piazza
Extra OH - see Piazza post
Labs today are final checkoffs + OH
Discussions tomorrow are OH

## Slide 57: Competition Prize Presentation

## Slide 58: What Next? Classes
Welcome to the upper-div!
CS150/EE141 (fall) if you liked digital systems design or transistor-level design
CS152 (spring) if you liked computer architecture
CS162 (operating systems and system programming) for more low-level software
CS164 for C.A.L.L.
CS161 for security

## Slide 59: What Next?
Architecture research at Berkeley:
https://eecs.berkeley.edu/Research/Areas/ARC/
Build real chips!
Become a CS61C Staff Member!
General path:
  Lab Assistant to Reader or Tutor to TA
Lab Assistants earn credit
Readers/Tutors are paid
TAs are paid + tuition + units
CS61C Fa15: Currently 668 enrolled

## Slide 60: Thanks to all Staff!
TAs:
Nathaniel Mailoa (Head TA)
Jay Patel (Head TA)
Derek Ahmed
Rebecca Herman
Harrison Wang
Jeffrey Wettstein
Tutors:
Brenton Chu
Nicolas Stone
Alex Sung
Austin Tai
Michelle Tsai
Readers:
Dasheng Chen
Molly Zhai