## Slide 1: Answers to Questions from Lecture 4
Q1: How old is the cyclotron resonance method of determining the effective mass of electrons and holes in semiconductors?
A1: The first successful cyclotron resonance experiments on germanium (Ge) were published in 1953 by Dresselhaus, Kip and Kittel of the Physics Dept. at UC Berkeley.
Soon afterwards (in 1954) Lax, Zeiger, and Rosenblum of MIT Lincoln Lab reported further measurements for Ge.
By 1955 both the Berkeley and Lincoln groups reported work on silicon.
[G. Dresselhaus, A. F. Kip, and C. Kittel, “Cyclotron Resonance of Electrons and Holes in Silicon and Germanium Crystals,” Physical Review, Vol. 98, p. 368, 1955.]
Lecture 4 supplement, Slide 1
EE130/230A Fall 2013

## Slide 2: Question re: Slide 11
Q2: Why is the effective mass of electrons much smaller in GaAs as compared to Si?
A2: The atomic "cores" of Ga and As are much larger than that of Si and hence exert more influence on conduction electrons moving about within the lattice (ref. Lecture 2 Slide 9).
Lecture 4 supplement, Slide 2
EE130/230A Fall 2013

## Slide 3: Question re: Slide 14
Q3: What is phonon density and why is it proportional to temperature?
A3: Phonons (lattice vibrations) have quantized frequencies and modes, with associated energy levels (“states”). Since total vibration energy increases proportionately with temperature, the probability of finding a phonon in a higher-energy state increases; hence the number of phonons increases with temperature – and the average time between lattice-scattering events decreases.
Lecture 4 supplement, Slide 3
EE130/230A Fall 2013

## Slide 4: Question re: Slide 19
Question: Why does the drift velocity saturate at high electric field strength?
Answer:
As the electric field strength increases, the force that it exerts on a charge carrier between scattering events increases and hence the carrier gains more kinetic energy. When the kinetic energy of a carrier reaches the energy of an optical phonon (~60 meV in silicon), it will generate an optical phonon upon a lattice collision event and lose all of its kinetic energy in the process. Hence optical phonon scattering limits the drift velocity at high electric field strength; the saturation velocity (vsat) is defined as this limit.
Additional notes:
Atoms vibrate about their equilibrium positions within the semiconductor crystal lattice. Acoustic phonons are coherent movements of atoms, i.e. adjacent atoms move together; optical phonons are out-of-phase movements of atoms, i.e. adjacent atoms move in opposite directions.
The carrier mobility is defined as the ratio of drift velocity (vd) to electric field strength (E). As E increases and vd approaches (and reaches) vsat, the mobility decreases because E /vd decreases with increasing E.
Lecture 4 supplement, Slide 4
EE130/230A Fall 2013