UNIVERSITY OF CALIFORNIA

College of Engineering

Department of Electrical Engineering and Computer Sciences

EECS 130 							      Professor Chenming Hu

Spring 2006

HOMEWORK SET NO. 4

Due: Thursday, 26th February, 2006

Problem 1:

Applying the depletion approximation to a linearly graded junction with Nd – Na = ax, derive expressions for

- the electric field distribution,

- the potential distribution,

- the built-in potential, and

- the depletion-layer width.

Problem 2:

Consider the following silicon P-N junction:

- If Na = 5(1016cm-3 in the P-region and Nd = 1(1017cm-3 in the N-region, under increasing reverse bias, which region (N or P) will become completely depleted first?  What is the reverse bias at this condition?  (Hint:  use Naxp  = Ndxn.  The doping densities of P+ and N+ are immaterial).

- Repeat part (a) with Na =  1(1016cm-3 and Nd = 1(1017cm-3.

- What are the small-signal capacitances (F/cm²) at the bias conditions in (a) and (b)?

Problem 3:

Consider a P+N junction diode with Nd = 1016cm-3 in the N-region. . τp is given to be 1 μsec.

- Determine the diffusion length L on the N-type side.

- What are the excess hole density and excess electron density at the depletion layer edge on the N-type side under (i) equilibrium and (ii) forward bias           V = 0.4V?

Problem 4:

Consider a silicon abrupt (step) PN-junction diode with uniform cross section and constant doping on either side of the junction.  The diode is made from 1(-cm P-type and 0.2(-cm N-type materials in which the recombination lifetimes are (n = 10-6s and (p = 10-8s, respectively.

- What is the value of the built-in-voltage?

- Calculate the density of the minority carriers at the edge of the depletion layer when the applied voltage is 0.589V (Which is 23 ( kT/q).

- Sketch the majority and minority carrier current as functions of distance from the junction on both sides of the junction, under the bias voltage of part (b).

- Calculate the location(s) of the plane (or planes) at which the minority-carrier and majority-carrier currents are equal in magnitude.

# Text boxes

P+

P

N

N+

1.2 (m

0.4 (m