UNIVERSITY OF CALIFORNIA

College of Engineering

Department of Electrical Engineering and Computer Sciences

EECS 130 							      Professor Chenming Hu

Spring 2006

HOMEWORK SET NO. 6

Due: Friday, 3rd March, 2006

**Before the Tuesday lecture, please review Sec. 5.1 through 5.4

1.      (a)	Solve Eq. 5.2.2 and Eq.5.3.1 for (s as a function of Vg.

- Find an expression for Vox as a function of Vg.

- Make a rough sketch of (s versus Vg and Vox versus Vg for –3V ( Vg ( 2V,

Vfb= =-0.9V, Na = 1017cm-3 and Tox = 3nm.

- Find Wdep as a function of Vg.

  - The figure below shows the total charge per unit area in the P-type Si as a function of Vg for an MOS capacitor at 300K.

- What is the oxide thickness?

- What is the doping concentration in Si?

- Find the voltage drop in oxide (Vox) when Vg – Vfb = -1V.

- Find the band bending in Si when Vg – Vfb = 0.5V.

  - Consider an MOS capacitor fabricated on P-type Si substrate with a doping of 5(1016cm-3 with oxide thickness of 10nm and N+ poly gate.

- Find Cox, Vfb and Vt.

- Find the accumulation charge (C/cm2) at Vg = Vfb - 1V.

- Find the depletion and inversion charge at Vg = 2V.

(d)	Plot the total substrate charge as a function of Vg for Vg from –2 to 2V.

4.	Answer the following question based on the C-V curve for an MOS capacitor shown

below.  The area of the capacitor is 104 µm2.  At E, C is 50pF

- Is the substrate doping N-type or P-type?

- What is the thickness of the oxide in the MOS capacitor?

- What is the doping concentration of the substrate, Nsub?

- What is the value of the capacitance at position C on the C-V curve shown above?

- Sketch the energy band diagram of the MOS structure at position A, B, C, D and E on the C-V curve.

- At location B on the C-V curve, what is the band bending, (s?

# Text boxes

-1

Qs(coul/cm2)

Vg-Vfb(V)

1

2

4(10-7

-5(10-8

-4.5(10-7

D

B

A

C

E

C(pF)

-1

0

0.5

1

Vg(V)

QS CV

HF CV