UNIVERSITY OF CALIFORNIA

College of Engineering

Department of Electrical Engineering and Computer Sciences

EE 130/230M	Prof. Liu & Dr. Xu

Spring 2013

Homework Assignment #13

Due at the beginning of class on Thursday, 5/2/13

Problem 1:  BJT Current Components and Output Characteristics

Consider a Si npn BJT with emitter area A = 10-7 cm2, maintained at room temperature (T = 300K), with parameters for each of the regions as shown in the table below:

| Parameter | Emitter | Base | Collector |
| --- | --- | --- | --- |
| Dopant concentration (cm-3) | 1018 (n-type) | 1017 (p-type) | 1015 (n-type) |
| Width (m) | 0.5 | 0.5 | 2.0 |
| Minority-carrier lifetime (s) | 10-7 | 10-6 | 10-5 |

Note that the emitter region and collector region are each short, so that

and

Note that the base region is short, so that

and

- Suppose that the BJT is biased at the edge of saturation:  the emitter junction is forward biased such that exp(qVBE/kT) = 1010, and the base-collector junction is zero biased (i.e. VBC = 0V).  Ignore band-gap narrowing in the emitter.  Calculate(, (T and (dc

(Note that you’ll first need to calculate the quasi-neutral emitter width W'E , quasi-neutral base width W, and quasi-neutral collector width W'C, then calculate IEp, IEn, ICp, and ICn)

- Sketch the output characteristic (IC vs. VCE) for 0 < VCE < 3 V and label it with the value of IB (from part (a)).  Is the effect of base width modulation significant?  Explain why or why not.

- How would your answers to parts (a) and (b) change if VBE were to be increased to double the value of IB?

Problem 2:  Ebers-Moll Model

When one of the BJT terminals is left floating (unconnected), the BJT behaves like a diode.  Consider a pnp BJT configured as shown:

Derive the I vs. VA relationship for this “diode” using the Ebers-Moll equations.  (I should be expressed only in terms of VA and the Ebers-Moll parameters.)

Problem 3:  BJT ( Deviations from the Ideal

Consider the npn Si BJT in Problem 1, with the emitter junction forward biased such that exp(qVBE/kT) = 1010.  Calculate

- What is the value of the Early voltage, VA?

Note: You should use the value of CJC (units F/cm2) for VBC = 0V.

- What is the punchthrough voltage (VCE = VCB + VBE for which the quasi-neutral base width W = 0)?

- Estimate the breakdown voltage VCEO using the formula

where VCBO is the reverse breakdown voltage of the base-collector pn junction.  Assume

that the critical electric field for avalanche breakdown of the base-collector junction is

5(105 V/cm.

- Based of your answers in parts (b) and (c), will punchthrough be observed in the common-emitter output characteristics (IC vs. VCE plot) before breakdown?

Problem 4: Gummel Plot

Generate a standard Gummel plot (log(IC) and log(IB) vs. VBE) showing non-ideal effects at very low current and very high current.  Indicate qualitatively how this plot would change for the cases below.  (Assume the common emitter d.c. current gain dc  is 100 for moderate current, recombination in the base is negligible, and that current due to holes collected into the base from the collector are negligible.)

- base doping increases by 10×

- emitter doping increases by 10×

- base width decreases by 50%

- temperature increases by 50(C