UNIVERSITY OF CALIFORNIA

College of Engineering

Department of Electrical Engineering and Computer Sciences

EE 130/230M	Prof. Liu & Dr. Xu

Spring 2013

Homework Assignment #14

Due at the beginning of class on Thursday, 5/9/13

(Note: This assignment is optional, i.e. for extra credit.)

Problem 1: BJT small-signal model

Suppose an incremental emitter current ie is applied to a BJT under active bias with quiescent (DC) current IE0 and base-emitter bias voltage VBE so that IE = IE0 + ie.  Using the simplified hybrid-pi circuit model shown below, show that the time

is required to bring the base-emitter voltage to a new steady-state value.  This is one of the delays that affects the unity-gain frequencyof a BJT.

(Hint: Apply Kirchoff’s current law to obtain a differential equation for vbe, and find the solution by applying appropriate boundary conditions for vbe at t = 0 and t(()

Problem 2: Base transit time and BJT transient response

Consider an ideal Si npn BJT maintained at 300K with uniform base doping 1017 cm-3, quasi-neutral base width 0.25m, minority-carrier lifetime in the base B = 10 ns, operating at the edge of saturation (VBC = 0V), at a collector current IC of 1 mA.

- Calculate the base transit time (t).

- Calculate the excess minority-carrier charge stored in the base (QB).  How will QB change as the BJT is biased into the active region (i.e. as VBC is increased), with VBE held constant?

- Suppose the BJT is operating in the active mode and the base current is suddenly doubled at time t = 0.  Derive an expression for collector current IC(t) for t > 0.

- Does a BJT switch off more quickly if it is biased in the active mode vs. the saturation mode?  Explain briefly.

Problem 3: Advanced MOSFET structures

- Why are thin-body MOSFET structures advantageous for channel-length (L) scaling as well as supply-voltage (VDD) scaling?  (Hint: Note that the drain-to-body pn junction capacitance is significantly reduced.)

- The thin-body MOSFET structure (TSi < 10 nm) is often referred to as a “fully depleted” MOSFET.  Why is this the case?  (Hint: The dopant concentration in the body region typically is less than 1018 cm-3.)

- What is the primary advantage of a multiple-gate (double-gate or tri-gate) thin-body MOSFET structure over a single-gate thin-body MOSFET structure?