UNIVERSITY OF CALIFORNIA

College of Engineering

Department of Electrical Engineering and Computer Sciences

EE 130/230M	Prof. Liu & Dr. Xu

Spring 2013

Solution to Homework Assignment #5

Problem 1: pn Junction Electrostatics

a) We have an abrupt junction with NA =1018 cm-3, ND =1017 cm-3, T = 300K.

The p-type region is degenerately doped (NA > 9.1×1018 cm-3), with significant bandgap narrowing

= 35 meV

from Slide 20 of Lecture 3.

For the p+n junction, then, the built-in potential is

= (1.12-0.035)/2 + 0.026×ln(1017/1010)=0.962 V

The total depletion width is =1.1×10-5cm=0.11 m

By using the relationship

we can determine the widths of the depletion layers on the p side and n side:

xp=0.01 m and xn=0.1 m

The peak electric field is E(0)==(1.6×10-19×1017/10-12) × (1.1×10-5)=-1.76×105 V/cm

b) NA =1018 cm-3, ND =1017 cm-3, T = 300K, VA = -1 V.

The built-in voltage is unchanged (0.962 V).

The total depletion width =1.57×10-5cm=0.157 m

xp=0.014 m and xn=0.142 m

The peak electric field is E(0)==(1.6×10-19×1017/10-12) × (1.57×10-5))=-2.51×105 V/cm

The energy-band diagrams, charge distributions, electric field distributions, and potential distributions are drawn below for VA = 0 and VA = -1V:

Equilibrium (VA=0)                   Reverse biased (VA=-1V)

Note that the depletion width on the p-side is (10×) smaller than the depletion width on the n-side, since the p-side dopant concentration is (10×) larger than the n-side dopant concentration, so that most of the voltage is dropped across the more lightly doped n-side.

Problem 2: p-i-n Diode

a) We have a p-i-n junction with NA =1018 cm-3, ND =1017 cm-3, T = 300K. The equilibrium (VA = 0) charge density distribution, electric field distribution and potential distribution are plotted below.

b) The built-in potential is equal to the difference in work function between the p-type side and the n-type side.  Since the dopant concentrations (and hence the work functions) are the same as in Problem 1, the built-in potential is the same: Vbi = 0.962V.

The integral of the electric field distribution is equal to the built-in potential.  If wp = width of the depletion layer on the p side, wint = width of the intrinsic layer, and wn = width of the depletion layer on the n side, then this means that

Note that the widths of the depletion layers in the doped regions are much smaller than for a pn junction (ref. Problem 1), so that most of the built-in-voltage is dropped across the intrinsic region.  As before, the depletion width on the more heavily doped p-side is smaller than the depletion width on the more lightly doped n-side.

c) Maximum electric field in a p-i-n junction:

Emax,p-i-n =-(1.6×10-19×1017/10-12) × (0.559×10-6)=-0.8944×104 V/cm.

This is much lower than the peak electric field (>105 V/cm) in a pn junction (ref. Problem 1).  Thus, a p-i-n junction can be biased at a larger reverse bias before breakdown occurs (when the peak electric field exceeds a critical value).

d) The small-signal capacitance of the p-i-n diode is

Since W is much larger (by a factor of ~9) for the p-i-n diode, its small-signal capacitance will be much smaller (by a factor of ~9) than that of a pn diode.  This makes the p-i-n diode advantageous for fast switching applications.

Problem 3: Current Distributions in a pn Junction

a) Assuming low-level injection, the minority carrier concentrations at the edges of the depletion region are given by:

b) The diffusion coefficients and minority carrier diffusion lengths are:

Hole current in the n-type quasi-neutral region and electron current in the p-type quasi-neutral region are:

c) In the n-type quasi-neutral region,

Jp= Jn =Jtotal/2=(0.015+0.00434)/2 = 0.00967 A/cm2

- Jp(x)= 0.015e-(x-xn)/Lp=> (x-xn)/Lp =0.439 => (x-xn)=4.17×10-4 cm = 5.17 m

The current distributions in the pn junction are shown below. Note that although the electron and hole components of current vary with position, the total current remains constant.

Problem 4: Comparison of Schottky Diode and pn Junction Diode I-V Characteristics

- The reverse-bias current in a Schottky diode is given by the equation:

Is =120×(m*n/m0) ×AT2e-ΦBn/kT =120×(0.26)×(10-1)2×(300)2×1e-0.65/0.026 =1.17×10-4A.

- The reverse-bias current in a p-n diode is given by the equation:

I0 =Aqni2(Dp/LpND)= =1.54×10-14A.

- The I-V characteristics for the Schottky junction and the pn junction are plotted below.

Clearly the Schottky diode has a much smaller forward voltage because IS << I0.  (The reverse bias current in a Schottky diode is 10 orders of magnitude larger than for the pn diode.)

- At I = 1 A:

For a Schottky diode, 1=Is eqVA/kT=>1=1.17×10-4 ×e(VA/0.026)=>VA=0.235 V

For a p-n diode, 1=Is eqVA/kT=>1=1.54×10-14 ×e(VA/0.026)=>VA=0.83 V

It takes significantly less voltage to turn on the Schottky diode compared to the pn diode.  Thus, Schottky diodes are used in low-voltage and high-current applications.