EE 40

Homework #6

Due Tuesday, April 22, 2003, 3:30 PM

40 Total Points Possible

Problem 1:	10 Points Possible

What logic operation does the CMOS circuit

at left perform on the binary inputs A and B?

Write the output as a Boolean function in

terms of logic voltages A and B.

Problem 2:	8 Points Possible

For the CMOS logic circuit at left, assume that  is a small positive

number, such that an NMOS transistor with VGS(N) = VTH(N) +   (or

PMOS transistor with VGS(P) = VTH(P) – ) would be “barely” turned on.

An NMOS transistor with VGS(N) = VDD – (VTH(N) + ) (or PMOS

transistor with VGS(P) = -VDD – (VTH(P) – )) would be “fully” turned on.

Make an “educated guess” for the mode of operation of each

transistor in the circuit at left.  Assume VTH(N) ( -VTH(P).

Problem 3:	12 Points Possible

For the circuit at left, assume that each transistor has a pull-up/pull-down resistance of 10 k, and that COUT = 50 fF.

Find:

- previous and present inputs that result in the shortest pull-down delay, and the associated tp

- previous and present inputs that result in the longest pull-down delay, and the associated tp

- previous and present inputs that result in the shortest pull-up delay, and the associated tp

- previous and present inputs that result in the longest pull-up delay, and the associated tp

Problem 4:	10 Points Possible

Consider the logic circuit below.  Each logic gate is constructed using the appropriate CMOS circuit given in lecture.  With

VDD = 5 V

VTH(N) = -VTH(P) = 1 V

COX = 5 fF/µm2 for both transistors

L = 1 µm for both transistors

W = 2 µm for both transistors

= 0 for both transistors

µN= 50000 mm2 / (V s)

µP= 25000 mm2 / (V s)

- Find the low-to-high and high-to-low propagation delays tp for the inverter in the circuit as shown.  Take into account the pull-up and pull-down resistances of the transistors (which you must calculate here), as well as the gate capacitances of the attached gates  (calculate also).

- Suppose I require that the maximum propagation delay through the inverter is 2 ns.  Determine the maximum fan-out: the maximum number of NAND or NOR gates that can be attached to the inverter output if the propagation delay through the inverter is to be 2 ns maximum.