CS252	HOMEWORK 3

Due Tues. 11/06/07

Problem 1:

Here is some code for a vector machine with a maximum vector length of 64 elements:

LP:	LV		V1, R5		# load V1 with new value

MULTSV	V2, F0, V1	# perform the calculation

MULTSV	V3, F1, V1

ADDV		V2, V2, V3

MULTSV	V4, F2, V1

ADDV		V2, V2, V4

SV		V2, R5		# store the result

SUBI		R5, R5, 8

BNEZ		R5, LP

a) Show the convoys in the above code. Do not worry about structural hazards; assume that there are enough functional units. (Note that when analyzing convoys you may ignore the last two instructions since those are not vector computations.)

b) Show the execution time in clock cycles of this loop with n elements (Tn); assume Tloop = 15 and Tstart = 7 for all vector codes. Assume Tstart is the startup time for each convoy. Show the equation, and give the value of execution time for vector length n=64.

Problem 2:

This shows a snooping protocol state diagram for a for each cache block, based on CPU requests:

This shows a snooping protocol state diagram for each cache block, based on requests from the bus:

Assume that address A1 and A2 are different addresses that map to the same cache block.  P1 and P2 are two processors that use the above snooping protocol.  Complete the table below to show the actions the result when the following events occur.  Extra blank lines are provided in case an event causes multiple actions; you may not need to use all the blank lines.

| Event | P1 state | P1 addr | P1 val | P2 state | P2 addr | P2 val | Bus action | Bus proc | Bus addr | Bus val | Mem addr | Mem val |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| P1 write 5 to A1 |  |  |  |  |  |  |  |  |  |  |  |  |
| P2 write 1 to A2 |  |  |  |  |  |  |  |  |  |  |  |  |
| P2 write 2 to A1 |  |  |  |  |  |  |  |  |  |  |  |  |
| P1 read A1 |  |  |  |  |  |  |  |  |  |  |  |  |

Problem 3:

Assume X1 and X2 are different values in the same cache block.  Assume that P1 and P2 are two different processors using the snooping protocol described in problem 2.  For the following events, describe if the access is a hit or a miss in the accessing processor, and if it generates invalidates in the other processor; for misses and invalidates, describe if they are true or false sharing misses (or mark not applicable).  Neither P1 nor P2 has either value, to begin with.

| Time | P1 | P2 | Hit or Miss? Invalidates? | If Miss or Invalidate, True or False sharing? |
| --- | --- | --- | --- | --- |
| 1 | Write X2 |  |  |  |
| 2 |  | Write X2 |  |  |
| 3 | Read X1 |  |  |  |
| 4 |  | Read X1 |  |  |
| 5 |  | Write X2 |  |  |
| 6 | Read X1 |  |  |  |

# Text boxes

Invalid

Shared

(read/only)

Exclusive

(read/write)

CPU Read

CPU Write

CPU Read hit

Place read miss

on bus

Place Write 
Miss on bus

CPU read miss

Write back block,

Place read miss

on bus

CPU Write

Place Write Miss on Bus

CPU Read miss

Place read miss

on bus

CPU Write Miss

Write back cache block

Place write miss on bus

CPU read hit

CPU write hit

Cache Block

State

Invalid

Exclusive

(read/write)

Write Back

Block; (abort

memory access)

Write miss 
for this block

Read miss 
for this block

Write miss 
for this block

Write Back

Block; (abort

memory access)

Shared

(read/only)