## Slide 1: CS162 Operating Systems and Systems Programming Lecture 13 Address Translation (Finished), Caching
March 9th, 2015
Prof. John Kubiatowicz
http://cs162.eecs.Berkeley.edu

## Slide 2: Recall: Paging
Physical Address
Offset
Page Table (One per process)
  Resides in physical memory
  Contains physical page and permission for each virtual page
    Permissions include: Valid bits, Read, Write, etc
Virtual address mapping
  Offset from Virtual address copied to Physical Address
    Example: 10 bit offset  1024-byte pages
  Virtual page # is all remaining bits
    Example for 32-bits: 32-10 = 22 bits, i.e. 4 million entries
    Physical page # copied from table into physical address
  Check Page Table bounds and permissions
Offset
Virtual
Page #
Virtual Address:
Access
Error
>
PageTableSize
PageTablePtr
page #0
page #2
page #3
page #4
page #5
V,R
page #1
V,R
V,R,W
V,R,W
N
V,R,W
page #1
V,R
Check Perm
Access
Error
Physical
Page #

## Slide 3: Recall: Simple Page Table Discussion
What needs to be switched on a context switch?
  Page table pointer and limit
Analysis
  Pros
    Simple memory allocation
    Easy to Share
  Con: What if address space is sparse?
    E.g. on UNIX, code starts at 0, stack starts at (231-1).
    With 1K pages, need 2 million page table entries!
  Con: What if table really big?
    Not all pages used all the time  would be nice to have working set of page table in memory
How about combining paging and segmentation?
  Segments with pages inside them?
  Need some sort of multi-level translation
Notes: What if page size is very small? VAX had a 512-byte page size = lots of space for page table entries
What if page size is really big? Wastes space inside of page (internal fragmentation)

## Slide 4: Memory Layout for Linux 32-bit
http://static.duartes.org/img/blogPosts/linuxFlexibleAddressSpaceLayout.png

## Slide 5: Fix for sparse address space: The two-level page table
Physical
Address:
Offset
Physical
Page #
4KB
10 bits
10 bits
12 bits
Virtual
Address:
Offset
Virtual
P2 index
Virtual
P1 index
4 bytes
PageTablePtr
Tree of Page Tables
Tables fixed size (1024 entries)
  On context-switch: save single PageTablePtr register
Valid bits on Page Table Entries
  Don’t need every 2nd-level table
  Even when exist, 2nd-level tables can reside on disk if not in use
4 bytes

## Slide 6: What is in a Page Table Entry?
What is in a Page Table Entry (or PTE)?
  Pointer to next-level page table or to actual page
  Permission bits: valid, read-only, read-write, write-only
Example: Intel x86 architecture PTE:
  Address same format previous slide (10, 10, 12-bit offset)
  Intermediate page tables called “Directories”
  P: Present (same as “valid” bit in other architectures)
  W: Writeable
  U: User accessible
  PWT: Page write transparent: external cache write-through
  PCD: Page cache disabled (page cannot be cached)
  A: Accessed: page has been accessed recently
  D: Dirty (PTE only): page has been modified recently
  L: L=14MB page (directory only). Bottom 22 bits of virtual address serve as offset
Page Frame Number
(Physical Page Number)
Free
(OS)
0
L
D
A
PCD
PWT
U
W
P
0
1
2
3
4
5
6
7
8
11-9
31-12

## Slide 7: Examples of how to use a PTE
How do we use the PTE?
  Invalid PTE can imply different things:
    Region of address space is actually invalid or
    Page/directory is just somewhere else than memory
  Validity checked first
    OS can use other (say) 31 bits for location info
Usage Example: Demand Paging
  Keep only active pages in memory
  Place others on disk and mark their PTEs invalid
Usage Example: Copy on Write
  UNIX fork gives copy of parent address space to child
    Address spaces disconnected after child created
  How to do this cheaply?
    Make copy of parent’s page tables (point at same memory)
    Mark entries in both sets of page tables as read-only
    Page fault on write creates two copies
Usage Example: Zero Fill On Demand
  New data pages must carry no information (say be zeroed)
  Mark PTEs as invalid; page fault on use gets zeroed page
  Often, OS creates zeroed pages in background

## Slide 8: Summary: Two-Level Paging
stack
1111 1111
stack
heap
code
data
Virtual memory view
0000 0000
0100 0000
1000 0000
1100 0000
page1 #
offset
Physical memory view
data
code
heap
stack
0000 0000
0001 0000
0101 000
0111 000
1110 0000
page2 #
111
110 null
101 null
100
011 null
010
001 null
000
11 11101
10 11100
01 10111
00 10110
11 01101
10 01100
01 01011
00 01010
11 00101
10 00100
01 00011
00 00010
11 null
10 10000
01 01111
00 01110
Page Tables
(level 2)
Page Table
(level 1)
1111 0000

## Slide 9: Summary: Two-Level Paging
stack
stack
heap
code
data
Virtual memory view
1001 0000
(0x90)
Physical memory view
data
code
heap
stack
0000 0000
0001 0000
1000 0000
(0x80)
1110 0000
111
110 null
101 null
100
011 null
010
001 null
000
11 11101
10 11100
01 10111
00 10110
11 01101
10 01100
01 01011
00 01010
11 00101
10 00100
01 00011
00 00010
11 null
10 10000
01 01111
00 01110
Page Tables
(level 2)
Page Table
(level 1)
In best case, total size of page tables ≈ number of pages used by program virtual memory. Requires two additional memory access!

## Slide 10: Recall: Segments + Pages
What about a tree of tables?
  Lowest level page tablememory still allocated with bitmap
  Higher levels often segmented
Could have any number of levels. Example (top segment):
What must be saved/restored on context switch?
  Contents of top-level segment registers (for this example)
  Pointer to top-level table (page table)
page #0
page #1
page #3
page #4
page #5
V,R
V,R
page #2
V,R,W
V,R,W
N
V,R,W
Offset
Physical Address
Virtual
Address:
Offset
Virtual
Page #
Virtual
Seg #
Base0
Limit0
V
Base1
Limit1
V
Base2
Limit2
V
Base3
Limit3
N
Base4
Limit4
V
Base5
Limit5
N
Base6
Limit6
N
Base7
Limit7
V
Base2
Limit2
V
Access
Error
>
page #2
V,R,W
Physical
Page #
Check Perm
Access
Error

## Slide 11: Recall Sharing (Complete Segment)
Process
A
Offset
Virtual
Page #
Virtual
Seg #
Base0
Limit0
V
Base1
Limit1
V
Base2
Limit2
V
Base3
Limit3
N
Base4
Limit4
V
Base5
Limit5
N
Base6
Limit6
N
Base7
Limit7
V
Base2
Limit2
V
page #0
page #1
page #2
page #3
page #4
page #5
V,R
V,R
V,R,W
V,R,W
N
V,R,W
Shared Segment
Process
B
Offset
Virtual
Page #
Virtual
Seg #
Base0
Limit0
V
Base1
Limit1
V
Base2
Limit2
V
Base3
Limit3
N
Base4
Limit4
V
Base5
Limit5
N
Base6
Limit6
N
Base7
Limit7
V
Base2
Limit2
V

## Slide 12: Multi-level Translation Analysis
Pros:
  Only need to allocate as many page table entries as we need for application
    In other wards, sparse address spaces are easy
  Easy memory allocation
  Easy Sharing
    Share at segment or page level (need additional reference counting)
Cons:
  One pointer per page (typically 4K – 16K pages today)
  Page tables need to be contiguous
    However, previous example keeps tables to exactly one page in size
  Two (or more, if >2 levels) lookups per reference
    Seems very expensive!

## Slide 13: X86_64: Four-level page table!
Physical
Address:
(40-50 bits)
12bit Offset
Physical Page #
9 bits
9 bits
12 bits
48-bit Virtual
Address:
Offset
Virtual
P2 index
Virtual
P1 index
8 bytes
PageTablePtr
Virtual
P3 index
Virtual
P4 index
9 bits
9 bits
4096-byte pages (12 bit offset) Page tables also 4k bytes (pageable)

## Slide 14
7 bits
9 bits
12 bits
64bit Virtual
Address:
Offset
Virtual
P2 index
Virtual
P1 index
Virtual
P3 index
Virtual
P4 index
9 bits
9 bits
Virtual
P5 index
Virtual
P6 index
9 bits
9 bits
No!
Too slow
Too many almost-empty tables
IA64: 64bit addresses: Six-level page table?!?
Notes: Only really use last two levels (1 GB)

## Slide 15: Inverted Page Table
With all previous examples (“Forward Page Tables”)
  Size of page table is at least as large as amount of virtual memory allocated to processes
  Physical memory may be much less
    Much of process space may be out on disk or not in use
Answer: use a hash table
  Called an “Inverted Page Table”
  Size is independent of virtual address space
  Directly related to amount of physical memory
  Very attractive option for 64-bit address spaces
Cons: Complexity of managing hash changes
  Often in hardware!
Offset
Virtual
Page #
Hash
Table
Offset
Physical
Page #

## Slide 16: IA64: Inverse Page Table (IPT)
Idea: index page table by physical pages instead of VM
VMpage0, pid 0
VMpage2, pid 0
VMpage1, pid 0
VMpage3, pid 0
0x0000
0x1000
0x2000
0x3000
0x4000
0x5000
0x6000
0x7000
Physical memory in 4kB pages
Page numbers in red
pid 0 | VMpage0
pid 1 | …
pid 0 | VMpage2
pid 0 | VMpage1
xx | free
pid 2 | …
pid 1 | …
pid 0 | VMpage3
Inverse Page Table
VMpage0
VMpage1
VMpage2
VMpage3
0x0
0x1
0x2
0x3
0x4
0x5
0x6
0x7
Process id 0
Virtual memory

## Slide 17: IPT address translation
Need an associative map from VM page to IPT address:
  Use a hash map
pid 0 | VMpage0
pid 1 | 
pid 0 | VMpage1
pid 0 | VMpage2
xx | free
pid 2 | 
pid 1 | 
pid 0 | VMpage3
Inverse Page Table
VMpage2 (52b) | Offset (12b)
0x0
0x1
0x2
0x3
0x4
0x5
0x6
0x7
Process 0 virtual address
0x3 | Offset (12b)
Hash VM page #
VMpage0, pid 0
VMpage2, pid 0
VMpage1, pid 0
VMpage3, pid 0
0x0000
0x1000
0x2000
0x3000
0x4000
0x5000
0x6000
0x7000
Physical address

## Slide 18: Summary: Inverted Table
1111 1111
stack
heap
code
data
Virtual memory view
0000 0000
0100 0000
1000 0000
1100 0000
page #
offset
Inverted Table
Hash(procID & virt. page #) =
phys. page #
1110 0000
h(11111) =
h(11110) =
h(11101) =
h(11100) =
h(10010)=
h(10001)=
h(10000)=
h(01011)=
h(01010)=
h(01001)=
h(01000)=
h(00011)=
h(00010)=
h(00001)=
h(00000)=
stack
Physical memory view
data
code
heap
stack
0000 0000
0001 0000
0101 0000
0111 0000
1110 0000
11101
11100
10111
10110
10000
01111
01110
01101
01100
01011
01010
00101
00100
00011
00010
1011 0000
Total size of page table ≈ number of pages used by program in physical memory. Hash more complex

## Slide 19: Address Translation Comparison
 | Advantages | Disadvantages
Segmentation | Fast context switching: Segment mapping maintained by CPU | External fragmentation
Paging (single-level page) | No external fragmentation, fast easy allocation | Large table size ~ virtual memory Internal fragmentation
Paged segmentation | Table size ~ # of pages in virtual memory, fast easy allocation | Multiple memory references per page access
Two-level pages |  | 
Inverted Table | Table size ~ # of pages in physical memory | Hash function more complex

## Slide 20: Administrivia
Midterm I coming up on Wednesday!
  March 11th, 7:00-10:00PM
  Rooms: 1 PIMENTEL; 2060 VALLEY LSB
    Will be dividing up in advance – watch for Piazza post
  All topics up to and including next Monday
  Closed book
  1 page hand-written notes both sides

## Slide 21: Making it real: X86 Memory model with segmentation (16/32-bit)

## Slide 22: X86 Segment Descriptors (32-bit Protected Mode)
Segments are either implicit in the instruction (say for code segments) or actually part of the instruction
  There are 6 registers: SS, CS, DS, ES, FS, GS
What is in a segment register?
  A pointer to the actual segment description: G/L selects between GDT and LDT tables (global vs local descriptor tables)
Two registers: GDTR and LDTR hold pointers to the global and local descriptor tables in memory
  Includes length of table (for < 213) entries
Descriptor format (64 bits):
G: Granularity of segment (0: 16bit, 1: 4KiB unit) DB: Default operand size (0; 16bit, 1: 32bit) A: Freely available for use by software P: Segment present DPL: Descriptor Privilege Level S: System Segment (0: System, 1: code or data) Type: Code, Data, Segment
Segment selector [13 bits]
G/L
RPL

## Slide 23: Recall: How are segments used?
One set of global segments (GDT) for everyone, different set of local segments (LDT) for every process
In legacy applications (16-bit mode):
  Segments provide protection for different components of user programs
  Separate segments for chunks of code, data, stacks
  Limited to 64K segments
Modern use in 32-bit Mode:
  Segments “flattened”, i.e. every segment is 4GB in size
  One exception: Use of GS (or FS) as a pointer to “Thread Local Storage”
    A thread can make accesses to TLS like this: mov eax, gs(0x0)
Modern use in 64-bit (“long”) mode
  Most segments (SS, CS, DS, ES) have zero base and no length limits
  Only FS and GS retain their functionality (for use in TLS)

## Slide 24: How is the translation accomplished?
What, exactly happens inside MMU?
One possibility: Hardware Tree Traversal
  For each virtual address, takes page table base pointer and traverses the page table in hardware
  Generates a “Page Fault” if it encounters invalid PTE
    Fault handler will decide what to do
    More on this next lecture
  Pros: Relatively fast (but still many memory accesses!)
  Cons: Inflexible, Complex hardware
Another possibility: Software
  Each traversal done in software
  Pros: Very flexible
  Cons: Every translation must invoke Fault!
In fact, need way to cache translations for either case!
CPU
MMU
Virtual
Addresses
Physical
Addresses

## Slide 25: Recall: Dual-Mode Operation
Can a process modify its own translation tables?
  NO!
  If it could, could get access to all of physical memory
  Has to be restricted somehow
To Assist with Protection, Hardware provides at least two modes (Dual-Mode Operation):
  “Kernel” mode (or “supervisor” or “protected”)
  “User” mode (Normal program mode)
  Mode set with bits in special control register only accessible in kernel-mode
Intel processor actually has four “rings” of protection:
  PL (Priviledge Level) from 0 – 3
    PL0 has full access, PL3 has least
  Privilege Level set in code segment descriptor (CS)
  Mirrored “IOPL” bits in condition register gives permission to programs to use the I/O instructions
  Typical OS kernels on Intel processors only use PL0 (“kernel”) and PL3 (“user”)

## Slide 26: How to get from KernelUser
What does the kernel do to create a new user process?
  Allocate and initialize address-space control block
  Read program off disk and store in memory
  Allocate and initialize translation table
    Point at code in memory so program can execute
    Possibly point at statically initialized data
  Run Program:
    Set machine registers
    Set hardware pointer to translation table
    Set processor status word for user mode
    Jump to start of program
How does kernel switch between processes?
  Same saving/restoring of registers as before
  Save/restore PSL (hardware pointer to translation table)

## Slide 27: Recall: UserKernel (System Call)
Can’t let inmate (user) get out of padded cell on own
  Would defeat purpose of protection!
  So, how does the user program get back into kernel?
System call: Voluntary procedure call into kernel
  Hardware for controlled UserKernel transition
  Can any kernel routine be called?
    No! Only specific ones.
  System call ID encoded into system call instruction
    Index forces well-defined interface with kernel

## Slide 28: UserKernel (Exceptions: Traps and Interrupts)
A system call instruction causes a synchronous exception (or “trap”)
  In fact, often called a software “trap” instruction
Other sources of Synchronous Exceptions (“Trap”):
  Divide by zero, Illegal instruction, Bus error (bad address, e.g. unaligned access)
  Segmentation Fault (address out of range)
  Page Fault (for illusion of infinite-sized memory)
Interrupts are Asynchronous Exceptions
  Examples: timer, disk ready, network, etc….
  Interrupts can be disabled, traps cannot!
On system call, exception, or interrupt:
  Hardware enters kernel mode with interrupts disabled
  Saves PC, then jumps to appropriate handler in kernel
  For some processors (x86), processor also saves registers, changes stack, etc.
Actual handler typically saves registers, other CPU state, and switches to kernel stack

## Slide 29: Closing thought: Protection without Hardware
Does protection require hardware support for translation and dual-mode behavior?
  No: Normally use hardware, but anything you can do in hardware can also do in software (possibly expensive)
Protection via Strong Typing
  Restrict programming language so that you can’t express program that would trash another program
  Loader needs to make sure that program produced by valid compiler or all bets are off
  Example languages: LISP, Ada, Modula-3 and Java
Protection via software fault isolation:
  Language independent approach: have compiler generate object code that provably can’t step out of bounds
    Compiler puts in checks for every “dangerous” operation (loads, stores, etc). Again, need special loader.
    Alternative, compiler generates “proof” that code cannot do certain things (Proof Carrying Code)
  Or: use virtual machine to guarantee safe behavior (loads and stores recompiled on fly to check bounds)

## Slide 30: Caching Concept
Cache: a repository for copies that can be accessed more quickly than the original
  Make frequent case fast and infrequent case less dominant
Caching underlies many of the techniques that are used today to make computers fast
  Can cache: memory locations, address translations, pages, file blocks, file names, network routes, etc…
Only good if:
  Frequent case frequent enough and
  Infrequent case not too expensive
Important measure: Average Access time = (Hit Rate x Hit Time) + (Miss Rate x Miss Time)

## Slide 31: Why Bother with Caching?
CPU
µProc
60%/yr.
(2X/1.5yr)
DRAM
9%/yr.
(2X/10 yrs)
DRAM
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
1982
Processor-Memory
Performance Gap: (grows 50% / year)
Performance
Time
“Moore’s Law”
(really Joy’s Law)
Processor-DRAM Memory Gap (latency)
“Less’ Law?”
Notes: Y-axis is performance
X-axis is time
Latency
Cliché:
Not e that x86 didn’t have cache on chip until 1989

## Slide 32: Another Major Reason to Deal with Caching
Cannot afford to translate on every access
  At least three DRAM accesses per actual DRAM access
  Or: perhaps I/O if page table partially on disk!
Even worse: What if we are using caching to make memory access faster than DRAM access???
Solution? Cache translations!
  Translation Cache: TLB (“Translation Lookaside Buffer”)
page #0
page #1
page #3
page #4
page #5
V,R
V,R
page #2
V,R,W
V,R,W
N
V,R,W
Offset
Physical Address
Virtual
Address:
Offset
Virtual
Page #
Virtual
Seg #
Base0
Limit0
V
Base1
Limit1
V
Base2
Limit2
V
Base3
Limit3
N
Base4
Limit4
V
Base5
Limit5
N
Base6
Limit6
N
Base7
Limit7
V
Access
Error
>
Physical
Page #
Check Perm
Access
Error

## Slide 33: Why Does Caching Help? Locality!
Temporal Locality (Locality in Time):
  Keep recently accessed data items closer to processor
Spatial Locality (Locality in Space):
  Move contiguous blocks to the upper levels
Address Space
0
2n - 1
Probability
of reference
Lower Level
Memory
Upper Level
Memory
To Processor
From Processor
Blk X
Blk Y
Notes: How does the memory hierarchy work? Well it is rather simple, at least in principle.
In order to take advantage of the temporal locality, that is the locality in time, the memory hierarchy will keep those more recently accessed data items closer to the processor because chances are (points to the principle), the processor will access them again soon.
In order to take advantage of the spatial locality, not ONLY do we move the item that has just been accessed to the upper level, but we ALSO move the data items that are adjacent to it.
+1 = 15 min. (X:55)

## Slide 34: Memory Hierarchy of a Modern Computer System
Take advantage of the principle of locality to:
  Present as much memory as in the cheapest technology
  Provide access at speed offered by the fastest technology
On-Chip
Cache
Registers
Control
Datapath
Secondary
Storage
(Disk)
Processor
Main
Memory
(DRAM)
Second
Level
Cache
(SRAM)
1s
10,000,000s
(10s ms)
Speed (ns):
10s-100s
100s
100s
Gs
Size (bytes):
Ks-Ms
Ms
Tertiary
Storage
(Tape)
10,000,000,000s
(10s sec)
Ts
Notes: The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in details in the next lecture on caches).
+1 = 16 min. (X:56)

## Slide 35: A Summary on Sources of Cache Misses
Compulsory (cold start or process migration, first reference): first access to a block
  “Cold” fact of life: not a whole lot you can do about it
  Note: If you are going to run “billions” of instruction, Compulsory Misses are insignificant
Capacity:
  Cache cannot contain all blocks access by the program
  Solution: increase cache size
Conflict (collision):
  Multiple memory locations mapped to the same cache location
  Solution 1: increase cache size
  Solution 2: increase associativity
Coherence (Invalidation): other process (e.g., I/O) updates memory
Notes: (Capacity miss) That is the cache misses are due to the fact that the cache is simply not large enough to contain all the blocks that are accessed by the program.
The solution to reduce the Capacity miss rate is simple: increase the cache size.
Here is a summary of other types of cache miss we talked about.
First is the Compulsory misses. These are the misses that we cannot avoid. They are caused when we first start the program.
Then we talked about the conflict misses. They are the misses that caused by multiple memory locations being mapped to the same cache location.
There are two solutions to reduce conflict misses. The first one is, once again, increase the cache size. The second one is to increase the associativity.
For example, say using a 2-way set associative cache instead of directed mapped cache.
But keep in mind that cache miss rate is only one part of the equation. You also have to worry about cache access time and miss penalty. Do NOT optimize miss rate alone.
Finally, there is another source of cache miss we will not cover today. Those are referred to as invalidation misses caused by another process, such as IO , update the main memory so you have to flush the cache to avoid inconsistency between memory and cache.
+2 = 43 min. (Y:23)

## Slide 36: How is a Block found in a Cache?
Index Used to Lookup Candidates in Cache
  Index identifies the set
Tag used to identify actual copy
  If no candidates match, then declare cache miss
Block is minimum quantum of caching
  Data select field used to select data within block
  Many caching applications don’t have data select field
Block
offset
Block Address
Tag
Index
Set Select
Data Select

## Slide 37: Review: Direct Mapped Cache
:
0x50
Valid Bit
:
Cache Tag
Byte 32
0
1
2
3
:
Cache Data
Byte 0
Byte 1
Byte 31
:
Byte 33
Byte 63
:
Byte 992
Byte 1023
:
31
Direct Mapped 2N byte cache:
  The uppermost (32 - N) bits are always the Cache Tag
  The lowest M bits are the Byte Select (Block Size = 2M)
Example: 1 KB Direct Mapped Cache with 32 B Blocks
  Index chooses potential block
  Tag checked to verify block
  Byte select chooses byte within block
Ex: 0x50
Ex: 0x00
Cache Index
0
4
31
Cache Tag
Byte Select
9
Ex: 0x01
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 KB direct mapped cache with block size equals to 32 bytes.
In other words, each block associated with the cache tag will have 32 bytes in it (Row 1).
With Block Size equals to 32 bytes, the 5 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K byte, the upper 32 minus 10 bits, or 22 bits of the address will be stored as cache tag.
The rest of the address bits in the middle, that is bit 5 through 9, will be used as Cache Index to select the proper cache entry.
+2 = 30 min. (Y:10)

## Slide 38: Review: Set Associative Cache
Cache Index
0
4
31
Cache Tag
Byte Select
8
Cache Data
Cache Block 0
Cache Tag
Valid
:
:
:
Cache Data
Cache Block 0
Cache Tag
Valid
:
:
:
Mux
0
1
Sel1
Sel0
OR
Hit
N-way set associative: N entries per Cache Index
  N direct mapped caches operates in parallel
Example: Two-way set associative cache
  Cache Index selects a “set” from the cache
  Two tags in the set are compared to input in parallel
  Data is selected based on the tag result
Compare
Compare
Cache Block
Notes: This is called a 2-way set associative cache because there are two cache entries for each cache index. Essentially, you have two direct mapped cache works in parallel.
This is how it works: the cache index selects a set from the cache. The two tags in the set are compared in parallel with the upper bits of the memory address.
If neither tag matches the incoming address tag, we have a cache miss.
Otherwise, we have a cache hit and we will select the data on the side where the tag matches occur.
This is simple enough. What is its disadvantages?
+1 = 36 min. (Y:16)

## Slide 39: Review: Fully Associative Cache
Fully Associative: Every block can hold any line
  Address does not include a cache index
  Compare Cache Tags of all Cache Entries in Parallel
Example: Block Size=32B blocks
  We need N 27-bit comparators
  Still have byte select to choose from within block
:
Cache Data
Byte 0
Byte 1
Byte 31
:
Byte 32
Byte 33
Byte 63
:
Valid Bit
:
:
Cache Tag
0
4
Cache Tag (27 bits long)
Byte Select
31
=
=
=
=
=
Ex: 0x01
Notes: While the direct mapped cache is on the simple end of the cache design spectrum, the fully associative cache is on the most complex end.
It is the N-way set associative cache carried to the extreme where N in this case is set to the number of cache entries in the cache.
In other words, we don’t even bother to use any address bits as the cache index.
We just store all the upper bits of the address (except Byte select) that is associated with the cache block as the cache tag and have one comparator for every entry.
The address is sent to all entries at once and compared in parallel and only the one that matches are sent to the output. This is called an associative lookup.
Needless to say, it is very hardware intensive. Usually, fully associative cache is limited to 64 or less entries.
Since we are not doing any mapping with the cache index, we will never push any other item out of the cache because multiple memory locations map to the same cache location.
Therefore, by definition, conflict miss is zero for a fully associative cache. This, however, does not mean the overall miss rate will be zero.
Assume we have 64 entries here. The first 64 items we accessed can fit in.
But when we try to bring in the 65th item, we will need to throw one of them out to make room for the new item. This bring us to the third type of cache misses: Capacity Miss.
+3 = 41 min. (Y:21)

## Slide 40: Where does a Block Get Placed in a Cache?
Example: Block 12 placed in 8 block cache
0 1 2 3 4 5 6 7
Block
no.
Direct mapped:
block 12 can go only into block 4 (12 mod 8)
Set associative:
block 12 can go anywhere in set 0 (12 mod 4)
0 1 2 3 4 5 6 7
Block
no.
Set
0
Set
1
Set
2
Set
3
Fully associative:
block 12 can go anywhere
0 1 2 3 4 5 6 7
Block
no.
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
32-Block Address Space:
1 1 1 1 1 1 1 1 1 1 2 2 2 2 2 2 2 2 2 2 3 3
Block
no.

## Slide 41: Review: Which block should be replaced on a miss?
Easy for Direct Mapped: Only one possibility
Set Associative or Fully Associative:
  Random
  LRU (Least Recently Used)
2-way 4-way 8-way Size LRU Random LRU Random LRU Random
16 KB 5.2% 5.7% 4.7% 5.3% 4.4% 5.0%
64 KB 1.9% 2.0% 1.5% 1.7% 1.4% 1.5%
256 KB 1.15% 1.17% 1.13% 1.13% 1.12% 1.12%

## Slide 42: Review: What happens on a write?
Write through: The information is written to both the block in the cache and to the block in the lower-level memory
Write back: The information is written only to the block in the cache.
  Modified cache block is written to main memory only when it is replaced
  Question is block clean or dirty?
Pros and Cons of each?
  WT:
    PRO: read misses cannot result in writes
    CON: Processor held up on writes unless writes buffered
  WB:
    PRO: repeated writes not sent to DRAM processor not held up on writes
    CON: More complex Read miss may require writeback of dirty data

## Slide 43: Caching Applied to Address Translation
Question is one of page locality: does it exist?
  Instruction accesses spend a lot of time on the same page (since accesses sequential)
  Stack accesses have definite locality of reference
  Data accesses have less page locality, but still some…
Can we have a TLB hierarchy?
  Sure: multiple levels at different sizes/speeds
Data Read or Write
(untranslated)
CPU
Physical
Memory
TLB
Translate
(MMU)
No
Virtual
Address
Physical
Address
Yes
Cached?
Save
Result

## Slide 44: What Actually Happens on a TLB Miss?
Hardware traversed page tables:
  On TLB miss, hardware in MMU looks at current page table to fill TLB (may walk multiple levels)
    If PTE valid, hardware fills TLB and processor never knows
    If PTE marked as invalid, causes Page Fault, after which kernel decides what to do afterwards
Software traversed Page tables (like MIPS)
  On TLB miss, processor receives TLB fault
  Kernel traverses page table to find PTE
    If PTE valid, fills TLB and returns from fault
    If PTE marked as invalid, internally calls Page Fault handler
Most chip sets provide hardware traversal
  Modern operating systems tend to have more TLB faults since they use translation for many things
  Examples:
    shared segments
    user-level portions of an operating system

## Slide 45: What happens on a Context Switch?
Need to do something, since TLBs map virtual addresses to physical addresses
  Address Space just changed, so TLB entries no longer valid!
Options?
  Invalidate TLB: simple but might be expensive
    What if switching frequently between processes?
  Include ProcessID in TLB
    This is an architectural solution: needs hardware
What if translation tables change?
  For example, to move page from memory to disk or vice versa…
  Must invalidate TLB entry!
    Otherwise, might think that page is still in memory!

## Slide 46: What TLB organization makes sense?
Needs to be really fast
  Critical path of memory access
    In simplest view: before the cache
    Thus, this adds to access time (reducing cache speed)
  Seems to argue for Direct Mapped or Low Associativity
However, needs to have very few conflicts!
  With TLB, the Miss Time extremely high!
  This argues that cost of Conflict (Miss Time) is much higher than slightly increased cost of access (Hit Time)
Thrashing: continuous conflicts between accesses
  What if use low order bits of page as index into TLB?
    First page of code, data, stack may map to same entry
    Need 3-way associativity at least?
  What if use high order bits as index?
    TLB mostly unused for small programs
CPU
TLB
Cache
Memory

## Slide 47: TLB organization: include protection
How big does TLB actually have to be?
  Usually small: 128-512 entries
  Not very big, can support higher associativity
TLB usually organized as fully-associative cache
  Lookup is by Virtual Address
  Returns Physical Address + other info
What happens when fully-associative is too slow?
  Put a small (4-16 entry) direct-mapped cache in front
  Called a “TLB Slice”
Example for MIPS R3000:
0xFA00 0x0003 Y N Y R/W 34 0x0040 0x0010 N Y Y R 0 0x0041 0x0011 N Y Y R 0
Virtual Address Physical Address Dirty Ref Valid Access ASID

## Slide 48: Example: R3000 pipeline includes TLB “stages”
Inst Fetch
Dcd/ Reg
ALU / E.A
Memory
Write Reg
TLB I-Cache RF Operation WB
E.A. TLB D-Cache
MIPS R3000 Pipeline
ASID
V. Page Number
Offset
12
20
6
0xx User segment (caching based on PT/TLB entry)
100 Kernel physical space, cached
101 Kernel physical space, uncached
11x Kernel virtual space
Allows context switching among
64 user processes without TLB flush
Virtual Address Space
TLB
  64 entry, on-chip, fully associative, software TLB fault handler

## Slide 49: Reducing translation time further
As described, TLB lookup is in serial with cache lookup:
Machines with TLBs go one step further: they overlap TLB lookup with cache access.
  Works because offset available early
Virtual Address
TLB Lookup
V
Access
Rights
PA
V page no.
offset
10
P page no.
offset
10
Physical Address

## Slide 50: Overlapping TLB & Cache Access (1/2)
Main idea:
  Offset in virtual address exactly covers the “cache index” and “byte select”
  Thus can select the cached byte(s) in parallel to perform address translation
Offset
Virtual Page #
index
tag / page #
byte
virtual address
physical address

## Slide 51: Overlapping TLB & Cache Access
Here is how this might work with a 4K cache:
What if cache size is increased to 8KB?
  Overlap not complete
  Need to do something else. See CS152/252
Another option: Virtual Caches
  Tags in cache are virtual addresses
  Translation only happens on cache misses
TLB
4K Cache
10
2
00
4 bytes
index
1 K
page #
disp
20
assoc
lookup
32
Hit/
Miss
FN
Data
Hit/
Miss
=
FN

## Slide 52: Putting Everything Together: Address Translation
Physical Address:
Offset
Physical
Page #
Virtual Address:
Offset
Virtual
P2 index
Virtual
P1 index
PageTablePtr
Page Table
(1st level)
Page Table
(2nd level)
Physical
Memory:

## Slide 53: Putting Everything Together: TLB
Page Table
(2nd level)
PageTablePtr
Page Table
(1st level)
Offset
Physical
Page #
Virtual Address:
Offset
Virtual
P2 index
Virtual
P1 index
Physical
Memory:
Physical Address:
…
TLB:

## Slide 54: Putting Everything Together: Cache
Page Table
(2nd level)
PageTablePtr
Page Table
(1st level)
Virtual Address:
Offset
Virtual
P2 index
Virtual
P1 index
…
TLB:
Offset
Physical
Memory:
Physical Address:
Physical
Page #
…
tag:
block:
cache:
index
byte
tag

## Slide 55: Next Up: What happens when …
virtual address
MMU
PT
instruction
physical address
page#
frame#
offset
page fault
Operating System
exception
Page Fault Handler
load page from disk
update PT entry
Process
scheduler
retry
frame#
offset

## Slide 56: Summary (1/3)
Page Tables
  Memory divided into fixed-sized chunks of memory
  Virtual page number from virtual address mapped through page table to physical page number
  Offset of virtual address same as physical address
  Large page tables can be placed into virtual memory
Multi-Level Tables
  Virtual address mapped to series of tables
  Permit sparse population of address space
Inverted page table
  Size of page table related to physical memory size
PTE: Page Table Entries
  Includes physical page number
  Control info (valid bit, writeable, dirty, user, etc)

## Slide 57: Summary (2/3)
The Principle of Locality:
  Program likely to access a relatively small portion of the address space at any instant of time.
    Temporal Locality: Locality in Time
    Spatial Locality: Locality in Space
Three (+1) Major Categories of Cache Misses:
  Compulsory Misses: sad facts of life. Example: cold start misses.
  Conflict Misses: increase cache size and/or associativity
  Capacity Misses: increase cache size
  Coherence Misses: Caused by external processors or I/O devices
Cache Organizations:
  Direct Mapped: single block per set
  Set associative: more than one block per set
  Fully associative: all entries equivalent
Notes: Let’s summarize today’s lecture. I know you have heard this many times and many ways but it is still worth repeating.
Memory hierarchy works because of the Principle of Locality which says a program will access a relatively small portion of the address space at any instant of time.
There are two types of locality: temporal locality, or locality in time and spatial locality, or locality in space.
So far, we have covered three major categories of cache misses.
Compulsory misses are cache misses due to cold start. You cannot avoid them but if you are going to run billions of instructions anyway, compulsory misses usually don’t bother you.
Conflict misses are misses caused by multiple memory location being mapped to the same cache location.
The nightmare scenario is the ping pong effect when a block is read into the cache but before we have a chance to use it, it was immediately forced out by another conflict miss.
You can reduce Conflict misses by either increase the cache size or increase the associativity, or both.
Finally, Capacity misses occurs when the cache is not big enough to contains all the cache blocks required by the program. You can reduce this miss rate by making the cache larger.
There are two write policy as far as cache write is concerned. Write through requires a write buffer and a nightmare scenario is when the store occurs so frequent that you saturates your write buffer.
The second write polity is write back. In this case, you only write to the cache and only when the cache block is being replaced do you write the cache block back to memory.
+3 = 77 min. (Y:57)

## Slide 58: Summary (3/3): Translation Caching (TLB)
A cache of translations called a “Translation Lookaside Buffer” (TLB)
  Relatively small number of entries (< 512)
  Fully Associative (Since conflict misses expensive)
  TLB entries contain PTE and optional process ID
On TLB miss, page table must be traversed
  If located PTE is invalid, cause Page Fault
On context switch/change in page table
  TLB entries must be invalidated somehow
TLB is logically in front of cache
  Thus, needs to be overlapped with cache access to be really fast
Notes: No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
Besides working at Sun, I also teach people how to fly whenever I have time.
Statistic have shown that if a pilot crashed after an engine failure, he or she is more likely to get killed in a multi-engine light airplane than a single engine airplane.
The joke among us flight instructors is that: sure, when the engine quit in a single engine stops, you have one option: sooner or later, you land. Probably sooner.
But in a multi-engine airplane with one engine stops, you have a lot of options. It is the need to make a decision that kills those people.