## Slide 1: CS162 Operating Systems and Systems Programming Lecture 17 Performance Storage Devices, Queueing Theory
April 1st, 2015
Prof. John Kubiatowicz
http://cs162.eecs.Berkeley.edu

## Slide 2: Recall: Memory-Mapped Display Controller
Memory-Mapped:
  Hardware maps control registers and display memory into physical address space
    Addresses set by hardware jumpers or programming at boot time
  Simply writing to display memory (also called the “frame buffer”) changes image on screen
    Addr: 0x8000F000—0x8000FFFF
  Writing graphics description to command-queue area
    Say enter a set of triangles that describe some scene
    Addr: 0x80010000—0x8001FFFF
  Writing to the command register may cause on-board graphics hardware to do something
    Say render the above scene
    Addr: 0x0007F004
Can protect with address translation
Display
Memory
0x8000F000
0x80010000
Physical Address
Space
Status
0x0007F000
Command
0x0007F004
Graphics
Command
Queue
0x80020000

## Slide 3: Recall: Transferring Data To/From Controller
addr
len
Programmed I/O:
  Each byte transferred via processor in/out or load/store
  Pro: Simple hardware, easy to program
  Con: Consumes processor cycles proportional to data size
Direct Memory Access:
  Give controller access to memory bus
  Ask it to transfer data blocks to/from memory directly
Sample interaction with DMA controller (from OSC):

## Slide 4: Goals for Today
Discussion of performance
Disks and SSDs
  Hardware performance parameters
  Queuing Theory
File Systems
  Structure,… Naming, Directories, and Caching
Note: Some slides and/or pictures in the following are
adapted from slides ©2005 Silberschatz, Galvin, and Gagne
Note: Some slides and/or pictures in the following are
adapted from slides ©2005 Silberschatz, Galvin, and Gagne. Many slides generated from my lecture notes by Kubiatowicz.

## Slide 5: Basic Performance Concepts
Response Time or Latency: Time to perform an operation (s)
Bandwidth or Throughput: Rate at which operations are performed (op/s)
  Files: mB/s, Networks: mb/s, Arithmetic: GFLOP/s
Start up or “Overhead”: time to initiate an operation
Most I/O operations are roughly linear
  Latency (n) = Ovhd + n/Bandwidth

## Slide 6: Example (fast network)
Consider a gpbs link (125 MB/s)
  With a startup cost S = 1 ms
Theorem: half-power point occurs at n=S*B:
  When transfer time = startup T(S*B) = S + S*B/B

## Slide 7: Example: at 10 ms startup (like Disk)

## Slide 8: What determines peak BW for I/O ?
Bus Speed
  PCI-X: 1064 MB/s = 133 MHz x 64 bit (per lane)
  ULTRA WIDE SCSI: 40 MB/s
  Serial Attached SCSI & Serial ATA & IEEE 1394 (firewire) : 1.6 Gbps full duplex (200 MB/s)
  USB 1.5 – 12 mb/s
Device Transfer Bandwidth
  Rotational speed of disk
  Write / Read rate of NAND flash
  Signaling rate of network link
Whatever is the bottleneck in the path

## Slide 9: Administrivia
Peer evaluations for project 1 not all in!
  Will not release final project grades until you do this
  Zero-sum game – if you do not contribute, you don’t get full credit!
Do not come to office hours with questions like:
  “Why doesn’t this work?”
  “I have no idea what is wrong”
  If you have a clear failing test, perhaps we can help
Midterm I: still grading (Really sorry!)
  But almost done!
  Hopefully done by section tomorrow
Regrades:
  You have 1 week after grades are released to request a regrade
  Be sure: If we receive a request, we may regrade whole exam (could lose points)
Midterm II: coming up
  April 22nd; More details upcoming

## Slide 10: Storage Devices
Magnetic disks
  Storage that rarely becomes corrupted
  Large capacity at low cost
  Block level random access (except for SMR – later!)
  Slow performance for random access
  Better performance for streaming access
Flash memory
  Storage that rarely becomes corrupted
  Capacity at intermediate cost (50x disk ???)
  Block level random access
  Good performance for reads; worse for random writes
  Erasure requirement in large blocks
  Wear patterns

## Slide 11: Are we in an inflection point?

## Slide 12: Hard Disk Drives (HDDs)
IBM/Hitachi Microdrive
Western Digital Drive
http://www.storagereview.com/guide/
Read/Write Head
Side View
IBM Personal Computer/AT (1986)
  30 MB hard disk - $500
  30-40ms seek time
  0.7-1 MB/s (est.)
Notes: Winchester disk drives developed by IBM: 1973 first drive
Uses “sealed” assembly with heads floating on air bearings – Bernoulli effect

## Slide 13: The Amazing Magnetic Disk
Unit of Transfer: Sector
  Ring of sectors form a track
  Stack of tracks form a cylinder
  Heads position on cylinders
Disk Tracks ~ 1µm (micron) wide
  Wavelength of light is ~ 0.5µm
  Resolution of human eye: 50µm
  100K on a typical 2.5” disk
Separated by unused guard regions
  Reduces likelihood neighboring tracks are corrupted during writes
  Track length varies across disk
  Outside: More sectors per track, higher bandwidth
  Disk is organized into regions of tracks with same # of sectors/track
  Only outer half of radius is used
    Most of the disk area in the outer regions of the disk
New: Shingled Magnetic Recording (SMR)
  Overlapping tracks  greater density, restrictions on writing
  Seagate (8TB), Hitachi (10TB)

## Slide 14: Magnetic Disk Characteristic
Cylinder: all the tracks under the head at a given point on all surfaces
Read/write: three-stage process:
  Seek time: position the head/arm over the proper track (into proper cylinder)
  Rotational latency: wait for the desired sector to rotate under the read/write head
  Transfer time: transfer a block of bits (sector) under the read-write head
Disk Latency = Queuing Time + Controller time + Seek Time + Rotation Time + Xfer Time
Highest Bandwidth:
  Transfer large group of blocks sequentially from one track
Sector
Track
Cylinder
Head
Platter
Software
Queue
(Device Driver)
Hardware
Controller
Media Time
(Seek+Rot+Xfer)
Request
Result
Notes: To read write information into a sector, a movable arm containing a read/write head is located over each surface.
The term cylinder is used to refer to all the tracks under the read/write head at a given point on all surfaces.
To access data, the operating system must direct the disk through a 3-stage process.
(a) The first step is to position the arm over the proper track. This is the seek operation and the time to complete this operation is called the seek time.
(b) Once the head has reached the correct track, we must wait for the desired sector to rotate under the read/write head. This is referred to as the rotational latency.
(c) Finally, once the desired sector is under the read/write head, the data transfer can begin.
The average seek time as reported by the manufacturer is in the range of 12 ms to 20ms and is calculated as the sum of the time for all possible seeks divided by the number of possible seeks.
This number is usually on the pessimistic side because due to locality of disk reference, the actual average seek time may only be 25 to 33% of the number published.
+2 = 34 min. (Y:14)

## Slide 15: Typical Numbers for Magnetic Disk
Parameter | Info / Range
Space/Density | Space: 8TB (Seagate), 10TB (Hitachi) in 3½ inch form factor! (Introduced in Fall of 2014) Areal Density: ≥ 1Terabit/square inch! (SMR, Helium, …)
Average seek time | Typically 5-10 milliseconds. Depending on reference locality, actual cost may be 25-33% of this number.
Average rotational latency | Most laptop/desktop disks rotate at 3600-7200 RPM (16-8 ms/rotation). Server disks up to 15,000 RPM. Average latency is halfway around disk yielding corresponding times of 8-4 milliseconds
Controller time | Depends on controller hardware
Transfer time | Typically 50 to 100 MB/s. Depends on: Transfer size (usually a sector): 512B – 1KB per sector Rotation speed: 3600 RPM to 15000 RPM Recording density: bits per inch on a track Diameter: ranges from 1 in to 5.25 in
Cost | Drops by a factor of two every 1.5 years (or even faster). $0.03-0.07/GB in 2013
Notes: As far as rotational latency is concerned, most disks rotate at 3,600 RPM or approximately 16 ms per revolution.
Since on average, the information you desired is half way around the disk, the average rotational latency will be 8ms.
The transfer time is a function of transfer size, rotation speed, and recording density.
The typical transfer speed is 2 to 4 MB per second.
Notice that the transfer time is much faster than the rotational latency and seek time.
This is similar to the DRAM situation where the DRAM access time is much shorter than the DRAM cycle time.
***** Do anybody remember what we did to take advantage of the short access time versus cycle time? Well, we interleave!
New International Disk Drive, Equipment, and Materials Association standard is 4KB sectors instead of 512 byte sectors
+2 = 36 min. (Y:16)

## Slide 16: Disk Performance Example
Assumptions:
  Ignoring queuing and controller times for now
  Avg seek time of 5ms,
  7200RPM  Time for rotation: 60000(ms/M)/7200(rev/M) ~= 8ms
  Transfer rate of 4MByte/s, sector size of 1 Kbyte  1024 bytes/4×106 (bytes/s) = 256 × 10-6 sec  .26 ms
Read sector from random place on disk:
  Seek (5ms) + Rot. Delay (4ms) + Transfer (0.26ms)
  Approx 10ms to fetch/put data: 100 KByte/sec
Read sector from random place in same cylinder:
  Rot. Delay (4ms) + Transfer (0.26ms)
  Approx 5ms to fetch/put data: 200 KByte/sec
Read next sector on same track:
  Transfer (0.26ms): 4 MByte/sec
Key to using disk effectively (especially for file systems) is to minimize seek and rotational delays

## Slide 17: Intelligence in the controller
Sectors contain sophisticated error correcting codes
  Disk head magnet has a field wider than track
  Hide corruptions due to neighboring track writes
Sector sparing
  Remap bad sectors transparently to spare sectors on the same surface
Slip sparing
  Remap all sectors (when there is a bad sector) to preserve sequential behavior
Track skewing
  Sector numbers offset from one track to the next, to allow for disk head movement for sequential ops
…

## Slide 18: Solid State Disks (SSDs)
1995 – Replace rotating magnetic media with non-volatile memory (battery backed DRAM)
2009 – Use NAND Multi-Level Cell (2 or 3-bit/cell) flash memory
  Sector (4 KB page) addressable, but stores 4-64 “pages” per memory block
  Trapped electrons distinguish between 1 and 0
No moving parts (no rotate/seek motors)
  Eliminates seek and rotational delay (0.1-0.2ms access time)
  Very low power and lightweight
  Limited “write cycles”
Rapid advance in capacity and cost ever since

## Slide 19: SSD Architecture – Reads
  Read 4 KB Page: ~25 usec
  No seek or rotational latency
  Transfer time: transfer a 4KB page
    SATA: 300-600MB/s => ~4 x103 b / 400 x 106 bps => 10 us
  Latency = Queuing Time + Controller time + Xfer Time
  Highest Bandwidth: Sequential OR Random reads
Host
Buffer
Manager
(software
Queue)
Flash
Memory
Controller
DRAM
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
SATA

## Slide 20: SSD Architecture – Writes (I)
  Writing data is complex! (~200μs – 1.7ms )
  Can only write empty pages in a block
  Erasing a block takes ~1.5ms
  Controller maintains pool of empty blocks by coalescing used pages (read, erase, write), also reserves some % of capacity
Rule of thumb: writes 10x reads, erasure 10x writes
https://en.wikipedia.org/wiki/Solid-state_drive

## Slide 21: Amusing calculation: is a full Kindle heavier than an empty one?
Actually, “Yes”, but not by much
Flash works by trapping electrons:
  So, erased state lower energy than written state
Assuming that:
  Kindle has 4GB flash
  ½ of all bits in full Kindle are in high-energy state
  High-energy state about 10-15 joules higher
  Then: Full Kindle is 1 attogram (10-18gram) heavier (Using E = mc2)
Of course, this is less than most sensitive scale (which can measure 10-9grams)
Of course, this weight difference overwhelmed by battery discharge, weight from getting warm, ….
According to John Kubiatowicz, New York Times, Oct 24, 2011

## Slide 22: Storage Performance & Price (jan 13)
 | Bandwidth (Sequential R/W) | Cost/GB | Size
HDD2 | 50-100 MB/s | $0.03-0.07/GB | 2-4 TB
SSD1,2 | 200-550 MB/s (SATA) 6 GB/s (read PCI) 4.4 GB/s (write PCI) | $0.87-1.13/GB | 200GB-1TB
DRAM2 | 10-16 GB/s | $4-14*/GB *SK Hynix 9/4/13 fire | 64GB-256GB
BW: SSD up to x10 than HDD, DRAM > x10 than SSD
Price: HDD x20 less than SSD, SSD x5 less than DRAM
1http://www.fastestssd.com/featured/ssd-rankings-the-fastest-solid-state-drives/
2http://www.extremetech.com/computing/164677-storage-pricewatch-hard-drive-and-ssd-prices-drop-making-for-a-good-time-to-buy

## Slide 23: SSD Summary
Pros (vs. hard disk drives):
  Low latency, high throughput (eliminate seek/rotational delay)
  No moving parts:
    Very light weight, low power, silent, very shock insensitive
  Read at memory speeds (limited by controller and I/O bus)
Cons
  Small storage (0.1-0.5x disk), expensive (20x disk ???)
    Hybrid alternative: combine small SSD with large HDD
  Asymmetric block write performance: read pg/erase/write pg
    Controller garbage collection (GC) algorithms have major effect on performance
  Limited drive lifetime
    1-10K writes/page for MLC NAND
    Avg failure rate is 6 years, life expectancy is 9–11 years
These are changing rapidly

## Slide 24: What goes into startup cost for I/O?
Syscall overhead
Operating system processing
Controller Overhead
Device Startup
  Mechanical latency for a disk
  Media Access + Speed of light + Routing for network
Queuing (next topic)

## Slide 25: I/O Performance
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
Performance of I/O subsystem
  Metrics: Response Time, Throughput
  Effective BW per op = transfer size / response time
    EffBW(n) = n / (S + n/B) = B / (1 + SB/n )
  Contributing factors to latency:
    Software paths (can be loosely modeled by a queue)
    Hardware controller
    I/O device service time
Queuing behavior:
  Can lead to big increases of latency as utilization increases
  Solutions?
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

## Slide 26: A Simple Deterministic World
Assume requests arrive at regular intervals, take a fixed time to process, with plenty of time between …
Service rate (μ = 1/TS) - operations per sec
Arrival rate: (λ = 1/TA) - requests per second
Utilization: U = λ/μ , where λ < μ
Average rate is the complete story
Queue
Server
arrivals
departures
TQ
TS
TA
TA
TA

## Slide 27: A Ideal Linear World
What does the queue wait time look like?
  Grows unbounded at a rate ~ (Ts/TA) till request rate subsides
Offered Load (TA/TS)
Delivered Throughput
0
1
1
time
Queue delay
time
Queue delay
Delivered Throughput
0
1
1
Offered Load (TA/TS)
Empty Queue
Saturation
Unbounded

## Slide 28: A Bursty World
Requests arrive in a burst, must queue up till served
Same average arrival time, but almost all of the requests experience large queue delays
Even though average utilization is low
Queue
Server
arrivals
departures
T Q
T S
Q depth
Server
Arrivals

## Slide 29: So how do we model the burstiness of arrival?
Chart: 
| 1E-3 | 0.01 | 0.02 | 0.04 | 0.08 | 0.16 | 0.32 | 0.64 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 10
f(x) | 0.999 | 0.99005 | 0.9802 | 0.96079 | 0.92312 | 0.85214 | 0.72615 | 0.52729 | 0.36788 | 0.13534 | 0.049787 | 0.018316 | 0.0067379 | 0.0024788 | 0.00091188 | 0.00033546 | 4.54e-05
Likelihood of an event occuring is independent of how long we’ve been waiting
Elegant mathematical framework if you start with exponential distribution
  Probability density function of a continuous random variable with a mean of 1/λ
  f(x) = λe-λx
  “Memoryless”
Lots of short arrival intervals (i.e., high instantaneous rate)
Few long gaps (i.e., low instantaneous rate)
x (λ)
mean arrival interval (1/λ)

## Slide 30: Background: General Use of random distributions
Server spends variable time with customers
  Mean (Average) m1 = p(T)T
  Variance 2 = p(T)(T-m1)2 = p(T)T2-m12
  Squared coefficient of variance: C = 2/m12 Aggregate description of the distribution.
Important values of C:
  No variance or deterministic  C=0
  “memoryless” or exponential  C=1
    Past tells nothing about future
    Many complex systems (or aggregates) well described as memoryless
  Disk response times C  1.5 (majority seeks < avg)
Mean
(m1)
mean
Memoryless
Distribution
of service times


## Slide 31: Introduction to Queuing Theory
Departures
Arrivals
Queuing System
What about queuing time??
  Let’s apply some queuing theory
  Queuing Theory applies to long term, steady state behavior  Arrival rate = Departure rate
Arrivals characterized by some probabilistic distribution
Departures characterized by some probabilistic distribution
Queue
Controller
Disk
Notes: Old and New Testament by Kleirock
Regret skipping as grad student

## Slide 32: Little’s Law
In any stable system
  Average arrival rate = Average departure rate
the average number of tasks in the system (N) is equal to the throughput (B) times the response time (L)
N (ops) = B (ops/s) x L (s)
Regardless of structure, bursts of requests, variation in service
  instantaneous variations, but it washes out in the average
  Overall requests match departures
arrivals
departures
N
B
L

## Slide 33: A Little Queuing Theory: Some Results
Assumptions:
  System in equilibrium; No limit to the queue
  Time between successive arrivals is random and memoryless
Parameters that describe our system:
  : mean number of arriving customers/second
  Tser: mean time to service a customer (“m1”)
  C: squared coefficient of variance = 2/m12
  μ: service rate = 1/Tser
  u: server utilization (0u1): u = /μ =   Tser
Parameters we wish to compute:
  Tq: Time spent in queue
  Lq: Length of queue =   Tq (by Little’s law)
Results:
  Memoryless service distribution (C = 1):
    Called M/M/1 queue: Tq = Tser x u/(1 – u)
  General service distribution (no restrictions), 1 server:
    Called M/G/1 queue: Tq = Tser x ½(1+C) x u/(1 – u))
Arrival Rate

Queue
Server
Service Rate
μ=1/Tser

## Slide 34: A Little Queuing Theory: An Example
Example Usage Statistics:
  User requests 10 x 8KB disk I/Os per second
  Requests & service exponentially distributed (C=1.0)
  Avg. service = 20 ms (From controller+seek+rot+trans)
Questions:
  How utilized is the disk?
    Ans: server utilization, u = Tser
  What is the average time spent in the queue?
    Ans: Tq
  What is the number of requests in the queue?
    Ans: Lq
  What is the avg response time for disk request?
    Ans: Tsys = Tq + Tser
Computation:
 (avg # arriving customers/s) = 10/s
Tser (avg time to service customer) = 20 ms (0.02s)
u (server utilization) =  x Tser= 10/s x .02s = 0.2
Tq (avg time/customer in queue) = Tser x u/(1 – u) = 20 x 0.2/(1-0.2) = 20 x 0.25 = 5 ms (0 .005s)
Lq (avg length of queue) =  x Tq=10/s x .005s = 0.05
Tsys (avg time/customer in system) =Tq + Tser= 25 ms

## Slide 35: Queuing Theory Resources
Handouts page contains Queueing Theory Resources:
  Scanned pages from Patterson and Hennesey book that gives further discussion and simple proof for general eq.
  A complete website full of resources
Midterms with queueing theory questions:
  Midterm IIs from previous years that I’ve taught
Assume that Queueing theory is fair game for Midterm II and/or the final!

## Slide 36: Optimize I/O Performance
Howto improve performance?
  Make everything faster 
  More Decoupled (Parallelism) systems
    multiple independent buses or controllers
  Optimize the bottleneck to increase service rate
    Use the queue to optimize the service
  Do other useful work while waiting
Queues absorb bursts and smooth the flow
Admissions control (finite queues)
  Limits delays, but may introduce unfairness and livelock
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

## Slide 37: When is the disk performance highest
When there are big sequential reads, or
When there is so much work to do that they can be piggy backed (c-scan)
OK, to be inefficient when things are mostly idle
Bursts are both a threat and an opportunity
<your idea for optimization goes here>
  Waste space for speed?

## Slide 38: Disk Scheduling
Disk can do only one request at a time; What order do you choose to do queued requests?
FIFO Order
  Fair among requesters, but order of arrival may be to random spots on the disk  Very long seeks
SSTF: Shortest seek time first
  Pick the request that’s closest on the disk
  Although called SSTF, today must include rotational delay in calculation, since rotation can be as long as seek
  Con: SSTF good at reducing seeks, but may lead to starvation
SCAN: Implements an Elevator Algorithm: take the closest request in the direction of travel
  No starvation, but retains flavor of SSTF
C-SCAN: Circular-Scan: only goes in one direction
  Skips any requests on the way back
  Fairer than SCAN, not biased towards pages in middle
2,3
2,1
3,10
7,2
5,2
2,2
Head
User
Requests
1
4
2
Disk Head
3

## Slide 39: Building a File System
File System: Layer of OS that transforms block interface of disks (or other block devices) into Files, Directories, etc.
File System Components
  Disk Management: collecting disk blocks into files
  Naming: Interface to find files by name, not by blocks
  Protection: Layers to keep data secure
  Reliability/Durability: Keeping of files durable despite crashes, media failures, attacks, etc
User vs. System View of a File
  User’s view:
    Durable Data Structures
  System’s view (system call interface):
    Collection of Bytes (UNIX)
    Doesn’t matter to system what kind of data structures you want to store on disk!
  System’s view (inside OS):
    Collection of blocks (a block is a logical transfer unit, while a sector is the physical transfer unit)
    Block size  sector size; in UNIX, block size is 4KB

## Slide 40: Translating from User to System View
What happens if user says: give me bytes 2—12?
  Fetch block corresponding to those bytes
  Return just the correct portion of the block
What about: write bytes 2—12?
  Fetch block
  Modify portion
  Write out Block
Everything inside File System is in whole size blocks
  For example, getc(), putc()  buffers something like 4096 bytes, even if interface is one byte at a time
From now on, file is a collection of blocks
File
System

## Slide 41: Disk Management Policies
Basic entities on a disk:
  File: user-visible group of blocks arranged sequentially in logical space
  Directory: user-visible index mapping names to files (next lecture)
Access disk as linear array of sectors. Two Options:
  Identify sectors as vectors [cylinder, surface, sector]. Sort in cylinder-major order. Not used much anymore.
  Logical Block Addressing (LBA). Every sector has integer address from zero up to max number of sectors.
  Controller translates from address  physical position
    First case: OS/BIOS must deal with bad sectors
    Second case: hardware shields OS from structure of disk
Need way to track free disk blocks
  Link free blocks together  too slow today
  Use bitmap to represent free space on disk
Need way to structure files: File Header
  Track which blocks belong at which offsets within the logical file structure
  Optimize placement of files’ disk blocks to match access and usage patterns

## Slide 42: Summary
Devices have complex protocols for interaction and performance characteristics
  Response time (Latency) = Queue + Overhead + Transfer
    Effective BW = BW * T/(S+T)
  HDD: controller + seek + rotation + transfer
  SDD: controller + transfer (erasure & wear)
Bursts & High Utilization introduce queuing delays
Systems (e.g., file system) designed to optimize performance and reliability
  Relative to performance characteristics of underlying device
Disk Performance:
  Queuing time + Controller + Seek + Rotational + Transfer
  Rotational latency: on average ½ rotation
  Transfer time: spec of disk depends on rotation speed and bit storage density
Queuing Latency:
  M/M/1 and M/G/1 queues: simplest to analyze
  As utilization approaches 100%, latency  
  Tq = Tser x ½(1+C) x u/(1 – u))