## Slide 1: CS162 Operating Systems and Systems Programming Lecture 25 Extra Topics: IoT, Quantum Computing
May 4th, 2015
Prof. John Kubiatowicz
http://cs162.eecs.Berkeley.edu

## Slide 2: 1997 - The Internet of Every Computer

## Slide 3: 2007 - The Internet of Every Body

## Slide 4: 2017 - The Internet of Everyday Things

## Slide 5: Why “Real” Information is so Important
Improve Productivity
Protect Health
High-Confidence Transport
Enhance Safety & Security
Improve Food & H20
Save Resources
Preventing Failures
Increase
Comfort
Enable New Knowledge

## Slide 6: Resources in a Smart Space (2011)
Potential Displays Everywhere
  Walls, Tables, Appliances, Smart Phones, Google Glasses….
Audio Output Everywhere
Inputs Everywhere
  Touch Surfaces
  Cameras/ Gesture Tracking
  Voice
Context Tracking
  Who is Where
  What do they want
  Which Inputs map to which applications

## Slide 7: 2013

## Slide 8: 2014

## Slide 9: 2013
The Nest makes headlines!

## Slide 10: 2014

## Slide 11: 2014

## Slide 12: Broad Technology Trends
Today: 1 million transistors per $
Moore’s Law: # transistors on cost-effective chip doubles every 18 months
Mote!
years
Computers
Per Person
103:1
1:106
Laptop
PDA
Mainframe
Mini
Workstation
PC
Cell
1:1
1:103
Bell’s Law: a new computer class emerges every 10 years
Same fabrication technology provides CMOS radios for communication and micro-sensors

## Slide 13: ‘Low-Tech’ Enabling Technology
Microcontroller
Radio
Communication
Flash
Storage
Sensors
IEEE 802.15.4
Network

## Slide 14: The Systems Challenge
applications
service
network
system
architecture
data
mgmt
Monitoring & Managing Spaces and Things
technology
sensing
Power
Comm.
actuate
Miniature, low-power connections to the physical world
Proc
Store
Notes: Now that we’ve set the context, here’s a picture of the rest of the presentation
I do
Kris does

## Slide 15: Key WSN Research Developments
Event-Driven Component-Base Operating System
  Framework for building System & Network abstractions
  Low-Power Protocols
  Hardware and Application Specific
Idle listening
  All the energy is consumed by listening for a packet to receive
  => Turn radio on only when there is something to hear
Reliable routing on Low-Power & Lossy Links
  Power, Range, Obstructions => multi-hop
  Always at edge of SNR => loss is common
  => monitoring, retransmission, and local rerouting
Trickle – don’t flood (tx rate < 1/density, and < info change)
  Connectivity is determined by physical points of interest, not network designer.
  never naively respond to a broadcast
  re-broadcast very very politely

## Slide 16: Internet of Every Thing – Realized 2008
Footprint, power, packet size, & bandwidth
Open version 27k / 4.6k
 | ROM | RAM
CC2420 Driver | 3149 | 272
802.15.4 Encryption | 1194 | 101
Media Access Control | 330 | 9
Media Management Control | 1348 | 20
6LoWPAN + IPv6 | 2550 | 0
Checksums | 134 | 0
SLAAC | 216 | 32
DHCPv6 Client | 212 | 3
DHCPv6 Proxy | 104 | 2
ICMPv6 | 522 | 0
Unicast Forwarder | 1158 | 451
Multicast Forwarder | 352 | 4
Message Buffers | 0 | 2048
Router | 2050 | 106
UDP | 450 | 6
TCP | 1674 | 50
(including runtime)
* Production implementation on TI msp430/cc2420
24038 | ROM
3598 | RAM

## Slide 17: Internet of Every Thing – standardized 2010

## Slide 18: Smart meter rollouts
http://www.edisonfoundation.net/iee/Documents/IEE_SmartMeterRollouts_0512.pdf
Proprietary / Zigbee
Open IPv6, …

## Slide 19: The Mote/TinyOS revolution…
SmartDust
WeC
Rene
Intel
rene’
99
98
00
0 1
03
02
04
06
05
07
SENSIT
Expedition
NEST
NETS/ NOSS
CENS STC
NSF
Cyber-Physical
Mica
Intel/UCB
dot
Intel
iMOTE
XBOW
cc-dot
XBOW
mica2
XBOW
rene2
Intel
cf-mica
Bosch
cc-mica
Dust Inc
blue cc-TI
digital sun
rain-mica
XBOW
mica
zeevo BT
Telos
XBOW
micaZ
Intel
MOTE2
Eyes
BTNode
trio
8 kB rom
½ kB ram
48 kB rom
10 kB ram
802.15.4
LoWPAN/IPv6
Epic
11
IETF RPL
10
Mote inside
uP => Arm Cortex
Radio => 802.15.4g narrow=band freq. hopper
TinyOS too
SOC from here

## Slide 20: TinyOS – Framework for Innovation
Storage
Processing
Wireless
Sensors
WSN mote platform
Radio Serial
Flash
ADC, Sensor I/F
MCU, Timers, Bus,…
Link
Network
Protocols
Blocks, Logs, Files
Scheduling, Management
Streaming drivers
Over-the-air
Programming
Applications and Services
Communication Centric
Resource-Constrained
Event-driven Execution

## Slide 21: Back to The Internet of Everything…?

## Slide 22: An More Global Application Model
A Swarm Application is a Connected graph of Components
  Globally distributed, but locality and QoS aware
  Avoid Stovepipe solutions through reusability
Many components are Shared Services written by programmers with a variety of skill-sets and motivations
  Well-defined semantics and a managed software version scheme
  Service Level Agreements (SLA) with micropayments
Many are “Swarmlets” written by domain programmers
  They care what application does, not how it does it
Sensors
with Aggregation
Distributed
Archival Storage
Channel
Real-Time Components
SwarmLet (“The Application”)
Transform and Archive
Channel
Channel
Channel
Channel
Notes: Note: We want to make it possible for everyone to construct sophisticated swarm applications by writing small components (Swarmlets)

## Slide 23: SWARMLETs
SWARMLET: a software component written by domain programmer that is easy to write but exhibits sophisticated behavior by exploiting services distributed within the infrastructure
Swarmlets specify their needs in terms of human-understandable requirements
  Necessary Services, Frame rates, Minimum Bandwidths
  Locality, Ownership, and Micropayment parameters for sensors and/or data
Swarmlets may evolve into Shared Services
Programmers of Services used by Swarmlets think in terms of contracts provided to Swarmlets

## Slide 24: Meeting the needs of the Swarm
Discover and Manage resource
Integrate sensors, portable devices, cloud components
Guarantee responsiveness, real-time behavior, throughput
Self-adapt to failure and provide performance predictability
Secure, high-performance, durable, available information
Monetize resources when necessary: micropayments
The FOG
Personal/Local
Swarm
Cloud Services

## Slide 25: Support for Swarm Applications
Resource Discovery
  Which resources /services are available?
  What are these resources and what are their capabilities?
  Who owns them and how much do I need?
Real Time Requirements
  Sophisticated multimedia interactions
  Control of/interaction with health-related devices
Responsiveness Requirements
  Provide a good interactive experience to users
Explicitly Parallel Components
  Components exploit parallelism when possible
Direct Interaction with Cloud storage and computation
  Potentially extensive use of remote services
  Serious security/data vulnerability concerns

## Slide 26: The Missing Link?
Home security/ emergency
Unpad
Energy-efficient
home
Health monitoring
Apps
Resources
Sensors/
Input devs
Actuators/
Output devs
Networks
Storage
Computing
SWARM-OS
SWARM-OS: A mediation layer that discovers resources and connects them with applications

## Slide 27: What about the “FOG” and “Cloud”? New Abstraction: the Cell
Properties of a Cell: Service Level Guarantees
  A user-level software component with guaranteed resources
  Has full control over resources it owns (“Bare Metal”)
  Contains at least one memory protection domain (possibly more)
  Contains a set of secured channel endpoints to other Cells
  Contains a security context which may protect and decrypt information
When mapped to the hardware, a cell gets:
  Gang-schedule hardware thread resources (“Harts”)
  Guaranteed fractions of other physical resources
    Physical Pages (DRAM), Cache partitions, memory bandwidth, power
  Guaranteed fractions of system services
Predictability of performance 
  Ability to model performance vs resources
  Ability for user-level schedulers to better provide QoS

## Slide 28: Cell Implementation Platform: Tessellation Version 2
Tessellation Operating System
  Provides basic Cell Implementation
  Build on the Xen Hypervisor
Why Xen?
  Provides clean starting point for resource containers
  Leverage mature OS (Linux) device support, critical drivers can be isolated in a stub domain
  Framework for developing VM schedulers
  Mini-OS, a lightweight POSIX-compatible Xen guest OS, is basis for the customizable app runtime
  Support for ARM and x86
Unikernels: Software Appliances
  Small compiled kernels with only enough components to support one application
  Every component has its own resource container
Dynamic resource optimization framework
Notes: Include here detailed descriptions of the slide content for use in the presentation

## Slide 29: Implementing Cells: Space-Time Partitioning
Spatial Partition: Performance isolation
  Each partition receives a vector of basic resources
    A number HW threads
    Chunk of physical memory
    A portion of shared cache
    A fraction of memory BW
    Shared fractions of services
Partitioning varies over time
  Fine-grained multiplexing and guarantee of resources
    Resources are gang-scheduled
Controlled multiplexing, not uncontrolled virtualization
Partitioning adapted to the system’s needs
Time
Space
Space

## Slide 30: Resource Discovery and Ontology
Dynamically discover resources, services, and cyber-physical components (sensors/actuators) that meet application requirements
  Find local components that meet some specification
  Use ontology to describe exactly what component do
  Distribute these resources (or fractions of services) to application cells in order to meet QoS requirements
Many partial solutions out there, no complete solutions
  Must deal with locality (discover local items) while at same time dealing with remote (global) services
  Must gracefully handle failover of components
One important aspect is that resources must be handed out only to authorized users
  Authorization can involve ownership, micropayments, etc..

## Slide 31: Brokering Service: The Hierarchy of Ownership
Discover Resources in “Domain”
  Devices, Services, Other Brokers
  Resources self-describing?
Allocate and Distribute Resources to Cells that need them
  Solve Impedance-mismatch problem
  Dynamically optimize execution
  Hand out Service-Level Agreements (SLAs) to Cells
  Deny admission to Cells which violate existing agreements
Complete hierarchy
  World graph of applications
Local
Broker
Sibling
Broker
Parent
Broker
Child
Broker
Notes: One way to handle the natural locality of resources is to utilize a hierarchical scheme to discover them. Brokers handle local discovery of child brokers and resources at the same level. Example, a broker on your person, one in the room, one in the building, etc. The brokerage domains naturally reflect both locality and ownership.

## Slide 32: DataCentric Vision
Hardware resources are a commodity
  Computation resource fails? Get another
  Sensor fails? Find another
  Change your location? Find new resources
All that really matters is the information
  Integrity, Privacy, Availability, Durability
  Hardware to prevent accidental information leakage
Permanent state handled by Universal Data Storage, Distribution, and Archiving
We need a new Internet for the Internet of Things?
  Communication and Storage are really duals
  Why separate them?

## Slide 33: The Global Data Plane
Archival Storage and Optimized Streaming
Personal Cache
Aggregate/Filter
Universal Tivo
Cloud Services
Cloud Services
Notes: Can we provide a better substrate on which to build Swarm Applications than raw IP? One option that we are considering is the Universal Data Plane (UDP). This substrate is a universal mechanism for transferring, queuing, streaming, and archiving of information. All sources and destinations of information are given location independent names and thus live in a giant virtual space. The level of indirection is performed by an overlay network (many of which were developed during the peer-to-peer research craze of the early 2000s). This substrate can provide facilities to the common SWARMLET programmer that are only available to big companies (i.e. Google, New York Times, etc).

## Slide 34: GDP Secure Log
Locality Optimization/QoS
  Flat 256-bit address space
  Routes adapted as elements move
  Hardware QoS exploited
  Multicast trees built as needed
Durability
  Replicas/Reed-Solomon coding
Single Writer/Append only
  Owner Key Signs entries
  LOG server rejects bad entries
  Tradeoff in granularity, i.e. frequency of signatures
Multiple Readers/Subscribers
  Random access/push based
LOG
Replica
Server
Writer: Signed Source of Packets
Subscriber
Subscriber
LOG
Replica Server
LOG
Server
Random Reader
Random Reader
Random Reader

## Slide 35: Simple Log-based Use-case
Lightweight Logs  One Log per Device
Log Input Secured via Owner Key/Checked by consumer
Optional encryption for privacy
Timestamps to help ensure freshness
Data
Distillation
Service
Sensors
w/key
Service
w/key
(MultiWriter,
Aggregator,
Control)
Actuator
LOG
LOG
LOG
LOG
LOG

## Slide 36: Build DataStores on top of GDP through Composition
Common Access APIs (CAAPIs): Support common data access methods such as:
  Key/Value Store
  Object Store/File System
  Data Base (i.e. Google Spanner)
CAPPIs exported by services that consume the LOG
  Much more convenient way to access data
The LOG is the Ground Truth for data, but data is projected into a more convenient form
  To do Random File access, Indexing, SQL queries, Latest value for given Key, etc
  Optional Checkpoints stored for quick restart/cloning

## Slide 37: Example: DataBase CAAPI
CAAPI Service can be taken down, replicated, and restarted
Time-stamp driven transactions (Google Spanner)
Cloud-based computation (Spark)
LOG
DataBase Service
(R/W)
DataBase Projection
(RAM)
CAAPI Service
w/key
DataBase Client
DataBase Client
Client
w/key
Client
w/key
Read/Write
Read/Write
LOG
LOG
DataBase Projection
(RAM)
Replica Service
(R/O)
LOG Replica
Slave CAAPI Service
w/o key
Long Distance Communication
Read/SQL

## Slide 38: Properties of the GDP (Summary)
Universal way to address every stream of information
  Publish/Subscribe view of information
  Large flat address space (at least 256 bits)
  Mechanisms for access control, privacy, and transactions
  Streams of data persisted automatically for later access
Location Independence  Above network level
  Build Swarmlets once and run them anywhere
  Migrate or replicate running swarmlets
  Locality optimization/QoS handled by underlying system
Common Access APIs (CAAPIs) provide standard Interfaces
  Key/Value Store, Data Bases, File Systems
Deep Archival Storage:
  Automatic Geographically Distributed Archival Storage
One system for sensors and big data

## Slide 39: The Revolution
10M
1B
10B
1T
100B
1990
2010
2020
Computers
People
Everything
Connectivity
Community
Awareness
2000

## Slide 40: The Revolution
10M
1B
10B
1T
100B
1990
2000
2010
2020
Computers
People
Everything
Cost to Connect
Things Connected
$100
$1
1¢

## Slide 41: Use Quantum Mechanics to Compute?
Weird but useful properties of quantum mechanics:
  Quantization: Only certain values or orbits are good
    Remember orbitals from chemistry???
  Superposition: Schizophrenic physical elements don’t quite know whether they are one thing or another
All existing digital abstractions try to eliminate QM
  Transistors/Gates designed with classical behavior
  Binary abstraction: a “1” is a “1” and a “0” is a “0”
Quantum Computing: Use of Quantization and Superposition to compute.
Interesting results:
  Shor’s algorithm: factors in polynomial time!
  Grover’s algorithm: Finds items in unsorted database in time proportional to square-root of n.
  Materials simulation: exponential classically, linear-time QM

## Slide 42: Quantization: Use of “Spin”
Particles like Protons have an intrinsic “Spin” when defined with respect to an external magnetic field
Quantum effect gives “1” and “0”:
  Either spin is “UP” or “DOWN” nothing between
North
South
Spin ½ particle:
(Proton/Electron)
Representation:
|0> or |1>

## Slide 43: Kane Proposal II (First one didn’t quite work)
Bits Represented by combination of proton/electron spin
Operations performed by manipulating control gates
  Complex sequences of pulses perform NMR-like operations
Temperature < 1° Kelvin!
Phosphorus
Impurity Atoms
Single Spin
Control Gates
Inter-bit
Control Gates

## Slide 44: Now add Superposition!
The bit can be in a combination of “1” and “0”:
  Written as: = C0|0> + C1|1>
  The C’s are complex numbers!
  Important Constraint: |C0|2 + |C1|2 =1
If measure bit to see what looks like,
  With probability |C0|2 we will find |0> (say “UP”)
  With probability |C1|2 we will find |1> (say “DOWN”)
Is this a real effect? Options:
  This is just statistical – given a large number of protons, a fraction of them (|C0|2 ) are “UP” and the rest are down.
  This is a real effect, and the proton is really both things until you try to look at it
Reality: second choice!
  There are experiments to prove it!

## Slide 45: A register can have many values!
Implications of superposition:
  An n-bit register can have 2n values simultaneously!
  3-bit example:
    = C000|000>+ C001|001>+ C010|010>+ C011|011>+ C100|100>+ C101|101>+ C110|110>+ C111|111>
Probabilities of measuring all bits are set by coefficients:
  So, prob of getting |000> is |C000|2, etc.
  Suppose we measure only one bit (first):
    We get “0” with probability: P0=|C000|2+ |C001|2+ |C010|2+ |C011|2 Result: = (C000|000>+ C001|001>+ C010|010>+ C011|011>)
    We get “1” with probability: P1=|C100|2+ |C101|2+ |C110|2+ |C111|2 Result: = (C100|100>+ C101|101>+ C110|110>+ C111|111>)
Problem: Don’t want environment to measure before ready!
  Solution: Quantum Error Correction Codes!

## Slide 46: Spooky action at a distance
Consider the following simple 2-bit state:
    = C00|00>+ C11|11>
  Called an “EPR” pair for “Einstein, Podolsky, Rosen”
Now, separate the two bits:
If we measure one of them, it instantaneously sets other one!
  Einstein called this a “spooky action at a distance”
  In particular, if we measure a |0> at one side, we get a |0> at the other (and vice versa)
Teleportation
  Can “pre-transport” an EPR pair (say bits X and Y)
  Later to transport bit A from one side to the other we:
    Perform operation between A and X, yielding two classical bits
    Send the two bits to the other side
    Use the two bits to operate on Y
    Poof! State of bit A appears in place of Y
Light-Years?

## Slide 47: Model: Operations on coefficients + measurements
Basic Computing Paradigm:
  Input is a register with superposition of many values
    Possibly all 2n inputs equally probable!
  Unitary transformations compute on coefficients
    Must maintain probability property (sum of squares = 1)
    Looks like doing computation on all 2n inputs simultaneously!
  Output is one result attained by measurement
If do this poorly, just like probabilistic computation:
  If 2n inputs equally probable, may be 2n outputs equally probable.
  After measure, like picked random input to classical function!
  All interesting results have some form of “fourier transform” computation being done in unitary transformation
Unitary
Transformations
Input
Complex
State
Measure
Output
Classical
Answer

## Slide 48: Shor’s Factoring Algorithm
The Security of RSA Public-key cryptosystems depends on the difficulty of factoring a number N=pq (product of two primes)
  Classical computer: sub-exponential time factoring
  Quantum computer: polynomial time factoring
Shor’s Factoring Algorithm (for a quantum computer)
  Choose random x : 2  x  N-1.
  If gcd(x,N)  1, Bingo!
  Find smallest integer r : xr  1 (mod N)
  If r is odd, GOTO 1
  If r is even, a  x r/2 (mod N)  (a-1)(a+1) = kN
  If a  N-1(mod N) GOTO 1
  ELSE gcd(a ± 1,N) is a non trivial factor of N.
Hard
Easy
Easy
Easy
Easy
Easy
Easy

## Slide 49: Finding r with xr  1 (mod N)
Finally: Perform measurement
  Find out r with high probability
  Get |y>|aw’> where y is of form k/r and w’ is related
Quantum
Fourier
Transform

## Slide 50: Quantum Computing Architectures
Why study quantum computing?
  Interesting, says something about physics
    Failure to build  quantum mechanics wrong?
  Mathematical Exercise (perfectly good reason)
  Hope that it will be practical someday:
    Shor’s factoring, Grover’s search, Design of Materials
    Quantum Co-processor included in your Laptop?
To be practical, will need to hand quantum computer design off to classical designers
  Baring Adiabatic algorithms, will probably need 100s to 1000s (millions?) of working logical Qubits  1000s to millions of physical Qubits working together
  Current chips: ~1 billion transistors!
Large number of components is realm of architecture
  What are optimized structures of quantum algorithms when they are mapped to a physical substrate?
  Optimization not possible by hand
    Abstraction of elements to design larger circuits
    Lessons of last 30 years of VLSI design: USE CAD

## Slide 51: Quantum Circuit Model
Quantum Circuit model – graphical representation
  Time Flows from left to right
  Single Wires: persistent Qubits, Double Wires: classical bits
    Qubit – coherent combination of 0 and 1:  = |0 + |1
  Universal gate set: Sufficient to form all unitary transformations
Example: Syndrome Measurement (for 3-bit code)
  Measurement (meter symbol) produces classical bits
Quantum CAD
  Circuit expressed as netlist
  Computer manpulated circuits and implementations

## Slide 52: Adding Quantum ECC
Quantum State Fragile  encode all Qubits
  Uses many resources: e.g. 3-level [[7,1,3]] code 343 physical Qubits/logical Qubit)!
Still need to handle operations (fault-tolerantly)
  Some set of gates are simply “transversal:”
    Perform identical gate between each physical bit of logical encoding
  Others (like T gate for [[7,1,3]] code) cannot be handled transversally
    Can be performed fault-tolerantly by preparing appropriate ancilla
Finally, need to perform periodical error correction
  Correct after every(?): Gate, Long distance movement, Long Idle Period
  Correction reducing entropy  Consumes Ancilla bits
Observation:   90% of QEC gates are used for ancilla production  70-85% of all gates are used for ancilla production
H
T
Not Transversal!
n-physical Qubits per logical Qubit
H
T
X
Encoded
/8 (T)
Ancilla
SX
T:
Correct
Correct
Correct
Correct
Correct
Correct
Correct
Correct
QEC
Ancilla
Correct
Errors
Correct
Syndrome
Computation

## Slide 53: Outline
Quantum Computing
Ion Trap Quantum Computing
Quantum Computer Aided Design
  Area-Delay to Correct Result (ADCR) metric
  Comparison of error correction codes
Quantum Data Paths
  QLA, CQLA, Qalypso
  Ancilla factory and Teleportation Network Design
Error Correction Optimization (“Recorrection”)
Shor’s Factoring Circuit Layout and Design

## Slide 54: MEMs-Based Ion Trap Devices
Ion Traps: One of the more promising quantum computer implementation technologies
  Built on Silicon
    Can bootstrap the vast infrastructure that currently exists in the microchip industry
  Seems to be on a “Moore’s Law” like scaling curve
    12 bits exist, 30 promised soon, …
    Many researchers working on this problem
  Some optimistic researchers speculate about room temperature
Properties:
  Has a long-distance Wire
    So-called “ballistic movement”
  Seems to have relatively long decoherence times
  Seems to have relatively low error rates for:
    Memory, Gates, Movement

## Slide 55: Quantum Computing with Ion Traps
Electrode Control
Qubits are atomic ions (e.g. Be+)
  State is stored in hyperfine levels
  Ions suspended in channels between electrodes
Quantum gates performed by lasers (either one or two bit ops)
  Only at certain trap locations
  Ions move between laser sites to perform gates
Classical control
  Gate (laser) ops
  Movement (electrode) ops
    Complex pulse sequences to cause Ions to migrate
    Care must be taken to avoid disturbing state
Demonstrations in the Lab
  NIST, MIT, Michigan, many others
Gate Location
Qubit Ions
Electrodes
Courtesy of Chuang group, MIT
Notes: If we are going to talk about automating design of quantum circuit layouts, we need to first talk about the underlying technology model

## Slide 56: An Abstraction of Ion Traps
Basic block abstraction: Simplify Layout
Evaluation of layout through simulation
  Yields Computation Time and Probability of Success
Simple Error Model: Depolarizing Errors
  Errors for every Gate Operation and Unit of Waiting
  Ballistic Movement Error: Two error Models
    Every Hop/Turn has probability of error
    Only Accelerations cause error
in/out ports
straight
3-way
4-way
turn
gate locations

## Slide 57: Ion Trap Physical Layout
q0
q1
q2
q3
q4
q5
q6
Qubits
Time
Input: Gate level quantum circuit
  Bit lines
  1-qubit gates
  2-qubit gates
Output:
  Layout of channels
  Gate locations
  Initial locations of ions
  Movement/gate schedule
  Control for schedule
q0
q3
q4
q5
q6
q1
q2
Notes: This paper focuses on the automation of physical layout of ion traps, here is a more precise definition of the problem we are solving

## Slide 58: Outline
Quantum Computering
Ion Trap Quantum Computing
Quantum Computer Aided Design
  Area-Delay to Correct Result (ADCR) metric
  Comparison of error correction codes
Quantum Data Paths
  QLA, CQLA, Qalypso
  Ancilla factory and Teleportation Network Design
Error Correction Optimization (“Recorrection”)
Shor’s Factoring Circuit Layout and Design

## Slide 59: Vision of Quantum Circuit Design
Classical Control
Teleportation Network
Schematic Capture (Graphical Entry)
Quantum Assembly
(QASM)
OR
QEC Insertion
Partitioning
Layout
Network Insertion
Error Analysis
…
Optimization
CAD Tool Implementation
Custom Layout and
Scheduling

## Slide 60: Important Measurement Metrics
Traditional CAD Metrics:
  Area
    What is the total area of a circuit?
    Measured in macroblocks (ultimately m2 or similar)
  Latency (Latencysingle)
    What is the total latency to compute circuit once
    Measured in seconds (or s)
  Probability of Success (Psuccess)
    Not common metric for classical circuits
    Account for occurrence of errors and error correction
Quantum Circuit Metric: ADCR
  Area-Delay to Correct Result: Probabilistic Area-Delay metric
  ADCR = Area  E(Latency) =
  ADCRoptimal: Best ADCR over all configurations
Optimization potential: Equipotential designs
  Trade Area for lower latency
  Trade lower probability of success for lower latency

## Slide 61: How to evaluate a circuit?
First, generate a physical instance of circuit
  Encode the circuit in one or more QEC codes
  Partition and layout circuit: Highly dependant of layout heuristics!
    Create a physical layout and scheduling of bits
    Yields area and communication cost
Then, evaluate probability of success
  Technique that works well for depolarizing errors: Monte Carlo
    Possible error points: Operations, Idle Bits, Communications
  Vectorized Monte Carlo: n experiments with one pass
  Need to perform hybrid error analysis for larger circuits
    Smaller modules evaluated via vector Monte Carlo
    Teleportation infrastructure evaluated via fidelity of EPR bits
Finally – Compute ADCR for particular result
Normal
Monte Carlo:
n times
Vector
Monte Carlo:
single pass

## Slide 62: Quantum CAD flow
QEC Insert
Circuit Synthesis
Hybrid Fault
Analysis
Circuit
Partitioning
Mapping, Scheduling,
Classical control
Communication
Estimation
Teleportation
Network Insertion
Input Circuit
Output Layout
ReSynthesis (ADCRoptimal)
Psuccess
Complete Layout
ReMapping
Error Analysis
Most Vulnerable Circuits
Fault-Tolerant
Circuit
(No layout)
Partitioned
Circuit
Functional System
QEC Optimization
Fault Tolerant
ADCR computation

## Slide 63: Example Place and Route Heuristic: Collapsed Dataflow
Gate locations placed in dataflow order
  Qubits flow left to right
  Initial dataflow geometry folded and sorted
  Channels routed to reflect dataflow edges
Too many gate locations, collapse dataflow
  Using scheduler feedback, identify latency critical edges
  Merge critical node pairs
  Reroute channels
Dataflow mapping allows pipelining of computation!
q0
q1
q2
q3
q0
q1
q2
q3
q0
q1
q2
q3
Notes: Greedy places gates with no global knowledge of the circuit structure, our second heuristic tries to exploit spatial locality in the given circuit by laying out gates in roughly dataflow order
Number of gate locations is same as circuit gates, so in the millions this doesn’t work but it is a start
Columns sorted to maximize left to right motion without turns
As mentione, qubits flow left to right naturally in this design, so this heuristic is especially well suited to circuits that operate repeatedly on streams of qubits at high throughput, inheirently pipelined

## Slide 64: Outline
Quantum Computing
Ion Trap Quantum Computing
Quantum Computer Aided Design
  Area-Delay to Correct Result (ADCR) metric
  Comparison of error correction codes
Quantum Data Paths
  QLA, CQLA, Qalypso
  Ancilla factory and Teleportation Network Design
Error Correction Optimization (“Recorrection”)
Shor’s Factoring Circuit Layout and Design

## Slide 65: Quantum Logic Array (QLA)
Anc
Comp
Anc
Comp
Anc
Comp
Anc
Comp
Anc
Comp
Anc
Comp
Anc
Comp
Anc
Comp
Anc
Comp
TP
EPR
EPR
EPR
EPR
EPR
EPR
EPR
EPR
EPR
EPR
EPR
EPR
TP
TP
TP
TP
TP
EPR
EPR
EPR
Correct
Correct
1 or 2-Qubit
Gate (logical)
Storage for
2 Logical Qubits
(In-Place)
n-physical
Qubits
Syndrome
Ancilla
Factory
Correct
Basic Unit:
  Two-Qubit cell (logical)
  Storage, Compute, Correction
Connect Units with Teleporters
  Probably in mesh topology, but details never entirely clear from original papers
First Serious (Large-scale) Organization (2005)
  Tzvetan S. Metodi, Darshan Thaker, Andrew W. Cross, Frederic T. Chong, and Isaac L. Chuang
Teleporter
NODE
EPR
EPR
EPR
EPR

## Slide 66: Running Circuit at “Speed of Data”
Parallel Circuit Latency
Often, Ancilla qubits are independent of data
  Preparation may be pulled offline
  Very clear Area/Delay tradeoff:
Ancilla qubits should be ready “just in time” to avoid ancilla decoherence from idleness
H
C
X
H
T
T
QEC
QEC
QEC
QEC
QEC
QEC
T-Ancilla
T-Ancilla
Q0
Q1
QEC Ancilla
QEC
Ancilla
QEC
Ancilla
QEC
Ancilla
QEC
Ancilla
QEC
Ancilla
Hardware Devoted to
Parallel Ancilla Generation
Serial Circuit Latency

## Slide 67: How much Ancilla Bandwidth Needed?
32-bit Quantum Carry-Lookahead Adder
  Ancilla use very uneven (zero and T ancilla)
  Performance is flat at high end of ancilla generation bandwidth
    Can back off 10% in maximum performance an save orders of magnitude in ancilla generation area
Many bits idle at any one time
  Need only enough ancilla to maintain state for these bits
  Many not need to frequently correct idle errors
Conclusion: makes sense to compute ancilla requirements and share area devoted to ancilla generation

## Slide 68: Ancilla Factory Design I
Encoded Ancilla
Verification Qubits
“In-place” ancilla preparation
Ancilla factory consists of many of these
  Encoded ancilla prepared
  in many places, then
  moved to output port
  Movement is costly!
In-place
Prep
In-place
Prep
In-place
Prep
In-place
Prep
0 Prep
Cat Prep
0 Prep
Cat Prep
0 Prep
Cat Prep
Verify
Verify
Verify
?
?
?
Bit
Correct
Phase
Correct

## Slide 69: Ancilla Factory Design II
Pipelined ancilla preparation: break into stages
  Steady stream of encoded ancillae at output port
  Fully laid out and scheduled to get area and bandwidth estimates
Physical
0 Prep
CNOTs
Cat Prep
Crossbar
CNOTs
Cat Prep
Crossbar
Verif
Verif
Physical
0 Prep
X/Z
Correct
Crossbar
X/Z
Correct
Junk Physical Qubits
Good Encoded Ancillae
Recycle cat state qubits and failures
Recycle used correction qubits

## Slide 70: The Qalypso Datapath Architecture
Dense data region
  Data qubits only
  Local communication
Shared Ancilla Factories
  Distributed to data as needed
  Fully multiplexed to all data
  Output ports ( ): close to data
  Input ports ( ): may be far from data (recycled state irrelevant)
Regions connected by teleportation networks
R
R
R

## Slide 71: Tiled Quantum Datapaths
Several Different Datapaths mappable by our CAD flow
  Variations include hand-tuned Ancilla generators/factories
Memory: storage for state that doesn’t move much
  Less/different requirements for Ancilla
  Original CQLA paper used different QEC encoding
Automatic mapping must:
  Partition circuit among compute and memory regions
  Allocate Ancilla resources to match demand (at knee of curve)
  Configure and insert teleportation network
Anc
Comp
Anc
Comp
Anc
Comp
Anc
Comp
Anc
Comp
Anc
Comp
Anc
Comp
Anc
Comp
Anc
Comp
EPR
EPR
EPR
EPR
EPR
EPR
EPR
EPR
EPR
EPR
EPR
EPR
TP
TP
TP
TP
Previous: QLA, LQLA
Anc
Mem
Anc
Mem
Anc
Comp
Anc
Comp
Anc
Comp
Anc
Mem
Anc
Mem
Anc
Mem
Anc
Mem
TP
TP
TP
TP
EPR
EPR
EPR
EPR
EPR
EPR
EPR
EPR
EPR
EPR
EPR
EPR
Previous: CQLA, CQLA+
TP
Anc
Comp
Anc
Anc
Mem
Anc
Comp
Anc
Mem
Anc
Mem
TP
TP
EPR
EPR
EPR
EPR
EPR
EPR
EPR
EPR
Anc
Comp
Our Group: Qalypso

## Slide 72: Which Datapath is Best?
Random Circuit Generation
  f(Gate Count, Gate Types, Qubit Count, Splitting factor)
  Splitting factor (r): measures connectivity of the circuit
    Example: 0.5 splits Qubits in half, adds random gates between two halves, then recursively splits results
    Closely related to Rent’s parameter
Qalypso clear winner (for all r)
  4x lower latency than LQLA
  2x smaller area than CQLA+
Why Qalypso does well:
  Shared, matched ancilla generation
  Automatic network sizing (not one Teleporter for every two Qubits)
  Automatic Identification of Idle Qubits (memory)
LQLA and CQLA+ perform close second
  Original datapaths supplemented with better ancilla generators, automatic network sizing, and Idle Qubit identification
  Original QLA and CQLA do very poorly for large circuits

## Slide 73: How to design Teleportation Network
What is the architecture of the network?
  Including Topology, Router design, EPR Generators, etc..
What are the details of EPR distribution?
What are the practical aspects of routing?
  When do we set up a channel?
  What path does the channel take?
EPR Stream
Y Teleporters
X Teleporters
Incoming Classical Information
(Unique ID, Dest, Correction Info)
Storage
Storage
Storage
Storage
CC
CC
CC
CC
Outgoing Message

## Slide 74: Basic Idea: Chained Teleportation
Positive Features
  Regularity (can build classical network topologies)
  T node linking not on critical path
  Pre-purification part of link setup
    Fidelity amplification of the line
  Allows continuous stream of EPR correlations to be established for use when necessary
G
T
T
G
T
G
T
G
T
G
T
P
P
Teleportation
Teleportation
Adjacent T nodes linked for teleportation

## Slide 75: Pre-Purification
Experiment: Transmit enough EPR pairs over network to meet required fidelity of channel
  Measure total global traffic
  Higher Fidelity local EPR pairs  less global EPR traffic
Benefit: decreased congestion at T Nodes
Error Rate Per Operation
Long-Distance EPR Pairs Per Data Communication
T
G
T

## Slide 76: Building a Mesh Interconnect
Grid of T nodes
Packet-switched network
- Options: Dimension-Order or Adaptive Routing
- Precomputed or on-demand start time for setup
T
T
T
T
T
T
T
T
P
P
P
P
P
P
P
P
G
G
G
G
G
G
G
G
G
G
, linked by G nodes
Each EPR qubit has associated classical message
Gate
Gate
Gate
Gate
Gate
Gate
Gate
Gate

## Slide 77: Outline
Quantum Computing
Ion Trap Quantum Computing
Quantum Computer Aided Design
  Area-Delay to Correct Result (ADCR) metric
  Comparison of error correction codes
Quantum Data Paths
  QLA, CQLA, Qalypso
  Ancilla factory and Teleportation Network Design
Error Correction Optimization (“Recorrection”)
Shor’s Factoring Circuit Layout and Design

## Slide 78: Reducing QEC Overhead
Standard idea: correct after every gate, and long communication, and long idle time
  This is the easiest for people to analyze
This technique is suboptimal (at least in some domains)
  Not every bit has same noise level!
Different idea: identify critical Qubits
  Try to identify paths that feed into noisiest output bits
  Place correction along these paths to reduce maximum noise
H
H
Correct
Correct
Correct
Correct
Correct
Correct
Correct
H
H
Correct

## Slide 79: Simple Error Propagation Model
4
3
4
1
1
2
1
1
2
3
3
1
2
1
2
1
EDist model of error propagation:
  Inputs start with EDist = 0
  Each gate propagates max input EDist to outputs
  Gates add 1 unit of EDist, Correction resets EDist to 1
Maximum EDist corresponds to Critical Path
  Back track critical paths that add to Maximum EDist
Add correction to keep EDist below critical threshold
Error Distance (EDist) Labels
Maximum EDist
propagation:
4=max(3,1)+1
H
Correct
Correct

## Slide 80: QEC Optimization
Modified version of retiming algorithm: called “recorrection:”
  Find minimal placement of correction operations that meets specified MAX(EDist)  EDistMAX
Probably of success not always reduced for EDistMAX > 1
  But, operation count and area drastically reduced
Use Actual Layouts and Fault Analysis
  Optimization pre-layout, evaluated post-layout
EDistMAX
iteration
QEC Optimization
EDistMAX
Partitioning
and
Layout
Fault
Analysis
Optimized
Layout
Input
Circuit
1024-bit QRCA and QCLA adders

## Slide 81: Recorrection in presence of different QEC codes
500 Gate Random Circuit (r=0.5)
Not all codes do equally well with Recorrection
  Both [[23,1,7]] and [[7,1,3]] reasonable candidates
  [[25,1,5]] doesn’t seem to do as well
Cost of communication and Idle errors is clear here!
However – real optimization situation would vary EDist to find optimal point
Probability of Success
Move Error Rate per Macroblock
EDistMAX=3
Probability of Success
Idle Error Rate per CNOT Time
EDistMAX=3

## Slide 82: Outline
Quantum Computing
Ion Trap Quantum Computing
Quantum Computer Aided Design
  Area-Delay to Correct Result (ADCR) metric
  Comparison of error correction codes
Quantum Data Paths
  QLA, CQLA, Qalypso
  Ancilla factory and Teleportation Network Design
Error Correction Optimization (“Recorrection”)
Shor’s Factoring Circuit Layout and Design

## Slide 83: Comparison of 1024-bit adders
1024-bit Quantum Adder Architectures
  Ripple-Carry (QRCA)
  Carry-Lookahead (QCLA)
Carry-Lookahead is better in all architectures
QEC Optimization improves ADCR by order of magnitude in some circuit configurations
ADCRoptimal for 1024-bit QCLA
ADCRoptimal for 1024-bit QRCA and QCLA

## Slide 84: Area Breakdown for Adders
Error Correction is not predominant use of area
  Only 20-40% of area devoted to QEC ancilla
  For Optimized Qalypso QCLA, 70% of operations for QEC ancilla generation, but only about 20% of area
T-Ancilla generation is major component
  Often overlooked
Networking is significant portion of area when allowed to optimize for ADCR (30%)
  CQLA and QLA variants didn’t really allow for much flexibility

## Slide 85: Investigating 1024-bit Shor’s
Full Layout of all Elements
  Use of 1024-bit Quantum Adders
  Optimized error correction
  Ancilla optimization and Custom Network Layout
Statistics:
  Unoptimized version: 1.351015 operations
  Optimized Version 1000X smaller
  QFT is only 1% of total execution time

## Slide 86: 1024-bit Shor’s Continued
Circuits too big to compute Psuccess
  Working on this problem
Fastest Circuit: 6108 seconds ~ 19 years
  Speedup by classically computing recursive squares?
Smallest Circuit: 7659 mm2
  Compare to previous estimate of 0.9 m2 = 9105 mm2