## Slide 1: Midterm Review
CS 168, Fall 2014
Sylvia Ratnasamy
http://inst.eecs.berkeley.edu/~cs168/

## Slide 2: Logistics
Test is in this classroom starting at 4:10pm
Closed book, closed notes, etc.
Single two-sided “cheat sheet”, handwritten
No calculators, electronic devices, etc.
  Test does not require any complicated calculation
I will have extra office hours
  Friday, Oct 17 1-2pm in 413 Soda Hall
  Monday, Oct 20 10-11am in 413 Soda Hall

## Slide 3: General Guidelines (1)
Test only assumes material covered in lecture & sections
  Text: only to clarify details and context for the above
The test doesn’t require you to do complicated calculations
  Use this as a hint to whether you are on the right track
You don’t need to memorize packet headers
  We’ll provide the IP header for your reference on the exam sheet
You do need to understand how things work
  not for the sake of knowing gory details but to understand pros/cons, when a solution is applicable/useful/useless, etc.

## Slide 4: General Guidelines (2)
Be prepared to:
  Weigh design options outside of the context we studied them in
  e.g., I had a TCP connection, then BGP went nuts…”
  Contemplate new designs we haven’t talked about
    e.g., I introduce a new IP address format; how does this affect..”
    e.g., I start with UDP, but want weak reliability of the form...”
    Don’t let this daunt you. Reason from what you know about the pros/cons of solutions we did study
      e.g., TCP is inefficient when…

## Slide 5: General Guidelines (3)
Exam format (tentative!)
  Q1) 20 multiple-choice questions
    ordered (roughly) from easiest to hardest
  Q2) Design questions: A set of “here’s a scenario, tell me if the following is true/false”-style questions
    ordered (roughly) from easiest to hardest within each scenario
  Q3+ more traditional questions
    (we think) 3 < 4 < 5 < … (< implies easier than)
    sub-questions within each question ordered easiest to hardest
Pace yourself accordingly!

## Slide 6: This Review
Walk through what we expect you to know: key topics, important aspects of each
Just because I didn’t cover it in review doesn’t mean you don’t need to know it
  But if I covered it today, you should know it
My plan: summarize, not explain
  Stop me when you want to discuss something further!

## Slide 7: Topics
Basic concepts (lectures 2, 3)
Architecture and principles (lecture 4)
Network layer (lecs. 4-9)
  Concepts: valid routing state, convergence, least-cost paths
  Overall context (inter- and intra-domain routing)
  Computing least-cost routes (DV, LS)
  IP addressing
  Inter-domain
  Router architecture
Transport (lecs. 9 -12)
  Role of the transport layer
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control: general concepts only

## Slide 8: Basic concepts
You should know:
  statistical multiplexing
  packet vs. circuit switching
  link characteristics
  packet delays

## Slide 9: How are network resources shared?
Two approachces
Reservations
On demand

## Slide 10: Intuition: reservations
12Mbps
Time
11Mbps
13Mbps
Link capacity = 30Mbps
Each source gets 10Mbps
Frequent overloading

## Slide 11: Intuition: on demand
No overloading
Time
Link capacity = 30Mbps

## Slide 12: Two approaches to sharing
Reservations  circuit switching
On demand  packet switching

## Slide 13: Two approaches to sharing
Packet switching
  network resources consumed on demand per-packet
  “admission control”: per packet
Circuit switching
  network resources reserved a priori at “connection” initiation
  "admission control": per connection

## Slide 14
Packet switching exploits statistical multiplexing better than circuit switching
Sharing using the statistics of demand
Good for bursty traffic (average << peak demand)
Similar to insurance, with the same failure mode

## Slide 15: Circuit Switching
src sends a reservation request to dst
(2) Switches “establish a circuit”
(3) src starts sending data
(4) src sends a “teardown circuit” message
dst
10Mb/s?
10Mb/s?
10Mb/s?
src
✔
✔
✔
Notes: multiple conversations in parallel
resources are shared

## Slide 16: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”
Switches “forward” packets based on their headers
Each packet travels independently
No link resources are reserved in advance

## Slide 17: Circuit Switching
Pros
  predictable performance
  simple/fast switching (once circuit established)
Cons
  inefficient when traffic is bursty
  complexity of circuit setup/teardown
  circuit setup adds delay
  switch fails  its circuit(s) fails

## Slide 18: Packet Switching
Pros
  efficient use of network resources
  simpler to implement
  robust: can “route around trouble”
Cons
  requires buffer management and congestion control
  unpredictable performance

## Slide 19: Performance Metrics
Delay
Loss
Throughput

## Slide 20: A network link
Link bandwidth
  number of bits sent/received per unit time (bits/sec or bps)
Propagation delay
  time for one bit to move through the link (seconds)
Bandwidth-Delay Product (BDP)
  number of bits “in flight” at any time
  BDP = bandwidth × propagation delay
bandwidth
Propagation delay
delay x bandwidth

## Slide 21: Delay
Consists of four components
  transmission delay
  propagation delay
  queuing delay
  processing delay
due to link properties
due to traffic mix and
switch internals

## Slide 22
transmission
End-to-end delay
propagation
queuing
processing
transmission
propagation
queuing
processing
transmission
propagation

## Slide 23: Packet Delay Sending 100B packets from A to B?
time=0
A
B
100Byte packet
Time
1Mbps, 1ms
Time to transmit one bit = 1/106s
Time to transmit 800 bits=800x1/106s
Time when that bit reaches B = 1/106+1/103s
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms

## Slide 24: Little’s Law (1961)
L = A x W
A: Average rate at which packets arrive at a queue
W: Average time packets wait at the queue
L: Avg. number of packets waiting in queue (q length)
Easy to compute L, harder to compute W
Notes: Row vs column

## Slide 25: Topics
Basic concepts (lectures 2,3)
Architecture and principles (lecture 4)
Network layer (lecs. 4-9)
  Concepts: valid routing state, convergence, least-cost paths
  Overall context (inter- and intra-domain routing)
  Computing least-cost routes (DV, LS)
  IP addressing
  Inter-domain
  Router architecture
Transport (lecs. 9 -12)
  Role of the transport layer
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control: general concepts only

## Slide 26: Architecture
You should know
  Layering: what/where/why
  Protocols: what/where/why
  Principles: layering, end-to-end argument, “narrow waist”
  Benefits and weaknesses/consequences of principles/choices
    E.g., layering is good because… but has hurt…

## Slide 27: Layering
Layering is a particular form of modularization
System is broken into a vertical hierarchy of logically distinct entities (layers)
Service provided by one layer is based solely on the service provided by layer below

## Slide 28: Internet Layers
Applications
…built on…
…built on…
…built on…
…built on…
Reliable (or unreliable) transport
Best-effort global packet delivery
Best-effort local packet delivery
Physical transfer of bits
Application
Transport
Network
Data link
Physical
L1
L2
L3
L4
L7

## Slide 29: What gets implemented where?
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch
Notes: Why go up? Why not stay down in the lower levels?

## Slide 30: Logical Communication
Layers interacts with peer’s corresponding layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 31: Physical Communication
Communication goes down to physical network
Then up to relevant layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 32: Protocols and Layers
Communication between peer layers on different systems is defined by protocols
Application
Transport
Network
Data link
Physical
L1
L2
L3
L4
L7
Application
Transport
Network
Data link
Physical
L1
L2
L3
L4
L7

## Slide 33: Protocols at different layers
There is just one network-layer protocol!
Application
Transport
Network
Data link
Physical
L1
L2
L3
L4
L7
SMTP
HTTP
DNS
NTP
TCP
UDP
IP
Ethernet
FDDI
PPP
optical
copper
radio
PSTN

## Slide 34: Layer Encapsulation
App
Transport
Network
Link
Physical
Ht
msg
Hn
Hl
Alice
Bob
Router
Ht
msg
Hn
Ht
msg
msg
Ht
msg
msg
Ht
msg
Hn
Hl
Ht
msg
Hn
Ht
msg
Hn
Hl
Ht
msg
Hn
Ht
msg
Hn
Hl

## Slide 35: Layers: pros and cons
Why layer?
Reduce complexity
Improve flexibility/innovation
  (Each layer can evolve independently)
Why not layer?
sub-optimal performance
cross-layer information often useful

## Slide 36: End-to-end argument: Intuition
Some application requirements can only be correctly implemented end-to-end
  reliability, security, etc.
End-systems
  Can satisfy the requirement without network’s help
  Will/must do so, since they can’t rely on the network
Notes: Contrary to wisdom of the day!
Talmud

## Slide 37: Implications of the E2E argument
In layered design, the E2E principle provides guidance on which layers are implemented where
Key argument for why IP offers only “best effort” delivery (leading to “dumb network / smart ends”)
  Reliability implemented at the end host (TCP)
  Often credited as key to the Internet’s success

## Slide 38: Architectural Wisdom
Layering
  reduce complexity, increase flexibility
IP as the “narrow waist”
  eases interoperability
“smart ends, dumb network” (E2E argument)
  No application knowledge in network  more general
  Minimal state in the network  more robust to failure

## Slide 39: Topics
Basic concepts (lectures 2,3)
Architecture and principles (lecture 4)
Network layer (lecs. 4-9)
  Concepts: valid routing state, convergence, least-cost paths
  Overall context (inter- and intra-domain routing)
  Routing algorithms that compute least-cost routes (DV, LS)
  IP addressing
  Inter-domain
  Router architecture
Transport (lecs. 9 -12)
  Role of the transport layer
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control: general concepts only

## Slide 40: Forwarding vs. Routing
Forwarding: “data plane”
  Directing one data packet
  Each router using local forwarding table
Routing: “control plane”
  Computing the forwarding tables that guide packets
  Jointly computed by routers using a distributed algorithm

## Slide 41: Routing: basic concepts
Valid routing state
Convergence
Least-cost paths

## Slide 42: “Valid” Routing State
Global forwarding state is “valid” if it produces forwarding decisions that always deliver packets to their destinations
Global routing state is valid if and only if:
    There are no dead ends (other than destination)
    There are no loops
Notes: What could go wrong?

## Slide 43: Convergence Delay
Time to achieve convergence
  E.g., all nodes have the same link-state database
Sources of convergence delay?
  time to detect failure
  time to flood link-state information
  time to re-compute forwarding tables
Performance during convergence period?
  lost packets due to blackholes
  looping packets
  out-of-order packets reaching the destination

## Slide 44: Least-cost path routing
Given: router graph & link costs
Goal: find least-cost path
from each source router
to each destination router
Distance-Vector and Link-State are examples

## Slide 45: “Least Cost” Routes
“Least cost” routes an easy way to avoid loops
  No sensible cost metric is minimized by traversing a loop
Least cost routes are destination-based
  i.e., do not depend on the source
Least-cost paths form a spanning tree

## Slide 46: Topics
Basic concepts (lectures 2,3)
Architecture and principles (lecture 4)
Network layer (lecs. 4-9)
  Concepts: valid routing state, convergence, least-cost paths
  Overall context (inter- and intra-domain routing)
  Routing algorithms that compute least-cost routes (DV, LS)
  IP addressing
  Inter-domain
  Router architecture
Transport (lecs. 9 -12)
  Role of the transport layer
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control: general concepts only

## Slide 47
“Interior Routers”
“Autonomous System (AS)” or “Domain” Region of a network under a single administrative entity
“Border Routers”
An “end-to-end” route

## Slide 48: Internet Routing
Internet Routing works at two levels
Each AS runs an intra-domain routing protocol that establishes routes within its domain
  Intra-domain routes are “least cost”
  e.g., Link State (OSPF) and Distance Vector (RIP)
ASes participate in an inter-domain routing protocol that establishes routes between domains
  Inter-domain routes determined by policy (need not be least-cost)
  e.g., Path Vector (BGP)

## Slide 49: Link State Routing
Every router knows its local “link state”
A router floods its link state to all other routers
Every router learns the entire network graph
Every router locally runs Dijkstra’s to compute its forwarding table
Will not test your ability to solve Dijkstra’s under pressure
But you should know the high level properties of LS
  every node maintains complete topology
  link updates flooded everywhere
  may have loops while nodes have inconsistent topology information

## Slide 50
Distributed algorithm (Bellman-Ford)
All routers run it “together”
  each router runs its own instance
  neighbors exchange and react to each other’s messages
Distance-vector routing
Notes: A distance-vector routing algorithm is a click distributed algorithm,
in the sense that click all routers run it together:
- they exchange messages
- and they keep reacting to each other’s messages.

## Slide 51: Distance Vector Routing
Each router knows the links to its neighbors
  Each router has provisional “least cost” estimate to every other router -- its distance vector (DV)
    E.g.: Router A: “A can get to B with cost 11”
Routers exchange this DV with their neighbors
Routers look over the set of options offered by their neighbors and select the best one
Iterative process converges to set of shortest paths

## Slide 52
y
7
2
cost(x,n) + dn(z)
minn{
}
w
x
u
1
z
for all neighbors n
dx(z) =
Bellman-Ford equation
Notes: ... which is called the Bellman-Ford equation.

## Slide 53: DV: You should understand
How DV works
  what’s in a DV; how nodes process and update DVs
The counting to infinity problem
  why it occurs
Poison Reverse
  when it does/doesn’t fix counting-to-infinity

## Slide 54: Counting-to-Infinity
Cause
  z routes through y, y routes through x (to reach dst)
  y loses connectivity to x
  y decides to route through z (to reach dst)
Can take a very long time to resolve

## Slide 55: Poisoned Reverse
How:
  If z routes to dst through y, z advertises to y that its cost to dst is infinite
  y never decides to route to dst through z
Often avoids the count-to-infinity problem

## Slide 56: Topics
Basic concepts (lectures 2,3)
Architecture and principles (lecture 4)
Network layer (lecs. 4-9)
  Concepts: valid routing state, convergence, least-cost paths
  Overall context (inter- and intra-domain routing)
  Routing algorithms that compute least-cost routes (DV, LS)
  IP addressing
  Inter-domain
  Router architecture
Transport (lecs. 9 -12)
  Role of the transport layer
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control: general concepts only

## Slide 57: Addressing Goal: Scalable Routing
State: Small forwarding tables at routers
Churn: Limited rate of change in routing tables
Ability to aggregate addresses is crucial for both
(one entry to summarize many addresses)

## Slide 58: Hierarchy in IP Addressing
32 bits are partitioned into a prefix and suffix components
Prefix is the network component; suffix is host component
Interdomain routing operates on the network prefix
“slash” notation: 12.34.158.0/23  network with a 23 bit prefix and 29 host addresses
00001100
00100010
10011110
00000101
Network (23 bits)
Host (9 bits)
12
34
158
5

## Slide 59: IP addressing  scalable routing?
Hierarchical address allocation helps routing scalability if allocation matches topological hierarchy
Problem: may not be able to aggregate addresses for “multi-homed” networks

## Slide 60
AT&T a.0.0.0/8
LBL a.b.0.0/16
UCB a.c.0.0/16
ESNet
UCB is “multi-homed” to AT&T and ESNet
  Multi-homed domain  domain has 2 (or more) providers
ESNet must maintain routing entries for both a.*.*.* and a.c.*.*

## Slide 61: IP addressing  scalable routing?
Hierarchical address allocation helps routing scalability if allocation matches topological hierarchy
Problem: may not be able to aggregate addresses for “multi-homed” networks
Two competing forces in scalable routing
  aggregation reduces number of routing entries
  multi-homing increases number of entries

## Slide 62: BGP and Inter-Domain Routing
Destinations are IP prefixes (12.0.0.0/8)
Nodes are Autonomous Systems (ASes)
Links represent both physical connections and business relationships
  customer-provider or peer-to-peer
BGP is the protocol for inter-domain routing

## Slide 63: Topology and policy is shaped by the business relationships between ASes
Three basic kinds of relationships between ASes
  AS A can be AS B’s customer
  AS A can be AS B’s provider
  AS A can be AS B’s peer
Business implications
  Customer pays provider
  Peers don’t pay each other
Notes: Ehy???

## Slide 64: BGP extends DV
With some important differences
  routes selected based on policy, not just shortest path
  path vector (useful to avoid loops)
  Selective route advertisement
  may aggregate routes (aggregating prefixes)

## Slide 65: Policy imposed in how routes are selected and exported
Selection: Which path to use?
  controls whether/how traffic leaves the network
Export: Which path to advertise?
  controls whether/how traffic enters the network
Can reach 128.3/16
blah blah
Route selection
A
P
C
B
Q
Route export
Notes: Arrows: routing messages!

## Slide 66: Typical Export Policy
Destination prefix advertised by… | Export route to…
Customer | Everyone (providers, peers, other customers)
Peer | Customers
Provider | Customers
We’ll refer to these as the “Gao-Rexford” rules
(capture common -- but not required! -- practice!)
You must know this!

## Slide 67: Typical Selection Policy
In decreasing order of priority
  make/save money (send to customer > peer > provider)
  maximize performance (smallest AS path length)
  minimize use of my network bandwidth (“hot potato”)
  …
BGP uses route attributes to implement the above
  ASPATH, LOCAL_PREF, MED, …
You should know the general idea/goal for each attribute; we won’t quiz you on the detailed implementation

## Slide 68: Policy Dictates Route Selection
traffic allowed
traffic not allowed
A
B
C
D
E
F
Q
Pr
Cu
Peer
Peer

## Slide 69: Topics
Basic concepts (lectures 2,3)
Architecture and principles (lecture 4)
Network layer (lecs. 4-9)
  Concepts: valid routing state, convergence, least-cost paths
  Overall context (inter- and intra-domain routing)
  Routing algorithms that compute least-cost routes (DV, LS)
  IP addressing
  Inter-domain
  Router architecture
Transport (lecs. 9 -12)
  Role of the transport layer
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control: general concepts only

## Slide 70: IP Packet Structure
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload
We’ll give you the header format but you should know what each field is and its use/misuse

## Slide 71: IPv4 and IPv6 Header Comparison
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
IPv4
IPv6
Field name kept from IPv4 to IPv6
Fields not kept in IPv6
Name & position changed in IPv6
New field in IPv6

## Slide 72: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect (Switching)
Fabric
Route/Control Processor
Linecards (output)
Processes packets on their way in
Processes packets before they leave
Transfers packets from input to output ports
Input and Output for the same port are on one physical linecard

## Slide 73: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect (Switching)
Fabric
Route/Control Processor
Linecards (output)
(1) Implement IGP and BGP protocols; compute routing tables
(2) Push forwarding tables to the line cards

## Slide 74: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect Fabric
Route/Control Processor
Linecards (output)
Constitutes the data plane
Constitutes the control plane
Notes: Control plane: software. Makes decisions over long time horizons.
Data plane: mostly hardware. A decision for each packet.

## Slide 75: Challenges in Router Design
@ Line cards: destination lookups at high speed
  e.g., find the longest prefix match (LPM) in the table that matches the packet destination address
@ Switch fabric: head-of-line blocking, scheduling the switch fabric at high speed
@ Route processor: complexity/correctness more a problem than performance
You should understand why these challenges arise but we don’t expect you to know how to fix them
  e.g., specifics of scheduling algorithms or LPM lookups

## Slide 76: Topics
Basic concepts (lectures 2,3)
Architecture and principles (lecture 4)
Network layer (lecs. 4-9)
  Concepts: valid routing state, convergence, least-cost paths
  Overall context (inter- and intra-domain routing)
  Routing algorithms that compute least-cost routes (DV, LS)
  IP addressing
  Inter-domain
  Router architecture
Transport (lecs. 9 -12)
  Role of the transport layer
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control: general concepts only

## Slide 77: Role of the Transport Layer
(1) Communication between application processes
  Mux and demux from/to application processes
  Implemented using ports
(2) Provide common end-to-end services for app layer
  Reliable, in-order data delivery
  Well-paced data delivery

## Slide 78: UDP vs. TCP
  Both UDP and TCP provide mux/demux-ing via ports
 | UDP | TCP
Data abstraction | Packets (datagrams) | Stream of bytes of arbitrary length
Service | Best-effort (same as IP) | Reliability In-order delivery Congestion control Flow control
Applications | Video, audio streaming | File transfer, chat

## Slide 79: Reliable Transport: General Concepts
Checksums (for error detection)
Timers (for loss detection)
Acknowledgments (feedback from receiver)
  cumulative: “received everything up to X”
  selective: “received X”
Sequence numbers (detect duplicates, accounting)
Sliding Windows (for efficiency)
You should know:
what these concepts are
why they exist
how TCP uses them

## Slide 80: Things to know about TCP
How TCP achieves reliability
RTT estimation
Connection establishment/teardown
Flow Control
Congestion Control (concepts only)
For each, know how the functionality is implemented and why it is needed

## Slide 81: E.g., RTT Estimation
Why? TCP uses timeouts to retransmit packets
But RTT may vary (significantly!) for different reasons and on different timescales
  due to temporary congestion
  due to long-lived congestion
  due to a change in routing paths
An incorrect RTT estimate might introduce spurious retransmissions or overly long delays
RTT estimators should react to change but not too quickly
  proposed solutions use EWMA, incorporate deviations

## Slide 82: E.g., Reliability
Why? IP is best-effort but many apps. need reliable delivery
  Having TCP take care of it simplifies application development
How
  checksums and timers (for error and loss detection)
  fast retransmit (for faster-than-timeout loss detection)
  cumulative ACKs (feedback from receiver -- what’s lost/what’s not)
  sliding windows (for efficiency)
  buffers at sender (to hold packets while waiting for ACKs)
  buffers at receiver (to reorder packets before delivery to app.)

## Slide 83: E.g., Connection Establishment
Why?
  TCP is a stateful protocol (CWND, buffer space, ISN, etc.)
  Need to initialize connection state at both ends
  Exchange initial sequence numbers
How? Three-way handshake
  Host A sends a SYN to host B
  Host B returns a SYN acknowledgment (SYN ACK)
  Host A sends an ACK (+ data) to acknowledge the SYN ACK
  Hosts exchange proposed Initial Sequence Numbers at each step

## Slide 84: E.g., Flow Control
Why?
  TCP offers a reliable in-order byte stream abstraction
  Hence, TCP at the receiver must buffer a packet until all packets before it (in byte-order) have arrived and the receiving application has consumed available bytes
  Hence receiver advances its window when the receiving application consumes data
  But sender advances its window when new data ACK’d
  Hence, risk the sender might overrun the receiver’s buffers
How? “Advertised Window” field in TCP header
  Receiver advertises the “right hand edge” of its window to sender
  Sender agrees not to exceed this amount

## Slide 85: E.g., Congestion Control
Why?
  Because a sender shouldn’t overload the network itself
  But yet, should make efficient use of available network capacity
  While sharing available capacity fairly with other flows
  And adapting to changes in available capacity
How?
  Dynamically adapts the size of the sending window (don’t worry about the exact algorithms used to do the adaptation)

## Slide 86: Final Questions?
Good luck!